| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | TS-0007 Mca Subscribe Services |
| Source:* | Tim Carey, ALU, timothy.carey@alcatel-lucent.com |
| Contact: | Tim Carey, ALU, timothy.carey@alcatel-lucent.com |
| Date:* | 2014-04-14 |
| Abstract:* | Add services for Data Exchange Services requests across the Mca using the Publish-Subscribe-Notify MEP R01: Modified to use attribute names from TS-0001 as appropriate, received editorial comments from LG R02: Received comments from AT&T |
| Agenda Item:* | TP#10 |
| Work item(s): | TS-0007 WI |
| Document(s) Impacted* | TS-0007 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Update TS for inclusion |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 6	M2M Services

This clause describes the M2M Services provided by the M2M Services Platform.

## 6.1	Introduction

The M2M Services defined in this clause are utilized by the Supporting Services described in the Annexes of this specification.

Figure 6.1-1: oneM2M Services

## 6.2	Service Subscription

The Service Subscription service provides the ability to:

- Validate the service capabilities (e.g., requests, notifications) that go across the Mca reference point by ensuring Supporting Service requested by the issuer is permitted within the context of the M2M Service Subscription

- Assist in authorization of a service capability by returning a role for the requested service capability

- Assist in returning the Broker instance needed to exchange data for publish and subscribe service capabilities.

### 6.2.1	Service Capabilities

#### 6.2.1.3	getBroker

This service capability obtains the Broker instance that will be used to subscribe and publish requests  based on the requested service capability (e.g., publishRequest, subscribeRequest), AE and Resource.

For the publishRequest service capability the AE is the from Originator and the resource is the toResource  representing a leaf node from the publication resource.

For the subscribeRequest service capability the AE is the to Application and the resource is the publication resource.

##### 6.2.1.3.1	Pre-conditions

A correlation between a Service Subscription, from Originator and Broker exist.

##### 6.2.1.3.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| subscriptionId | IN | NO | The M2M Service Subscription Identifier (M2M-Sub-ID) |
| serviceId | IN | NO | The M2M Service Identifier (M2M-Serv-ID) of the service capability |
| to | IN | NO | The identifier of the AE that is to target of the request (M2M-AppInst-ID) |
| broker | OUT | NO | The returned instance of the Broker service associated with the subscription. |
| responseType | OUT | NO | Response types: Service exists for Service Subscription does not exist for Service |

Table 6.2.1.1.2-1 validateBusService Signature

##### 6.2.1.3.3	Post-Conditions

Not Applicable

##### 6.2.1.3.4	Exceptions

Not Applicable

##### 6.2.1.3.5	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.2.1.3.6	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations that are interworked are:

- TBD

Editors note: The oneM2M Resource Interworking will be identified if a M2M Service Subscription operation is identified

##### 6.2.1.3.7	oneM2M Roles Association

Editors note: The oneM2M Roles Association will be identified once Annex G of TS-0001 has identified the roles for the M2M Services

## 6.X	Data Exchange

## 6.X.1	Overview

- The Data Exchange service provides the ability to exchange payloads between AEs across the Mca reference point using supported data exchange patterns. This service utilizes an underyling transport adapter to provide the transportation functions.

- The supported data exchange patterns are:

#### Subscribe-Publish-Notify

#### 6.X.1.1	Subscribe-Publish-Notify Data Exchange

- This data exchange pattern permits AEs to subscribe to publication resources. When an AE publishes data to a specific publication resource, the AEs that have subscribe to the publication resource are notified of the publication by receiving the published data.

#### 6.X.1.1.1	Supporting Rules

A publication resource is an entity that represents the mechanism used by underlying publish and subscribe protocols which represent one or more queues in the underlying protocol. A publication resource in the data exchange service provides capabilities to reference one or more queues in the underlying protocol using a tree mechanism where wildcards are placed to represent all elements of the tree branch or leaf.

##### 6.X.1.1.1.1	Publication Resources

When a AE publishes a payload to a publication resource, the publication resource is evaluated to obtain the leaf node of the tree. The AEs that have subscribed to leaf nodes of the tree receive the message via the notify service capability.

##### 6.X.1.1.1.2	Delivery Policy

As part of the notify service capability the Service Layer attempts to honor the delivery policy of the subscriber and publisher. The delivery policy is the attempt by the Service Layer to provide a reliable delivery of the payload that was published using the mechanisms of the underlying Broker. The reliable delivery of a payload is defined in the deliveryPolicy parameter.

| Attribute | Description |
| --- | --- |
| retryLimit | The number of retries by the Broker to connected subscribers before assuming failure of the notification. |

Table 6.X.1.1.1..2-1 Parameter: deliveryPolicy

##### 6.X.1.1.1.3	Message Retainment Policy

When a message is published, the M2M Service Layer, using the resources of the underlying Broker, attempts to retain messages according to a retainment policy. Retainment of messages permits AEs that are subscribed  to the publication resource but not connected to the underlying Broker to receive messages, upto the retainLimit once the AE connects to the Broker.  The message retainment policy is defined in the retainmentPolicy parameter.

| Attribute | Description |
| --- | --- |
| retainLimit | The maximum number of messages retained by the Broker for a subscriber that is not connected to the underlying Broker. |

Table 6.X.1.1.1..3-1 Parameter: retainmentPolicy

###### 6.X.1.1.1.4	Service Subscription Integration

In order for the Data Exchange Service to take advantage of the underlying transport, there shall be an association between the AE and the identifier of the underlying transport within the context of the Service Subscription.

### 6.X.2	Service Capabilities

#### 6.X.2.1	subscribe

This service capabiltiy provides the ability for AEs to subscribe to receive payloads based on a publication resource.

As part of the subsciption, the subscribing AE can provide a deliveryPolicy to enhance the robustness of the notification to AEs that have subscribed to the publication resource identified in the request.

###### 6.X.2.1.1	Pre-conditions

The pre-conditions for MCA Received Requests are met.

A correlation between a Service Subscription, from Orginator and Broker exist.

###### 6.X.2.1.2	Signature - subscribe

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | See Table A.2.1.1.2-1 |
| subscriptionId | IN | NO | See Table A.2.1.1.2-1 |
| from | IN | NO | See Table A.2.1.1.2-1 |
| publicationResource | IN | NO | The publication resource. See 6.X.1.1.1.1 |
| deliveryPolicy | IN | YES | The delivery policy when notifying the subscriber. See 6.X.1.1.1.2 |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Exception: Request may not have been completed |

Table 6.X.2.1.2-1 Data Exchange Service – subscribe capability

6.X.2.1.3	Service Interactions

The interactions of  service capabilities required for this service capability:

- Issue the subscribe request to the Supporting Service to validate the request and obtain the Broker instance for the transfer of the payload.

- Issue the request to the broker to subscribe the from Originator for the publicationResource

- Issue the subscribe complete subscription request to the Supporting Service

Table 6.X.2.1.2-1 Data Exchange Service – subscribe capability

##### 6.X.2.1.4	Post-Conditions

Not Applicable

##### 6.X.2.1.5	Exceptions

Not Applicable

##### 6.X.2.1.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.X.2.1.7	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations that are interworked are:

- TBD

Editors note: The oneM2M Resource Interworking will be identified if a M2M Service Subscription operation is identified

##### 6.X.2.1.8	oneM2M Roles Association

Editors note: The oneM2M Roles Association will be identified once Annex G of TS-0001 has identified the roles for the M2M Services

#### 6.X.2.2	publish

This service capabiltiy provides the ability for AEs to publish payloads to a leaf node of a publication resource.

As part of the publication, the publishing AE can provide delivery and retainment policies to enhance the robustness of the publication to AEs that have subscribed to the Resource identified in the request.

##### 6.X.2.2.1	Pre-conditions

The pre-conditions for MCA Received Requests are met.

A correlation between a Service Subscription, from Originator and Broker exist.

##### 6.X.2.2.2	Signature – publish

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | See Table A.2.1.1.2-1 |
| subscriptionId | IN | NO | See Table A.2.1.1.2-1 |
| from | IN | NO | See Table A.2.1.1.2-1 |
| toResource | IN | NO | The leaf node of a publication resource. See 6.X.1.1.1.1 |
| deliveryPolicy | IN | YES | The delivery policy when notifying the subscriber. See 6.X.1.1.1.2 |
| retainmentPolicy | IN | YES | The retainment policy for unconnected subscribers. See 6.X.1.1.1.3 |
| payload | IN | NO | The payload to published. |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Exception: Request may not have been completed |

Table 6.X.2.2.2-1 Data Exchange Service – publish capability

##### 6.X.2.2.3	Service Interactions

The interactions of  service capabilities required for this service capability:

- Issue the publish request to the Supporting Service to validate the request

- Issue the request to the broker to publish the payload from the from Originator to the toResource

- Issue the complete publication request to the Supporting Service

Table 6.X.2.2.2-1 Data Exchange Service –publish (In-Out) capability

##### 6.X.2.2.4	Post-Conditions

Not Applicable

##### 6.X.2.2.5	Exceptions

Not Applicable

##### 6.X.2.2.6	Policies for Use

Message Exchange Patterns: In-Out, In-Only

The In-Only message exchange pattern would return a transport layer acknowledgement if supported by the underlying transport layer protocol. Response types or Exceptions are not returned in this message exchange pattern.

Transaction Pattern: Participation allowed

##### 6.X.2.2.7	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations that are interworked are:

- TBD

Editors note: The oneM2M Resource Interworking will be identified if a M2M Service Subscription operation is identified

##### 6.X.2.2.8	oneM2M Roles Association

Editors note: The oneM2M Roles Association will be identified once Annex G of TS-0001 has identified the roles for the M2M Services

#### 6.X.2.3	notify

This service capabiltiy provides the ability to notify AEs that have subscribed to the publication resource identified in the request.

##### 6.X.2.3.1	Pre-conditions

A correlation between a Service Subscription, to Application and Broker exist.

##### 6.X.2.3.2	Signature – notify

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | See Table A.2.1.1.2-1 |
| subscriptionId | IN | NO | See Table A.2.1.1.2-1 |
| to | IN | NO | See Table A.2.1.1.2-1 |
| fromResource | IN | NO | The leaf node of a publication resource. See 6.X.1.1.1.1 |
| deliveryPolicy | IN | YES | The delivery policy when notifying the subscriber. See 6.X.1.1.1.2 |
| payload | IN | NO | The Payload of the message to notify to the AE |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Exception: Request may not have been completed |

Table 6.X.2.3.2-1 Data Exchange Service – notify capability

##### 6.X.2.3.3	Post-Conditions

Not Applicable

##### 6.X.2.3.4	Exceptions

Not Applicable

##### 6.X.2.3.5	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.X.2.3.6	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations that are interworked are:

- TBD

Editors note: The oneM2M Resource Interworking will be identified if a M2M Service Subscription operation is identified

##### 6.X.2.3.7	oneM2M Roles Association

Editors note: The oneM2M Roles Association will be identified once Annex G of TS-0001 has identified the roles for the M2M Services

## 6.4	Event Collection

- The Event Collection service provides the capability to record events for accounting purposes.

- Editors Note: Event Collection for accounting purposes is FFS.

## 6.5	Broker

## 6.5.1	Overview

The Broker service provides the ability to adapt the Publish-Subscribe-Notify data exchange patterns to the underlying transport protocol and deployment configuration.

The Broker maintains the subscriptions to the publication resources

### 6.5.2	Service Capabilities

#### 6.5.2.1	subscribe

This service capabiltiy provides the ability for AEs to subscribe to receive payloads based on a publication resource.

As part of the publication, the publishing AE can provide a deliveryPolicy to enhance the robustness of the notification to AEs that have subscribed to the Resource identified in the request.

##### 6.5.2.1.1	Pre-conditions

A correlation between a Service Subscription, from Originator and Broker exist.

##### 6.5.2.1.2	Signature – subscribe

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | See Table A.2.1.1.2-1 |
| subscriptionId | IN | NO | See Table A.2.1.1.2-1 |
| from | IN | NO | See Table A.2.1.1.2-1 |
| publicationResource | IN | NO | The publication resource. See 6.X.1.1.1.1 |
| deliveryPolicy | IN | YES | The delivery policy when notifying the subscriber. See 6.X.1.1.1.2 |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Exception: Request may not have been completed |

Table 6.X.2.2.2-1 Broker – subscribe capability

##### 6.5.2.1.3	Post-Conditions

Not Applicable

##### 6.5.2.1.4	Exceptions

Not Applicable

##### 6.5.2.1.5	Policies for Use

Message Exchange Patterns: In-Out

The In-Only message exchange pattern would return a transport layer acknowledgement if supported by the underlying Transaction Pattern: Participation allowed

#### 6.5.2.2	publish

This service capabiltiy provides the ability for AEs to publish payloads to a leaf node of a publication resource.

As part of the publication, the publishing AE can provide delivery and retainment policies to enhance the robustness of the publication to AEs that have subscribed to the Resource identified in the request.

##### 6.5.2.2.1	Pre-conditions

A correlation between a Service Subscription, from Originator and Broker exist.

##### 6.5.2.2.2	SIgnature – publish

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | See Table A.2.1.1.2-1 |
| subscriptionId | IN | NO | See Table A.2.1.1.2-1 |
| from | IN | NO | See Table A.2.1.1.2-1 |
| toResource | IN | NO | The leaf node of a publication resource. See 6.X.1.1.1.1 |
| deliveryPolicy | IN | YES | The delivery policy when notifying the subscriber. See 6.X.1.1.1.2 |
| retainmentPolicy | IN | YES | The retainment policy for unconnected subscribers. See 6.X.1.1.1.3 |
| payload | IN | NO | Payload to be published. |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Exception: Request may not have been completed |

Table 6.X.2.2.2-1 Broker – publish capability

##### 6.5.2.3.3	Post-Conditions

Not Applicable

##### 6.5.2.3.4	Exceptions

Not Applicable

##### 6.5.2.3.5	Policies for Use

Message Exchange Patterns: In-Out

The In-Only message exchange pattern would return a transport layer acknowledgement if supported by the underlying Transaction Pattern: Participation allowed

##### 6.5.2.3.6	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations that are interworked are:

- TBD

Editors note: The oneM2M Resource Interworking will be identified if a M2M Service Subscription operation is identified

##### 6.5.2.3.7	oneM2M Roles Association

Editors note: The oneM2M Roles Association will be identified once Annex G of TS-0001 has identified the roles for the M2M Services

#### 6.5.2.3	notify

This service capabiltiy provides the ability for the Broker to notify AEs that have subscribed to the publication resource identified in the request.

##### 6.5.2.3.1	Pre-conditions

The Broker maintains the AEs (to Application, clientId) that have subscribed to publicationResources.

The Broker maintains the Service Subscription (subscriptionId) for AE subscriptions to publicationResources.

A correlation between a Service Subscription, to Application and Broker exist.

##### 6.5.2.3.2	Signature – notify

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| payload | IN | NO | See Table A.2.1.1.2-1 |
| fromResource | IN | NO | The leaf node of a publication resource. See 6.X.1.1.1.1 |
| deliveryPolicy | IN | YES | The delivery policy when notifying the subscriber. See 6.X.1.1.1.2 |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Issuer does not have a Broker for the requested toResource Issuer has requested an invalid deliveryPolicy Exception: Request may not have been completed |

Table 6.X.2.3.2-1 Broker – notify capability

##### 6.5.2.3.3	Service Interactions

For each AE subscribed to the resource perform the interactions of  service capabilities required for this service capability:

- Issue the notify request to the Supporting Service to validate the request

- Issue the request to the SE: Data Exchange

- Issue the complete publication request to the Supporting Service

Table 6.5.2.3.2-1 Broker –notify (In-Out) capability

##### 6.5.2.3.4	Post-Conditions

Not Applicable

##### 6.5.2.3.5	Exceptions

Not Applicable

##### 6.5.2.3.6	Policies for Use

Message Exchange Patterns: In-Out, In-Only

The In-Only message exchange pattern would return a transport layer acknowledgement if supported by the underlying transport layer protocol. Response types or Exceptions are not returned in this message exchange pattern.

Transaction Pattern: Participation allowed

##### 6.5.2.3.7	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations that are interworked are:

- TBD

Editors note: The oneM2M Resource Interworking will be identified if a M2M Service Subscription operation is identified

##### 6.5.2.3.8	oneM2M Roles Association

Editors note: The oneM2M Roles Association will be identified once Annex G of TS-0001 has identified the roles for the M2M Services

# 7	M2M Service Components

This clause describes the M2M Service Components provided by the M2M Services Platform.

## 7.1.1	Service Component Interaction Cross Reference

Table 7.1-1 Service Component Cross Reference

## 7.5	Transport Adapter (TRA)

The TRA component provides Services are used to integrate or adapt Data Exchange requests to the underlying Data Exchange transport (e.g., XMPP or MQTT Broker).

## 7.5.1	TRA to Service Cross Reference

Broker: All Service Capabilities

SE:Data Exchange: notify

## 7.6	Accounting (ACC)

The ACC Component provides Services that are record events necessary to charge for the Services provided to AEs.

## 7.6.1	Accounting to Service Cross Reference

Event Collection: All Service Capabilities

## 7.6	Service Exposure (SE)

The SE Component acts as the primary interface for AEs to interact with the M2M Service Layer across the Mca reference point.

## 7.6.1	Service Exposure to Service Cross Reference

SE Data Exchange: All Service Capabilities

Service Subscription: getBroker

Broker: publish, subscribe

# Annex B (Informative): Data Exchange Services

## B.1	Overview

This annex illustrates the usage of the services for  requests to exchange data from AEs across the Mca Reference Point.

### B.2	Supporting Services

### B.2.1	Subscribe-Publish-Notify Message Exchange

This service provides the capability to exchange data using the publish and subscribe message patterns where AEs:

- Request to receive payloads from a publication resource by subscribing to the publication resource.

- Request to publish a payload to a resource.

- B.2.1.2	Service Capabilities

#### B.2.1.2.1	subscribeRequest

#### This service capabiltiy provides the ability to validate a subscription request from an AE.

##### B.2.1.2.1.1	Pre-conditions

The pre-conditions for MCA Received Requests are met.

A correlation between a Service Subscription, from Originator and Broker exist.

##### B.2.1.2.1.2	Signature - subscribeRequest

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | See Table A.2.1.1.2-1 |
| subscriptionId | IN | NO | See Table A.2.1.1.2-1 |
| from | IN | NO | See Table A.2.1.1.2-1 |
| publicationResource | IN | NO | The publication resource. See 6.X.1.1.1.1 |
| deliveryPolicy | IN | YES | The delivery policy when notifying the subscriber. See 6.X.1.1.1.2 |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Issuer does not have a Broker for the requested Resource Delivery policy not supported by the underlying Broker |

Table B.2.1.2.1.2-1 Data Exchange Service – subscribeRequest capability

##### B.2.1.2.1.3	Service Interactions

The interactions of  service capabilities required for this service capability:

- Determine the Broker to be used for the from Originator and publicationResource

- Perform the Common Request Services for requests across the Mca reference point

- Validate the deliveryPolicy

Figure B.2.1.2.1.3-1 subscribeRequest and subscribeComplete Interaction Diagram

##### B.2.1.2.1.4	Post-Conditions

Success case: The request  is permitted.

Failure case: The request  is not permitted and a response type is transmitted back the from Originator.

##### B.2.1.2.1.5	Exceptions

No unique exceptions for this service capability.

Consumed services may throw exceptions which are forwarded by this service capability.

##### B.2.1.2.1.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern:  Participation allowed

Maximum Response: 250ms

##### B.2.1.2.2	subscribeComplete

This service capabiltiy provides the ability to complete the actions required once the subscription request has been completed in the Broker.

###### B.2.1.2.2.1	Pre-conditions

No unique pre-conditions for this service capability.

###### B.2.1.2.2.2	Signature - subscribeComplete

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | See Table A.2.1.1.2-1 |
| subscriptionId | IN | NO | See Table A.2.1.1.2-1 |
| from | IN | NO | See Table A.2.1.1.2-1 |
| publicationResource | IN | NO | The publication resource. See 6.X.1.1.1.1 |
| deliveryPolicy | IN | YES | The delivery policy when notifying the subscriber. See 6.X.1.1.1.2 |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Exception: Request may not have been completed |

Table B.2.1.2.2.2-1 Data Exchange Service – subscribeComplete capability

###### B.2.1.2.2.3	Service Interactions

The interactions of  service capabilities required for this service capability as shown in Figure B.2.1.2.1.3-1:

- Upon a successful subscribe by the Broker, record the event for accounting purposes

###### B.2.1.2.2.4	Post-Conditions

Success case: The request  is permitted.

Failure case: The request  is not permitted and a  response type is transmitted back the from Originator.

###### B.2.1.2.2.5	Exceptions

No unique exceptions for this service capability.

Consumed services may throw exceptions which are forwarded by this service capability.

###### B.2.1.2.2.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern:  Participation allowed

Maximum Response: 50ms

#### B.2.1.2.3	publishRequest

#### This service capabiltiy provides the ability to validate a publication request from an AE..

#### As part of the publication, the publishing AE can provide delivery and retainment policies to enhance the robustness of the publication to AEs that have subscribed to the Resource identified in the request.

##### B.2.1.2.3.1	Pre-conditions

The pre-conditions for MCA Received Requests are met.

A correlation between a Service Subscription, from Originator and Broker exist.

##### B.2.1.2.3.2	Signature - publishRequest

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | See Table A.2.1.1.2-1 |
| subscriptionId | IN | NO | See Table A.2.1.1.2-1 |
| from | IN | NO | See Table A.2.1.1.2-1 |
| toResource | IN | NO | The leaf node of a publication resource. See 6.X.1.1.1.1 |
| deliveryPolicy | IN | YES | The delivery policy when notifying the subscriber. See 6.X.1.1.1.2 |
| retainmentPolicy | IN | YES | The retainment policy for unconnected subscribers. See 6.X.1.1.1.3 |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Issuer does not have a Broker for the requested toResource Issuer has requested an invalid deliveryPolicy Issuer has requested an invalid retainmentPolicy Delivery policy not supported by the underlying Broker Retainment policy not supported by the underlying Broker Exception: Request may not have been completed |

Table B.2.1.2.3.2-1 Data Exchange Service – publishRequest capability

##### B.2.1.2.3.3	Service Interactions

The interactions of  service capabilities required for this service capability:

- Determine the Broker to be used for the from Originator and toResource

- Perform the Common Request Services for requests across the Mca reference point

- Validate the deliveryPolicy and retainmentPolicy for the Broker

- Upon a successful publication to the Broker, record the event for accounting purposes

Figure B.2.1.2.3.3-1 publishRequest and publishComplete Interaction Diagram

##### B.2.1.2.3.4	Post-Conditions

Success case: The request  is permitted.

Failure case: The request  is not permitted and a response type is transmitted back the  from Originator.

##### B.2.1.2.3.5	Exceptions

No unique exceptions for this service capability.

Consumed services may throw exceptions which are forwarded by this service capability.

##### B.2.1.2.3.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

Maximum Response: 300ms

##### B.2.1.2.4	publishComplete

This service capabiltiy provides the ability to complete the actions required once the publication request has been completed in the Broker.

###### B.2.1.2.4.1	Pre-conditions

No unique pre-conditions for this service capability.

###### B.2.1.2.4.2	Signature - publishComplete

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | See Table A.2.1.1.2-1 |
| subscriptionId | IN | NO | See Table A.2.1.1.2-1 |
| from | IN | NO | See Table A.2.1.1.2-1 |
| toResource | IN | NO | The leaf node of a publication resource. See 6.X.1.1.1.1 |
| deliveryPolicy | IN | YES | The delivery policy when notifying the subscriber. See 6.X.1.1.1.2 |
| retainmentPolicy | IN | YES | The retainment policy for unconnected subscribers. See 6.X.1.1.1.3 |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Exception: Request may not have been completed |

Table B.2.1.2.3.2-1 Data Exchange Service – pubishComplete capability

###### B.2.1.2.4.3	Service Interactions

The interactions of  service capabilities required for this service capability as shown in Figure B.2.1.2.1.3-1:

- Upon a successful subscribe by the Broker, record the event for accounting purposes

###### B.2.1.2.4.4	Post-Conditions

Success case: The request  is permitted.

Failure case: The request  is not permitted and a  response type is transmitted back the from Originator.

###### B.2.1.2.4.5	Exceptions

No unique exceptions for this service capability.

Consumed services may throw exceptions which are forwarded by this service capability.

###### B.2.1.2.4.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern:  Participation allowed

Maximum Response: 50ms

##### B.2.1.2.5	notifyRequest

This service capabiltiy provides the ability to validate a notification request to an AE.

As part of the notification, delivery policy that is requested to be used is validated and adjusted if necessary.

###### B.2.1.2.5.1	Pre-conditions

A correlation between a Service Subscription, to Application and Broker exist.

The pre-conditions for MCA Received Requests are met.

###### B.2.1.2.5.2	Signature - notifyRequest

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | See Table A.2.1.1.2-1 |
| subscriptionId | IN | NO | See Table A.2.1.1.2-1 |
| to | IN | NO | See Table A.2.1.1.2-1 |
| fromResource | IN | NO | The leaf node of a publication resource. See 6.X.1.1.1.1 |
| deliveryPolicy | IN-OUT | YES | The delivery policy when notifying the subscriber. See 6.X.1.1.1.2 |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Issuer does not have a Broker for the requested toResource Issuer has requested an invalid deliveryPolicy Exception: Request may not have been completed |

Table B.2.1.2.5.2-1 Data Exchange Service – notifyRequest capability

###### B.2.1.2.5.3	Service Interactions

The interactions of  service capabilities required for this service capability:

- Perform the Common Request Services for requests across the Mca reference point

- Validate that deliveryPolicy requested by the Broker is allowed for the to Application and subscriptionId

Figure B.2.1.2.5.3-1 notifyRequest and notifyComplete Interaction Diagram

###### B.2.1.2.5.4	Post-Conditions

Success case: The request  is permitted.

Failure case: The request  is not permitted and a response type is transmitted back the from Originator.

###### B.2.1.2.5.5	Exceptions

No unique exceptions for this service capability.

Consumed services may throw exceptions which are forwarded by this service capability.

###### B.2.1.2.5.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

Maximum Response: 300ms

##### B.2.1.2.6	notifyComplete

This service capabiltiy provides the ability to complete the actions required once the notification request has been completed in the Data Exchange service.

###### B.2.1.2.6.1	Pre-conditions

No unique pre-conditions for this service capability.

###### B.2.1.2.6.2	Signature - notifyComplete

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | See Table A.2.1.1.2-1 |
| subscriptionId | IN | NO | See Table A.2.1.1.2-1 |
| to | IN | NO | See Table A.2.1.1.2-1 |
| fromResource | IN | NO | The leaf node of a publication resource. See 6.X.1.1.1.1 |
| deliveryPolicy | IN | YES | The delivery policy when notifying the subscriber. See 6.X.1.1.1.2 |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Exception: Request may not have been completed |

Table B.2.1.2.63.2-1 Data Exchange Service – pubishComplete capability

###### B.2.1.2.6.X	Service Interactions

The interactions of  service capabilities required for this service capability as shown in Figure B.2.1.2.5.3-1:

- Upon a successful notification by the Data Exchange, record the event for accounting purposes

###### B.2.1.2.6.4	Post-Conditions

Success case: The request  is permitted.

Failure case: The request  is not permitted and a  response type is transmitted back the from Originator.

###### B.2.1.2.6.5	Exceptions

No unique exceptions for this service capability.

Consumed services may throw exceptions which are forwarded by this service capability.

###### B.2.1.2.6.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern:  Participation allowed

Maximum Response: 50ms