| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Huawei Technologies |
| Format:* | TP#10 |
| Date:* | <2014-04-10> |
| Contact:* | Qi Yu, Huawei Technologies, yuqi@huawei.com |
| Reason for Change/s:* | This contribution proposes to add the information flows for <instance > resource at section 10.2. R01: Editorial change. R02: Update section 9.6.7 R03: Clarify the relation between the container and instance R04: Upate section 9.6.7 according to the comments. R05: Modify the descrition according to comments. R06: Use contentInstance instead of instance. Delete the chang 1 since it has reflected at the TS0001 v0.6.1. |
| CR against: Release* | Release 1.0.0 |
| CR against: TS/TR* | TS-0001-Functional_Architecture-V0_4_3 |
| Clauses/Sub Clauses* | Section 10.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

# The <instance> resource is defined at section 9.6.7 . However there are no related information flows at section 10.2. This CR proposes to add Create, Retrieve and Delete procedures for <instance> resource and update the related  resource.

### -----------------------Start of change 2-------------------------------------------

## 10.2	Resource Type-Specific Procedures

### 10.2.X <contentInstance> Resource

#### 10.2.X.1 Introduction

This clause describes the management procedures for the <contentInstance> resource. Since<contentInstance> resource is immutable once created, there is no procedure for updating.

10.2.X.2 <contentInstance> CREATE

This flow is used for creating a <contentInstance> resource.

Originator: the Originator may be an Application Entity or a CSE.

Receiver: Creation shall be allowed if the Originator is authorised to create a child resource according to the access control policiesdefined for the parent <container> resource. If the newly created <contentInstance>  resource violates any of the policies defined in the parent <container> resource (e.g. maxNrOfInstances or maxByteSize), then the oldest <contentInstance> resources shall be removed from the <container>  to enable the creation of the new contentInstance

Then the Receiver shall change the "latest"attribute of  the <container> resource to refer to the newly created <contentInstance> resource.

# Table 10.2.X.2-1: <contentInstance> CREATE

| CREATE: Description |
| --- |
| Pre-Conditions | The Originating AE or CSE has to be successfully authenticated and access to the Receiver has been granted. |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the table with the specific details for the following attributes from section 9.6.7 are mandatory for the request: fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <container> resource where the <contentInstance > resource is intended to be created, cn: The resource content shall provide the information as defined in section 9.6.7. The following attributes from section 9.6.7 are mandatory for the Request: “contentSize” “content” |
| Local processing on Hosting CSE | No change from the basic procedure (clause 10.1.1) |
| Information on Response message | All parameters defined in Table 8.1.5-1 are applicable as indicated in the table with the specific details for: cn: URI of the created <contentInstance> resource according to section 10.1.1. |
| Post-Conditions | None |
| Exceptions | All exceptions described in the basic procedures (section 10.1.1) are applicable. |

10.2.X.3 <contentInstance> RETRIEVE

This flow is used for retrieving the attributes of a <contentInstance> resource.

Originator: the Originator may be an Application Entity or a CSE.

Receiver: Once the Originator has been successfully authenticated and access to the Receiver has been granted (as described in section 11.3.4), the Receiver shall retrieve the <contentInstance> resource.

# Table 10.2.x.3-1: <contentInstance> RETRIEVE

| RETRIEVE: Description |
| --- |
| Pre-Conditions | The targeted <contentInstance> has been created. |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the Table with the sepcific details for: cn: void |
| Local processing on Hosting CSE | No change from the basic procedure (clause 10.1.2) |
| Information on Response message | All parameters defined in Table 8.1.5-1 are applicable as indicated in the Table with the specific details for: cn: attributes of the <contentInstance> resource as defined in seciton 9.6.7 |
| Post-Conditions | None |
| Exceptions | All exceptions described in the basic procedure (section 10.1.2) are applicable. |

#### 10.2.X.4 <contentInstance> DELETE

This flow is used for deleting a <contentInstance> resource residing under a <container> resource.

Originator: the Originator may be an Application Entity or a CSE.

Receiver: Once the Originator has been successfully authenticated and access to the Receiver has been granted (as described in section 11.3.4), the Receiver shall delete the <contentInstance> and update the "latest"attribute of  the parent <container> resource.

# Table 10.2.x.4-1: <contentInstance> DELETE

| DELETE: Description |
| --- |
| Pre-Conditions | The targeted <contentInstance> has been created. |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicated in the table. |
| Local processing on Hosting CSE | No change from the basic procedure (clause 10.1.4). |
| Information on Response message | No change from the basic procedure (clause 10.1.4) |
| Post-Conditions | None |
| Exceptions | All exceptions described in the basic procedure (section 10.1.4) are applicable. |

### -----------------------End of change 2---------------------------------------------