| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Heedong Choi, LG Electronics, heedong.choi@lge.com |
| Format:* | ARC |
| Date:* | 2014-05-26 |
| Contact:* | Heedong Choi, LG Electronics, heedong.choi@lge.com |
| Reason for Change/s:* | To update the <schedule> resource due to the missing relationship |
| CR against: Release* | Pre-release |
| CR against: TS/TR* | TS-0001 v0.6.1 |
| Clauses/Sub Clauses* | 9.6.3 and 9.6.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or (missing) functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

As described in the clause 9.6.9 Resource Type schedule, the <schedule> resource contains scheduling information. In the current ARC TS 0.6.1, The <schedule> resource may be located as a child of:

- <remoteCSE> type resource, usage is to indicate the time periods when the entities of a node are reachable.

- <subscription> type resource (named notificationSchedule), usage is to indicate the time periods during which the subscribers may be notified.

Because the current ARC TS doesn’t have any <schedule> resources related to the Originator, the Originator cannot obtain the Originator’s schedule information such as a node and applications. However, the schedule information of the Originator may be need according its usage.

Also, we have recently agreed the following points in MAS and ARC WG (if I remember correctly):

- <schedule> resource is out from the <node> resource.

- <schedule> resource is a child resource of <CSEBase>, <AE> and <remoteCSE> according its usage.

Althoug the <schedule> resource had been deleted under the <node> resource, the <schedule> resource does not exist under the <CSEBase> and <AE> in the current ARC TS 0.6.1.

So, this contribution proposes to add the <schedule> resource under the <CSEBase> and <AE> resources.

## -----------------------Start of change 1-------------------------------------------

### 9.6.3	Resource Type CSEBase

A <CSEBase> resource shall represent a CSE. This <CSEBase> resource shall be the root for all the resources that are residing on the CSE.

Figure 9.6.3-1: Structure of <CSEBase> resource

[9.6.3.a0] Editor's Note; The picture above needs to be updated as per the new structure of CSEBase resource.

The <CSEBase> resource shall contain the child resources in Table 9.6.3-1.

Table 9.6.3-1: Child resources of <CSEBase> resource

| Child Resource Name of <CSEBase> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <remoteCSE> | 0..n | See clause 9.6.4 |
| [variable] | <node> | 0..n | See clause 9.6.18 |
| [variable] | <AE> | 0..n | See clause 9.6.5 |
| [variable] | <container> | 0..n | See clause 9.6.6 |
| [variable] | <group> | 0..n | See clause 9.6.13 |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |
| [variable] | <mgmtCmd> | 0..n | See clause 9.6.16 |
| [variable] | <locationPolicy> | 0..n | See clause 9.6.10 |
| [variable] | <statsConfig> | 0..n | See clause 9.6.22 |
| [variable] | <statsCollect> | 0..n | See clause 9.6.24 |
| [variable] | <schedule> | 0..n | See clause 9.6.9 |

The <CSEBase> resource shall contain the attributes described in Table 9.6.3-2.

Table 9.6.3-2: Attributes of <CSEBase> resource

| Attribute Name of <CSEBase> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 | RW | See clause 9.6.1 where this common attribute is described. |
| labels | 0..1 | RW | See clause 9.6.1 where this common attribute is described. |
| cseType | 1 | WO | Indicates the type of CSE node represented by the created resource. |
| CSE-ID | 1 | WO | The globally unique CSE identifier. |
| supportedResourceType | 1 | RO | List of the resource types which are supported in CSE. this attribute contains subset of resource types listed in clause 9.2 |
| pointOfAccess | 0..n | RW | Represents the list of physical addresses to be used by remote CSEs to connect to this CSE (e.g., IP address, FQDN). This attribute is used to announce its value to remote CSEs. |
| nodeLink | 0..1 | RO | A reference (URI) of a <node> resource that stores the node specific information. |
| Trigger-Recipient-ID | 0..1 | RW | See clause 7.1.10 where this attribute is described. |
| notificationCongestionPolicy | 0..1 | RO | This attribute applies to CSEs generating subscription notifications. It specifies the rule which is applied when the storage of notifications for each subscriber (an AE or CSE) reaches the maximum storage limit for notifications for that subscriber. E.g., Delete stored notifications of lower notificationStoragePriority to make space for new notifications of higher notificationStoragePriority, or delete stored notifications of older creationTime to make space for new notifications when all notifications are of the same notificationStoragePriority. |

## -----------------------End of change 1-------------------------------------------

## -----------------------Start of change 2-------------------------------------------

### 9.6.5	Resource Type AE

The <AE> resource represents information about an Application Entity known to a given Common Services Entity.

Figure 9.6.5-1: Structure of <AE> resource

[9.6.5.a]  Editor's Note: To update the picture to include "announceTo" and "announcedAttribute" attribute.

[9.6.5a1] Editor's Note: The picture above needs to be updated as per the new strucutre of AE resource.

The <AE> resource shall contain the child resources in Table 9.6.5-1.

Table 9.6.5-1: Child resources of <AE> resource

| Child Resource Name of <AE> | Child Resource Type | Multiplicity | Description | <AEAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| [variable] | <container> | 0..n | See clause 9.6.6 | <container> <containerAnnc> |
| [variable] | <group> | 0..n | See clause 9.6.13 | <group> <groupAnnc> |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 | <accessControlPolicy> <accessControlPolicyAnnc> |
| [variable] | <pollingChannel> | 0..n | See clause 9.6.21. When the Registrar CSE of this AE is request-unreachable, the AE should create this <pollingChannel> resource and perform long polling. | <pollingChannel> |
| [variable] | <schedule> | 0..n | See clause 9.6.9 | <scheduleAnnc> |

The <AE> resource shall contain the attributes described in Table 9.6.5-2.

Table 9.6.5-2: Attributes of <AE> resource

| Attribute Name of <AE> | Multiplicity | RW/ RO/ WO | Description | <AEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described. | NA |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. | NA |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. | MA |
| accessControlPolicyIDs | 1 | RW | See clause 9.6.1 where this common attribute is described. | MA |
| creationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. | NA |
| labels | 0..1 | RO | See clause 9.6.1 where this common attribute is described. | MA |
| announceTo | 1 | RW | See clause 9.6.1 where this common attribute is described. | NA |
| announcedAttribute | 1 | RW | See clause 9.6.1 where this common attribute is described. | NA |
| name | 1 | RO | The (usually human readable) name of the application, as declared by the application developer (e.g., "HeatingMonitoring") | OA |
| App-ID | 1 | RO | Application Identifier | OA |
| AE-ID | 1 | RO | The identifier of the Application Entity (see clause 7.1.2). | OA |
| pointOfAccess | 0..n | RW | The list of addresses for communicating with the registered Application Entity over Mca reference point via the transport services provided by Underlying Network (e.g., IP address, FQDN, URI). This attribute shall be accessible only by the AE and the hosting CSE. | OA |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that is managed and understood by the AE; to be passed to the AE. | OA |
| nodeLink | 0..1 | RO | A reference (URI) of a <node> resource that stores the node specific information. | OA |

## -----------------------End of change 2-------------------------------------------

## -----------------------Start of change 3-------------------------------------------

### 9.6	Resource Types

Table 9.6-1 introduces the defined normal and virtual resource types and their related child or parent resource types. Details of each resource type follow in the remainder of this clause.

Table 9.6-1 lists the supported <resourceTypes>. An addition of suffix "Annc" to such <resourceTypes> indicates the associated announced resource type.

Table 9.6-1 Resource Summary

| Resource Type | Short Description | Child Resource Types | Parent Resource Types | Clause |
| --- | --- | --- | --- | --- |
| accessControlPolicy | Stores a representation of privileges. It is associated with resources that shall be accessible to entities external to the hosting CSE. It controls "who" is allowed to do "what" and the context in which it can be used for accessing the resources. . | subscription | AE, remoteCSE, CSEBase | 9.6.2 |
| contentInstance | Represents a data instance in the container resource. | subscription | container | 9.6.7 |
| AE | Stores information about the AE. It is created as a result of successful registration of an AE with the registrar CSE. | subscription, container, group, accessControlPolicy, mgmtObj, commCapabilities, pollingChannel, schedule | remoteCSE, CSEBase | 9.6.5 |
| cmdhBuffer | Defines CMDH buffer usage limits | subscription | cmdhPolicy | D.12.7 |
| cmdhDefaults | Defines CMDH default values | cmdhDefEcValue, cmdhEcDefParamValues subscription | cmdhPolicy | D.12.1 |
| cmdhEcDefParamValues | Represent a specific set of default values for the CMDH related parameters | subscription | cmdhDefaults | D.12.3 |
| cmdhDefEcValue | Defines a value for the ec (event category) parameter of an incoming request when it is not defined. | subscription | cmdhDefaults | D.12.2 |
| cmdhLimits | Defines limits for CMDH related parameter values | subscription | cmdhPolicy | D.12.4 |
| cmdhNetworkAccessRules | Defines rules for the usage of underlying networks | cmdhNwAccessRule subscription | cmdhPolicy | D.12.5 |
| cmdhNwAccessRule | Defines a rule for the usage of underlying networks | schedule subscription | cmdhNetworkAccessRules | D.12.6 |
| cmdhPolicy | A set of rules defining which CMDH parameters will be used by default | cmdhDefaults, cmdhLimits, cmdhNetworkAccessRules, cmdhBuffer subscription | None | D.12 |
| container | Shares data instances among entities. Used as a mediator that takes care of buffering the data to exchange "data" between AEs and/or CSEs. The exchange of data between AEs (e.g., an AE on a Node in a field domain and the peer-AE on the infrastructure domain) is abstracted from the need to set up direct connections and allows for scenarios where both entities in the exchange do not have the same reachability schedule. | container, contentInstance, subscription, | application, container, remoteCSE, CSEBase | 9.6.6 |
| CSEBase | The structural root for all the resources that are residing on a CSE. It shall store information about the CSE itself. | remoteCSE, node, application, container, group, accessControlPolicy, subscription, mgmtObj, mgmtCmd, locationPolicy, statsConfig, schedule | None | 9.6.3 |
| delivery | Forwards requests from CSE to CSE | subscription | None documented | 9.6.11 |
| eventConfig | Defines events that trigger statistics collection | subscription | statsConfig | 9.6.23 |
| execInstance | The Execution Instance resource contains all execution instances of the same management command mgmtCmd. | subscription | mgmtCmd | 9.6.17 |
| group | Stores information about resources of the same type that need to be addressed as a Group. Operations addressed to a Group resource shall be executed in a bulk mode for all members belonging to the Group. | fanOutPoint subscription | Application, remoteCSE, CSEBase | 9.6.13 |
| locationPolicy | Includes information to obtain and manage geographical location. It is only referred from container, the contentInstances of the container provides location information. | subscription | CSEBase | 9.6.10 |
| fanOutPoint | Virtual resource containing target for group requests It is used for addressing bulk operations to all the resources that belong to a group. | None | group | 9.6.14 |
| mgmtCmd | Management Command resource represents a method to execute management procedures required by existing management protocols. | execInstance subscription | CSEBase | 9.6.16 |
| mgmtObj | Management Object resource represents management functions that provides an abstraction to be mapped to external management technology. It represents the node and the software installed in the node | parameters subscription | remoteCSE, CSEBase | 9.6.15 Annex D |
| m2mServiceSubscription | Data pertaining to the M2M Service Subscription | nodeInfo subscription | None documented | 9.6.19 |
| node | Represents specific Node information | mgmtObj subscription | CSEBase, remoteCSE | 9.6.18 |
| nodeInfo | Node information | subscription | m2mServiceSubscription | 9.6.20 |
| parameters | Provides a mechanism to describe the management object in a generic way to easily import information from existing management protocols. | parameters subscription | mgmtObj, parameters | 9.6.16 |
| pollingChannel | Represent a channel that can be used for a request-unreachable entity | None | remoteCSE, application | 9.6.21 |
| remoteCSE | Represents a remote CSE for which there has been a registration procedure with the registrar CSE identified by the CSEBase resource. | application, container, group, accessControlPolicy, subscription, mgmtObj, pollingChannel, schedule | CSEBase | 9.6.4 |
| request | Expresses/access context of an issued Request | subscription | None documented | 9.6.12 |
| schedule | Contains scheduling information for delivery of messages | subscription | CSEBase, remoteCSE, AE, subscription, cmdhNwAccessRule | 9.6.9 |
| statsCollect | Defines triggers for the IN-CSE to collect statistics for applications | subscription | CSEBase (in IN-CSE) | 9.6.24 |
| statsConfig | Stores configuration of statistics for applications | eventConfig subscription | CSEBase (in IN-CSE) | 9.6.22 |
| subscription | Subscription resource represents the subscription information related to a resource. Such a resource shall be a child resource for the subscribe-to resource. | schedule | accessControlPolicy, application, cmdhBuffer, cmdhDefaults, cmdhEcDefParamValues, cmdhDefEcValue, cmdhLimits, cmdhNetworkAccessRules, cmdhNwAccessRule, cmdhPolicy, container, CSEBase, delivery, eventConfig, execInstance, group, contentInstance, locationPolicy, mgmtCmd, mgmtObj, m2mServiceSubscription, node, nodeInfo, parameters, remoteCSE, request, schedule, statsCollect, statsConfig | 9.6.8 |

## -----------------------End of change 3-------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?