| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 ARC |
| Source:* | Qualcomm Ltd UK (ETSI), InterDigital Communications, NTT DOCOMO |
| Format:* | ARC 10 bis or 10.1 |
| Date:* | 2014-04-28 |
| Contact:* | Josef Blanz (jblanz@qti.qualcomm.com) Catalina Mladin (Catalina.Mladin@InterDigital.com) Syed Husain (shusain2016@gmail.com) |
| Reason for Change/s:* | Clean-up of CMDH CSF description |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0001 v0.4.3 |
| Clauses/Sub Clauses* | 6.2.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or (missing) functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes to clean-up the CMDH CSF description based on the reasoning provided in ARC-2014-1218R01. The current description has redundant sentences, and contains several “shall” requirements which are unverifiable. By simplifying the CMDH CSF description it still conveys the original intent, and removes ambiguity for the readers of the spec.

### -----------------------Start of change 1-------------------------------------------

### Communication Management and Delivery Handling

#### 6.2.2.1	General Concepts

The Communication Management and Delivery Handling (CMDH) CSF  provides communications with other CSEs, AEs and NSEs.

The CMDH CSF decides at what time to use which communication connection for delivering communication (e.g. CSE-to-CSE communication) and, when needed and allowed, to buffer communication requests so that they can be forwarded at a later time. This processing in the CMDH CSF is carried out in line with provisioned CMDH policies and delivery handling parameters that can be specific to each request for communication.

For communication using the Underlying Network data transport services, the Underlying Network can support the equivalent delivery handling functionality. In such case the CMDH CSF uses the Underlying Network, and it may act as a front end to access the Underlying Network equivalent delivery handling functionality.

#### 6.2.2.2	Detailed Descriptions

The service that  AEs or  CSEs can request from the CMDH CSF is to transport some given data to a specific target (CSE or AE) according to given delivery parameters, while staying within the constraints of provisioned communication management and delivery handling policies.

The content of the data provided by the Originator of a request is not visible to the CMDH CSF and does not influence its behaviour. Consequently the CMDH CSF is not aware of the specific operation requested at the target entity, including the parameters passed to the operation and the destination CSF. This means that all attributes intended to be delivered to the destination entity (e.g. which CSF is the destination on the target entity, what that CSF should do with the data etc.) are  hidden to the CMDH CSF.

The target entity may be reached either directly or via CSE(s) of Middle Node(s).

As part of the delivery request, the CMDH CSF can be provided with acceptable delivery parameters for the Originator (e.g., acceptable expiration time for delivery).

### The functions supported by the CMDH CSF are as follows:

Ability for the M2M Service Provider to derive CMDH policies describing details for the usage of the specific Underlying Network(s). These policies may be based on the M2M Service Subscription associated with Application and Service Entities (AEs and CSEs) in the Field Domain and on the agreements on usage of Underlying Network communication resources.  CMDH Policies can be provisioned into the respective CSEs in the Field Domain.

For delivery of communication, ability to select appropriate communication path to use at any given time in line with  provisioned CMDH policies and  with CMDH-related parameters  set by the Originator of requests,  and, when needed and allowed, how long to buffer communication requests so that they can be forwarded at a later time. This policy-driven use of communication resources allows an M2M Service Provider to control which Originators of requests are allowed to consume – possibly costly – communication resources at certain times.

For the delivery of communication, ability to be aware of the availability of the Underlying Networks.

Ability to manage the proper use of buffers for store-and-forward processing through use of CMDH policies.

### -----------------------End of change 1---------------------------------------------

### -----------------------End of all changes ---------------------------------------------

# Comments

I propose deleting as I don’t think it adds clarity. If fact it uses the “target CSF” language which conflict with the next sentence

This editor’s note can be removed as WG2 ARC has reached agreement on what topologies with multiple MNs are supported: Loops must be avoided.

The use of multiple underlying networks has been clarified in the resource structure for CMDH policies. The accepted structure allows for definition of network usage rules for multiple underlying networks. Therefore, complexity can be scaled to match the capabilities of the node that hosts the CMDH CSF. This editor’s note can be removed.