| CHANGE REQUEST |
| --- |
| Group Name:* | ARC#11 |
| Source:* | Seungkyu Park, LG Electronics, seungk.park@lge.com Thierry Garnier, Gemalto N.V, thierry.garnier@gemalto.com |
| Format:* | Plenary / Teleconference |
| Date:* | 2014-5-12 |
| Contact:* | Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Reason for Change/s:* | This contribution is to change the multiplecity of objectID and objectPath to 0..n |
| CR against: Release* | Release1 |
| CR against: TS/TR* | TS-0001, ver 0.6.1 |
| Clauses/Sub Clauses* | 9.6.15 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution is to change the multiplicity of the objectID and objectPath to 0..n (currently it is 0..1). The reason for this is the <mgmtObj> can be mapped to multiple resources from the management technologies. In this case, the objectID and objectPath needs to be multiple. For instance, the [deviceInfo] Resource is mapped to two MOs in case of OMA DM 1.3.

### -----------------------Start of change 1-------------------------------------------

### 9.6.15	Resource Type mgmtObj

The mgmtObj resource contains management data which represents individual M2M management functions. It represents a general structure to map to external management technology (e.g., OMA DM [i.5], BBF TR-069 [i.4] and LWM2M [i.6] data models. Each instance of <mgmtObj> shall be mapped to single external management technology.

Figure 9.6.15-1: Structure of <mgmtObj> resource

[9.6.15.b-1] Editor's Note; The picture above needs to be updated as per the new strucutre of mgmtObj resource.

The <mgmtObj> resource shall contain the child resource in Table 9.6.15-1.

# Table 9.6.15-1: Child resources of <mgmtObj> resource

| Child Resource Name of <mgmtObj> | Child Resource Type | Multiplicity | Description |  |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |  |

The <mgmtObj> resource shall contain the attributes described in Table 9.6.15-2.

# Table 9.6.15-2: Attributes of <mgmtObj> resource

| Attribute Name of <mgmtObj> | Multiplicity | RW/ RO/ WO | Description |  |
| --- | --- | --- | --- | --- |
| resourceType | 1 | WO | See clause 9.6.1 where this common attribute is described |  |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |  |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described |  |
| accessControlPolicyIDs | 1 | RW | See clause 9.6.1 where this common attribute is described |  |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described |  |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described |  |
| labels | 0..1 | RO | See clause 9.6.1 where this common attribute is described |  |
| mgmtDefinition | 1 | WO | Specifies the type of <mgmtObj> resource e.g., software, firmware, memory. The list of the value of the attribute can be seen in Annex D. |  |
| objectIDs | 0..1 | WO | Contains the list of URNs that uniquely identify the external management technology data models used for this <mgmtObj> resource as well as the managed function and version it represents. This attribute shall be provided during the creation of the <mgmtObj> resource and shall not be modifiable afterwards. If the <mgmtObj> resource is mapped to multiple external management technology data models, this attribute shall list all URNs for each mapped external management technology data model. This is mandatory for the <mgmtObj>, for which the data model is not specified by oneM2M but mapped from external management technology data model specified in other device management protocols. |  |
| objectPaths | 0..1 | WO | Contains the list of local paths of the external management object instances on the managed entity which is represented by the <mgmtObj> resource in the hosting CSE. This attribute shall be provided during the creation of the <mgmtObj>, so that the hosting CSE can correlate the created <mgmtObj> with the external management object instance on the managed entity for further management operations. It shall not be modifiable after creation. The format of this attribute shall be a local external management object path in the form as specified by existing management protocols. (e.g., "./anyPath/Fw1" in OMA DM [i.5], "Device.USBHosts.Host.3." in BBF TR-069 [i.4]). The combination of the objectPath and the objectID attribute, allows to address the external technology data models. |  |
| mgmtLink | 0..n | RW | The attribute contains references to another <mgmtObj> resource in case a hierarchy of <mgmtObj> is needed |  |
| [objectAttribute] | 0..n | RW | Each [objectAttribute] is mapped from a leaf node of a hierarchical structured management object (including oneM2M data model and the existing management data models) based on the mapping rules below the table. |  |
| description | 0..1 | RW | Text format description of mgmtObj. |  |

When mapping resources from management technologies to a corresponding <mgmtObj> resource, the following rules shall apply:

- The root resource of external management objects maps to the <mgmtObj> resource

- For the child resource of the root resource of specific technology:

- Rule1: If the child external management object cannot have a child external management object, the external management object maps to the [objectAttribute] attribute of the <mgmtObj> resource with the same resource name.

- Rule2: If the child external management object can have another child external management object, the external management object maps to a new <mgmtObj> resource.  The URI of the new <mgmtObj> resource is stored as an mgmtLink attribute of the <mgmtObj> resource which is mapped from the parent external management object.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?