| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Format:* | ARC |
| Date:* | 2014-05-28 |
| Contact:* | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Reason for Change/s:* | To clean up discovery introduction |
| CR against: Release* | Pre-release |
| CR against: TS/TR* | TS-0001 v0.7.0 |
| Clauses/Sub Clauses* | 10.2.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or (missing) functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution tries to solve the following issues.

- Temporary resource no longer exists ( remove the related texts

- The scope of discovery is not the entire of resources in a CSE ( discovery begins the resource specified in the discovery request

- A match happens when all the filter criteria are met.

- Redundant texts and stage 3 texts(e.g., query string) are removed

## -----------------------Start of change 1-------------------------------------------

### 10.2.5	Resource Discovery Procedure

#### 10.2.5.1	Introduction

The resource discovery procedures allow discovering of resources residing on a CSE. Resource discovery shall be accomplished using the RETRIEVE method by an Originator which shall also include the root of where the discovery begins: e.g., <CSEBase>.

Filter criteria conditions may be provided as parameters to the Retrieve method. The filter criteria conditions describe the rules for resource discovery, e.g. resource types, creation time, and matching string. The filter criteria can also contain the parameters for specifying the maximum size of the answer (upper limit), and/or sorting criteria for specifying in which order the searching result should be organized. Table 8.1.2-1 describes filterCriteria parameter which this specification supports.

A match shall happen when a resource matches all the configured filter criteria conditions and a successful response contains a list for the matched resources addressable in any of the forms expressed in clause 9.3.1. However, if Disrestype parameter is specified in a discovery request, the Hosting CSE shall choose the addressing form specified at Disrestype parameter.

The discovery results may be modified by the Hosting CSE to restrict the scope of discoverable resources according to the Originator's access control policy or M2M service subscription.

The Hosting CSE may also implement a configured upper limit on the size of the answer. In such a case when both the Originator and the Hosting CSE have the upper limits, the smaller of the upper limit in the Hosting CSE and the upper limit of the Originator shall apply.

## -----------------------End of change 1-------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?