| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | TS-0007 Response Code Cleanup |
| Source:* | Tim Carey, ALU, timothy.carey@alcatel-lucent.com |
| Contact: | Tim Carey, ALU, timothy.carey@alcatel-lucent.com |
| Date:* | 2014-05-29 |
| Abstract:* | Provide a clearer description of several response codes for capabilities that have been agreed. |
| Agenda Item:* | TP#11 |
| Work item(s): | TS-0007 WI |
| Document(s) Impacted* | TS-0007 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Update TS for inclusion |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

#### 6.2.1.1	validateSupportingService

This service capability ensures that a valid M2M Service Subscription exists for  a service capability that is either received by the M2M Service Platform from an AE or is transmitted to the AE from the M2M Service Platform.

##### 6.2.1.1.1	Pre-conditions

A correlation between the serviceId that defines the Supporting Service and the subscriptionId has been defined in order to obtain the serviceId.

##### 6.2.1.1.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| subscriptionId | IN | NO | The M2M Service Subscription Identifier (M2M-Sub-ID) |
| serviceId | IN | NO | The M2M Service Identifier (M2M-Serv-ID) |
| responseType | OUT | NO | Response types: Service exists for the requested Service Identifier Subscription does not exist for Service |

Table 6.2.1.1.2-1 validateSupportingService Signature

#### 6.2.1.3	getBroker

This service capability obtains the Broker instance that will be used to subscribe and publish requests  based on the requested service capability (e.g., publishRequest, subscribeRequest), AE and Resource.

For the publishRequest service capability the AE is the from Originator and the resource is the toResource  representing a leaf node from the publication resource.

For the subscribeRequest service capability the AE is the to Application and the resource is the publication resource.

##### 6.2.1.3.1	Pre-conditions

A correlation between a Service Subscription, from Originator and Broker exist.

##### 6.2.1.3.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| subscriptionId | IN | NO | The M2M Service Subscription Identifier (M2M-Sub-ID) |
| serviceId | IN | NO | The M2M Service Identifier (M2M-Serv-ID) of the service capability |
| to | IN | NO | The identifier of the AE that is to target of the request (M2M-AppInst-ID) |
| broker | OUT | NO | The returned instance of the Broker service associated with the subscription. |
| responseType | OUT | NO | Response types: Service exists for the requested Service Identifier Subscription does not exist for Service |

Table 6.2.1.1.2-1 validateBusService Signature