| CHANGE REQUEST |
| --- |
| Group Name:* | ARC 11.0 |
| Source:* | Yali Guo, Haier, guoyali@haierubic.com |
| Format:* | F2F conference |
| Date:* | 2014-05-30 |
| Contact:* | Yali Guo, Haier, guoyali@haierubic.com |
| Reason for Change/s:* | To clarify the registree can send a request message directly to its registrar CSE, and the registrar CSE can also send a request message directly to its registree. |
| CR against: Release* | Rel-1 |
| CR against: TS/TR* | TS-0001-Functional_Architecture-V0_6_1 |
| Clauses/Sub Clauses* | 8.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The term “registree” and “registrar CSE” are used to describe the relationship of registration, however, there should be no limitation of the communication direction between a registree and its registrar CSE. i.e. the registree can send a request message directly to its registrar CSE for CRUD operations, and the registrar CSE can also send a request message directly to its registree.

For example, an ASN-CSE is registered to a MN-CSE, the ASN-CSE can send a request message directly to the MN-CSE, and the MN-CSE can also initiate to send a request message directly to the ASN-CSE, in case the request message is not for registration.

But in the current specification, the first receiver of a request message is the originator’s registrar CSE, this means if a MN-CSE want to send a request message to an ASN-CSE registered to itself, the MN-CSE can’t send the request message directly to the ASN-CSE, it can only send the request message to its registrar CSE, may be another MN-CSE or IN-CSE.

## Proposal

It’s proposed to clarify that the registrar CSE can send a request message directly to its registree.

### -----------------------Start of the 1st change -------------------------------------------

## 8.2	Procedures for Accessing Resources

This clause describes the procedures for accessing the resources. The term "hop" in the descriptions here refers to the number of Transit CSEs that forward a request from the Originator CSE to the Hosting CSE.

### All the descriptions and message flows in this clause are illustrative for the direction from a Registree acting as an originator to a Registrar acting as a Receiver only. The flows from a Registrar CSE to a Registree CSE are symmetric with respct to the one described in this section. Both IN-CSE and MN-CSE have ability to route a received request or response messages to one of its Registrees. If the hosting CSE is not known by a MN-CSE that receives a request or response message, that MN-CSE shall forward the message to its own Registrar CSE by default.8.2.1	Accessing Resources in CSEs - Blocking Requests

For the procedures described herein, the addressed resource can be stored in different CSEs. Table 8.2.1-1 describes the possible scenarios, where the addressed resource may be on the Registrar CSE or on a CSE located elsewhere in the oneM2M System.

In this sub-clause - for simplicity - it is assumed that the Originator of a Request can always wait long enough to get a Response to the Request after the requested operation has finished. This implies potentially long or unknown blocking times (time for which a pending Request has not been responded to) for the Originator of a Request.

For scenarios that avoid such possibly long blocking times, clause 8.2.2 specifies mechanisms to handle synchronous and asynchronous resource access procedures via returning appropriate references.

# Table 8.2.1-1: Accessing Resources in different CSEs, from registree to registrar CSE

| Number of Transit CSEs | Description | Reference |
| --- | --- | --- |
| No Hops | The Originator of the Request accesses a resource. The Originator of the Request can be an AE or a CSE. Registrar CSE and Hosting CSE are the same entity. The hosting CSE shall check the Access Control Privileges for accessing the resource. Depending on the expected result content, the hosting CSE shall respond to the Originator of the Request, either with a Success or Failure Response | Figure 8.2.1-1 |
| 1 Hop | The Originator of the Request accesses a resource. The Originator of the Request may be an AE or a CSE. Registrar CSE and Hosting CSEs are different entities. Registrar CSE shall forward the Request to the Hosting CSE if the Registrar CSE is registered with the Hosting CSE, for accessing the resource Hosting CSE shall check the Access Control Privileges for accessing the resource and depending on the expected result content respond with a Success or Failure Response. | Figure 8.2.1-2 |
| Multi Hops | The Originator of the Request accesses a resource. The Originator of the Request may be an AE or a CSE. Registrar CSE, Transit CSE(s) and the Hosting CSE are different entities. Registrar CSE shall: Forward the Request to a Transit-1 CSE (e.g., MN-CSE) that the Registrar CSE is registered with, if configured through policies to do so or; Forward the request to an IN-CSE if the Registrar CSE is registered with IN-CSE and if configured through policies to do so. Transit-N CSE shall: Forward the request to the Hosting CSE if it is registered with the Hosting CSE or Forward the Request to another Transit-(N+1) CSE (e.g., another MN-CSE) that the Transit-N CSE is registered with. or Forward the request to an IN-CSE if the Transit-N CSE is registered with the IN-CSE. In case the request reaches the IN-CSE, the IN-CSE shall: Perform the processing defined under ‘Hosting CSE below if the targeted resource is hosted on IN-CSE Forward the request to another IN-CSE if the resource belongs to another M2M SP or Forward the request to the Hosting CSE if the latter is known (e.g. announcements) by the IN-CSE. Hosting CSE shall check the Access Control Privileges for accessing the resource and depending on the expected result content respond with a Success or Failure Response. | Figure 8.2.1-3 |

# Figure 8.2.1-1: Originator accesses a resource on the Registrar CSE (No Hops)

# Figure 8.2.1-2: AE/CSE accesses a resource at the Hosting CSE (One Hop)

# Figure 8.2.1-3: Originator accesses a resource at the Hosting CSE (Multi Hops)

#### 8.2.1.1 	M2M Requests Routing Policies

CSEs can use policies to govern routing of M2M requests to the next hop towards its target. Routing, through these policies, can be based, for example, on the target CSE, target M2M domain, specific types of resources if applicable, priority of a request, etc.

These policies are not defined in this release of this document. It is the responsibility of M2M SP and the CSE administrator to ensure the appropriateness of these policies for routing purposes

### -----------------------End of changes ---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?