| CHANGE REQUEST |
| --- |
| Group Name:* | TP#11 |
| Source:* | Huawei Technologies Co., Ltd. LG Electronics |
| Format:* | Plenary |
| Date:* | 2014-5-26 |
| Contact:* | Jiaxin Yin, Yinjiaxin@huawei.com Hongbeom Ahn, Hongbeom.ahn@lge.com |
| Reason for Change/s:* | Request Identifier should be optional. |
| CR against: Release* | One |
| CR against: TS/TR* | TS0001 v0.7.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

### -----------------------Start of change 1-------------------------------------------

### 9.6.18	Resource Type node

The <node> resource represents specific information that provides properties of an oneM2M Node that can be utilized by other oneM2M operations.  The <node> resource has <mgmtObj> as its child resources.  The <mgmtObj> resources represent the Node's context information (e.g., memory and battery), network topology, device information, device capability etc. The <mgmtObj> resources are also resources to perform management of the Nodes.

This node specific information stored in this resource type such as memory and battery can be obtained either by the existing device management technologies (OMA DM [i.5], BBF TR-069 [i.4]) or any other way (e.g., JNI  [i.21])). Since <mgmtObj> resource type represents the management functions including both ways, the types of sub-resources are <mgmtObj> resource type.

For the case that the <node> resource belongs to an ADN, please see the description of nodeLink attribute in the <AE> resource (clause 9.6.5).

This resource also represents M2M node information that is needed as part of the M2M Service Subscription resource. It shall contain information about the node as well as application identifiers running on that node.

Figure 9.6.18-1: Structure of <node> resource

[9.6.18.c-1] Editor's Note: To update the picture to include "hostedCSEID attribute.

[9.6.18.c-2] Editor's Note: Verify if  the picture above needs to be updated as per the new strucutre of node resource.

The <node> resource shall contain the child resources in Table 9.6.18-1.

Table 9.6.18-1: Child resources of <node> resource

| Child Resource Name of <node> | Child Resource Type | Multiplicity | Description |  |
| --- | --- | --- | --- | --- |
| [variable] | <mgmtObj> with mgmtDefinition of value “memory” | 0..1 | This resource provides the memory (typically RAM) information of the node. (e.g., the amount of total volatile memory), See clause D.4. |  |
| [variable] | <mgmtObj> with mgmtDefinition of value “battery” | 0..n | The resource provides the power information of the node. (e.g., remaining battery charge). See clause D.7. |  |
| [variable] | <mgmtObj> with mgmtDefinition of value “areaNwkInfo” | 0..1 | This resource describes the list of Nodes attached behind the MN node and its physical or underlying relation among the nodes in the M2M Area Network. This attribute is defined in case the Node is MN. See clause D.5. |  |
| [variable] | <mgmtObj> with mgmtDefinition of value “areaNwkDeviceInfo” | 0..n | This resource describes the information about the Node in the M2M Area Network. See clause D.6. |  |
| [variable] | <mgmtObj> with mgmtDefinition of value “firmware” | 0..1 | This resource describes the information about the firmware of the Node include name, version etc, See clause D.2. |  |
| [variable] | <mgmtObj> with mgmtDefinition of value “software” | 0..n | This resource describes the information about the software of the Node. See clause D.3. |  |
| [variable] | <mgmtObj> with mgmtDefinition of value “deviceInfo” | 0..n | The resource contains information about the identity, manufacturer, model number of the device. See clause D.8. |  |
| [variable] | <mgmtObj> with mgmtDefinition of value “deviceCapability” | 0..n | The resource contains information about the capability supported by the Node. See clause D.9. |  |
| [variable] | <mgmtObj> with mgmtDefinition of value “reboot” | 0..1 | The resource is the place to reboot or reset the Node. See clause D.11 |  |
| [variable] | <mgmtObj> with mgmtDefinition of value “eventLog” | 0..1 | The resource contains the information about the log of events of the Node. See clause D.12. |  |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |  |

The <node> resource shall contain the attributes described in Table 9.6.18-2.

# Table 9.6.18-2: Attributes of <node> resource

| Attribute Name of <node> | Multiplicity | RW/ RO/ WO | Description |  |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described. |  |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |  |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |  |
| accessControlPolicyIDs | 0..1 | RW | See clause 9.6.1 where this common attribute is described. |  |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |  |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |  |
| labels | 0..1 | RW | See clause 9.6.1 where this common attribute is described. |  |
| nodeID | 1 | RW | The ID of the Node which is specified in the resource type. This attribute is identical to M2M-Node-ID. |  |
| hostedCSEID | 0..1 | RW | The ID of the CSEBase that is hosted on this node if type of node is ASN/MN/IN. |  |
| App-ID | 0..n | RW | See clause 7.1.3. Application ID pertaining to (an) application(s) running on this node. |  |

### 9.6.19	Resource Type m2mServiceSubscription

This resource represents an M2M Service Subscription. It is used to represent all data pertaining to the M2M Service Subscription (the technical part of the contract between an M2M Application Service Provider and an M2M Service Provider).

Figure 9.6.19-1: Structure of <m2mServiceSubscription> resource

[9.6.19.a0] Editor's Note: Verify if  the picture above needs to be updated as per the new strucutre of the resource.

[9.6.19.b]  Editor's Note: the M2M-Sub-ID storage is FFS

The <m2mServiceSubscription> resource shall contain the child resources in Table 9.6.19-1.

Table 9.6.19-1: Child resources of <m2mServiceSubscription> resource

| Child Resource Name of <m2mServiceSubscription> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |
| nodeInfo | <node> | 0..n | See clause 9.6.20 |

The <m2mServiceSubscription> resource shall contain the attributes in Table 9.6.19-2.

# Table 9.6.19-2: Attributes of <m2mServiceSubscription> resource

| Attribute Name of <m2mServiceSubscription> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 | RW | See clause 9.6.1 where this common attribute is described. If no accessControlPolicyIDs is given at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute |
| creationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| labels | 0..1 | RO | See clause 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| subsSer&RoleList | 0..n | WO | This attribute indicates the list of subscribed services and roles. |
| App-ID | 0..n | RW | The value of this attribute shall be set to an application identifier as defined in clause 7.1.3 pertaining to applications in the infrastructure domain (IN-AE) of this M2M service subscription. |
| subsGroup | 0..n | RW | This attribute contains a group created by the subscriber for the purpose of helping easy setting of Access Control Privileges. An example of the subscriber defined group is all node applications within this service subscription with App-ID set to a specific value. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3---------------------------------------------

### 10.2.14	<node> Resource Procedure

#### 10.2.14.1	Create <node>

This procedure shall be used for creating a <node> resource.

Originator: The Originator shall request to create a new <node> resource. The request shall address different resources depending on the type of node that is issuing the request, as described in 9.6.18. Following that, the Originator can create the child resources (defined in the 9.6.18) to acquire node specific information as occasion demands of the Originator. The Originator shall be an AE or a CSE.

Receiver: The Receiver or Hosting CSE shall:

- Check whether the Originator is authorized to request the procedure.

- Check whether the provided attributes of the <node> resource represent a valid Request.

- Upon successful validation of the above procedures, create a new <node> resource with given name in the Hosting CSE with the provided attributes.

Table 10.2.14.1-1: <node> CREATE

| Description |
| --- |
| Pre-Conditions | Originator has already registered. |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table with the specific details for: cn: The representation of the <node> resource described in clause 9.6.18. The following attributes from clause 9.6.18 are mandatory for the request: “resourceType” which shall be set to the appropriate tag that identify the <node> resource as defined in 9.6.1 The following attributes from clause 9.6.18 are optional for the request: “accessControlPolicyID” “expirationTime” “labels” “appID” “hostedCSEID” NOTE: if the Originator is a CSE, it could take the information that is stored in the <node> resource under its own <CSEBase> resource and provide the information in the cn. |
| Local processing on Hosting CSE | No change from the basic procedure described in clause 10.1.1 |
| Information on Response message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table with the specific details for: cn: URI of the created <node> resource , according to clause 10.1.1 |
| Post-Conditions | If the Originator is either ASN or MN-CSE registered with a CSE: The registered CSE checks the announceTo attributes whether the created <node> resource under the <CSEBase> is announced or not. If so, the created <node> resource is automatically announced by the registered CSE. |
| Exceptions | All exception described in the basic procedure (clause 10.1.1) are applicable. |

#### 10.2.14.2	Retrieve <node>

This flow is used for retrieving the attributes of a <node> resource.

Originator: The Originator shall request to obtain <node> resource information by using RETRIEVE operation. The Originator can be either an Application Entity or a CSE.

Receiver: The Receiver shall:

- Check if the Originator has RETRIEVE privileges on the <node> resource and the request is valid.

- Upon successful validation, the Hosting CSE shall respond to the Originator with the appropriate responses.

Table 10.2.14.2-1: <node> RETRIEVE

| Description |
| --- |
| Pre-Conditions | The targeted <node> has been already created |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table with the specific details for: cn: void |
| Local processing on Hosting CSE | No change from the basic procedure described in clause 10.1.2 |
| Information on Response message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table with the specific details for: cn: attributes of the <node> resource as defined in clause 9.6.18. |
| Post-Conditions | None |
| Exceptions | All exception described in the basic procedure (clause 10.1.2) are applicable. |

#### 10.2.14.3	Update <node>

This flow is used for updating the attributes and the actual data of a <node> resource and its child resources.

Originator: The Originator shall request to update attributes of an existing <node> resource by using an UPDATE operation. The request shall address the specific <node> resource reside in a CSE. The Originator may be either an AE or a CSE.

Receiver: The Receiver of an UPDATE request shall check whether the Originator is authorized to request operation. The Receiver shall check whether the provided attributes of the <node> resource represent a valid request for updating <node> resource.

Table 10.2.14.3-1: <node> UPDATE

| Description |
| --- |
| Pre-Conditions | The targeted <node> has been already created |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table with the specific details for: cn: attributes of the <node> resource as defined in 9.6.18 which need be updated, with the exception of the Read Only (RO) attributes cannot be modified |
| Local processing on Hosting CSE | No change from the generic procedure from clause 10.1.3. |
| Information on Response message | No change from the generic procedure from clause 10.1.3. |
| Post-Conditions | None |
| Exceptions | All exception described in the basic procedure (clause 10.1.3) are applicable. |

#### 10.2.14.4	Delete <node>

This procedure shall be used for deleting an existing <node> resource.

Originator: The Originator shall request to delete an existing <node> resource by using DELETE operation. The Originator can be either an AE or a CSE.

Receiver or Hosting CSE: The Receiver shall check if the Originator has DELETE permission on the <node> resource and the request is valid. Upon successful validation, the CSE shall remove the resource from its repository and shall respond to the Originator with appropriate responses.

Table 10.2.14.4-1: <node> DELETE

| Description |
| --- |
| Pre-Conditions | The targeted <node> has been already created |
| Information on Request message | All parameters defined in Table 8.1.2.1-1 are applicable as indicate in the table. |
| Local processing on Hosting CSE | No change from the generic procedure from clause 10.1.4. |
| Information on Response message | No change from the generic procedure from clause 10.1.4. |
| Post-Conditions | The targeted resource and all the children resources shall not exist anymore. Also all the related credential shall be deleted. [10.2.14.4.a] Editor’s Note: if and how credentials are cleaned is FFS, in scope of WG4. |
| Exceptions | All exception described in the basic procedure (clause 10.1.4) are applicable. |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4---------------------------------------------

## 9.6	Resource Types

Table 9.6-1 introduces the defined normal and virtual resource types and their related child or parent resource types. Details of each resource type follow in the remainder of this clause.

Table 9.6-1 lists the supported <resourceTypes>. An addition of suffix "Annc" to such <resourceTypes> indicates the associated announced resource type.

Table 9.6-1 Resource Summary

| Resource Type | Short Description | Child Resource Types | Parent Resource Types | Clause |
| --- | --- | --- | --- | --- |
| accessControlPolicy | Stores a representation of privileges. It is associated with resources that shall be accessible to entities external to the hosting CSE. It controls "who" is allowed to do "what" and the context in which it can be used for accessing the resources | subscription | AE, remoteCSE, CSEBase | 9.6.2 |
| contentInstance | Represents a data instance in the container resource | subscription | container | 9.6.7 |
| AE | Stores information about the AE. It is created as a result of successful registration of an AE with the registrar CSE | subscription, container, group, accessControlPolicy, mgmtObj, commCapabilities, pollingChannel | remoteCSE, CSEBase | 9.6.5 |
| cmdhBuffer | Defines CMDH buffer usage limits | subscription | cmdhPolicy | D.12.7 |
| cmdhDefaults | Defines CMDH default values | cmdhDefEcValue, cmdhEcDefParamValues subscription | cmdhPolicy | D.12.1 |
| cmdhEcDefParamValues | Represent a specific set of default values for the CMDH related parameters | subscription | cmdhDefaults | D.12.3 |
| cmdhDefEcValue | Defines a value for the ec (event category) parameter of an incoming request when it is not defined | subscription | cmdhDefaults | D.12.2 |
| cmdhLimits | Defines limits for CMDH related parameter values | subscription | cmdhPolicy | D.12.4 |
| cmdhNetworkAccessRules | Defines rules for the usage of underlying networks | cmdhNwAccessRule subscription | cmdhPolicy | D.12.5 |
| cmdhNwAccessRule | Defines a rule for the usage of underlying networks | schedule subscription | cmdhNetworkAccessRules | D.12.6 |
| cmdhPolicy | A set of rules defining which CMDH parameters will be used by default | cmdhDefaults, cmdhLimits, cmdhNetworkAccessRules, cmdhBuffer subscription | None | D.12 |
| container | Shares data instances among entities. Used as a mediator that takes care of buffering the data to exchange "data" between AEs and/or CSEs. The exchange of data between AEs (e.g. an AE on a Node in a field domain and the peer-AE on the infrastructure domain) is abstracted from the need to set up direct connections and allows for scenarios where both entities in the exchange do not have the same reachability schedule | container, contentInstance, subscription, | application, container, remoteCSE, CSEBase | 9.6.6 |
| CSEBase | The structural root for all the resources that are residing on a CSE. It shall store information about the CSE itself | remoteCSE, node, application, container, group, accessControlPolicy, subscription, mgmtObj, mgmtCmd, locationPolicy, statsConfig | None | 9.6.3 |
| delivery | Forwards requests from CSE to CSE | subscription | None documented | 9.6.11 |
| eventConfig | Defines events that trigger statistics collection | subscription | statsConfig | 9.6.23 |
| execInstance | The Execution Instance resource contains all execution instances of the same management command mgmtCmd | subscription | mgmtCmd | 9.6.17 |
| group | Stores information about resources of the same type that need to be addressed as a Group. Operations addressed to a Group resource shall be executed in a bulk mode for all members belonging to the Group | fanOutPoint subscription | Application, remoteCSE, CSEBase | 9.6.13 |
| locationPolicy | Includes information to obtain and manage geographical location. It is only referred from container, the contentInstances of the container provides location information | subscription | CSEBase | 9.6.10 |
| fanOutPoint | Virtual resource containing target for group requests It is used for addressing bulk operations to all the resources that belong to a group | None | group | 9.6.14 |
| mgmtCmd | Management Command resource represents a method to execute management procedures required by existing management protocols | execInstance subscription | CSEBase | 9.6.16 |
| mgmtObj | Management Object resource represents management functions that provides an abstraction to be mapped to external management technology. It represents the node and the software installed in the node | parameters subscription | remoteCSE, CSEBase | 9.6.15 Annex D |
| m2mServiceSubscription | Data pertaining to the M2M Service Subscription | node subscription | None documented | 9.6.19 |
| node | Represents specific Node information | schedule, mgmtObj subscription | CSEBase, remoteCSE | 9.6.18 |
| parameters | Provides a mechanism to describe the management object in a generic way to easily import information from existing management protocols | parameters subscription | mgmtObj, parameters | 9.6.16 |
| pollingChannel | Represent a channel that can be used for a request-unreachable entity | None | remoteCSE, application | 9.6.21 |
| remoteCSE | Represents a remote CSE for which there has been a registration procedure with the registrar CSE identified by the CSEBase resource | application, container, group, accessControlPolicy, subscription, mgmtObj, pollingChannel, node | CSEBase | 9.6.4 |
| request | Expresses/access context of an issued Request | subscription | None documented | 9.6.12 |
| schedule | Contains scheduling information for delivery of messages | subscription | node, subscription, cmdhNwAccessRule | 9.6.39 |
| statsCollect | Defines triggers for the IN-CSE to collect statistics for applications | subscription | CSEBase (in IN-CSE) | 9.6.24 |
| statsConfig | Stores configuration of statistics for applications | eventConfig subscription | CSEBase (in IN-CSE) | 9.6.22 |
| subscription | Subscription resource represents the subscription information related to a resource. Such a resource shall be a child resource for the subscribe-to resource | schedule | accessControlPolicy, application, cmdhBuffer, cmdhDefaults, cmdhEcDefParamValues, cmdhDefEcValue, cmdhLimits, cmdhNetworkAccessRules, cmdhNwAccessRule, cmdhPolicy, container, CSEBase, delivery, eventConfig, execInstance, group, contentInstance, locationPolicy, mgmtCmd, mgmtObj, m2mServiceSubscription, node, parameters, remoteCSE, request, schedule, statsCollect, statsConfig | 9.6.8 |

### -----------------------End of change 4---------------------------------------------