| CHANGE REQUEST |
| --- |
| Group Name:* | TP#11 |
| Source:* | Huawei Technologies Co., Ltd. |
| Format:* | Plenary |
| Date:* | 2014-5-26 |
| Contact:* | Jiaxin Yin, Yinjiaxin@huawei.com |
| Reason for Change/s:* | Request Identifier should be optional. |
| CR against: Release* | One |
| CR against: TS/TR* | TS0001 v0.7.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Currently request identifier is included in the request and response for the purpose of correlating requests and responses. However, the correlation of request and response can be provided by transport networks like HTTP or CoAP. Request and response can be correlated by HTTP within the same HTTP connection. Request and response can also be correlated by CoAP by MsgID and token option provided by CoAP. There is no reason to mandate request identifier in these cases, because the attribute is useless. Besides, in constrained networks like occasions CoAP is used, the bandwidth is greatly limited. A very long and useless but madatory Request Identifier would be a greate consumption of valueable bandwith. Therefore, the contribution proposes to change Request Identifier from Mandatory to Optional.

### -----------------------Start of change 1-------------------------------------------

### 8.1.2	Request

The Request from an Originator to a Receiver includes the following parameters:

to: URI of the target resource for the operation. The to parameter shall conform to clause 9.3.1

NOTE 1:  The to target resource needs to be known by the Originator. It can be known either by pre-provisioning (clause 11.2) or by discovery (clause 10.2.5 for discovery). Discovery of CSEBase is not supported in this release of the document. It is assumed knowledge of CSEBase is by pre-provisioning only.

NOTE 2: 	The term target resource always refers to the resource which is addressed for the specific operation. For example the to of a Create operation for a resource “example” would be “/m2m.provider.com/exampleBase” the to parameter for the operation Retrieve of the same resource “example” is “/m2m.provider.com/exampleBase/example”.

fr:  Identifier representing the Originator.

NOTE 3:	The fr parameter can be used by the Receiver to check the Originator identity for access privilege verification.

cn: resource content to be transferred.

role: optional, required when role based access control is applied <associated text and procedure TBD>

[8.1.2.0a] Editor's Note:  Need to figure out the impact of Role in different procedures.

op: operation to be executed: Create (C), Retrieve (R), Update (U), Delete (D), Notify (N)

The op parameter shall indicate the operation to be executed at the Receiver:

Create (C): to is the URI of the target resource where the new resource (parent resource)

Retrieve (R): an existing to addressable resource is read and provided back to the Originator.

Update (U): the content of an existing to addressable resource is replaced with  the new content as in cn parameter.

Delete (D): an existing to addressable resource and all its sub-resources are deleted from the Resource storage.

Notify (N):  information to be sent to the Receiver, processing on the Receiver is not indicated by the Originator.

The ty parameter shall be present in Request for the following operations:

Create: ty is the type of the resource to be created.

cn: resource content to be transferred.

The cn parameter shall be present in Request for the following operations:

Create: cn is the content of the new resource with the resource type ty.

Update: cn is the content to be replaced in an existing resource. For the Update operation that is used for Execute operation, cn does not exist.

Retrieve: cn is the filter to be applied for discovery purposes.

Notify: cn is the notification information.

Note that the cn parameter can also be empty.

Other allowed parameters shall be as follows:

nm:  optional name of the resource to be created.

Example usage of the name includes a name that the Originator of the Create resource wishes to be used as the identifier of the newly created resource. For creating a container with the name “myContainer” the request will provide the parameter nm with the value “myContainer” and the created resource would be: /<CSEBase>/myContainer.

ot: optional originating timestamp of when the message was built.

Example usage of the originating timestamp includes: to measure and enable operation (e.g., message logging, correlation, message prioritization/scheduling, accept performance requests, charging, etc.) and to measure performance (distribution and processing latency, closed loop latency, SLAs, analytics, etc.)

rqet: optional request message expiration timestamp.

Example usage of the request expiration timestamp includes to indicate when request messages (including delay-tolerant) should expire due to their staleness being no longer of value, and to inform message scheduling/prioritization. When a request has set request expiration timestamp to a specific time and the Request demands an operation on a Hosting CSE that is not the CSE currently processing the request, then the current CSE shall keep on trying to deliver the Request to the Hosting CSE until the request expiration timestamp time, in line with provisioned policies.

rset: optional result message expiration timestamp.

Example usage of the result expiration timestamp includes to indicate when result messages (including delay-tolerant) should expire due to expected staleness of the result, being no longer of value, and to inform message scheduling/prioritization. It can be used to set the maximum allowed total request/result message sequence round trip deadline.

rt: optional response message type: Indicates  what the response to the issued request shall contain and when the response is sent to the Originator:

nonBlockingRequestSynch: In case the request is accepted by the Local CSE, the Local CSE responds after acceptance with an Acknowledgement confirming that the Local CSE will further process the request. The Local CSE includes in the response to an accepted request a reference that can be used to access the status of the request and the result of the requested operation at a later time. Processing of Non-Blocking Requests is defined in clause 8.2.2 and in particular for the synchronous case in clause 8.2.2.2.

nonBlockingRequestAsynch: In case the request is accepted by the Local CSE, the Local CSE responds after acceptance with an Acknowledgement confirming that the Local CSE will further process the request. The result of the requested operation needs to be sent as a notification to the Originator. Processing of Non-Blocking Requests is defined in clause 8.2.2 and in particular for the asynchronous case in clause 8.2.2.3.

blockingRequest: In case the request is accepted by the Local CSE, the Local CSE responds with the result of the requested operation after completion of the requested operation. Processing of Blocking Requests is defined in clause 8.2.1.

Example usage of the response type set to nonBlockingRequestSynch: An Originator that is optimized to minimize communication time and energy consumption wants to express a Request to the local CSE and get an acknowledgement on whether the Request got accepted. After that the Originator may switch into a less power consuming mode and retrieve a Result of the requested Operation at a later time.

Further example usage of response type set to nonBlockingRequestSynch includes when the result content is extremely large, or when the result consists of multiple content parts from a target group which are to be aggregated asynchronously over time.

rc: optional result content: Indicates what are the expected components of the result of the requested operation. The Originator of a request may not need to get back a result of an operation at all. This shall be indicated in the rc parameter. Which exact settings of rc are possible depends on the requested operation specified in op. Possible values of rc are:

attributes: Representation of the requested resource shall be returned as content, without the URI(s) of the child resource(s). This is the default value. For example, if the request is to retrieve a <container> resource, the URI(s) of the <contentInstance> child-resource(s) is not provided. This setting is not valid for a Notify operation.

attributes+child-resources: Representation of the requested resource, along with the URI(s) of the child resource(s), possibly limited by a maximum number of retrieved links, shall be returned as content. For example, if the request is to retrieve a <container> resource, the <container> resource and the URI(s) of the <contentInstance> child-resource(s) are provided. This setting is not valid for a Notify operation

child-resource: URI(s) of the child resources, possibly limited by a maximum number of retrieved URI(s), without any representation of the actual requested resource shall be returned as content. For example, if the request is to retrieve a <container> resource, only the URI(s) of the <contentInstance> child-resource(s) is provided. This setting is not valid for  a Notify operation

nothing: Nothing shall be returned as operational result content. This setting is not valid for a retrieve operation. This setting is the default when a Notification was requested by the op parameter.

announced-resource: Representation of the announced resource at local CSE shall be returned without the URI(s) of the child resource(s). If such information is not available at the local CSE, information at original resource Hosting CSE as per attribute setting shall be returned. This option shall not be used if the optional parameter fc (filter criteria) is included. This setting is not valid for a Notify operation.

[8.1.2.f0] Editor's Note: Example usage of all rc enumerated values needed. What is the use case for "nothing"?

[8.1.2.f1] Editor's Note: Do we need to support use case for "no response expected" in this release.

rp: optional response persistence: indicates the duration for which the address containing the responses is to persist.

Example usage of response persistence includes requesting sufficient persistence for analytics to process the response content aggregated asynchronously over time. If a result expiration timestamp is specified then the response persistence should last beyond the  result expiration time.

ri: optional request Identifier

Example usage of request identifier includes enabling the correlation between a Request and one of the many received Responses.

oet: optional operation execution time: indicates the time when the specified operation op is to be executed by the target CSE. A target CSE shall execute the specified operation of a Request having its operational execution time indicator set, starting at the operational execution time. If the execution time has already passed or if the indicator is not set, then the specified operation shall be immediately executed, unless the request expiration time, if set, has been reached.

Example usage of operational execution time includes asynchronous distribution of flows, which are to be executed synchronously at the operational execution time.

NOTE 4:	Time-based flows could not supported depending upon time services available at CSEs.

ec: optional event category: Indicates the event category that should be used to handle this request. Event categories are impacting how Requests to access remotely hosted resources are processed in the CMDH CSF. Selection and scheduling of connections via CMDH are driven by policies that can differentiate event categories.

Example usage of "event category" set to specific value X: When the request is demanding an operation to be executed on a Hosting CSE that is different from the Registrar CSE, the request may be stored in the CSE that is currently processing the request on the way to the Hosting CSE until it is allowed by provisioned policies for that event category X to use a communication link to reach the next CSE on a path to the Hosting CSE or until the request expiration timestamp is expired.

da: optional delivery aggregation on/off: Use CRUD operations of <delivery> resources to express forwarding of one or more original requests to the same target CSE(s).

NOTE 5:	Since da is optional, there could be a default value to be used when not present in the Request. This parameter could not be exposed to AEs via Mca.

Example usage of delivery aggregation set on: The CSE processing a request shall use aggregation of requests to the same target CSE by requesting CREATE of a <delivery> resource on the next CSE on the path to the target CSE.

gid: optional group request identifier: Identifier added to the group request that is to be fanned out to each member of the group.

fc:  optional filter criteria: conditions for filtered retrieve operation are described in Table 8.1.2-1.

Disrestype: Optional Discovery result type. This parameter applies to discovery related requests (see clause 10.2.5) to indicate the preference of the Originator for the format of returned information in the result of the operation. This parameter shall take on one of the following values reflecting the options in clause 9.3.1:

Hierarchical URI option

Non-hierarchical URI option

CSE-ID, and resource identifier option

Example usage of the discovery result type set to Non-hierarchical URI option. The request originator is only willing to receive non-hierarchal URIs for discovered resources.

The absence of the parameter implies that the result shall be in Hierarchical URI format.

[8.1.2.g]  Editors Note: This may be impacted by the management of access control policy which will be enhanced to take into account Hierarchical and non-Hierarchical URI.

Rapportur Note: Discussions during ARC#10bis.  Contribution expected for the resolution of the above stated Editor's Note.

Table 8.1.2-1: filterCriteria conditions

| Condition tag | Multiplicity | Matching condition |
| --- | --- | --- |
| createdBefore | 0..1 | The creationTime attribute of the resource is chronologically before the specified value. |
| createdAfter | 0..1 | The creationTime attribute of the resource is chronologically after the specified value. |
| modifiedSince | 0..1 | The lastModifiedTime attribute of the resource is chronologically after the specified value. |
| unmodifiedSince | 0..1 | The lastModifiedTime attribute of the resource is chronologically before the specified value. |
| expireBefore | 0..1 | The expirationTime attribute of the resource is chronologically before the specified value. |
| expireAfter | 0..1 | The expirationTime attribute of the resource is chronologically after the specified value. |
| labels | 0..n | The labels attributes of the resource matches the specified value. |
| resourceType | 0..n | The resourceType attribute of the resource is the same as the specified value. It also allows discriminating between normal and announced resources. |
| sizeAbove | 0..1 | The contentSize attribute of the <contentInstance> resource is equal to or greater than the specified value. |
| sizeBelow | 0..1 | The contentSize attribute of the <contentInstance> resource is smaller than the specified value. |
| contentType | 0..n | The typeOfContent attribute of the <contentInstance> resource matches the specified value |
| limit | 0..1 | Limitation the number of matching resources to the specified value. |
| attribute | 0..n | Attribute token name to be provided to reduce the scope of filtering to resource attributes. |

Example usage of filter criteria conditions in a HTTP query: an HTTP GET operation can be requested applying also a filter in the query part of the request itself:

GET /root?label=one&label=two&createdBefore=2014-01-01T00:00:00&limit=128

The example discovers a maximum of 128 resources matching the following logical condition: createdBefore < 2014-01-01T00:00:00 AND (label = one OR label = two).

Once the Request is delivered, the Receiver shall analyze the Request to determine the target resource.

If the target resource is addressing another M2M node, the Receiver shall route the request appropriately.

If the target resource is addressing the Receiver, it shall:

Check the existence of to addressed resource.

Identify the resource type by ty.

Check the privileges for fr Originator to perform the requested operation.

Perform the requested operation (using cn content when provided) according to the provided request parameters as described above.

Depending on the request result content, respond to the Originator with indication of successful or unsuccessful operation results. In some specific cases (e.g., limitation in the binding protocol or based on application indications), the Response could be avoided.

The message flow procedure started with an Originator Request message shall be considered closed when either:

A Request message is expired according to the rqet (request expiration timestamp).

A Response message is delivered to the Originator.

#### 8.1.2.1	Summary of Request Message Parameters

Table 8.1.2.1-1summarises the parameters specified in clause 8.1.2 for the Request message, showing any differences as applied to C, R, U, D or N operations. "M" indicates mandatory, "O" indicates optional, "N/A" indicates "not applicable".

# Table 8.1.2.1-1: Summary of Request Message Parameters

| Request message parameter \ Operation | Create: a new resource is created | Retrieve: an existing resource is read and the result is provided | Update: the content of an existing resource is replaced with new content | Delete: an existing resource and all its sub-resources are deleted | Notify: the content / address is transferred |
| --- | --- | --- | --- | --- | --- |
| Operation (op) - operation to be executed | M | M | M | M | M |
| To (to) – the address of the target resource on the target CSE | M | M | M | M | M |
| From (fr) – the identifier of the message Originator | M | M | M | M | M |
| Request Identifier (ri) – uniquely identifies a Request message | O | O | O | O | O |
| Resource Type (ty) - of resource to be created | M | N/A | N/A | N/A | N/A |
| Name (nm) - of resource to be created | O | N/A | N/A | N/A | N/A |
| Content (cn) - to be transferred | O | O | O | N/A | M |
| Originating Timestamp (ot) - when the message was built | O | O | O | O | O |
| Request Expiration Timestamp (rqet) – when the request message expires | O | O | O | O | O |
| Result Expiration Timestamp (rset) -when the result message expires | O | O | O | O | O |
| Operational Execution Time (oet) - the time when the specified operation is to be executed by the target CSE. | O | O | O | O | O |
| Response Type (rt) – Registrar CSE response shall either indicate that the Request was accepted, or include the operation result | O | O | O | O | O |
| Result Destination (rd) – either a reference to where the result is stored, or the result is sent to the Originator | O | O | O | O | N/A |
| Result Persistence (rp) - the duration for which the reference containing the responses is to persist | O | O | O | O | N/A |
| Result Content (rc) – the expected components of the result | O | O | O | O | N/A |
| Event Category (ec) – indicates how and when the system should deliver the message | O | O | O | O | O |
| Delivery Aggregation (da) - aggregation of requests to the same target CSE is to be used | O | O | O | O | O |
| Group Request Identifier (gid) - Identifier added to the group request that is to be fanned out to each member of the group. | O | O | O | O | O |
| Filter Criteria (fc) – conditions for filtered retrieve operation | N/A | O | N/A | N/A | N/A |
| Discovery Result Type (Disrestype) - format of information returned for Discovery operation | N/A | O | N/A | N/A | N/A |

### 8.1.3	Response

The Response received by the Originator of a Request accessing resources over the Mca and Mcc reference points shall contain mandatory and may contain optional parameters. Certain parameters may be mandatory or optional depending upon the Requested operation (CRUDN) or the mandatory response code. In this clause, the mandatory parameters are detailed first, following by those that are conditional, followed by those that are optional:

Mandatory Parameters:

rs: response code: This parameter indicates whether the operation was successful, unsuccessful or is an acknowledgement

A “successful” code indicates to the Originator that the Requested operation has been executed successfully by the Hosting CSE.

An “unsuccessful” code indicates to the Originator that the Requested operation has not been executed successfully by the Hosting CSE.

An “acknowledgement” indicates to the Originator that the Request has been received and accepted by the attached CSE, i.e., by the CSE that received the Request from the issuing Originator directly, but the Request operation has not been executed yet. The success or failure of the execution of the Requested operation is to be conveyed later.

Details of successful, unsuccessful, and acknowledge codes are provided in the oneM2M Core Protocol Technical Specification (TS-0004)  [i.2].

Conditional Parameters:

cn: resource content:

If rs is “successful” then

The cn parameter may be present in a Response in the following cases:

Create: cn is the address and/or the content of the created resource.

Update: cn is the content replaced in an existing resource.

Delete: cn is the content actually deleted.

The cn parameter shall be present in a Response in the following cases:

Retrieve: cn is the retrieved resource content or aggregated contents of discovered resources.

If present in the Request, result contents rc, indicates which components of the result of the requested operation are to be included in the Response.

If rs is “unsuccessful” then cn may be present in a Response to provide more error information.

If rs is “acknowledgment” then cn is not present

ra: address for the temporary storage of end node Responses. Present only for non-blocking as indicated by the Request parameter rt.

Optional parameters:

ri: Request Identifier.  The ri in the Response shall match the ri in the corresponding Request.

to: ID of the Originator. In case this is a response carrying the result of an operation triggered by a non-blocking request, "rd" information can be used.

fr: ID of the Receiver.

ot: originating timestamp of when the message was built.

rset: result expiration timestamp. The Receiver shall echo the result expiration timestamp if set in the Request message, or may set the result expiration timestamp itself.

Example usage of the Receiver setting the result expiration timestamp is when the value of the delivery time is dependent upon some changing Receiver context e.g., Result message deadline for aircraft position based upon velocity.

cs: status codes (e.g., authorization timeout, etc.).

### 8.1.4	Summary of Response Message Parameters

Table 8.1.4-1 summarises the parameters specified in clauses 1.3 for the Response messages, showing any differences as applied to successful C, R, U, D or N operations, and unsuccessful operations. "M" indicates mandatory, "O" indicates optional, "N/A" indicates "not applicable".

# Table 8.1.4-1: Summary of Response Message Parameters

| Response message parameter \ success or not | Rs = Ack | Rs = successful: Op = Create: a new resource is created | Rs= successful: Op= Retrieve: an existing resource is read and the result is provided | RS= successful. Op= Update: the content of an existing resource is replaced with new content | RS= successful. Op = Delete: an existing resource and all its sub-resources are deleted | Rs= successful Op= Notify: the content / address is transferred | RS = unsuccessful Op = C,R,U,D or N |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Response Code (rs) - successful, unsuccessful, ack | M | M | M | M | M | M | M |
| Request Identifier (ri) – uniquely identifies a Request message | O | O | O | O | O | O | O |
| Content (cn) - to be transferred | N/A | O (The address and/or the content of the created resource) | M (the retrieved resource content or aggregated contents of discovered resources) | O (The content replaced in an existing resource) | O (The content actually deleted) | N/A | O (Additional error info) |
| To (to) –the identifier of the Originator | O | O | O | O | O | O | O |
| From (fr) – the identifier of the Receiver | O | O | O | O | O | O | O |
| Originating Timestamp (ot) - when the message was built | O | O | O | O | O | O | O |
| Result Expiration Timestamp (rset) – when the message expires | O | O | O | O | O | N/A | O |
| Status codes (cs) - (e.g., authorization timeout, etc.) | O | O | O | O | O | O | O |
| Response Address (ra) - address for the temporary storage of end node Responses. | O | O | O | O | O | N/A | N/A |

### -----------------------End of change 1---------------------------------------------