| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Heedong Choi, LG Electronics, heedong.choi@lge.com |
| Format:* | ARC |
| Date:* | 2014-06-01 |
| Contact:* | Heedong Choi, LG Electronics, heedong.choi@lge.com |
| Reason for Change/s:* | Solve the Editor’s Note [10.2.12.c] |
| CR against: Release* | Pre-release |
| CR against: TS/TR* | TS-0001 v0.6.1 |
| Clauses/Sub Clauses* | 10.2.12, 9.6.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or (missing) functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

During previous TP#10, various locations were suggested for the notification threshold, the consensus has reached an agreement as follows:

[10.2.12.c]  Editor’s Note: The specific threshold mentioned above needs to be added as an attribute in the <CSEBase> resource type.

So, this contribution is to propose the specific threshold for the notification procedure under the <CSEBase> resource.

## -----------------------Start of change 1-------------------------------------------

### 10.2.12	Notification Procedures for Resource Subscription

This procedure shall be used to notify Receiver(s) of modifications of a resource for an associated <subscription> resource.

Originator: The Originator can be a CSE which is hosting a <subscription> resource. The Originator shall consider sending a notification request containing the subscribed information following the detection of a modification of the subscribed-to resource that matches the specified filterCriteria as specified in the <subscription> resource.

The Originator shall contain a notification structure and send this to Receiver(s).

In case the notification is forwarded or aggregated by transit CSEs, the originator shall contain attributes related to notification policies such as latestNotify or batchNotify in the notification so that transit CSE is able to enforce the policy defined by the subscriber.

[10.2.12.a]  Editor’s Note: The notification policy enforcement between subscription resource hosting CSE and the notification target CSE need to be FFS.

Receiver: The Receiver can be AE(s) or a CSE(s) which shall be presented in the notificationURI attribute of the <subscription> resource. The Receiver responds positively to the Request. The Receiver can also be a transit CSE in case the notification is forwarded or aggregated.

A considered Notification Request shall be sent when notification policies are satisfied.

The expirationCounter shall be decreased by one when the Originator successfully sends the notification request to Receiver(s). If the counter meets zero, the corresponding subscription resource is deleted.

The batchNotify policy is based on a minimum number of notification events and a maximum time to wait for that number of events. Notification events shall be temporarily stored for some duration (e.g., 10 minutes) or until a specified number are stored (e.g., 20 notifications) before sending - then sent when the first of these two conditions are satisfied. The sending order is first-in first out (FIFO). notificationEventCat is checked at the time of batch transmission and applied to each notification in the batch. Stored notification events may be dropped according to the notificationStoragePriority and the notificationCongestionPolicy (see clause 9.6.3).

The rateLimit policy is based upon a maximum specified number of events (e.g., 10, 000) that can be sent within some specified rateLimitWindow duration (e.g., 60 seconds). The ratelimitWindows are sequential (not rolling). A considered Notification Request may only be sent whenever the current total number of events sent is less than the maximum number of events within the current rateLimitWindow duration. Notification events that do not meet this policy are temporarily stored or dropped according to the notificationStoragePriority and the notificationCongestionPolicy (see clause 9.6.3). In the event that transmission of a batch triggers rate-limiting, the transmission of the batch shall complete, and the rate limiting mechanism may hold off sending subsequent notifications within the rateLimit unit time in which transmissions have exceeded the allowed notifications.

The interimEventsNotify policy indicates the notification action to be taken following a period of connectionless (e.g., reachability schedule, network malfunction), when Receiver(s) again become reachable. When a notification is ready to be sent, the Originator shall verify with CMDH CSF whether connectivity to the Receiver is currently allowed for the notification request. If that is the case, the notification shall be passed on to CMDH CSF for delivery. However, during the period of loss of connectivity the interimEventsNotify policy is applied if the notification message needs not to be immediately sent.

The interimEventsNotify attribute specifies how many of the most recent eligible notifications during the connectionless (interim) period shall be sent to Receiver(s) relative to Receiver(s) reconnect time. When a notification becomes eligible in the connectionless period, it is temporarily stored in the Originator. After the connection recovery, the Originator shall determine which notifications to send according to the interimEventsNotify attribute and send notifications (if available) to Receiver(s). The interimEventsNotify attribute shall be classified into "sendNo" (i.e., ignore prior notifications), "sendLatest" (i.e., send the last pending notification), "sendAll" (i.e., send all pending notifications).

Figure 10.2.12-1: Notification Mechanism when interimEventsNotify (sendNo) is used

Figure 10.2.12-2: Notification Mechanism when interimEventsNotify (sendLatest) is used

Figure 10.2.12-3:  Notification Mechanism when interimEventsNotify (sendAll) is used

The priorSubscriptionNotify policy indicates the notification action to be taken following a new subscription. It enables sending of event notifications, which happened before the new subscription was created. When a new subscription is created, the most recent number "n" subscription events prior to the new subscription shall be sent to Receiver(s), if available.

The latestNotify indicates if the subscriber is only interested in the latest state of the subscribed-to resource. In the case the Receiver is a transit CSE which forwards or aggregates the notifications before sending to the subscriber or the other transit CSEs, upon receiving the notification with the latestNotify attribute, the Receiver shall identify the latest notification with the same subscription reference while storing the notifications locally. When the receiver as an transit CSE needs to send the pending notifications, it shall send the latest notification.

[10.2.12.b] Editor’s Note: How the latestNotify is carried in the notification is FFS.

The notificationDeliveryPriority policy indicates how to prioritise sending of notifications when notifications need to be sent. A notification with the higher priority indicated by the notificationDeliveryPriority attribute shall be sent before notifications with the lower priority. In order not to constantly defer notifications with the lower priority; expiration time of the notification needs to be taken into account. In case the connectivity is lost and the notification priority exceeds the notificationThreshold attribute in the <CSEBase> resource, then if the loss of connectivity is due to the Originator’s schedule then the schedule will be over-ridden and that notification shall be sent immediately.

The notificationEventCat policy indicates an Event Category of the subscription that will be included in the notification request to be able for the Receiver to correctly handle the notification. When the notificationEventCat policy is not configured by the subscriber, it shall be determined as a default value by the CMDH policy.

Table 10.2.12-1:  Notification Procedure

| Description |
| --- |
| Call Flow Type | NOTIFY |
| Pre-Conditions | Notification is triggered regarding subscription information in a <subscription> resource |
| Information on Request message | fr: ID of the Originator to: notificaitonURI specified in <subscription> resource cn: notification data that represents the modified content of subscribed-to resource may be included subscription reference (i.e., URI of the corresponding <subscription> resource) that generates this notification shall be included changed resource status shall be included when resourceStatus filter criteria condition is configured monitored operation shall be included when operationMonitor filter criteria condition is configured |
| Information on Response message | No change from the basic procedure |
| Post-Conditions | None |
| Exceptions | None |

## -----------------------End of change 1-------------------------------------------

## -----------------------Start of change 2-------------------------------------------

### 9.6.3	Resource Type CSEBase

A <CSEBase> resource shall represent a CSE. This <CSEBase> resource shall be the root for all the resources that are residing on the CSE.

Figure 9.6.3-1: Structure of <CSEBase> resource

[9.6.3.a0] Editor's Note; The picture above needs to be updated as per the new structure of CSEBase resource.

The <CSEBase> resource shall contain the child resources in Table 9.6.3-1.

Table 9.6.3-1: Child resources of <CSEBase> resource

| Child Resource Name of <CSEBase> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <remoteCSE> | 0..n | See clause 9.6.4 |
| [variable] | <node> | 0..n | See clause 9.6.18 |
| [variable] | <AE> | 0..n | See clause 9.6.5 |
| [variable] | <container> | 0..n | See clause 9.6.6 |
| [variable] | <group> | 0..n | See clause 9.6.13 |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |
| [variable] | <mgmtCmd> | 0..n | See clause 9.6.16 |
| [variable] | <locationPolicy> | 0..n | See clause 9.6.10 |
| [variable] | <statsConfig> | 0..n | See clause 9.6.22 |
| [variable] | <statsCollect> | 0..n | See clause 9.6.24 |

The <CSEBase> resource shall contain the attributes described in Table 9.6.3-2.

Table 9.6.3-2: Attributes of <CSEBase> resource

| Attribute Name of <CSEBase> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 | RW | See clause 9.6.1 where this common attribute is described. |
| labels | 0..1 | RW | See clause 9.6.1 where this common attribute is described. |
| cseType | 1 | WO | Indicates the type of CSE node represented by the created resource. |
| CSE-ID | 1 | WO | The globally unique CSE identifier. |
| supportedResourceType | 1 | RO | List of the resource types which are supported in CSE. this attribute contains subset of resource types listed in clause 9.2 |
| pointOfAccess | 0..n | RW | Represents the list of physical addresses to be used by remote CSEs to connect to this CSE (e.g., IP address, FQDN). This attribute is used to announce its value to remote CSEs. |
| nodeLink | 0..1 | RO | A reference (URI) of a <node> resource that stores the node specific information. |
| Trigger-Recipient-ID | 0..1 | RW | See clause 7.1.10 where this attribute is described. |
| notificationCongestionPolicy | 0..1 | RO | This attribute applies to CSEs generating subscription notifications. It specifies the rule which is applied when the storage of notifications for each subscriber (an AE or CSE) reaches the maximum storage limit for notifications for that subscriber. E.g., Delete stored notifications of lower notificationStoragePriority to make space for new notifications of higher notificationStoragePriority, or delete stored notifications of older creationTime to make space for new notifications when all notifications are of the same notificationStoragePriority. |
| notificationThreshold | 0..1 | RW | Indicates the threshold for the priority-based notification procedure of a <subscription> resource. E.g., a notification with higher notificationDeliveryPriority than notificationThreshold is preferentially sent. |

## -----------------------End of change 2-------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?