| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Heedong Choi, LG Electronics, heedong.choi@lge.com |
| Format:* | ARC |
| Date:* | 2014-06-01 |
| Contact:* | Heedong Choi, LG Electronics, heedong.choi@lge.com |
| Reason for Change/s:* | Clarify the interimEvetsNotify attribute |
| CR against: Release* | Pre-release |
| CR against: TS/TR* | TS-0001 v0.6.1 |
| Clauses/Sub Clauses* | 9.6.8, 10.2.12 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or (missing) functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution tries to clarify the interimEvetsNotify attribute in the subscription resource.

For easy understanding, the attribute name is changed to the pendingNotificationAction.

Although a notification is occurred in the Originator after the successful subscription procedure, the corresponding notification may not be sent to the Receiver due to a period of unreachability. The examples of an unreachable period are as follows:

reachability schedule (named <schedule> resource under the <remoteCSE> resources) is not allowed

notification schedule (named <notificationSchedule> resource under the <subscription> resource) is not allowed

node or network malfunction

Pending notification(s) during an unreachable period shall be processed by a certain policy. To take into account it, the pendingNotificationAction attribute is applied. The pendingNotificationAction attribute indicates the notification action to be taken following a period of unreachability.

The specific procedures are as follows:

First, the notification action(pendingNotificationAction) is configured by the subscriber. Here, it is classified into “sendNo” (i.e., ignore all pending notifications), “sendLatest” (i.e., send the last pending notification) and “sendAll” (i.e., send all pending notifications).

If the Originator has the pendingNotificationAction attribute after detection of a modification of the subscribed-to resource, the Originator checkes the reachability information for applying the pendingNotificationAction attribute.

The Originator takes care of pending notification(s) by using the notification action. After the reachability recovery, the processed notification is sent to the Receiver.

For example, if the pendingNotificationAction attribute is configured “sendNo”, pending notifications during a unreachable period shall be deleted by the Originator. When the Receiver becomes reachable, the Originator sent the processed notification to the Receiver.

## -----------------------Start of change 1-------------------------------------------

### 9.6.8	Resource Type subscription

Table 9.6.8-2: Attributes of <subscription> resource

| Attribute Name of <subscription> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | WO | See clause 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| labels | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 | RW | See clause 9.6.1 where this common attribute is described. If no accessControlPolicyIDs is given at the time of creation, the accesControlPolicies of the parent resource is linked to this attribute. |
| filterCriteria | 0..1 | RW | Filtering conditions that when applied and provide a not empty matching set of resources, then a notification can be sent to notificationURI. |
| expirationCounter | 0..1 | RW | When the number of notifications becomes the same as this counter, the <subscription> resource shall be deleted. |
| notificationURI | 1..n | RW | URI where the resource subscriber will receive notifications. |
| aggregationURI | 0..1 | RW | URI to aggregate notifications from group members of a <group> resource. |
| batchNotify | 0..1 | RW | Indicates that notifications should be batched for delivery. When set, notification events are temporarily stored until either a specified number is ready to send or until a duration after the first notification event has expired. |
| rateLimit | 0..1 | RW | Indicates that notifications should be rate-limited. When set, notification events that exceed a specified number within a specified time are temporarily stored then sent when the number of events sent per specified time falls below the limit. |
| priorSubscriptionNotify | 0..1 | WO | Indicates that when this subscription is created, whether notification events prior to subscription should be sent, e.g., send prior "n" notifications, if available. |
| pendingNotificationAction | 0..1 | RW | Indicates the notification action to be taken following a period of unreachability. When set, pending notification(s) during an unreachable period are processed by the corresponding pendingNotificationAction. |
| notificationStoragePriority | 0..1 | RW | Indicates a priority for this subscription relative to other subscriptions belonging to this same subscriber for retention of notification events when storage is congested. The storage congestion policy which uses this attribute as input is specified in clause 9.6.3. |
| latestNotify | 0..1 | RW | Indicates if the subscriber wants only the latest notification or all the notification. If the subscriber only wants the latest notification, older notifications can be discarded. The attribute is mutual exclusive with batchNotify. |
| notificationStructure | 1 | RW | Type of information that shall be contained in notifications. E.g., modified attribute only of a subscribed-to resource, a whole subscribed-to resource, and/or URI of a corresponding <subscription> resource. |
| notificationDeliveryPriority | 0..1 | RW | Indicates a delivery priority for the notification. That is, this attribute defines the how to handle sending of notifications when notifications need to be sent. |
| notificationEventCat | 0..1 | RW | Defines the Event Categories for the notification message triggered by the <subscription> resource. |

## -----------------------End of change 1-------------------------------------------

## -----------------------Start of change 2-------------------------------------------

### 10.2.12	Notification Procedures for Resource Subscription

This procedure shall be used to notify Receiver(s) of modifications of a resource for an associated <subscription> resource.

Originator: The Originator can be a CSE which is hosting a <subscription> resource. The Originator shall consider sending a notification request containing the subscribed information following the detection of a modification of the subscribed-to resource that matches the specified filterCriteria as specified in the <subscription> resource.

The Originator shall contain a notification structure and send this to Receiver(s).

In case the notification is forwarded or aggregated by transit CSEs, the originator shall contain attributes related to notification policies such as latestNotify or batchNotify in the notification so that transit CSE is able to enforce the policy defined by the subscriber.

[10.2.12.a]  Editor’s Note: The notification policy enforcement between subscription resource hosting CSE and the notification target CSE need to be FFS.

Receiver: The Receiver can be AE(s) or a CSE(s) which shall be presented in the notificationURI attribute of the <subscription> resource. The Receiver responds positively to the Request. The Receiver can also be a transit CSE in case the notification is forwarded or aggregated.

A considered Notification Request shall be sent when notification policies are satisfied.

The expirationCounter shall be decreased by one when the Originator successfully sends the notification request to Receiver(s). If the counter meets zero, the corresponding subscription resource is deleted.

The batchNotify policy is based on a minimum number of notification events and a maximum time to wait for that number of events. Notification events shall be temporarily stored for some duration (e.g., 10 minutes) or until a specified number are stored (e.g., 20 notifications) before sending - then sent when the first of these two conditions are satisfied. The sending order is first-in first out (FIFO). notificationEventCat is checked at the time of batch transmission and applied to each notification in the batch. Stored notification events may be dropped according to the notificationStoragePriority and the notificationCongestionPolicy (see clause 9.6.3).

The rateLimit policy is based upon a maximum specified number of events (e.g., 10, 000) that can be sent within some specified rateLimitWindow duration (e.g., 60 seconds). The ratelimitWindows are sequential (not rolling). A considered Notification Request may only be sent whenever the current total number of events sent is less than the maximum number of events within the current rateLimitWindow duration. Notification events that do not meet this policy are temporarily stored or dropped according to the notificationStoragePriority and the notificationCongestionPolicy (see clause 9.6.3). In the event that transmission of a batch triggers rate-limiting, the transmission of the batch shall complete, and the rate limiting mechanism may hold off sending subsequent notifications within the rateLimit unit time in which transmissions have exceeded the allowed notifications.

The pendingNotificationAction indicates the notification action to be taken following an unreachable period (due to lack of Originator’s notification schedule or reachability schedule, node or network malfunction). When a notification is generated and the corresponding <subscription> resource has pendingNotificationAction, the Originator shall verify the reachability to the Receiver with both the Originator’s and Receiver’s <schedule> resource If there is a reachability, the notification is immediately sent. Otherwise, the pendingNotificationAction is applied. The pendingNotificationAction shall be "sendNo" (i.e., ignore all pending notifications), "sendLatest" (i.e., send the last pending notification), "sendAll" (i.e., send all pending notifications).

## -----------------------End of change 2-------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?