| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | TS-0007 Mca Request Services |
| Source:* | George Foti, Ericsson, George.Foti@ericsson.com |
| Contact: | George Foti, Ericsson, George.Foti@ericsson.com |
| Date:* | 2014-05-30 |
| Abstract:* |  |
| Agenda Item:* |  |
| Work item(s): | TS-0007 WI |
| Document(s) Impacted* | TS-0007 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Update TS for inclusion |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------Start of change 1-------------------------------------------

# 6	M2M Services

This clause describes the M2M Services provided by the M2M Services Platform.

## 6.1	Introduction

The M2M Services defined in this clause are utilized by the Business Services described in the Annexes of this specification.

Figure 6.1-1: oneM2M Services

## 6.X	Registration Services

## 6.x.1 Overview

The Registration service provides the ability for:

- Initial Registration of an AE

- Refresh an existing Registration

- AE Initiated termination of an existing Registration

- Retrieve an AE Registration status

- Revoke an AE existing Registration

### 6.X.2	Service Capabilities

#### 6.X.2.1	Initial Registration of an AE

This service capability enables an AE to register with the M2M System

##### 6.X.2.1.1	Pre-conditions

##### The AE has not registered with the M2M Service Platform

##### 6.X.2.1.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | The identifier of the originator that is issuing the request. |
| requestedAEId | IN | YES | The Application Instance Identifier (AE-ID) that the Originator has requested to be used for future exchanges between the AE and the M2M System. See TS00001 for details |
| pointOf Access (POA) | IN | NO | The point of Access of the registered AE. See TS00001 for details |
| App-ID | IN | NO | The Application Identifer (App-ID). See TS00001 for details |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator. |
| applicationToken | IN | YES | The Application Token. To be confirmed |
| returnCode | OUT | NO | Return codes: AE successfully registered AE not successfully registered |
| expirationTime | OUT | Conditionaly optional | If different than the requested expiration time |
| AE-ID | OUT | Conditionaly optional | AE-ID is provided back in the response if not provided by the AE |

Table 6.X.2.1.2-1 AE Initial Registration Signature

##### 6.X.2.1.3	Post-Conditions

AE is registered and can start using service capabilities.

##### 6.X.2.1.4	Exceptions

Not Applicable

##### 6.X.2.1.5	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

### 6.X.2.1.6	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations:

- Create AE

### 6.X.2.1.7	oneM2M Roles Association

Editors note: The oneM2M Roles Association will be identified once Annex G of TS-0001 has identified the roles for the M2M Services

#### 6.X.2.2	Refreshing an existing Registration of an AE

This service capability enables an AE to refresh an exiating registration with the M2M System

##### 6.X.2.2.1	Pre-conditions

##### The AE has successfully registered with the M2M System

##### 6.X.2.2.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | The identifier of the originator that is issuing the request. |
| requestedAEId | IN | NO | The Application Instance Identifier (AE-ID). See TS00001 for details |
| pointOf Access (POA) | IN | NO | The point of Access of the registered AE. See TS00001 for details |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator. |
| returnCode | OUT | NO | Return codes: AE successfully refreshed Registration Does not exist |
| expirationTime | OUT | Conditional optional | If different than the requested expiration time |

Table 6.X.2.2.2-1 AE Refresh Registration Signature

##### 6.X.2.2.3	Post-Conditions

Not Applicable

##### 6.X.2.2.4	Exceptions

Not Applicable

##### 6.X.2.2.5	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

### 6.X.2.2.6	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations:

- Update AE

### 6.X.2.2.7	oneM2M Roles Association

Editors note: The oneM2M Roles Association will be identified once Annex G of TS-0001 has identified the roles for the M2M Services

#### 6.X.2.3	AE Initiated termination of an existing Registration

This service capability enables an AE to deregister from the M2M System

##### 6.X.2.3.1	Pre-conditions

##### The AE successfully registered with the M2M System

##### 6.X.2.3.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | The identifier of the originator that is issuing the request. |
| requestedAEId | IN | NO | The Application Instance Identifier (AE-ID). See TS00001 for details |
| returnCode | OUT | NO | Return codes: AE successfully De-registsred Registration Does not exist |

Table 6.X.2.3.2-1 AE Refresh Registration Signature

##### 6.X.2.3.3	Post-Conditions

AE is no longer registsred and cannot use any services

##### 6.X.2.3.4	Exceptions

Not Applicable

##### 6.X.2.3.5	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

### 6.X.2.3.6	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations:

- Delete AE

### 6.X.2.3.7	oneM2M Roles Association

Editors note: The oneM2M Roles Association will be identified once Annex G of TS-0001 has identified the roles for the M2M Services

#### 6.X.2.4	Retrieve Registration Status

This service capability enables any M2M component to retrieve the registration status for an AE

##### 6.X.2.4.1	Pre-conditions

##### N/A

##### 6.X.2.4.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | The identifier of the originator that is issuing the request. |
| requestedAEId | IN | NO | The Application Instance Identifier (AE-ID). See TS00001 for details |
| returnCode | OUT | NO | Return codes: AE successfully Retrieved Registration does not exist |
| pointOf Access (POA) | IN | NO | The point of Access of the registered AE. See TS00001 for details |
| App-ID | IN | NO | The Application Identifer (App-ID). See TS00001 for details |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator. |

Table 6.X.2.4.2-1 AE Reading of Registration Signature

##### 6.X.2.4.3	Post-Conditions

N/A

##### 6.X.2.4.4	Exceptions

Not Applicable

##### 6.X.2.4.5	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

### 6.X.2.4.6	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations:

- Read AE

### 6.X.2.4.7	oneM2M Roles Association

Editors note: The oneM2M Roles Association will be identified once Annex G of TS-0001 has identified the roles for the M2M Services

#### 6.X.2.5	Revoke an AE existing Registration

This service capability enables the M2M system to revoke an existing AE registration

##### 6.X.2.5.1	Pre-conditions

##### The AE successfully registered with the M2M Service Platform

##### 6.X.2.5.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| Issuer | IN | NO | The identifier of the originator that is issuing the request. |
| AE-ID | IN | NO | he Application Instance Identifier (AE-ID) |
| returnCode | OUT | NO | Return codes: AE successfully De-registsred Registration does not exist |

Table 6.X.2.3.2-1 AE Refresh Registration Signature

##### 6.X.2.5.3	Post-Conditions

AE is no longer registsred and cannot use any services

##### 6.X.2.5.4	Exceptions

Not Applicable

##### 6.X.2.5.5	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

### 6.X.2.5.6	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations:

- Delete AE

### 6.X.2.5.7	oneM2M Roles Association

Editors note: The oneM2M Roles Association will be identified once Annex G of TS-0001 has identified the roles for the M2M Services

### -----------------------Start of change 2 -------------------------------------------

## 7.3	Infrastructure Component (INF)

The INF Component provides Services that are exposed to other  M2M Service Components across the Msc reference point.  The Services within the INF Component are common and utility type Services needed to enable other M2M Services.

## 7.3.1	INF to Service Cross Reference

Authorization: All Service Capabilities

ServiceSubscription: retrieveAuthorization

Registration Services: Return registration Status, Revoke of an AE existing Registration

## 7.6	Service Exposure (SE)

The SE Component acts as the primary interface for AEs to interact with the M2M Service Layer across the Mca reference point.

## 7.6.1	Service Exposure to Service Cross Reference

SE Data Exchange: All Service Capabilities

Service Subscription: getBroker

Broker: publish, subscribe

Registration Services: Initial Registration of an AE, Refreshing an existing Registration of an AE, AE Initiated termination of an existing Registration.

### -----------------------Start of change 3 -------------------------------------------

### X.1.1	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| Name of the parameter. | IN, OUT, IN-OUT | YES, No, Conditional optional on the IN, conditional optional on the OUT | Description of the parameter in the context of the service capability. |

Table X.1.1-1 Service Capability Signature