| CHANGE REQUEST |
| --- |
| Group Name:* | TP11 |
| Source:* | InterDigital |
| Format:* | ARC #11 |
| Date:* | <2014-06-01> |
| Contact:* | Guang Lu, InterDigital, Guang.Lu@InterDigital.com |
| Reason for Change/s:* | Call flow clean up - Remove CSFs from SCA call flows |
| CR against: Release* | 1 |
| CR against: TS/TR* | oneM2M-TS-0001 , V-0.7.0 |
| Clauses/Sub Clauses* | 10.2.15 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Since the CSF texts are informative, this CR removed all references of CSFs in section 10.2.15. The CR was submitted to ARC 10bis but was not treated so it was reapplied to TS 0001 v0.7.0 and submitted to ARC11.

Updated “statsModel” to “statModel” to be consistent with section 9.6.24.

### ----------------------------------Start of change 1 -----------------------------------------

### 10.2.15	Service Charging and Accounting Procedures

#### 10.2.15.1	Introduction

This clause is informative and provides a use case example to explain how the Infrastructure Node provides statistics for AEs using the <statsConfig> and <statsCollect> resources as defined in clauses 9.6.22, 9.6.23.and 9.6.24.

##### 10.2.15.1.1	Service Event-based Statistics Collection for Applications

Figure 10.2.15.1-1 shows an example of service layer event-based charging based on the Infrastructure Node.

Step 1-2:	A statistics collection resource called <statsConfigSCA1> was created at the IN-CSE by a billing application. Note that the <statsConfig> can also be provisioned. In this use case, the <statsConfigSCA1> has the <eventConfig> sub-resource. For this specific use case, the <eventConfig> can be set as following: The "eventID" is set with a unique ID to differentiate from other chargeable events. The "eventType" defines what event will trigger the generation of service statistics collection record and is set to "Data Operation" for this case. "eventStart" and "eventEnd" apply to timer based event so they will not be included in this event. "transactionType" will be "RETRIEVE". "dataSize" does not apply so it is not included.

Step 3-5:	In this example, AE1 already registered to IN-CSE. IN-CSE can make the statistics collection configuration accessible by AE. Based on the <statsConfigSCA1>, AE1 creates a statistics collection trigger for itself, stored in <statsCollectAE1>. AE1 will fill in the information for the collection rule. For example, it fills the "collectingEntityID" with the App-ID of AE1, and the "collectedEntityID" empty, which means to collect for any entities. "status" is set to "Active". The "statModel" is "event-based". The "subscriberID" is set to the M2M-Sub-ID for AE1. The "eventID" is set with the same ID value as the "eventID" in the  <statsConfigSCA1>.  This event collection trigger can be saved at the IN-CSE and IN-CSE will assign a unique ID in attribute "statsCollectID".

Step 6-8:	When the configure event happens, i.e. when AE2 performed a RETRIEVE operation to the data owned by AE1 at IN-CSE, the event is recorded by IN-CSE. IN-CSE generates a service statistics collection record that sends it to AE1. AE1 can choose to use such information for its own billing.

Step 9:	The AE of billing application can update or retrieve the charging policies and collection scenarios that it has the access control privilege.

Figure 10.2.15.1-1: Event-based Statistics Collection for Applications

#### 10.2.15.2	CREATE <statsConfig>

This procedure shall be used for the Originator to establish a set of configurations for statistics collection at the Receiver.

The configurations shall be stored at the <statsConfig> resource and each instance of the <statsConfig> resource shall represent a specific configuration.

Originator: The Originator shall be an AE or the IN-CSE that wants to set up the statistics collection configurations. According to the definition of the <statsConfig>, the Originator shall:

provide the sub-resource <eventConfig> for Event based statistics collection.

This sub-resource is used to define different events to be collected, each identified by a unique "eventID".

eventID: The "eventID" shall uniquely identify an event. The Originator may provide a value in the Request. The Receiver shall verify whether the ID is unique or not, and if not, provides a new value.

eventType: The "eventType" is a mandatory attribute. The Originator shall provide an eventType. An example of an eventType is "Data Operation", which means that chargeable events information recording is triggered when the charged entity conducts a data operation. "Data Operation" can be further refined by the "transactionType" attribute.

eventStart: The "eventStart" is an optional attribute. The Originator shall provide a start time for the event only if the "eventType" is set to "Timer based".

eventEnd: The "eventEnd" is an optional attribute. The Originator shall provide an end time for the event only if the "eventType" is set to "Timer based".

transactionType: The "transactionType" is an optional attribute. Examples of "transactionType" can be "CREATE", "RETRIEVE".

dataSize: The "dataSize" is an optional attribute. The Originator shall provide a value for it only if the "eventType" is set to "Storage based".

Receiver: The Receiver shall be an IN-CSE. The Receiver shall validate whether the Originator has proper permissions for creating a <statsConfig> resource, and whether the values provides in the Request message are valid. Upon successful validation, the Receive shall create a new <statsConfig> resource with the provided values.

Table 10.2.15.2-1: CREATE Call Flow

| Description |
| --- |
| Call flow type | CREATE |
| Pre-conditions | Originator needs to create a <statsConfig> resource at the Receiver |
| Information on Request message | op: Create fr: ID of the Originator to: URI of the parent of the target resource to be created cn: contain the resource representation of <statsConfig> The Originator can provide the <eventConfig> sub-resource to enable event-based configuration for statistics collection The Originator may specify other Optional parameters as discussed in clause 8.1.2 Request |
| Local processing on Receiver CSE | No change from the generic procedure |
| Generic Information on Response message | No change from the generic procedure |
| Post-conditions | None |
| Exceptions | No change from the generic procedure |

#### 10.2.15.3	RETRIEVE <statsConfig>

The RETRIEVE call flow shall be used for the Originator to retrieve the existing <statsConfig> resource from the Receiver.

Originator: The Originator shall be an AE that is allowed to retrieve configuration information available for AEs within an IN-CSE

Receiver: The Receiver shall be the IN- CSE containing the <statsConfig> resource. The Receiver shall verify if the Originator has the READ permission on the <statsConfig> resource targeted. Upon successful validation, the Receiver CSE shall respond to the Originator with the resource representation.

Table 10.2.15.3-1: RETRIEVE Call Flow

| Description |
| --- |
| Call flow type | RETRIEVE |
| Pre-conditions | Originator needs to retrieve the <statsConfig> resource at the Receiver |
| Information on Request message | op: Retrieve fr: ID of the Originator to: URI of the <statsConfig> resource or its attribute or sub-resource to be retrieved cn: void The Originator may specify other Optional parameters as discussed in clause 8.1.2 Request |
| Local processing on Receiver CSE | No change from the generic procedure |
| Generic Information on Response message | No change from the generic procedure |
| Post-conditions | None |
| Exceptions | No change from the generic procedure |

#### 10.2.15.4	UPDATE <statsConfig>

An UPDATE procedure on the <statsConfig> resource is used for the Originator to update charging related policies at the Receiver.

Originator: The Originator shall be the AE that created the <statsConfig> resource. The same AE shall be able to update the resource.

Receiver: The Receiver shall be a CSE containing the <statsConfig> resource. The Receiver shall check if the Originator has the WRITE permission to update the addressed resource.

Table 10.2.15.4-1: UPDATE Call Flow

| Description |
| --- |
| Call flow type | UPDATE |
| Pre-conditions | The Originator needs to update the charging policies that it established at the Receiver by using the <statsConfig> resource |
| Information on Request message | op: Update fr: ID of the Originator to: URI of the <statsConfig> resource or its attribute or sub-resource to be updated cn: the Originator provides the sub-resource or attributes to be updated The Originator can update attributes under <eventConfig> to update event-based configuration for statistics collection The Originator may specify other Optional parameters as discussed in clause 8.1.2 Request |
| Local processing on Receiver CSE | No change from the generic procedure |
| Generic Information on Response message | No change from the generic procedure |
| Post-conditions | None |
| Exceptions | No change from the generic procedure |

#### 10.2.15.5	DELETE <statsConfig>

Originator: The Originator shall be the AE that created the <statsConfig> resource.

Receiver: The Receiver shall be a CSE containing the <statsConfig> resource.

Table 10.2.15.5-1: DELETE Call Flow

| Description |
| --- |
| Call flow type | DELETE |
| Pre-conditions | Originator needs to DELETE the <statsConfig> resource at the Receiver |
| Information on Request message | op: Delete fr: ID of the Originator to: URI of the <statsConfig> resource to be deleted cn: void The Originator may specify other Optional parameters as discussed in clause 8.1.2 Request |
| Local processing on Receiver CSE | No change from the generic procedure |
| Generic Information on Response message | No change from the generic procedure |
| Post-conditions | None |
| Exceptions | No change from the generic procedure |

#### 10.2.15.6	CREATE <statsCollect>

This procedure shall be used for the Originator to establish collection scenarios at the Receiver.

The collection scenarios are stored at the  <statsCollect> resource. Multiple collection scenarios can be created based on one <statsConfig>.

Originator: The Originator shall be an AE that wants to set up the collection scenarios to an IN- CSE. According to the definition of the <statsCollect>  resource, the Originator shall populate the attributes defined for the <statsCollect> resource except for "statsCollectID". (see clause 9.6.24). The "statsCollectID" shall be unique in the same service provider domain. To ensure the uniqueness, the IN-CSE shall create the statsCollectID.

Here are other attributes in the <statsCollect> resources:

collectingEntityID: The "collectingEntityID" is a mandatory attribute. The Originator shall provide the ID as defined in  clause 7.1 to identify the entity that charges.

collectedEntityID: The "collectedEntityID" is a mandatory attribute. The Originator shall provide the ID as defined in  clause 7.1 to identify the entity that being charged.

status: The "status" is a mandatory attribute. The Originator shall set the value for this attribute to specify the status of the rule. Examples of values can be "ACTIVE", "INACTIVE".

statModel: The "statModel" is a mandatory attribute. The Originator shall set the value to indicate a collection model. Examples of values can be "subscriber-based", "event-based".

subscriberID: The "subscriberID" is a mandatory attribute. It is the service subscriber ID for the collected entity. The Originator shall provide the "M2M-Sub-ID" as defined in clause 7.1.

collectPeriod: The "collectPeriod" is an optional attribute. It applies to the subscriber-based charging model. The Originator shall provide a value of the information recording collection period. An example of the value can be "monthly".

eventID: The "eventID" is an optional attribute. The Originator shall provide a value only if the "statModel" is "event-based". The Originator shall provide the eventID that is defined in the resource <statsConfig>. Since there can be many different chargeable events defined by different charging policies, the eventID uniquely identifies the specific chargeable event for this charging rule.

Receiver: The Receiver shall be an IN-CSE. The Receiver shall validate whether the Originator has proper permissions for creating a <statsCollect> resource. Upon successful validation, create a new <statsCollect> resource with the provided attributes. The IN-CSE shall also create a unique "statsCollectID".

Once a <statsCollect> is created and the "status" is "ACTIVE, the IN-CSE shall generate service statistics collection record when the conditions defined by the rules are met.

Table 10.2.15.6-1: CREATE Call Flow

| Description |
| --- |
| Call flow type | CREATE |
| Pre-conditions | Originator needs to create a <statsCollect> resource at the Receiver |
| Information on Request message | op: Create fr: ID of the Originator to: URI of the parent of the target resource to be created cn: contain the resource representation of <statsCollect> The Originator may specify other Optional parameters as discussed in clause 8.1.2 Request |
| Local processing on Receiver CSE | No change from the generic procedure |
| Generic Information on Response message | No change from the generic procedure |
| Post-conditions | None |
| Exceptions | No change from the generic procedure |

#### 10.2.15.7	RETRIEVE <statsCollect>

The RETRIEVE call flow shall be used for the Originator to retrieve the existing <statsCollect> resource from the Receiver.

Originator: The Originator shall be an AE that is allowed to retrieve the collection scenario information from the IN-CSE.

Receiver: The Receiver shall be the IN- CSE containing the <statsCollect> resource. The Receiver shall verify if the Originator has the READ permission on the <statsCollect> resource targeted. Upon successful validation, the Receiver CSE shall respond to the Originator with the resource representation.

Table 10.2.15.7-1: RETRIEVE Call Flow

| Description |
| --- |
| Call flow type | RETRIEVE |
| Pre-conditions | Originator needs to retrieve the <statsCollect> resource at the Receiver |
| Information on Request message | op: Retrieve fr: ID of the Originator to: URI of the <statsCollect> resource or its attribute to be retrieved cn: void The Originator may specify other Optional parameters as discussed in clause 8.1.2 Request |
| Local processing on Receiver CSE | No change from the generic procedure |
| Generic Information on Response message | No change from the generic procedure |
| Post-conditions | None |
| Exceptions | No change from the generic procedure |

#### 10.2.15.8	UPDATE <statsCollect>

An UPDATE procedure on the <statsCollect> resource is used for the Originator to update charging related policies at the Receiver.

Originator: The Originator shall be the AE that created the <statsCollect> resource. The same AE shall be able to update the resource.

Receiver: The Receiver shall be a CSE containing the <statsCollect> resource. The Receiver shall check if the Originator has the WRITE permission to update the addressed resource.

Table 10.2.15.8-1: UPDATE Call Flow

| Description |
| --- |
| Call flow type | UPDATE |
| Pre-conditions | The Originator needs to update the collection scenarios that it established at the Receiver by updating the <statsCollect> resource |
| Information on Request message | op: Update fr: ID of the Originator to: URI of the <statsCollect> resource or its attribute to be updated cn: the Originator provides the attributes to be updated The Originator may specify other Optional parameters as discussed in clause 8.1.2 Request |
| Local processing on Receiver CSE | No change from the generic procedure |
| Generic Information on Response message | No change from the generic procedure |
| Post-conditions | None |
| Exceptions | No change from the generic procedure |

#### 10.2.15.9	DELETE <statsCollect>

Originator: The Originator shall be the AE that created the <statsCollect> resource.

Receiver: The Receiver shall be a CSE containing the <statsCollect> resource .

Table10. 2.15.9-1: DELETE Call Flow

| Description |
| --- |
| Call flow type | DELETE |
| Pre-conditions | Originator needs to DELETE the <statsCollect> resource at the Receiver |
| Information on Request message | op: Delete fr: ID of the Originator to: URI of the <statsCollect> resource to be deleted cn: void The Originator may specify other Optional parameters as discussed in clause 8.1.2 Request |
| Local processing on Receiver CSE | No change from the generic procedure |
| Generic Information on Response message | No change from the generic procedure |
| Post-conditions | None |
| Exceptions | No change from the generic procedure |

#### 10.2.15.10	Service Statistics Collection Record

When the Service Statistics Collection is supported, the Information Elements shall be generated according to table 10.2.15.10-1.

The contents of each Service statistics collection record are decided by the specific collection scenario that triggered the information recording.

Table 10.2.15.10-1: Information Elements for Service Statistics Collection Record

| Information Element | Mandatory / optional | Description |
| --- | --- | --- |
| statsCollectID | M | It is the unique ID that identifies a specific statistics collection scenario, which triggers information recording for a specific event. |
| collectingEntityID | M | This is the unique ID of the entity that collects the statistics. It can be an AE-ID or CSE-ID |
| collectedEntityID | M | This is the unique ID of the entity whose service layer operation statistics are being collected. It can be an AE-ID or CSE-ID. |
| subscriberID | M | The M2M service subscription ID M2M-Sub-ID if the collected entity |
| event | O | This indicates a specific event type in each record, such as timer based, data operation, storage triggering. It is only present if the statModel is "event based" |
| eventStart | O | The start time for the recording the M2M event record |
| eventEnd | O | The end time for the recording the M2M event record |
| transactionType | O | Specifies the detailed type of a transaction, such as CREATE, RETRIEVE, etc. |
| dataSize | O | Storage Memory in Kbytes, where applicable, to store data associated events with container related operations |
| Vendor Specific Information | O | Defines Vendor specific information |

### -----------------------------------End of change 1------------------------------------------