| CHANGE REQUEST |
| --- |
| Group Name:* | TP#11 |
| Source:* | Huawei Technologies Co., Ltd. |
| Format:* | Plenary |
| Date:* | 2014-6-10 |
| Contact:* | Jiaxin Yin, Yinjiaxin@huawei.com |
| Reason for Change/s:* | The contribution is for the update of latestNotify to clarify more about the usage of the attribute. |
| CR against: Release* | One |
| CR against: TS/TR* | TS0001 v0.7.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The contribution is a bug fix to the current latestNotify attribute as some delegates think it should be combined with CMDH Policy.

### -----------------------Start of change 1---------------------------------------------

### 9.6.8	Resource Type subscription

The <subscription> resource contains subscription information for its subscribed-to resource. The subscribed-to resource is the resource that has the <subscription> resource as the child resource.

The <subscription> resource shall be represented as child resource of the subscribed-to resource. For example, <container> resource has <subscription> resource as a child resource (see clause 9.6.6). A <subscription> resource shall be deleted when a parent subscribed-to resource is deleted.

The <subscription> resource shall represent a subscription to a subscribed-to resource. An Originator shall be able to create a resource of <subscription> resource type when the originator has RETRIEVE permission to the subscribe-to resource. The Originator of a <subscription> resource becomes a resource subscriber.

When a modification to the subscribed-to resource occurs, that modification is compared to the filterCriteria attribute to determine whether a notification is to be sent to the resource subscriber.

Figure 9.6.8-1: Structure of <subscription> resource

[9.6.8.a] Editor's Note: Verify if the picture needs to be re-drawn.

The <subscription> resource shall contain the child resources in table 9.6.8-1.

# Table 9.6.8-1: Child resources of <subscription> resource

| Child Resource Name of <subscription> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| notificationSchedule | <schedule> | 0..1 | See clause 9.6.9 |

The <subscription> resource shall contain the attributes described in table 9.6.8-2.

# Table 9.6.8-2: Attributes of <subscription> resource

| Attribute Name of <subscription> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | WO | See clause 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| labels | I | RW | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 | RW | See clause 9.6.1 where this common attribute is described. If no accessControlPolicyIDs is given at the time of creation, the accesControlPolicies of the parent resource is linked to this attribute. |
| filterCriteria | 0..1 | RW | Filtering conditions that when applied and provide a not empty matching set of resources, then a notification can be sent to notificationURI. |
| expirationCounter | 0..1 | RW | When the number of notifications becomes the same as this counter, the <subscription> resource shall be deleted. |
| notificationURI | 1..n | RW | URI where the resource subscriber will receive notifications. |
| aggregationURI | 0..1 | RW | URI to aggregate notifications from group members of a <group> resource. |
| batchNotify | 0..1 | RW | Indicates that notifications should be batched for delivery. When set, notification events are temporarily stored until either a specified number is ready to send or until a duration after the first notification event has expired. |
| rateLimit | 0..1 | RW | Indicates that notifications should be rate-limited. When set, notification events that exceed a specified number within a specified time are temporarily stored then sent when the number of events sent per specified time falls below the limit. |
| priorSubscriptionNotify | 0..1 | WO | Indicates that when this subscription is created, whether notification events prior to subscription should be sent, e.g. send prior "n" notifications, if available. |
| interimEventsNotify | 0..1 | RW | Indicates the notification action to be taken following a period of unreachability, when the resource subscriber becomes reachable (e.g. send "n" interim notifications, if available.) |
| notificationStoragePriority | 0..1 | RW | Indicates a priority for this subscription relative to other subscriptions belonging to this same subscriber for retention of notification events when storage is congested. The storage congestion policy which uses this attribute as input is specified in clause 9.6.3. |
| latestNotify | 0..1 | RW | Indicates if the subscriber wants only the latest notification when buffered notifications are transmitted on each connection towards the subscriber. If the subscriber only wants the latest notification, older notifications can be discarded. The attribute is mutual exclusive with batchNotify. |
| notificationStructure | 1 | RW | Type of information that shall be contained in notifications. E.g. modified attribute only of a subscribed-to resource, a whole subscribed-to resource, and/or URI of a corresponding <subscription> resource. |
| notificationDeliveryPriority | 0..1 | RW | Indicates a delivery priority for the notification. That is, this attribute defines the how to handle sending of notifications when notifications need to be sent. |
| notificationEventCat | 0..1 | RW | Defines the Event Categories for the notification message triggered by the <subscription> resource. |

The filterCriteria attribute shall be configured a priori in <subscription> resource and only if an event matches the filterCriteria conditions, then a notification shall be delivered.

Table 9.6.8-3 describes the filterCriteria conditions.

Table 9.6.8-3: filterCriteria conditions

| Condition tag | Multiplicity | Matching condition |
| --- | --- | --- |
| createdBefore | 0..1 | The creationTime attribute of the resource is chronologically before the specified value. |
| createdAfter | 0..1 | The creationTime attribute of the resource is chronologically after the specified value. |
| modifiedSince | 0..1 | The lastModifiedTime attribute of the resource is chronologically after the specified value. |
| unmodifiedSince | 0..1 | The lastModifiedTime attribute of the resource is chronologically before the specified value. |
| expireBefore | 0..1 | The expirationTime attribute of the resource is chronologically before the specified value. |
| expireAfter | 0..1 | The expirationTime attribute of the resource is chronologically after the specified value. |
| labels | 0..n | The labels attributes of the resource matches the specified value. |
| resourceType | 0..n | The resourceType attribute of the resource is the same as the specified value. It also allows discriminating between normal and announced resources. |
| sizeAbove | 0..1 | The contentSize attribute of the <contentInstance> resource is equal to or greater than the specified value. |
| sizeBelow | 0..1 | The contentSize attribute of the <contentInstance> resource is smaller than the specified value. |
| contentType | 0..n | The typeOfContent attribute of the <contentInstance> resource matches the specified value |
| resourceStatus | 0..n | When the resource is changed by the operations or expiration, the resource status of the resource is the same as the specified value. Possible values are: created, updated, deleted. |
| operationMonitor | 0..n | The operations accessing the resource matches with the specified value. It allows monitoring which operation is attempted to the subscribed resource regardless of whether the operation is performed. This feature is useful when to find malicious AEs. Possible string arguments are: create, retrieve, update, delete. |
| attribute | 0..n | Attribute token name to be provided to reduce the scope of filtering to resource attributes. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

#### 10.2.11.2	Create <subscription>

This procedure shall be used to request a new subscription to be notified for the modifications of a subscribed-to resource. Generic create procedure is described in clause 10.1.1.1.

Originator: The Originator can be an AE or a CSE. The Originator shall request to create a <subscription> resource. The Request shall address a subscribable resource.

The Request shall include notificationURI(s).

Receiver: Which is also the Hosting CSE shall validate the followings:

- if the subscribed-to resource, addressed in the to parameter in the Request, is a subscribable resource;

- if the Originator has  privileges for retrieving the subscribed-to resource;

- if the Originator has privileges to send notifications to the entity(ies) hosting notificationURI(s) when the Originator is not a hosting notificationURI;

- if it has access control privileges to send notifications to the entity(ies) that hosting notificationURI(s).

[10.2.11.2.b] Editor's Note: The validation process described in the last two bullet points above needs to be investigated further, This is FFS.

If all those checks are successfully done, the Hosting CSE shall send positive Response to the Originator.

If the latestNotify attribute is set, the Hosting CSE shall assign attribute ec of value ‘latest’  of the notifications generated pertaining to the subscription created.

# Table 10.2.11.2-1: <subscription> CREATE

| Description |
| --- |
| Call Flow Type | CREATE |
| Pre-Conditions | The Originator configures proper permissions and access control privileges described above |
| Information on Request message | All parameters defined in table 8.1.2.1-1 are applicable as indicated in the table with the specific details for: cn: The representation of the <subscription> resource for which the attributes are described in clause 9.6.8 The following attributes from clause 9.6.8 are mandatory for the request: "resourceType" which shall be set to the appropriate tag that identify the subscription resource as defined in clause 9.6.1 "notificationURI" "notificationStructure" All attributes indicated as optional in clause 9.6.8 are optional for the request. |
| Local processing on Hosting CSE | Check access privileges regarding creation of the <subscription> resource and sending notification to the notificationURI. |
| Information on Response message | No change from the generic procedure in clause 10.1.1.1 |
| Post-Conditions | None |
| Exceptions | All exceptions described in the basic procedure (clause 10.1.1.1) are applicable. |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3---------------------------------------------

#### 10.2.11.4	Update <subscription>

This procedure shall be used to update an existing subscription, e.g. extension of its lifetime or the modification of the notificationURI. Generic update procedure is described in clause 10.1.3.

Originator: The Originator can be an AE or a CSE. The Originator may send new value(s) for read-write attribute(s) of a <subscription> resource.

Receiver: Once the Originator has been successfully authenticated and access to the resource is granted by the Receiver (which is also the Hosting CSE), the Receiver shall update <subscription> resource.

If the latestNotify attribute is set, the Hosting CSE shall assign attribute ec of value ‘latest’  of the notifications generated pertaining to the subscription created.

# Table 10.2.11.4-1: <subscription> UPDATE

| Description |
| --- |
| Call Flow Type | UPDATE |
| Pre-Conditions | The Originator has UPDATE permission to the <subscription> resource |
| Information on Request message | All parameters defined in table 8.1.2.1-1 are applicable as indicated in the Table. |
| Local processing on Hosting CSE | No change from the generic procedure |
| Information on Response message | No change from the generic procedure |
| Post-Conditions | None |
| Exceptions | All exceptions described in the basic procedure (clause 10.1.1) are applicable. |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 10.2.12	Notification Procedures for Resource Subscription

This procedure shall be used to notify Receiver(s) of modifications of a resource for an associated <subscription> resource.

Originator: The Originator can be a CSE which is hosting a <subscription> resource. The Originator shall consider sending a notification request containing the subscribed information following the detection of a modification of the subscribed-to resource that matches the specified filterCriteria as specified in the <subscription> resource.

The Originator shall contain a notification structure and send this to Receiver(s).

In case the notification is forwarded or aggregated by transit CSEs, the originator shall contain attributes related to notification policies such as latestNotify or batchNotify in the notification so that transit CSE is able to enforce the policy defined by the subscriber.

[10.2.12.a]  Editor's Note: The notification policy enforcement between subscription resource hosting CSE and the notification target CSE need to be FFS.

Receiver: The Receiver can be AE(s) or a CSE(s) which shall be presented in the notificationURI attribute of the <subscription> resource. The Receiver responds positively to the Request. The Receiver can also be a transit CSE in case the notification is forwarded or aggregated.

A considered Notification Request shall be sent when notification policies are satisfied.

The expirationCounter shall be decreased by one when the Originator successfully sends the notification request to Receiver(s). If the counter meets zero, the corresponding subscription resource is deleted.

The batchNotify policy is based on a minimum number of notification events and a maximum time to wait for that number of events. Notification events shall be temporarily stored for some duration (e.g. 10 minutes) or until a specified number are stored (e.g. 20 notifications) before sending - then sent when the first of these two conditions are satisfied. The sending order is first-in first out (FIFO). notificationEventCat is checked at the time of batch transmission and applied to each notification in the batch. Stored notification events may be dropped according to the notificationStoragePriority and the notificationCongestionPolicy (see clause 9.6.3).

The rateLimit policy is based upon a maximum specified number of events (e.g. 10, 000) that can be sent within some specified rateLimitWindow duration (e.g. 60 seconds). The ratelimitWindows are sequential (not rolling). A considered Notification Request may only be sent whenever the current total number of events sent is less than the maximum number of events within the current rateLimitWindow duration. Notification events that do not meet this policy are temporarily stored or dropped according to the notificationStoragePriority and the notificationCongestionPolicy (see clause 9.6.3). In the event that transmission of a batch triggers rate-limiting, the transmission of the batch shall complete, and the rate limiting mechanism may hold off sending subsequent notifications within the rateLimit unit time in which transmissions have exceeded the allowed notifications.

The interimEventsNotify policy indicates the notification action to be taken following a period of connectionless (e.g. reachability schedule, network malfunction), when Receiver(s) again become reachable. When a notification is ready to be sent, the Originator shall verify with CMDH CSF whether connectivity to the Receiver is currently allowed for the notification request. If that is the case, the notification shall be passed on to CMDH CSF for delivery. However, during the period of loss of connectivity the interimEventsNotify policy is applied if the notification message needs not to be immediately sent.

The interimEventsNotify attribute specifies how many of the most recent eligible notifications during the connectionless (interim) period shall be sent to Receiver(s) relative to Receiver(s) reconnect time. When a notification becomes eligible in the connectionless period, it is temporarily stored in the Originator. After the connection recovery, the Originator shall determine which notifications to send according to the interimEventsNotify attribute and send notifications (if available) to Receiver(s). The interimEventsNotify attribute shall be classified into "sendNo" (i.e. ignore prior notifications), "sendLatest" (i.e. send the last pending notification), "sendAll" (i.e. send all pending notifications).

# Figure 10.2.12-1: Notification Mechanism when interimEventsNotify (sendNo) is used

# Figure 10.2.12-2: Notification Mechanism when interimEventsNotify (sendLatest) is used

Figure 10.2.12-3:  Notification Mechanism when interimEventsNotify (sendAll) is used

The priorSubscriptionNotify policy indicates the notification action to be taken following a new subscription. It enables sending of event notifications, which happened before the new subscription was created. When a new subscription is created, the most recent number "n" subscription events prior to the new subscription shall be sent to Receiver(s), if available.

The latestNotify indicates if the subscriber is only interested in the latest state of the subscribed-to resource. In the case the Receiver is a transit CSE which forwards or aggregates the notifications before sending to the subscriber or the other transit CSEs, upon receiving the notification with the ec set to ‘latest’, the Receiver shall identify the latest notification with the same subscription reference while storing the notifications locally. When the receiver as an transit CSE needs to send the pending notifications, it shall send the latest notification.

[10.2.12.b] Editor's Note: How the latestNotify is carried in the notification is FFS.

The notificationDeliveryPriority policy indicates how to prioritise sending of notifications when notifications need to be sent. A notification with the higher priority indicated by the notificationDeliveryPriority attribute shall be sent before notifications with the lower priority. In order not to constantly defer notifications with the lower priority; expiration time of the notification needs to be taken into account. In case the connectivity is lost and the notification priority exceeds a specific threshold, then if the loss of connectivity is due to the Originator's schedule then the schedule will be over-ridden and that notification shall be sent immediately.

[10.2.12.c]  Editor's Note: The specific threshold mentioned above needs to be added as an attribute in the <CSEBase> resource type.

The notificationEventCat policy indicates an Event Category of the subscription that will be included in the notification request to be able for the Receiver to correctly handle the notification. When the notificationEventCat policy is not configured by the subscriber, it shall be determined as a default value by the CMDH policy.

# Table 10.2.12-1: Notification Procedure

| Description |
| --- |
| Call Flow Type | NOTIFY |
| Pre-Conditions | Notification is triggered regarding subscription information in a <subscription> resource |
| Information on Request message | fr: ID of the Originator to: notificaitonURI specified in <subscription> resource cn: notification data that represents the modified content of subscribed-to resource may be included subscription reference (i.e. URI of the corresponding <subscription> resource) that generates this notification shall be included changed resource status shall be included when resourceStatus filter criteria condition is configured monitored operation shall be included when operationMonitor filter criteria condition is configured |
| Information on Response message | No change from the basic procedure |
| Post-Conditions | None |
| Exceptions | None |

### -----------------------End of change 4---------------------------------------------