| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | NEC |
| Format:* | TP11 |
| Date:* | 2014-06-11 |
| Contact:* | Barbara Pareglio (barbara.pareglio@neclab.eu); Martin Bauer (martin.bauer@neclab.eu) |
| Reason for Change/s:* | Changed definition of Node and added Device Node |
| Clause/Sub Clause Affected* | 3, 6 |
| Agenda Item:* | Contribution |
| Work item(s): |  |
| Document(s) Impacted* | oneM2M-TS 0001 Technical Architecture v 0 7 0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this into the TS (oneM2M-TS-0001) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Proposal

The current contribution is an update of ARC-2014-1251R03-Device_Node based on the agreed changes at ARC 11.0. It also uses the latest version 0.7.0 of TS 0001 as a basis for changes.

Note that the changes to figure 6.1-1 (addition of Non-oneM2M Node (NoDN) to IN) need to be done to an _editable_ version of the figure in TS 0001!

======================== START 1ST CHANGE ===========================

# 6	Configurations supported by oneM2M Architecture

## 6.1	Relationships among oneM2M Entities

Figure 6.1-1 illustrates the relationships among oneM2M entities supported by the oneM2M architecture as shown in Figure 5.2.1-1. The illustration does not constrain the multiplicity of the entities nor require that all relationships shown are present.

# Figure 6.1-1: Configurations supported by oneM2M Architecture

Nodes:

Nodes are logical entities that are individually identifiable in the M2M System. Nodes are either CSE-Capable or Non-CSE-Capable:

A CSE-Capable Node is a logical entity that contains at least one oneM2M Common Services Entity and contains zero or more oneM2M Application Entities. The ASN, IN and MN are examples of CSE-Capable Nodes.

A Non-CSE-Capable Node is a logical entity that does not contain a oneM2M Common Services Entity and contains zero or more oneM2M Application Entities. The ADN is an example of a Non-CSE-Capable Node.

CSEs resident in different Nodes can be different and are dependent on the services supported by the CSE and the characteristics (e.g. different memory, firmware) of the physical entity that contains the CSE’s Node.

# Description of Node types:

The oneM2M architecture enables the following types of Nodes. As logical objects, such Nodes may or may not be mapped to physical objects.

# Application Service Node (ASN):

An Application Service Node is a Node that contains one Common Services Entity and contains at least one Application Entity. There may be zero or more ASNs in the Field Domain of an M2M System.

The CSE in an Application Service Node communicates over the Mcc reference point with one CSE residing in a Middle Node or in an Infrastructure Node.

The CSE in an Application Service Node communicates over the Mca reference point with AEs residing in the same ASN.

An Application Service Node communicates over Mcn with NSEs.

Example of physical mapping: an Application Service Node could reside in an M2M Device.

# Application Dedicated Node (ADN):

An Application Dedicated Node is a Node that contains at least one Application Entity and does not contain a Common Services Entity. There may be zero or more ADNs in the Field Domain of an M2M System.

All AEs in the Application Dedicated Node communicate over the Mca reference point with the same CSE residing in a Middle Node or in an Infrastructure Node.

Example of physical mapping: an Application Dedicated Node could reside in a constrained M2M Device.

# Middle Node (MN):

A Middle Node is a Node that contains one Common Services Entity and contains zero or more Application Entities. There may be zero or more Middle Nodes in the Field Domain of an M2M System.

The CSE in a Middle Node communicates over the Mcc reference point with one CSE residing in a Middle Node or in an Infrastructure Node and with one or more other CSEs residing in Middle Nodes or in Application Service Nodes.

In addition, the CSE in the Middle Node can communicate over the Mca reference point with AEs residing in the same MN or residing in an ADN.

A CSE in a Middle Node communicates over Mcn with NSEs.

Example of physical mapping: a Middle Node could reside in an M2M Gateway.

# Infrastructure Node (IN):

An Infrastructure Node is a Node that contains one Common Services Entity and contains zero or more Application Entities. There is exactly one Infrastructure Node in the Infrastructure Domain per oneM2M Service Provider. A CSE in an IN may contain CSE functions not applicable to other node types.

The CSE in the Infrastructure Node communicates over the Mcc reference point with one or more CSEs residing in Middle Node(s) and/or Application Service Node(s).

The CSE in the Infrastructure Node communicates over the Mca reference point with one or more AEs residing in the same IN or residing in an ADN.

The CSE in the Infrastructure Node communicates over the Mcn reference point with NSEs, and over the Mcc' reference point with CSEs residing in the Infrastructure Nodes of other M2M Service Providers.

Example of physical mapping: an Infrastructure Node could reside in an M2M Service Infrastructure.

Non-oneM2M Node (NoDN):

A non-oneM2M Node is a Node that does not contain oneM2M Entities (neither AEs nor CSEs). Such Nodes represent devices attached to the oneM2M system for interworking purposes, including management.

A Non-oneM2M Node communicates (as shown by dotted lines in Figure 6.1-1) with the oneM2M System according to Annex F.

The Infrastructure Domain of a single M2M Service Provider contains exactly one Infrastructure Node.

The Field Domain of a single M2M Service Provider contains at least:

- one Application Service Node

or

- one Middle Node and one or more Application Dedicated Nodes

======================== END 1ST CHANGE =============================

======================== START 2ND CHANGE ===========================

# 3	Definitions, symbols and abbreviations

## 3.1	Definitions

For the purposes of the present document, the following terms and definitions apply:

application layer: comprises oneM2M Applications and related business and operational logic

attribute: stores information pertaining to the resource.

child resource: sub-resource of another resource that is its parent resource

NOTE:	The parent resource contains references to the child resources(s).

common services layer: consists of oneM2M service functions that enable oneM2M Applications (e.g. management, discovery and policy enforcement)

Common Services Function (CSF): informative architectural construct which conceptually groups together a number of sub-functions

NOTE:	Those sub-functions are implemented as normative resources and procedures. A set of CSFs is contained in the CSE.

Device Entity (6.2.9.2)

# Device Management Resource

execution environment: logical entity that represents an environment capable of running software modules

hosting CSE: CSE where the addressed resource is hosted

# M2M service provider domain: is the part of the M2M System that is associated with a specific M2M Service Provider

managed entity: may be either an M2M Device, M2M Gateway, or a device in the M2M Area Network or the M2M Application Layer or M2M Service Layer software components

# Management Adapter

# Management Client Management Resource

# Management Server

network services layer: provides transport, connectivity and service functions

Node: logical entity that is identifiable in the M2M System.

originator: is the actor that initiates a Request

NOTE:	An Originator can either be an Application or a CSE.

receiver: is the actor that receives the Request

NOTE:	A Receiver can either be a CSE or an Application.

registree: is an AE or CSE that registers with another CSE

registrar CSE: CSE is the CSE where an Application or another CSE has registered

# Request (7.1.7)

# Response (7.1.7

resource: is a uniquely addressable entity in oneM2M architecture

NOTE:	A resource is transferred and manipulated using CRUDN operations. A resource can contain child resource(s) and attribute(s).

# Role

service charging and accounting: set of functionalities within the M2M Service Layer that enable configuration of information collection and charging policies, collection of Charging Records based on the policies, and correlation of Charging Records to users of M2M common services

service charging record: formatted collection of information about a chargeable operation

service layer offline charging: mechanism where charging information does not affect, in real-time, the service rendered

service layer online charging: mechanism where charging information can affect, in real-time, the service rendered, including real time credit control

software package: is an entity that can be deployed on the Execution Environment

NOTE:	It can consist of entities such as software modules, configuration files, or other entities.

software module: is  ....

structured data: is data that either has a structure according to a specified Information Model or are otherwise organized in a defined manner

======================== END 2ND CHANGE =============================

# Text boxes

Non-oneM2M Node (NoDN)

Non-oneM2M device