| CHANGE REQUEST |
| --- |
| Group Name:* | TP12 |
| Source:* | Huawei Technologies Co., Ltd. |
| Format:* | Plenary |
| Date:* | <2014-7-15> |
| Contact:* | Jiaxin Yin, Yinjiaxin@huawei.com |
| Reason for Change/s:* | The contribution made changes to solve the inconsistency in partial addressing and DM execution. |
| CR against: Release* | <Release One> |
| CR against: TS/TR* | TS0001 v0.9.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

### -----------------------Start of change 1-------------------------------------------

#### 10.2.8.6	Execute <mgmtObj>

This procedure shall be used to execute a management command on a managed entity through an existing <mgmtObj> resource on the hosting CSE.

# Table 10.2.8.6-1: <mgmtObj> EXECUTE

| <mgmtObj> EXECUTE |
| --- |
| Associated Reference Point | Mcc and Mca |
| Information on Request message | op: D fr: Identifier of the IN-AE, or the CSE that initiates the Request to: The URI of the <mgmtObj> resource. |
| Pre-Processing at Originator | The Originator shall be an IN-AE. The Originator shall request to execute a management command which is represented by an <mgmtObj> resource or its attribute by using an UPDATE operation. The request shall address the executable <mgmtObj> resource and shall express the management command in the cn. After the execution request, the Originator shall request to retrieve the execution result or status from the executable <mgmtObj> resource or its attribute/child resource by using a RETRIEVE operation as specified in clause 10.2.7.3. |
| Processing at Receiver | For the EXECUTE operation , the Receiver shall: Check if the Originator has the WRITE privilege on the addressed <mgmtObj> resource or its attribute. Check if there is an existing management session between the management server and the managed entity. If not, request the management server to establish a management session towards the managed entity. Send the management request to execute the corresponding management command (e.g. "Exec" in OMA DM [i.5]) on the managed entity based on external management technology. Respond to the Originator with the appropriate response based on the response from the external management technology. If available, the response shall contain execution results. Retrieve the execution result or status from the executable <mgmtObj> resource or its attribute, perform the procedures as described in clause 10.2.7.3. Upon receiving a management notification (e.g. OMA-DM [i.5] "Generic Alert" message or BBF TR-069 [i.4] "Inform" message) from a managed entity regarding the execution result or status, the Receiver shall send the management request to retrieve the execution result or status of the external management object information received from the managed entity and update the corresponding <mgmtObj> resource or its attribute. |
| Information on Response message | Error code if the external management technology procedure can not be executed |
| Post-Processing at Originator | None |
| Exceptions | Corresponding external management technology procedure cannot be executed in managed entity (e.g. not reachable, external management object not found) |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

# D.2	Resource firmware

The [firmware] resource is used to share information regarding the firmware on the device. The resource type of [battery] resource is <mgmtObj>resource.

Figure D.2-1: Structure of [firmware] resource

The [firmware] resource shall contain the child resources specified in table D.2-1.

Table D.2-1: Child resources of [firmware] resource

| Child Resources of [firmware] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 where the type of this resource is described. |

The [firmware] resource shall contain the attributes specified in table D.2-2.

Table D.2-2: Attributes of [firmware] resource

| Attributes of [firmware] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | WO | See clause 9.6.1 where this common attribute is described. |
| resourceID | 1 | WO | See clause 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| labels | 0..1 | RO | See clause 9.6.1 where this common attribute is described. |
| mgmtDefinition | 1 | WO | See clause 9.6.15. Has fixed value "firmware" to indicate the resource is for firmware management. |
| objectIDs | 0..1 | WO | See clause 9.6.15. |
| objectPaths | 0..1 | WO | See clause 9.6.15. |
| description | 0..1 | RW | See clause 9.6.15. |
| version | 1 | RW | The version of the firmware. |
| name | 1 | RW | The name of the firmware to be used on the device. |
| URL | 1 | RW | The URL from which the firmware image can be downloaded. |
| update | 1 | RW | The action that downloads and installs a new firmware in a single operation. The action is triggered by assign value “EXECUTE” to the attribute. |
| updateStatus | 1 | RO | Indicates the status of the update. |

# D.3	Resource software

The [software] resource is used to share information regarding the software on the device. The resource type of [software] resource is <mgmtObj>resource.

Figure D.3-1: Structure of [software] resource

The [software] resource shall contain the child resource specified in table D.3-1.

Table D.3-1: Child resources of [software] resource

| Child Resources of [software] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 where the type of this resource is described. |

The [software] resource shall contain the attributes specified in table D.3-2.

Table D.3-2: Attributes of [software] resource

| Attributes of [software] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | WO | See clause 9.6.1 where this common attribute is described. |
| resourceID | 1 | WO | See clause 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| labels | 0..1 | RO | See clause 9.6.1 where this common attribute is described. |
| mgmtDefinition | 1 | WO | See clause 9.6.15. Has fixed value "software" to indicate the resource is for software management. |
| objectIDs | 0..1 | WO | See clause 9.6.15. |
| objectPaths | 0..1 | WO | See clause 9.6.15. |
| description | 0..1 | RW | See clause 9.6.15. |
| version | 1 | RW | The version of the software. |
| name | 1 | RW | The name of the software to be used on the device. |
| URL | 1 | RW | The URL from which the software package can be downloaded. |
| install | 1 | RW | The action that downloads and installs new software in a single operation. The action is triggered by assign value “EXECUTE” to the attribute. |
| uninstall | 1 | RW | The action that un-installs the software. The action is triggered by assign value “EXECUTE” to the attribute. |
| installStatus | 1 | RO | Indicates the status of the install. |
| activate | 0..1 | RW | The action that activates software previously installed. |
| deactivate | 0..1 | RW | The action that deactivates software. The action is triggered by assign value “EXECUTE” to the attribute. |
| activeStatus | 0..1 | RW | The status of active or deactivate action. The action is triggered by assign value “EXECUTE” to the attribute. |

The state machine for managing the software in oneM2M is shown in figure D.3-2.

Figure D.3-2: State machine for [software] management

The following (figure D.3-3) is the state machine after install starts from the deactivated state.

Figure D.3-3: State machine for [software] management after install

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

# D.10	Resource Type reboot

The [reboot] resource is used to reboot a device. The resource type of  [reboot] resource is <mgmtObj> resource.

Figure D.10-1: Structure of [reboot] resource

The [reboot] resource shall contain the child resources specified in table D.10-1.

Table D.10-1: Child resources of [reboot] resource

| Child Resources of [reboot] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 where the type of this resource is described. |

The [reboot] resource shall contain the attributes specified in table D.10-2.

Table D.10-2: Attributes of [reboot] resource

| Attributs of [reboot] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | WO | See clause 9.6.1 where this common attribute is described. |
| resourceID | 1 | WO | See clause 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| labels | 0..1 | RO | See clause 9.6.1 where this common attribute is described. |
| mgmtDefinition | 1 | WO | See clause 9.6.15. This attribute shall have the fixed value "reboot". |
| objectIDs | 0..1 | WO | See clause 9.6.15. |
| objectPaths | 0..1 | WO | See clause 9.6.15. |
| description | 0..1 | RW | See clause 9.6.15. |
| reboot | 1 | RW | The action that allows rebooting the device. The action is triggered by assign value “EXECUTE” to the attribute. |
| factoryReset | 1 | RW | The action that allows making the device returning to the factory settings. The action is triggered by assign value “EXECUTE” to the attribute. |

# D.11	Resource Type eventLog

The [eventLog] resource is used to record the event log for a device. The resource type of [eventLog] resource is <mgmtObj> resource.

Figure D.11-1: Structure of [eventLog] resource

The [eventLog] resource shall contain the child resources specified in table D.11-1.

Table D.11-1: Child resources of [eventLog] resource

| Child Resources of [eventLog] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 where the type of this resource is described. |

The [eventLog] resource shall contain the attributes specified in table D.11-2.

Table D.11-2: Attributes of [eventLog] resource

| Attributes of [eventLog] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | WO | See clause 9.6.1 where this common attribute is described. |
| resourceID | 1 | WO | See clause 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1 where this common attribute is described. |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| labels | 0..1 | RO | See clause 9.6.1 where this common attribute is described. |
| mgmtDefinition | 1 | WO | See clause 9.6.15. This attribute shall have the fixed value "eventLog". |
| objectIDs | 0..1 | WO | See clause 9.6.15. |
| objectPaths | 0..1 | WO | See clause 9.6.15. |
| description | 0..1 | RW | See clause 9.6.15. |
| logTypeId | 1 | RW | Identifies the types of log to be recorded. E.g. security log, system log. |
| logData | 1 | R | Diagnostic data logged upon event of interests defined by this diagnostic function. |
| logActionStatus | 1 | RO | Indicates the status of the Action. E.g. Started, Stopped. |
| logStart | 1 | RW | The action that allows starting the log corresponding to the mentioned logTypeId. The action is triggered by assign value “EXECUTE” to the attribute. |
| logStop | 1 | RW | The action that allows stopping the log corresponding to the mentioned logTypeId. The action is triggered by assign value “EXECUTE” to the attribute. |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4---------------------------------------------

# Table 8.1.2.1-1: Summary of Request Message Parameters

| Request message parameter\Operation | Create | Retrieve | Update | Delete | Notify |
| --- | --- | --- | --- | --- | --- |
| Operation (op) - operation to be executed | M | M | M | M | M |
| To (to) - the address of the target resource on the target CSE | M | M | M | M | M |
| From (fr) - the identifier of the message Originator | M | M | M | M | M |
| Request Identifier (ri) - uniquely identifies a Request message | M | M | M | M | M |
| Resource Type (ty) - of resource to be created | M | N/A | N/A | N/A | N/A |
| Name (nm) - of resource to be created | O | N/A | N/A | N/A | N/A |
| Content (cn) - to be transferred | M | O | M | N/A | M |
| Originating Timestamp (ot) - when the message was built | O | O | O | O | O |
| Request Expiration Timestamp (rqet) - when the request message expires | O | O | O | O | O |
| Result Expiration Timestamp (rset) -when the result message expires | O | O | O | O | O |
| Operational Execution Time (oet) - the time when the specified operation is to be executed by the target CSE. | O | O | O | O | O |
| Response Type (rt) - Registrar CSE response shall either indicate that the Request was accepted, or include the operation result | O | O | O | O | O |
| Result Persistence (rp) - the duration for which the reference containing the responses is to persist | O | O | O | O | N/A |
| Result Content (rc) - the expected components of the result | O | O | O | O | N/A |
| Event Category (ec) - indicates how and when the system should deliver the message | O | O | O | O | O |
| Delivery Aggregation (da) - aggregation of requests to the same target CSE is to be used | O | O | O | O | O |
| Group Request Identifier (gid) - Identifier added to the group request that is to be fanned out to each member of the group. | O | O | O | O | O |
| Filter Criteria (fc) - conditions for filtered retrieve operation | N/A | O | N/A | N/A | N/A |
| Discovery Result Type (Disrestype) - format of information returned for Discovery operation | N/A | O | N/A | N/A | N/A |

### -----------------------End of change 4---------------------------------------------

# Text boxes

Uninstalled

Execute: ./[software]/Install

Execute: ./[software]/Uninstall

Removed

Installed

Delete: ./[software]