| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | TS-0007 Mca Request Services |
| Source:* | George Foti, Ericsson, George.Foti@ericsson.com |
| Contact: | George Foti, Ericsson, George.Foti@ericsson.com |
| Date:* | 2014-07-17 |
| Abstract:* |  |
| Agenda Item:* |  |
| Work item(s): | TS-0007 WI |
| Document(s) Impacted* | TS-0007 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Update TS for inclusion |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------Start of change 1-------------------------------------------

# 6	M2M Services

This clause describes the M2M Services provided by the M2M Services Platform.

## 6.1	Introduction

The M2M Services defined in this clause are utilized by the Business Services described in the Annexes of this specification.

Figure 6.1-1: oneM2M Services

## 6.X	Registration Services

## 6.x.1 Overview

The Registration service provides the ability for:

- Initial Registration of an AE

- Refresh an existing Registration

- AE Initiated termination of an existing Registration

- Retrieve an AE Registration status

- Revoke an AE existing Registration

### 6.X.2	Service Capabilities

#### 6.X.2.1	registerAE

This service capability enables an AE or a third party provisioned with the proper ACP to register with the M2M System

##### 6.X.2.1.1	Pre-conditions

##### The AE has not registered with the M2M Service Platform

##### 6.X.2.1.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | See Table A.2.1.1.2-1. |
| M2M-Profile-ID | IN | NO | See Table A.2.1.1.2-1. |
| requestedAEId | IN | YES | The Application Instance Identifier (AE-ID) that the Originator has requested to be used for future exchanges between the AE and the M2M System |
| pointOf Access (POA) | IN | NO | The point of Access of the registered AE. See TS00001 section 7.3.3.1 for details |
| App-ID | IN | NO | The Application Identifer (App-ID). |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator |
| returnCode | OUT | NO | Return codes: AE successfully registered AE not successfully registered |
| AE-ID | OUT | NO | AE-ID is provided back in the response |

Table 6.X.2.1.2-1 AE Initial Registration Signature

##### 6.X.2.1.3	Services Interaction

The interactions of service capabilities required for this service capability:

Issue the request to Supporting Services to fetch the service profile for the registering AE

Validate the request and ensure that the AE is associated with the service profile

Issue the update request to the Supporting Service to update the service subscription profile with the allocated AE-ID.

##### 6.X.2.1.4	Post-Conditions

AE is registered and can start using service capabilities

The returned AE-ID shall be used in any subsequent operation related to that  application

##### 6.X.2.1.5	Exceptions

Not Applicable

##### 6.X.2.1.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

### 6.X.2.1.7	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations:

- Create AE

#### 6.X.2.2	refreshAERegistration

This service capability enables an AE or a third party provisioned with the proper ACP to refresh an existing registration with the M2M System

##### 6.X.2.2.1	Pre-conditions

##### The AE has successfully registered with the M2M System

##### 6.X.2.2.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | See Table A.2.1.2.2-1. |
| M2M-Profile-ID | IN | NO | See Table A.2.1.1.2-1. |
| AE-ID | IN | NO | The Application Instance Identifier (AE-ID). |
| pointOf Access (POA) | IN | YES | The point of Access of the registered AE. POA is optional only if identical to the one in the refreshed registration |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator. |
| returnCode | OUT | NO | Return codes: AE successfully refreshed Registration Does not exist |

Table 6.X.2.2.2-1 AE Refresh Registration Signature

##### 6.X.2.2.3	Service Interactions

The interactions of service capabilities required for this service capability:

Issue the request to Supporting Services to fetch the service profile for the registered AE-ID

Validate the requestand ensure that the AE-ID is associated with the service profile

##### 6.X.2.2.4	Post-Conditions

Not Applicable

##### 6.X.2.2.5	Exceptions

Not Applicable

##### 6.X.2.2.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

### 6.X.2.2.7	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations:

- Update AE

#### 6.X.2.3	deregisterAE

This service capability enables an AE or a third party provisioned with the proper ACP to deregister from the M2M System

##### 6.X.2.3.1	Pre-conditions

##### The AE successfully registered with the M2M System

##### 6.X.2.3.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | See Table A.2.1.2.2 |
| M2M-Profile-ID | IN | NO | See Table A.2.1.1.2-1. |
| AE-ID | IN | NO | The Application Instance Identifier (AE-ID). |
| returnCode | OUT | NO | Return codes: AE successfully De-registsred Registration Does not exist |

Table 6.X.2.3.2-1 AE Deregister Registration Signature

##### 6.X.2.3.3	Service Interactions

The interactions of service capabilities required for this service capability:

Issue the request to Supporting Services to fetch the service profile for the deregistering AE-ID

Validate the request and ensure that the AE-ID is associated with the service profile

Issue the update request to the Supporting Service to update the service subscription profile with the to remove the AE-ID.

##### 6.X.2.3.4	Post-Conditions

AE is no longer registsred and cannot use any services

##### 6.X.2.3.5	Exceptions

Not Applicable

Transaction Pattern: Participation allowed

### 6.X.2.3.6	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations:

- Delete AE

#### 6.X.2.4	Retrieve Registration Status

This service capability enables a third party provided having the ACP for this operation, to retrieve the registration status for an AE

##### 6.X.2.4.1	Pre-conditions

##### N/A

##### 6.X.2.4.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| issuer | IN | NO | See Table A.2.1.2.2-1 |
| M2M-Service-Subscription-Profile-ID | IN | NO | See Table A.2.1.1.2-1. |
| AE-Id | IN | NO | The Application Instance Identifier (AE-ID). |
| returnCode | OUT | NO | Return codes: AE successfully Retrieved Registration does not exist |
| pointOf Access (POA) | OUT | NO | The point of Access of the registered AE. |
| App-ID | OUT | NO | The Application Identifer (App-ID). |
| expirationTime | OUT | NO | The expiration time of the registration as requested by the Originator. |

Table 6.X.2.4.2-1 AE Reading of Registration Signature

##### 6.X.2.4.3	Service Interaction

The interactions of service capabilities required for this service capability:

Issue the request to Supporting Services to fetch the service profile for the registeredAE-ID

Validate the request and ensure that the AE-ID is associated with the service profile and return the requested information.

##### 6.X.2.4.4	Post-Conditions

N/A

##### 6.X.2.4.5	Exceptions

Not Applicable

##### 6.X.2.4.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

### 6.X.2.4.7	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations:

- Read AE

#### 6.X.2.5	revokeAERegistration

This service capability enables a third party having the ACP for this operation to revoke an existing AE registration

##### 6.X.2.5.1	Pre-conditions

##### The AE successfully registered with the M2M Service Platform

##### 6.X.2.5.2	Signature

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| Issuer | IN | NO | See Table A.2.1.2.2-1 |
| M2M-Profile-ID | IN | NO | See Table A.2.1.1.2-1. |
| AE-ID | IN | NO | he Application Instance Identifier (AE-ID) |
| returnCode | OUT | NO | Return codes: AE successfully De-registsred Registration does not exist |

Table 6.X.2.5.2-1 revoke AE Registration Signature

##### 6.X.2.5.3	Service Interaction

The interactions of service capabilities required for this service capability:

Issue the request to Supporting Services to fetch the service profile for the deregistering AE-ID

Validate the request and ensure that the AE-ID is associated with the service profile

Issue the update request to the Supporting Service to update the service subscription profile with the to remove the AE-ID.

##### 6.X.2.5.4	Post-Conditions

AE is no longer registsred and cannot use any services

##### 6.X.2.5.5	Exceptions

Not Applicable

##### 6.X.2.5.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

### 6.X.2.5.7	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations:

- Delete AE

### -----------------------Start of change 2 -------------------------------------------

## 7.3	Infrastructure Component (INF)

The INF Component provides Services that are exposed to other  M2M Service Components across the Msc reference point.  The Services within the INF Component are common and utility type Services needed to enable other M2M Services.

## 7.3.1	INF to Service Cross Reference

Authorization: All Service Capabilities

ServiceSubscription: retrieveAuthorization

Registration Services: Return registration Status, Revoke of an AE existing Registration

## 7.6	Service Exposure (SE)

The SE Component acts as the primary interface for AEs to interact with the M2M Service Layer across the Mca reference point.

## 7.6.1	Service Exposure to Service Cross Reference

SE Data Exchange: All Service Capabilities

Service Subscription: getBroker

Broker: publish, subscribe

Registration Services: Initial Registration of an AE, Refreshing an existing Registration of an AE, AE Initiated termination of an existing Registration.

### -----------------------Start of change 3-------------------------------------------

Update Table A Table A.2.1.2.2-1 to include service-Profile-ID