| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 ARC |
| Source:* | Interdigital |
| Format:* | ARC |
| Date:* | <2014-07-15> |
| Contact:* | Guang Lu, InterDigital, Guang.Lu@InterDigital.com |
| Reason for Change/s:* | Clarifies that for the case where oneM2M is binded to an underlying transport protocol that natively supports non-blocking requests (e.g. CoAP), non-blocking requests to CSE resources are also possible without CMDH functionality. |
| CR against: Release* | 0.8 (oneM2M Functional Architecture Baseline Draft) |
| CR against: TS/TR* | oneM2M-TS-0001 - V-0.8.0 |
| Clauses/Sub Clauses* | 9.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The current architecture implies that to support  non-blocking requests to CSE resources, CMDH functionality (e.g. <request> and <delivery>) is required.  However, for the case where oneM2M is binded to an underlying transport protocol that natively supports non-blocking requests (e.g. CoAP), non-blocking requests to CSE resources are also possible without CMDH functionality.

This CR makes this clarification.

### -----------------------Start of change 1-------------------------------------------

### 8.2.2	Accessing Resources in CSEs - Non-Blocking Requests

#### 8.2.2.1 	Definition and Scope

Accessing a resource in a CSE via a non-blocking request involves the hosting CSE returning an Acknowledgement of the request to the Originator.  A subsequent response containing the results is either returned by the hosting CSE to the Originator in a separate response or the results are retrieved by the Originator from the hosting CSE  (e.g. based on a reference that the CSE provides to the Originator within the Acknowledgement).

A transport protocol may (e.g. CoAP) or may not (e.g. HTTP) natively support non-blocking requests.  For the case where it does,  accessing CSE resources in a non-blocking manner may leverage the existing non-blocking capabilities of the underlying transport.  For cases the transport protocol does not support non-blocking request , this document defines CSE functionality (see section 8.2.2.2, 8.2.2.3 and 8.2.24) to support non-blocking access to CSE resources.

#### 8.2.2.2	Response with Reference to Result of Requested Operation

In case the Originator of a Request has asked for only a response with an Acknowledgement of the Request and a reference to the result of the requested operation - see rt parameter in clause 8.1.2 - it is necessary to provide a prompt response to the Originator with a reference to an internal resource on the Registrar CSE or another specified reference, so that the Originator can retrieve the outcome of the requested operation at a later time. The details of such an internal resource are defined in clause 9.6.11. The reference is provided in the response to the Request. The abbreviation "Req-Ref" is used for simplicity

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?