| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 ARC |
| Source:* | Interdigital |
| Format:* | ARC |
| Date:* | <2014-07-15> |
| Contact:* | Guang Lu, InterDigital, Guang.Lu@InterDigital.com |
| Reason for Change/s:* | The current architecture lacks sufficient definition for partial addressing functionality. |
| CR against: Release* | 0.8 (oneM2M Functional Architecture Baseline Draft) |
| CR against: TS/TR* | oneM2M-TS-0001 - V-0.8.0 |
| Clauses/Sub Clauses* | 9.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Recent discussions between ARC and PRO have identified that there is a lack of definition in the TS-0001 for partial addressing.  This contributions attempts to address this by adding a section for partial addressing (9.3.3)

### -----------------------Start of change 1-------------------------------------------

## 9.3	Resource Addressing

### 9.3.1	Generic Principles

There are three different methods for addressing a resource within the oneM2M resource structure. They are as follows:

Hierarchical URI Method: The resource can be addressed by a URI, over Mca, Mcc, and Mcc', with the actual path portion of the URI defining the entire relationship for the target resource within the resource structure. This is a structured representation of the resources within a CSE where the parent relationship chain is embedded in the resource address.

EXAMPLE 1:	IN-CSEID.m2m.myoperator.org/CSERoot/myAppX/myContainerY.

Non-Hierarchical URI Method: The resource can be addressed by a URI, over Mca, Mcc, and Mcc', with the resource identifier given by its Hosting CSE during the resource creation procedure. Hence the actual parent relationship chain is not known a priori and the hosting CSE needs to resolve the logical location of the target resource in the chain of relationship within the resource structure.

EXAMPLE 2:	"IN-CSEID.m2m.myoperator.org/CSERoot/mCY" where the same container of the previous example is directly addressed. mCY is the resource identifier that was given by the Hosting CSE for myContainerY.

ID Base Method: The resource can be addressed via two parameters over Mca; namely the CSE-ID of the host where the resource is located, and/or the resource identifier of the actual target resource. This case is applicable only to intra-domain routing. To proxy this request onwards over the Mcc interface, if applicable, the Registrar CSE can proxy the request to the IN CSE including these two parameters; optionally the Registrar CSE shall use the CSE-ID to generate the complete target host name in accordance with the rules define in clause 6.4.1.1.

Note in this scenario it is assumed that the actual node identifiers are used in the host name to enable the generation of the host name. The CSEBase is used to identify the CSE-ID.

This method is an optimization of the second method, since the host name included in the URI has to be generated, as an option, in this case by the Registrar CSE before it can send the request to the target CSE (via the IN node).

EXAMPLE 3:	The same resource addressed in the previous bullet will be provided by the requesting entity to the receiving CSE by means of the identifiers "CSE4-CSEID" and "mCY" and then it will be resolved to "CSE4-CSEID.IN-CSEID.m2m.myoperator.org/CSERoot/mCY".

These 3 methods shall all be supported by all M2M nodes, notably the Registrar CSEs receiving requests, before they proxy these requests any further, where applicable.

The CSEBase, which is the first element in the path portion of the URI, allows to easily distinguish different CSEs on the same IP host.

### 9.3.2	Resource addressing via a FQDN URI

Resources shall be uniquely addressable via FQDN URI as one of the methods in clause 9.3.1. The following are examples of addressable resources.

/<CSEBase>/Entity Instance_1.

/<CSEBase>/Entity Instance_n.

/<CSEBase>/Application Instance_1.

/<CSEBase>/Application Instance_n.

/<CSEBase>/Container1/Container_2.

A <CSEBase> is the root for addressing all other resources it contains. The <CSEBase> shall represent the first element of the path representing a resource in an absolute URI, as per [i.12].

The authority part of the absolute URI, as per [i.14] and [i.12] shall be  the FQDN or IP address for the CSE hosting the resources and shall conform to the naming convention described in clause 6.4.1.1.

### 9.3.3	Partial Addressing

Partial Addressing allows addressing and manipulation (i.e. Create,Retrieve, Update and Delete) of an individual resource attribute, or part of an attribute for the case where the attribute is a list or complex attribute.

Note: Partial addressing for multiple attributes of a resource or multiple parts of an attribute is not supported in this release of the document.

Partial addressing shall be used to perform the following:

- Retrieve an individual resource attribute or part of a resource attribute

- Delete an individual resource attribute or part of a resource attribute.  Note that deleting a resource attribute may result in the hosting CSE initializing the attribute to a default value

- Update an individual resource attribute or part of a resource attribute

- Subscribe to an individual resource attribute or part of a resource attribute and receive notifications regarding changes to the attribute or part of the attribute

Partial addressing shall be supported for each of three resource addressing schemes described in clause 9.3.1 via the following conventions.

Hierarchical URI Method: An individual attribute or part of an attribute shall be addressed using the hierarchical URI, with the actual path portion of the URI defining the entire relationship for the target resource attribute or partial attribute.

EXAMPLE 1:	IN-CSEID.m2m.myoperator.org/CSERoot/myAppX/myContainerY/accessControlPolicyIDs

EXAMPLE 2: 	IN-CSEID.m2m.myoperator.org/CSERoot/myAppX/myContainerY/accessControlPolicyIDs[0]

Non-Hierarchical URI Method: An individual attribute or part of an attribute shall be addressed using the resource identifier given by its Hosting CSE during the resource creation procedure coupled with the attribute name and an an index to part of the attribute if desired.

Below is the same example using non-hierarchical URI. mCY is the resource identifier that was given by the Hosting

CSE for myContainerY.

EXAMPLE 3:	IN-CSEID.m2m.myoperator.org/CSERoot/mCY/accessControlPolicyIDs

EXAMPLE 4: 	 IN-CSEID.m2m.myoperator.org/CSERoot/mCY/accessControlPolicyIDs[0]

ID Base Method: An individual attribute or part of an attribute shall be addressed via two parameters over Mca; namely the CSE-ID of the host where the resource is located, and/or the resource identifier of the actual target resource coupled with the attribute name and  an index to part of the attribute if desired. This case is applicable only to intra-domain routing. To proxy this request onwards over the Mcc interface, if applicable, the Registrar CSE can proxy the request to the IN CSE including these two parameters; optionally the Registrar CSE shall use the CSE-ID to generate the complete target host name in accordance with the rules define in clause 6.4.1.1.

EXAMPLE 5:	The same resource addressed in the previous bullet will be provided by the requesting entity to the receiving CSE by means of the identifiers "CSE4-CSEID" and "mCY/accessControlPolicyIDs" and then it will be resolved to "CSE4-CSEID.IN-CSEID.m2m.myoperator.org/CSERoot/mCY/accessControlPolicyIDs".

EXAMPLE 6:	The same resource addressed in the previous bullet will be provided by the requesting entity to the receiving CSE by means of the identifiers "CSE4-CSEID" and "mCY/accessControlPolicyIDs[0]" and then it will be resolved to "CSE4-CSEID.IN-CSEID.m2m.myoperator.org/CSERoot/mCY/accessControlPolicyIDs[0]".

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?