| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 Architecture |
| Source:* | ALU, Ericsson, LGE, Telecom Italia |
| Format:* | ARC12 |
| Date:* | 2014-07-20 |
| Contact:* | Omar Elloumi |
| Reason for Change/s:* | Additional cleaning for subscription management |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0001 v0.8.0 |
| Clauses/Sub Clauses* | Several clauses |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

## ---------------------------------------1st change----------------------------

### 7.1.6	M2M Service Subscription Identifier (M2M-Sub-ID)

The M2M-Sub-ID enables the M2M Service Provider to bind application(s), M2M nodes, CSEs and services identified by service identifiers, as well as adminstrative information, such as billing addressing , etc.. to a particular M2M Service Subscription between an M2M subscriber (e.g General Motors) and the M2M Service Provider. The M2M-Sub-ID is unique for every M2M subscriber

The M2M Service Subscription Identifier has the following characteristics:

belongs to the M2M Service Provider;

identifies the subscription to an M2M Service Provider;

enables communication with the M2M Service Provider;

can differ from the M2M Underlying Network Subscription Identifier.

There can be multiple M2M Service Subscription Identifiers per M2M Underlying Network subscription.

The M2M-Sub-ID shall  not be exposed over any interface.

### 7.1.7	M2M Request Identifier (M2M-Request-ID)

The M2M-Request-ID tracks a Request initiated by an AE over the Mca reference point, and by a CSE over the Mcc reference point, if applicable, end to end. It is also included in the Response to the Request over the Mca or Mcc reference points.

To enable an AE to track Requests and corresponding Responses over the Mca reference point, AEs shall include a distinct M2M Request Identifier per request over the Mca Reference point to the CSE for any initiated request.

The CSE shall make such M2M Request Identifier received from the AE globally unique by appending its CSE-ID to it.

If the CSE creates an M2M Request Identifier, then the CSE shall maintain a binding between the M2M Request Identifier received from the AE and the M2M Request Identifier it created in its interactions towards other peer CSEs. The CSE shall include the M2M Request Identifier received from the AE in its Response to the AE. This binding shall be maintained by the CSE until the Request message sequence is completed. Note that the Request initiated by the CSE could be the result of an application Request, or a request initiated autonomously by the CSE to fulfil a service.

In case the receiving CSE is not reachable over the underlying network, the IN-CSE initiates procedure for "waking up" the Node hosting the receiving CSE by using procedures such as device triggering over the Mcn reference point. For Device Triggering, the triggering reference number used to co-relate device triggering response is independent of the M2M Request Identifier. An IN-CSE may use the same value of an M2M-Request-Identifier in an incoming request for the triggering reference number in its interaction with the underlying network.

A CSE receiving a Request from a peer CSE shall include the received M2M Request Identifier in all additional Requests unspanned (i.e. 1:1) it has to generate (including propagation of the incoming Request) and that are associated with the incoming Request, where applicable.

Note that the M2M Request Identifier can be made globally unique by including the CSE-ID in combination with any random number.

### 7.1.8	M2M External Identifier (M2M-Ext-ID)

The M2M-Ext-ID is used by an M2M Service Provider (M2M SP) when services targeted to a CSE, identified by a CSE-ID, are requested from the Underlying Network.

The M2M External Identifier allows the Underlying Network to identify the M2M Device (e.g., ASN, MN) associated with the CSE-ID. To that effect, the Underlying Network maps the M2M-Ext-ID to the Underlying Network specific Identifier it allocated to the target M2M Device. In addition, the M2M SP shall maintain the association between the CSE-ID, the M2M-Ext-ID and the identity of the Underlying Network.

Both pre-provisioned and dynamic association between the CSE-ID with the M2M-Ext-ID are supported.

NOTE 1:	For each CSE-ID, there is only one M2M-Ext-ID for a specific UNetwork-ID. Hence an M2M SP interworking with multiple Underlying Networks has different M2M-Ext-IDs associated with the same CSE-ID, one per Underlying Network and selects the appropriate M2M-Ext-ID for any service request it initiates towards an Underlying Network.

NOTE 2:	The mapping by the Underlying Network of the M2M-Ext-ID to the M2M Device is Underlying Network specific.

NOTE 3:	The Underlying Network provider and the M2M Service Provider collaborate for the assignment of an M2M-Ext-ID to each CSE identified by CSE-ID. At the same time, the Underlying Network provider maintains association of the M2M-Ext-ID with the Underlying Network specific Identifier allocated to the M2M device that hosts such CSE.

For pre-provisioned M2M-Ext-IDs, the M2M-Ext-ID along with the associated CSE-ID shall be made available at the Infrastructure Node. The CSE at M2M device does not need to have knowledge of the M2M-Ext-ID assigned to it.

For dynamic M2M-Ext-IDs, the M2M-Ext-ID specific to the Underlying Network shall be made available at the M2M device in the Field Domain. Such M2M-Ext-ID shall be conveyed to the IN-CSE during CSE Registration.

### 7.1.9	Underlying Network Identifier (UNetwork-ID)

The UNetwork-ID is used for identifying an Underlying Network. UNetwork-ID is a static value and unique within a M2M Service Provider domain.

One or more Underlying Networks may be available at an M2M Node offering different sets of capabilities, availability schedules etc. Based on the "policy" information at the Node and the capabilities offered by the available Underlying Networks, appropriate Underlying Network can be chosen by using UNetwork-ID. For example, based on "policy", scheduling of traffic triggered by a certain event category in certain time periods may be allowed over Underlying Network "WLAN" but may not be allowed over Underlying Network "2G Cellular".

### 7.1.10	Trigger Recipient Identifier (Trigger-Recipient-ID)

The Trigger-Recipient-ID is used when device triggering services are requested from the Underlying Network, to identify an instance of an ASN/MN-CSE on an execution environment, to which the trigger is routed. For example, when 3GPP device triggering is used, the Trigger-Recipient-ID maps to the Application-Port-Identifier (TS 123 682 [i.17]).

NOTE 1:	For pre-provisioned M2M-Ext-IDs, Trigger-Recipient-ID is provisioned at the Infrastructure Node along with the M2M-Ext-ID and the associated CSE-ID.

NOTE 2:	For dynamic M2M-Ext-IDs, Trigger-Recipient-ID specific to the Underlying Network is provisioned at each M2M device in the Field Domain. Such Trigger-Recipient-ID is conveyed to the IN-CSE during CSE Registration.

### 7.1.11	M2M Service Identifier (M2M-Serv-ID)

The M2M-Serv-ID is an identifier of a M2M Service offered by an M2M SP. It is an essential part of the M2M Service Subscription which stores a set of M2M-Serv-IDs pertaining to the set of subscribed services. Beyond the set of services depicted in this specification it shall be possible for an M2M Service Provider to offer other services. Those will be identified by means of M2M SP specific M2M-Serv-IDs.

### 7.1.12	M2M-SP-ID, CSE-ID and AE-ID and resource Identifier formats

As a general rule, the identifiers of AEs, CSEs and resources are globally unique. In order to optimize their use, the identifiers shall be shortened when their scope can be derived from their context of use by the CSEs and the AEs.  Such shortened identifiers are defined as 'relative' identifiers.

TheM2M system shall use the identifiers M2M-SP-ID, CSE-ID and AE-ID and resource identifiers according to the formats and the rules specified in the following table (table 7.1.12-1).

Table 7.1.12-1: Identifiers formats and use

|  | Format Name | Format | Rule of use |
| --- | --- | --- | --- |
| AE-ID EQUIVALENT formats | CSE-Relative-AE-ID (with respect to the context of the CSE hosting the AE) | /<unique identifier inside the CSE> | On the Mca reference point: to refer to AEs that are hosted by the directly attached (Registrar) CSE. The hosting CSE is responsible for guaranteeing that the CSE-Relative-AE-ID is unique in the context of the hosting CSE. |
|  | SP-relative -AE-ID (with respect to the context of the SP hosting the AE) | CSE-ID/<unique identifier inside the CSE> | On the Mca and Mcc reference points: to refer to AEs that are hosted by the M2M Service Provider domain to which AE is attached. |
|  | Global-CSE-ID | M2M-SP-ID/CSE-ID/<unique identifier inside the CSE> | On the Mca and Mcc reference points: to refer to AEs that are hosted by a different M2M Service Provider domain with respect to the one to which the AE is attached and on the Mcc’ reference point for all the AEs |
| CSE-ID EQUIVALENT formats | SP-Relative-CSE-ID (with respect to the context of the SP hosting the CSE) | /CSEBase | On the Mca and Mcc reference points: to refer to CSEs that are hosted by the same M2M Service Provider domain |
|  | Global-CSE-ID | M2M-SP-ID/CSEBase | On Mca and Mcc reference points: to refer to CSEs that are hosted by different M2M Service Provider domains and on the Mcc’ reference point for all the CSEs |
| M2M-SP-ID format | (always globally unique) | /FQDN | When The M2M-SP-ID is used, the FQDN format applies |
| Resource identifier (URI) equivalent formats | SP-Relative-resource-URI (with respect to the context of the M2M Service Provider hosting the CSE) | ResourceURI | On the Mca and Mcc reference points: to refer to resources that are hosted by the same M2M Service Provider domain |
|  | Global-URI | M2M-SP-ID/ResourceURI | On Mca and Mcc reference points: to refer to resources that are hosted by a different M2M Service Provider domain and on the Mcc’ reference point for all the resources |

As a consequence, the hosting CSE shall convert the AEs global and relative identifier according to table 7.1.12-1 when a request is transmitted across the Mcc and Mca reference points.

As a consequence, the IN-CSE shall convert the AEs, CSEs and resource global and relative identifiers according to table 7.1.12-1when a request is transmitted across the Mcc’ reference point.

### 7.1.13 Service Role identifier (SRole-ID)

In each M2M Service, one or multiple M2M Service Role(s) shall be defined by the M2M Service Provider. An M2M Service Role is defined as a set of privileges pertaining to resource types which are associated with M2M Service. See Annex G for examples of M2M Service Provider defined Service Roles.

### 7.1.14	M2M Service Profile Identifier (M2M-Profile-ID)

The M2M-Profile-ID enables the M2M Service Provider to bind application(s)  and M2M service identifiers to M2M nodes.

An M2M-Profile-ID shall be allocated to every M2M Node

The M2M Service Profile Identifier has the following characteristics:

belongs to the M2M Service Provider;

identifies the services and aplications applicable for an M2M node.

## 7.2	M2M Identifiers lifecycle and characteristics

# Table 7.2-1: M2M Identifiers lifecycle and characteristics

| Identifier | Assigned by | Assigned to | Assigned during | Lifetime | Uniqueness | Used during | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- |
| M2M Service Provider Identifier | Out of scope | AE, CSE | Out of scope | Out of scope | Global | Provisioning |  |
| Application Entity Identifier | AE or Registrar CSE | AE | AE start-up | Application Entity Registration | Global | - Application Entity Registration - Security Context Establishment - All other operations initiated by the AE | Security requirements apply for Security Context Establishment |
| Application Identifier | Out of scope | Out of scope | Pre-provisioned | Out of scope | Specific to M2M service deployment | - Application Entity registration |  |
| CSE Identifier | M2M SP | CSE | Security Provisioning | Life of the CSE | Global | - Information flows (clause 10) - Security Context Establishment | Security requirements apply for Security Context Establishment |
| M2M Node Identifier | Out of Scope | M2M Node hosting CSE | Pre-provisioned | Life of the M2M Node | Global | - Device Management | Needs to be Read Only |
| M2M Subscription Identifier | M2M SP, Out of Scope | Application Entities, and one or more CSEs belonging to the same M2M subscriber | At service signup | Life of the M2M Service Subscription with the M2M Service Provider | Global | - Charging and Information Recorded - Role based access control - Authentication | Multiple CSEs can be allocated the same M2M Subscription Identifier |
| M2M Service Profile Identifier | M2M SP | Every M2M node | At service signup | Life of the M2M Service Subscription with the M2M Service Provider | Global for roaming cases otherwise local | Information Flows (Clause 10) | The ID has to be pre-provsioned after signup, but may need to be updated during the subscription lifetime due to changes in the subercibed services |
| M2M-Request-ID | Mcc: CSE Mca: Application Entity | A request initiated by an AE or CSE | Mcc: When a request is initiated by a CSE, or handling of a request received by a CSE. Mca: When a request is initiated by an AE | Equal to the lifetime of the Request and its corresponding Response | Mcc: Global Mca: Local or global | Requests and corresponding responses |  |
| External Identifier | Jointly between the Underlying Network provider and M2M SP. | M2M Node belonging to a CSE that wants to utilize services of the Underlying Network. | Administrative Agreement. | Life of the CSE. | Local or global, decided by the specific Underlying Network provider | Requests initiated by a CSE over the Mcn reference point, where applicable. | Pre-Provisioned Mode: Made available at the Infrastructure Node. Dynamic Mode: Made available at M2M device. Conveyed to IN-CSE during CSE Registration. |
| Underlying Network Identifier | M2M SP | Underlying Networks | Pre-provisioned | Life of the Underlying Network | Local to M2M SP domain | UL Network selection |  |
| Trigger Recipient Identifier | Execution Environment | ASN/MN-CSE | ASN/MN-CSE start-up or wake-up | Life of the CSE | Execution Environment-wide | Device Triggering procedures, where applicable | Pre-Provisioned Mode: Made available at Infrastructure Node along with M2M-Ext-ID. Dynamic Mode: Made available at M2M device. Conveyed to IN-CSE during CSE Registration along with M2M-Ext-ID. |
| M2M Service Identifier | M2M Service Provider, Out of Scope | A service defined by the M2M Service Provider which consists of a set of functions defined by this document. | Out of Scope | Out of Scope | Local to the M2M Service Provider | For M2M Service Subscription |  |
| SRole-ID | M2M Service Provider | M2M Service Provider sets the set of service roles that a subscriber can choose from. M2M service subscription lists one or multiple subscribed to service roles. | Out of Scope | Out of scope | M2M Service Provider | Access Control Policy, M2M service subscription management |  |

## ---------------------------------------end 1st change----------------------------

## ---------------------------------------2nd change----------------------------

## 9.6	Resource Types

Table 9.6-1 introduces the normal and virtual resource types and their related child or parent resource types. Details of each resource type follow in the remainder of this clause.

Table 9.6-1 lists the supported <resourceTypes>. An addition of suffix "Annc" to such <resourceTypes> indicates the associated announced resource type.

Table 9.6-1 Resource Summary

| Resource Type | Short Description | Child Resource Types | Parent Resource Types | Clause |
| --- | --- | --- | --- | --- |
| activeCmdhPolicy | Provides a link to the currently active set of CMDH policies. | None | CSEBase | D.12.1 |
| accessControlPolicy | Stores a representation of privileges. It is associated with resources that shall be accessible to entities external to the hosting CSE. It controls "who" is allowed to do "what" and the context in which it can be used for accessing the resources | subscription | AE, remoteCSE, CSEBase | 9.6.2 |
| contentInstance | Represents a data instance in the container resource | subscription | container | 9.6.7 |
| AE | Stores information about the AE. It is created as a result of successful registration of an AE with the registrar CSE | subscription, container, group, accessControlPolicy, mgmtObj, commCapabilities, pollingChannel | remoteCSE, CSEBase | 9.6.5 |
| cmdhBuffer | Defines CMDH buffer usage limits | subscription | cmdhPolicy | D.12.8 |
| cmdhDefaults | Defines CMDH default values | cmdhDefEcValue, cmdhEcDefParamValues subscription | cmdhPolicy | D.12.2 |
| cmdhEcDefParamValues | Represent a specific set of default values for the CMDH related parameters | subscription | cmdhDefaults | D.12.4 |
| cmdhDefEcValue | Defines a value for the ec (event category) parameter of an incoming request when it is not defined | subscription | cmdhDefaults | D.12.3 |
| cmdhLimits | Defines limits for CMDH related parameter values | subscription | cmdhPolicy | D.12.5 |
| cmdhNetworkAccessRules | Defines rules for the usage of underlying networks | cmdhNwAccessRule subscription | cmdhPolicy | D.12.6 |
| cmdhNwAccessRule | Defines a rule for the usage of underlying networks | schedule subscription | cmdhNetworkAccessRules | D.12.7 |
| cmdhPolicy | A set of rules defining which CMDH parameters will be used by default | cmdhDefaults, cmdhLimits, cmdhNetworkAccessRules, cmdhBuffer subscription | CSEBase | D.12 |
| container | Shares data instances among entities. Used as a mediator that takes care of buffering the data to exchange "data" between AEs and/or CSEs. The exchange of data between AEs (e.g. an AE on a Node in a field domain and the peer-AE on the infrastructure domain) is abstracted from the need to set up direct connections and allows for scenarios where both entities in the exchange do not have the same reachability schedule | container, contentInstance, subscription, | application, container, remoteCSE, CSEBase | 9.6.6 |
| CSEBase | The structural root for all the resources that are residing on a CSE. It shall store information about the CSE itself | remoteCSE, node, application, container, group, accessControlPolicy, subscription, mgmtObj, mgmtCmd, locationPolicy, statsConfig | None | 9.6.3 |
| delivery | Forwards requests from CSE to CSE | subscription | CSEBase | 9.6.11 |
| eventConfig | Defines events that trigger statistics collection | subscription | statsConfig | 9.6.23 |
| execInstance | The Execution Instance resource contains all execution instances of the same management command mgmtCmd | subscription | mgmtCmd | 9.6.17 |
| group | Stores information about resources of the same type that need to be addressed as a Group. Operations addressed to a Group resource shall be executed in a bulk mode for all members belonging to the Group | fanOutPoint subscription | Application, remoteCSE, CSEBase | 9.6.13 |
| locationPolicy | Includes information to obtain and manage geographical location. It is only referred from container, the contentInstances of the container provides location information | subscription | CSEBase | 9.6.10 |
| fanOutPoint | Virtual resource containing target for group requests It is used for addressing bulk operations to all the resources that belong to a group | None | group | 9.6.14 |
| mgmtCmd | Management Command resource represents a method to execute management procedures required by existing management protocols | execInstance subscription | CSEBase | 9.6.16 |
| mgmtObj | Management Object resource represents management functions that provides an abstraction to be mapped to external management technology. It represents the node and the software installed in the node | parameters subscription | remoteCSE, CSEBase | 9.6.15 Annex D |
| m2mServiceSubscriptionProfile | Data pertaining to the M2M Service Subscription | authorizedNode subscription | None documented | 9.6.19 |
| Node | Represents specific Node information | schedule, mgmtObj subscription | CSEBase, remoteCSE | 9.6.18 |
| authorizedNode | Node information | subscription | m2mServiceSubscriptionProfile | 9.6.20 |
| parameters | Provides a mechanism to describe the management object in a generic way to easily import information from existing management protocols | parameters subscription | mgmtObj, parameters | 9.6.16 |
| pollingChannel | Represent a channel that can be used for a request-unreachable entity | None | remoteCSE, application | 9.6.21 |
| remoteCSE | Represents a remote CSE for which there has been a registration procedure with the registrar CSE identified by the CSEBase resource | application, container, group, accessControlPolicy, subscription, mgmtObj, pollingChannel, node | CSEBase | 9.6.4 |
| request | Expresses/access context of an issued Request | subscription | CSEBase | 9.6.12 |
| schedule | Contains scheduling information for delivery of messages | subscription | node, subscription, cmdhNwAccessRule | 9.6.39 |
| statsCollect | Defines triggers for the IN-CSE to collect statistics for applications | subscription | CSEBase (in IN-CSE) | 9.6.24 |
| statsConfig | Stores configuration of statistics for applications | eventConfig subscription | CSEBase (in IN-CSE) | 9.6.22 |
| subscription | Subscription resource represents the subscription information related to a resource. Such a resource shall be a child resource for the subscribe-to resource | schedule | accessControlPolicy, application, cmdhBuffer, cmdhDefaults, cmdhEcDefParamValues, cmdhDefEcValue, cmdhLimits, cmdhNetworkAccessRules, cmdhNwAccessRule, cmdhPolicy, container, CSEBase, delivery, eventConfig, execInstance, group, contentInstance, locationPolicy, mgmtCmd, mgmtObj, m2mServiceSubscriptionProfile, node, authorizedNode, parameters, remoteCSE, request, schedule, statsCollect, statsConfig | 9.6.8 |

## ---------------------------------------end 2nd change----------------------------

## ---------------------------------------3rd change----------------------------

### 9.6.19	Resource Type m2mServiceSubscriptionProfile

The <m2mServiceSubscriptionProfile> resource represents an M2M Service Subscription. It is used to represent all data pertaining to the M2M Service Subscription, i.e., the technical part of the contract between an M2M Application Service Provider and an M2M Service Provider.

Figure 9.6.19-1: Structure of <m2mServiceSubscriptionProfile> resource

The <m2mServiceSubscriptionProfile> resource shall contain the child resources specified in table 9.6.19-1.

Table 9.6.19-1: Child resources of <m2mServiceSubscriptionProfile> resource

| Child Resources of <m2mServiceSubscriptionProfile> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |
| authorizedNode | <nodeInfo> | 0..n | See clause 9.6.20 |

The <m2mServiceSubscriptionProfile> resource shall contain the attributes specified in table 9.6.19-2.

# Table 9.6.19-2: Attributes of <m2mServiceSubscriptionProfile> resource

| Attributes of <m2mServiceSubscriptionProfile> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| resourceID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1 where this common attribute is described. If no accessControlPolicyIDs is given at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute |
| creationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| labels | 0..1(L) | RW | See clause 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| serviceRoles | 0..1(L) | RW | This attribute contains a list of Service Role IDs (S-RoleIDs) that are subscribed to in this service subscription. If the multiplicity of this attribute is 0, the role does not apply. |

### 9.6.20	Resource Type authorizedNode

The <authorizedNode> resource represents M2M Node information that is needed as part of the M2M Service Subscription resource. It shall contain information about the M2M Node as well as application identifiers of the Applications running on that Node.

Figure 9.6.20-1: Structure of <authorizedNode> resource

The <authorizedNode> resource shall contain the child resource specified in table 9.6.20-1.

Table 9.6.20-1: Child resources of <authorizedNode> resource

| Child Resources of <authorizedNode> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |

The <authorizedNode> resource shall contain the attributes specified in table 9.6.20-2.

Table 9.6.20-2: Attributes of <authorizedNode> resource

| Attributes of <authorizedNode> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| resourceID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1 where this common attribute is described. If no accessControlPolicyIDs is given at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute. |
| creationTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| labels | 0..1 | RW | See clause 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| nodeID | 1 | WO | M2M-Node-ID of the node that is represented by this instance.. |
| CSE-ID | 0..1 | WO | CSE-ID pertaining to this node (for nodes that have a CSE). |
| deviceIdentifier | 0..1 | WO | A list of device identifiers. A deviceIdentifier identifes a device using a Universally Unique IDentifier (UUID). The UUID specifies a valid, hex digit character string as defined in [RFC4122]. The format of the URN is urn:uuid:########-####-####-############ OPS URN: Identify a device using the format <OUI> "-" <ProductClass> "-" <SerialNumber> as defined in Section 3.4.4 of TR-069 [i-4]. The format of the URN is urn:dev:ops:<OUI> "-" <ProductClass> "-" <SerialNumber>. OS URN: Identify a device using the format <OUI> "-"<SerialNumber> as defined in Section 3.4.4 of TR-069 [i.4]. The format of the URN is urn:dev:os:<OUI> "-"<SerialNumber>. IMEI URN: Identify a device using an International Mobile Equipment Identifiers of 3GPP-TS_23.003 [i.26]. The IMEI URN specifies a valid, 15 digit IMEI. The format of the URN is urn:imei:############### ESN URN: Identify a device using an Electronic Serial Number. The ESN specifies a valid, 8 digit ESN. The format of the URN is urn:esn:######## MEID URN: Identify a device using a Mobile Equipment Identifier. The MEID URN specifies a valid, 14 digit MEID. The format of the URN is urn:meid:############## |

## ---------------------------------------end 3rd change----------------------------

## ---------------------------------------4th change----------------------------

#### 10.1.1.1	Non-registration related CREATE procedure

This procedure is valid for all resources which are not related to registration.

Originator requests to create a resource by using the CREATE method. See clause 8.1.2 for the parameters to be included in the Request message.

Registrar CSE, when the Originator is an AE, shall validate the create request based on the resource type (ty) against the M2M Service Subscription Profile of the AE.

Hosting CSE  If the request is allowed by the given privileges, the Receiver shall create the resource.

# Figure 10.1.1.1-1: Procedure for CREATEing a Resource

Step 001: The Originator shall send the following parameters in the CREATE Request message:

op: 	C (Create);

to: 	URI of the target resource where the new resource should be created (parent resource);

# fr: 	ID of the Originator (either the AE or CSE);

[10.1.1.1.b] Editor's Note: AE or CSE may not have the ID upon its registration request. Alternative information for fr is FFS.

ty:	Type of resource to be created;

nm:	optional name of the resource to be provided by the Originator, where permitted by the resource type as specified in clause 9.6.

NOTE:	Some of the resources defined in clause 9.6 have a predefined name. For these resources the parameter nm is not applicable.

cn: 	attributes of the resource to be provided by the Originator. Of particular importance for the CREATE Request message is the common attribute resourceType (clause 9.6.1) which identifies the type of the resource to be Created.

[10.1.1.1.c] Editor's Note: which parameters are deducted to be mandatory/optional in the request is for FFS. Clause 8.1 should provide a generic mechanism to identify mandatory params for a request by looking at how the resource is defined. E.g. If the attribute in the resource definition is identified as mandatory and it is of type RW, then it is also intended as mandatory in the request.

[10.1.1.1.d] Editor's Note: references to elements defined in sect 8 have been added here. They may be removed if we decide to move sect 8.1.2-4 to stage 3 doc. In this case, these references will be removed and sect 1 of this document would replace sect 8.1.2-4 in the TS-0001.

Step 002: The Receiver shall:

- Check if the Originator has the appropriate privileges for performing the request. Privileges are part of the attribute accessControlPolicyIDs of the targeted resource. In case that such an attribute does not exist, the Receiver shall check the accessControlPolicyIDs of the parent resource.

[10.1.1.1.e] Editor's Note: how far should the Receiver go back to a parent to look for an accessControlPolicyIDs is FFS

- Verify that the suggested nm, if provided by the Originator in the Create Request message, does not already exist  among child resources of the target resource. If nm is not provided by the Originator, assign nm.

Assign a resource identifier (see resourceID attribute in common attribute table 9.6.1-1) to the resource to be created.

Assign/modify default values for certain mandatory attributes of the resource, where allowed by the resource itself and if not provided by the Originator itself.

the Receiver shall assign a value to the following common attributes specified in clause 9.6.1:

a)	parentID;

b)	creationTime;

c)	expirationTime: if not provided by the Originator, the Receiver shall assign the maximum value possible (within the restriction of the Receiver policies). If the value provided by the Originator cannot be supported, due to either policy or subscription restrictions, the Receiver will assign a new value.

d)	lastModifiedTime: which is equals to the creationTime;

e)	Any other RO (Read Only) attributes within the restriction of the Receiver policies.

On successful validation of the Create Request, the Receiver shall create the requested resource.

Step 003: The Receiver shall respond with a Response message that shall contain the following parameters:

to:	Optional. ID of the Originator. In case this is a response carrying the result of an operation triggered by a non-blocking request , rd information can be used.

# fr:	Optional. ID of the Receiver.

cn:	URI and optionally the content of the created resource. The Receiver shall provide the content if the created resource contains attributes which were modified by the Receiver in step 002.

See clauses 8.1.3 and 8.1.4 for the parameters to be included in the Response message.

# General Exceptions:

- The Originator does not have the privileges to create a resource on the Receiver. The Receiver responds with an error.

The resource with the specified name (if provided) already exists at the Receiver. The Receiver responds with an error.

The provided information in cn is not accepted by the Receiver (e.g. missing mandatory parameter). The Receiver responds with an error.

## ---------------------------------------end 4th change----------------------------

## ---------------------------------------5th change----------------------------

##### 10.1.1.2.2	Application Entity Registration procedure

The procedure for AE registration follows the procedure described in clause 10.1.1.1 with the following exception:

Originator: The Originator shall be the registering AE.

Receiver: The Receiver shall allow the creation of the <AE> resource according to the access control policy. The Receiver shall use, if present, the suggested name from the information parameter nm in the request. If the suggested name of the resource cannot be used (i.e. a resource with that name already exists) the Receiver shall reject the CREATE Request. If the request does not provide the optional nm, then the Receiver shall create the resource and assign a name to it. The Receiver shall derive the serviceProfileID and nodeID provided from the security credentials of the AE (see 11.2.2). The receiver shall fetch the service subscription profile.

Step 001: The Originator shall send the following information in the CREATE Request message:

fr:	AE-ID or empty.

Step 002: for the <AE> resource the Receiver cannot perform the action described in the first step of clause 10.1.1.1.

All the other parameters of the request and the steps that follow do not deviate from clause 10.1.1.1.

## ---------------------------------------end 5th change----------------------------

## ---------------------------------------6th change----------------------------

### 10.2.16	<m2mServiceSubscriptionProfile> Resource

#### 10.2.16.1	Create <m2mServiceSubscriptionProfile>

This flow is used for creating a <m2mServiceSubscriptionProfile> resource.

Table 10.2.16.1-1: <m2mServiceSubscriptionProfile> CREATE

| < m2mServiceSubscriptionProfile > CREATE |
| --- |
| Associated Reference Point | Mca, Mcc |
| Information on Request message | All parameters defined in table 8.1.2.1-1 apply with the specific details for: to: the Receiver or hosting CSE shall be an IN-CSE cn: The resource content shall provide the information as defined in clause 9.6.19. |
| Pre-Processing at Originator | According to clause 10.1.1.1 |
| Processing at Receiver | According to clause 10.1.1.1 |
| Information on Response message | All parameters defined in table 8.1.2.1-1 apply with the specific details for: cn: URI of the created < m2mServiceSubscriptionProfile > resource, according to clause 10.1.1 |
| Post-Processing at Originator | According to clause 10.1.1.1 |
| Exceptions | According to clause 10.1.1.1 |

#### 10.2.16.2	Retrieve <m2mServiceSubscriptionProfile>

This flow is used for retrieving the attributes of a <m2mServiceSubscriptionProfile> resource.

Table 10.2.16.2-1: <m2mServiceSubscriptionProfile> RETRIEVE

| <m2mServiceSubscriptionProfile> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc, Mcc’ |
| Information on Request message | All parameters defined in table 8.1.2.1-1 apply with the specific details for: to: the Receiver or hosting CSE shall be an IN-CSE cn: void |
| Pre-Processing at Originator | According to clause 10.1.2 |
| Processing at Receiver | According to clause 10.1.2 |
| Information on Response message | All parameters defined in table 8.1.2.1-1 apply with the specific details for: cn: attributes of the <m2mServiceSubscriptionProfile> resource as defined in clause 9.6.19 |
| Post-Processing at Originator | According to clause 10.1.2. |
| Exceptions | According to clause 10.1.2 |

#### 10.2.16.3	Update <m2mServiceSubscriptionProfile>

This flow is used for updating the attributes of a <m2mServiceSubscriptionProfile> resource.

Table 10.2.16.3-1: <m2mServiceSubscriptionProfile> UPDATE

| <m2mServiceSubscriptionProfile> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc |
| Information on Request message | All parameters defined in table 8.1.2.1-1 are applicable as indicate in the table with the specific details for: to: the Receiver or hosting CSE shall be an IN-CSE cn: attributes of the <m2mServiceSubscriptionProfile> resource as defined in 9.6.19 which need be updated, with the exception of the following that cannot be modified: “lastModifiedTime”, ” subsSer&RoleList”. |
| Pre-Processing at Originator | According to clause 10.1.3 |
| Processing at Receiver | According to clause 10.1.3 |
| Information on Response message | According to clause 10.1.3 |
| Post-Processing at Originator | According to clause 10.1.3 |
| Exceptions | According to clause 10.1.3 |

#### 10.2.16.4	Delete <m2mServiceSubscriptionProfile>

This flow is used for deleting a <m2mServiceSubscriptionProfile> resource residing under a <m2mServiceSubscriptionProfile> resource.

Table 10.2.16.4-1: <m2mServiceSubscriptionProfile> DELETE

| <m2mServiceSubscriptionProfile> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc |
| Information on Request message | All parameters defined in table 8.1.2.1-1 apply with specific details for: to: the Receiver or hosting CSE shall be an IN-CSE |
| Pre-Processing at Originator | According to clause 10.1.4 |
| Processing at Receiver | According to clause 10.1.4 |
| Information on Response message | According to clause 10.1.4 |
| Post-Processing at Originator | According to clause 10.1.4 |
| Exceptions | According to clause 10.1.4 |

### 10.2.17	<authorizedNode> Resource

#### 10.2.17.1	Create <authorizedNode>

This flow is used for creating a <authorizedNode> resource which is sub-resource of <m2mServiceSubscriptionProfile> resource.

Table 10.2.17.1-1: <authorizedNode> CREATE

| <authorizedNode> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc |
| Information on Request message | All parameters defined in table 8.1.2.1-1 apply with the specific details for: to: the Receiver or hosting CSE shall be an IN-CSE cn: The resource content shall provide the information as defined in clause 9.6.20. |
| Pre-Processing at Originator | According to clause 10.1.1.1 |
| Processing at Receiver | According to clause 10.1.1.1 |
| Information on Response message | All parameters defined in table 8.1.2.1-1 apply with the specific details for: cn: URI of the created <authorizedNode> resource, according to clause 10.1.1 |
| Post-Processing at Originator | According to clause 10.1.1.1 |
| Exceptions | According to clause 10.1.1.1 |

#### 10.2.17.2	Retrieve <authorizedNode>

This flow is used for retrieving the attributes of a <authorizedNode> resource which is sub-resource of <m2mServiceSubscriptionProfile> resource.

Table 10.2.17.2-1: <authorizedNode> RETRIEVE

| <authorizedNode> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc, Mcc’ |
| Information on Request message | All parameters defined in table 8.1.2.1-1 apply with the specific details for: to: the Receiver or hosting CSE shall be an IN-CSE cn: void |
| Pre-Processing at Originator | According to clause 10.1.2 |
| Processing at Receiver | According to clause 10.1.2 |
| Information on Response message | All parameters defined in table 8.1.2.1-1 apply |
| Post-Processing at Originator | According to clause 10.1.2. |
| Exceptions | According to clause 10.1.2 |

#### 10.2.17.3	Update <authorizedNode>

This flow is used for updating the attributes of a <authorizedNode> resource which is sub-resource of <m2mServiceSubscriptionProfile> resource.

Table 10.2.17.3-1: <authorizedNode> UPDATE

| <authorizedNode> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc |
| Information on Request message | All parameters defined in table 8.1.2.1-1 are applicable as indicate in the table with the specific details for: to: the Receiver or hosting CSE shall be an IN-CSE cn: attributes of the <authorizedNode> resource as defined in 9.6.16 which need be updated, with the exception of the following that cannot be modified: “lastModifiedTime” |
| Pre-Processing at Originator | According to clause 10.1.3 |
| Processing at Receiver | According to clause 10.1.3 |
| Information on Response message | According to clause 10.1.3 |
| Post-Processing at Originator | According to clause 10.1.3 |
| Exceptions | According to clause 10.1.3 |

#### 10.2.17.4	Delete <authorizedNode>

This flow is used for deleting a <authorizedNode> resource residing under a <m2mServiceSubscriptionProfile> resource.

Table 10.2.17.4-1: <authorizedNode> DELETE

| <authorizedNode> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc |
| Information on Request message | All parameters defined in table 8.1.2.1-1 apply with the specific details for: to: the Receiver or hosting CSE shall be an IN-CSE |
| Pre-Processing at Originator | According to clause 10.1.4 |
| Processing at Receiver | According to clause 10.1.4 |
| Information on Response message | According to clause 10.1.4 |
| Post-Processing at Originator | According to clause 10.1.4 |
| Exceptions | According to clause 10.1.4 |

## ---------------------------------------end 6th change----------------------------

## ---------------------------------------7th change----------------------------

# Annex G (informative): List of M2M Services

This annex provides a list of M2M Services supported in this document as well as the list of associated roles mapped to each M2M Service.

Table G-1: M2M Services

| M2M Service (name) | M2M-Serv-ID | Roles |
| --- | --- | --- |
| Application and service management | 01 | 001-Software management |
| Device management | 02 | 002-Device Configuration 003-Device Diagnostics and Monitoring 004-Device Firmware Management 005-Device Topology |
| Location | 03 | 006-Location |
| Data exchange | 04 | 007-Basic data |
| Device onboarding | 05 | 008-onboarding |
| Security | 06 | 009-Security Administration |

Use of M2M Service Subscription across M2M Service Provider domains is subject to M2M Service Providers agreement.

The following table provides an example of mapping of Service Roles to resource types and operations. Such a table is to be configured by the SP to allow for the validation of requests according to the service subscription.

Table G-2: Mapping of Service Roles to Resource Types/Allowed Operations

| Service Role | Resource Type/Allowed Operations |
| --- | --- |
| 001: Software management | mgmtObj / CRUD mgmtCmd / CRUD software / CRUD |
| 002: Device Configuration | mgmtObj / CRUD mgmtCmd / CRUD deviceInfo / CRUD |
| 003: Device Diagnostics and Monitoring | mgmtObj / CRUD mgmtCmd / CRUD deviceInfo / CRUD deviceCapability / CRUD |
| 004: Device Firmware Management | mgmtObj / CRUD mgmtCmd / CRUD firmware / CRUD |
| 005: Device Topology | mgmtObj / CRUD mgmtCmd / CRUD areaNwkInfo / CRUD areaNwkDeviceInfo / CRUD |
| 006: Location | locationPolicy / CRUD container / CRUD subscription / CRUD |
| 007: Basic data | container / CRUD subscription / CRUD |
| 008: onboarding | m2mServiceSubscriptionProfile / CRUD authorizedNode / CRUD |
| 009: Security Administration | accessControlPolicy / CRUD |

## ---------------------------------------end 7th change----------------------------