| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Heedong Choi, LG Electronics, heedong.choi@lge.com |
| Format:* | ARC |
| Date:* | 2014-07-28 |
| Contact:* | Heedong Choi, LG Electronics, heedong.choi@lge.com |
| Reason for Change/s:* | To update the event category for consistency |
| CR against: Release* | Pre-release |
| CR against: TS/TR* | TS-0001 v0.8.0 |
| Clauses/Sub Clauses* | 8.1.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or (missing) functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The current clarification for ec is well grouped in ‘immediate’, ‘bestEffort’ and ‘latest’, however it is not fully covered the current ARC TS. One of them is the notification procedure.

In the notification procedure, we have agreed that the urgent notification will be sent regardless of Originator’s schedule. Because the corresponding notification is considered the urgent notification, it may need to set to ‘immediate’. However, the notification with the predefined ‘immediate’ cannot send because it is only available when communication over an underlying network is possible.

So, this contribution proposes to add another value of ec.

## -----------------------Start of change 1-------------------------------------------

### 8.1.2	Request

…

The following values for ‘ec’ shall have a specified pre-defined meaning:

  - ec = ‘immediate’: Requests of this category shall be sent immediately when the Originator’s schedule is allowed and shall not be subject to any further CMDH processing, i.e., when the current time fits to any of <schedule> resource of the Originator, the request will not be subject to storing in CMDH buffers. In particular, CMDH processing will respect values for rqet, rset given in the original request and not fill in any default values if they are missing.

  - ec = ‘urgent’: Requests of this category shall be sent immediately regardless of the Originator’s schedule and shall not be subject to any further CMDH processing, i.e., when the current time doesn’t fit to any of <schedule> resource of the Originator, the request will be sent by temporarily ignoring the Originator’s schedule.

  - ec = ‘bestEffort’: Requests of this category can be stored in CDMH buffers at the discretion of the CSE that is processing the request for an arbitrary time and shall be forwarded via Mcc on a best effort basis. The CSE does not assume any responsibility to meet any time limits for delivering the information to the next CSE. Also the maximum amount of buffered requests for this category is at the discretion of the processing CSE.

  - ec = ‘latest’:

    - If this category is used in a request asking for a CRUD operation on a resource, the following shall apply:
CRUD requests using this category shall undergo normal CMDH processing as outlined further below in this specification and in [i.2] with a maximum buffer size of one pending request for a specific pair of fr and to parameters that appear in the request. If a new  request message is received by the CSE with a pair of parameters fr and to that has already been buffered for a pending request, the newer request will replace the buffered older request.

    - If this category is used in a notification request triggered by a subscription, the following shall apply:
Notification requests triggered by a subscription using this category shall undergo normal CMDH processing as outlined further below in this specification and in [i.2] with a maximum buffer size of one pending notification request per subscription reference that appears in a notification request. If a new notification request is received by the CSE with a subscription reference that has already been buffered for a pending notification request, the newer request will replace the buffered older request.

If no further CMDH policies are provisioned for this event category, the forwarding process shall follow the ‘bestEffort’ rules defined above.

The M2M Service Provider shall be able to provision CMDH policies describing details for the usage of the specific Underlying Network(s) and the applicable rules as defined in the [cmdhPolicy] resource type for other ec values not listed above.

## -----------------------End of change 1-------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?