| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | TS-0007 Mca Registration Supporting Services |
| Source:* | George Foti, Ericsson, George.Foti@ericsson.com |
| Contact: | George Foti, Ericsson, George.Foti@ericsson.com |
| Date:* | 2014-09-15 |
| Abstract:* |  |
| Agenda Item:* |  |
| Work item(s): | TS-0007 WI |
| Document(s) Impacted* | TS-0007 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Update TS for inclusion |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M. Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Contents

Annex Y (Informative): Registration Services	3

Y.1	Overview	3

Y.2	Mca Registration Service Processing and Supporting Services	3

Y.2.1	Message Exchanges	3

Y.2.1.2	Service Capabilities	3

s

-----------------------Start of change 1---------------------------

# Annex Y (Informative): Registration Services

## Y.1	Overview

This annex illustrates the usage of the services for requests to register AEs across the Mca Reference Point and between M2M Service Components across the Msc reference point.

### Y.2	Mca Registration Service Processing and Supporting Services

AEs communicate with the M2M System over the Mca reference point through the SE component. The SE component accepts the request from the AE and provides the request to the Supporting Service in order allow the M2M Service Provider to ensure the request is properly authorized and recorded. In addition, the M2M Service Provider is able to orchestrate other capabilities that have not been specified.

### Y.2.1	Message Exchanges

#### Y.2.1.2	Service Capabilities

##### Y.2.1.2.1	registerAE

This service capability enables an AE or a third party provisioned with the proper authorization to register with the M2M System. This service capability shall be restricted across the Mca reference point

###### Y.2.1.2.1.1	Pre-conditions

The AE has not registered with the M2M System.

The pre-conditions for Mca Received Requests are met.

###### Y.2.1.2.1.2	Signature - registerAE

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| pointOf Access | IN | NO | The point of Access of the registered AE. |
| applicationId | IN | NO | The Application Identifer (App-ID). |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator |
| aeId | OUT | NO | AE-ID is provided back in the response |
| responseType | OUT | NO | Unique response types for this service: AE successfully registered AE not successfully registered |

Table  Y.2.1.2.1.2-1  Registration Services – registerAE capability

###### Y.2.1.2.1.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Perform the Common Request Services for requests across the Mca reference point

- Record the event

- Notify Device onboarding Support Service for a first registration contact with the M2M system for the AE if a subscription exists.

Figure Y.2.1.2.1.3-1 Registration Services – registerAE Diagram

###### Y.2.1.2.1.4	Post-Conditions

Success case: The request is permitted.

Failure case: The request is not permitted and a response type is transmitted back to the AE

###### Y.2.1.2.1.5	Exceptions

No unique exceptions for this service capability.

Consumed services may throw exceptions which are forwarded by this service capability.

###### Y.2.1.2.1.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

Maximum Response: 250ms

##### Y.2.1.2.2	refreshAERegistration

This service capability enables an AE or a third party provisioned with the proper authorization to refresh an existing registration with the M2M System

###### Y2.1.2.2.1	Pre-conditions

The pre-conditions for Mca Received Requests are met.

The AE is registered and allocated an AE-ID by the M2M System.

###### Y.2.1.2.2.2	Signature - refreshAERegsitration

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO |  |
| pointOfAccess | IN | YES | The point of Access of the registered AE. POA is optional only if identical to the one in the refreshed registration |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator. |
| responseType | OUT | NO | Unique response types for this service: AE successfully refreshed Registration Does not exist |

Table Y.2.1.2.2.2-1 Regsitration Services : refreshAERegistration capability

###### Y.2.1.2.2.3	Service Interactions

The interactions of service capabilities required for this service capability as shown in Figure Y.2.1.2.1.3-1

- Perform the Common Request Services for requests across the Mca reference point

- Record the event

Figure Y.2.1.2.2.3-1 Registration Services  – refreshAERegistration Diagram

###### Y.2.1.2.2.4	Post-Conditions

Success case: The request is permitted.

Failure case: The request is not permitted and a response type is transmitted to the AE

###### Y.2.1.2.2.5	Exceptions

No unique exceptions for this service capability.

Consumed services may throw exceptions which are forwarded by this service capability.

###### Y.2.1.2.2.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

Maximum Response: 50ms

##### Y.2.1.2.3	deregisterAE

This service capability enables an AE or a third party provisioned with the proper ACP to deregister from the M2M System..

###### Y.2.1.2.3.1	Pre-conditions

The pre-conditions for Mca Received Requests are met.

The AE-ID is registered .

###### Y.2.1.2.3.2	Signature – deregisterAE

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO |  |
| responseType | OUT | NO | Unique response types for this service: AE successfully De-registsred Registration Does not exist |

Table Y.2.1.2.3.2-1 RegistrationServcies – deregisterAE capability

###### Y.2.1.2.3.3	Service Interactions

The interactions of service capabilities required for this service capability as shown in Figure Y.2.1.2.1.3-1

- Perform the Common Request Services for requests across the Mca reference point

- Record the event

Figure Y.2.1.2.3.3-1 Registration Services  – deregristerAE Diagram

###### Y.2.1.2.3.4	Post-Conditions

Success case: The request is permitted.

Failure case: The request is not permitted and a response type is transmitted back to the AE

###### Y.2.1.2.3.5	Exceptions

No unique exceptions for this service capability.

Consumed services may throw exceptions which are forwarded by this service capability.

###### Y.2.1.2.3.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

Maximum Response: 300ms