| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | TS-0007 event collection services |
| Source:* | Guang Lu |
| Contact: | Guang.Lu@InterDigital.com |
| Date:* | 2014-09-13 |
| Abstract:* | This contribution defined the Event Collection service and its service capabilities |
| Agenda Item:* |  |
| Work item(s): | TS-0007 WI |
| Document(s) Impacted* | TS-0007 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | If agreed, update TS for inclusion |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Rationale	3

6.10 Event Collection	6

6.10.1	Overview	6

6.10.2	Service Capabilities	6

6.10.2.1	setEventCollectionPolicy	6

6.10.2.1.1	Pre-conditions	6

6.10.2.1.2	Signature – setEventCollectionPolicy	6

6.10.2.1.3	Post-Conditions	9

6.10.2.1.4	Exceptions	9

6.10.2.1.5	Policies for Use	9

6.10.2.1.6	Service Interactions	9

6.10.2.1.7	oneM2M Resource Interworking	9

6.10.2.2	getEventCollectionPolicy	10

6.10.2.2.1	Pre-conditions	10

6.10.2.2.2	Signature – getEventCollectionPolicy	10

6.10.2.2.3	Post-Conditions	10

6.10.2.2.4	Exceptions	10

6.10.2.2.5	Policies for Use	10

6.10.2.2.6	Service Interactions	11

6.10.2.2.7	oneM2M Resource Interworking	11

6.10.2.3	setEventCollectionTriggers	11

6.10.2.3.1	Pre-conditions	11

6.10.2.3.2	Signature – setEventCollectionTriggers	11

6.10.2.3.3	Post-Conditions	12

6.10.2.3.4	Exceptions	12

6.10.2.3.5	Policies for Use	12

6.10.2.3.6	Service Interactions	12

6.10.2.3.7	oneM2M Resource Interworking	13

6.10.2.4	getEventCollectionTriggers	13

6.10.2.4.1	Pre-conditions	13

6.10.2.4.2	Signature – getEventCollectionTriggers	13

6.10.2.4.3	Post-Conditions	14

6.10.2.4.4	Exceptions	14

6.10.2.4.5	Policies for Use	14

6.10.2.4.6	Service Interactions	14

6.10.2.4.7	oneM2M Resource Interworking	14

6.10.2.5	recordEvent	14

6.10.2.5.1	Pre-conditions	15

6.10.2.5.2	Signature – recordEvent	15

6.10.2.5.3	Post-Conditions	15

6.10.2.5.4	Exceptions	15

6.10.2.5.5	Policies for Use	15

6.10.2.5.6	Service Interactions	15

6.10.2.5.7	oneM2M Resource Interworking	16

6.10.2.6	getRecords	16

6.10.2.6.1	Pre-conditions	16

6.10.2.6.2	Signature – getRecords	16

6.10.2.6.3	Post-Conditions	16

6.10.2.6.4	Exceptions	16

6.10.2.6.5	Policies for Use	16

6.10.2.6.6	Service Interactions	16

6.10.2.6.7	oneM2M Resource Interworking	17

6.10.2	Event Record Template	17

Annex G (informative): List of M2M Services [2]	18

# Rationale

This contribution defines the services for Event Collection. This section describes the rationale of the service definitions and how it works.  Figure 1 shows the SOA event collection architecture. The Event Collection Service contains three logical functions. Event Collection Policy provides the service to set up event collection policies. Event Collection Triggers provides the service to define specific collectable triggers. Event Collection Execution provides the service for event recording when the trigger happens. Each logical function contains two functions as shown in yellow boxes, and these functions are defined in this contribution.

Figure 1 SOA Event Collection Architecture

Use of Event Collection Service

The following two figures show the sequences of event collection. For readability, the operations are divided by two parts: part 1 is the configuration of event collection policy and event triggers, and part 2 is the event collection

when triggers happened.

Figure 2 Part 1 - Event Collection Configuration

Step 1-3: An AE or CSE (identified as AE1 or CSE1) configures event collection policy at the Service Exposure. The Service Exposure entity passes the message to the Event Collection service. The message contains the information element of “eventConfig” which defines the specific policies. The policy is stored at the Event Collection service entity.

Step 4 -5: Another AE or CSE (identified as AE2 or CSE2) can retrieve the event collection policy available for discovery.

Step 6-8: AE2 or CSE2 configures event collection triggers based on the event collection policy it obtained. Such triggers are stored at the Event Collection entity.

Figure 3 Part 2 – Event Recording

Step 9-10: The Event Collection service entity passes the event collection triggers to the appropriate services, such as Data Exchange service. The other services store a local version of the triggers.

Step 11-13: When the conditions of the configured event happens, the other services generate the event and request the Event Collection entity to record the event. For example, when the Data Exchange service receives the subscribeComplete message, it triggers the recordEvent message and sends it to the Event Collection service entity. The Event Collection service entity stores the event records.

Step 14-15: AE2 or CSE2 obtains the event records from the Event Collection service entity. For example, it can obtain all events related to itself for a period of time.

-----------------------Start of change 1 (new content)---------------------------------

## 6.10 Event Collection

### 6.10.1	Overview

The Event Collection service provides the capability to record events for accounting purposes.

### 6.10.2	Service Capabilities

#### 6.10.2.1	setEventCollectionPolicy

This service capability provides the ability for AEs and CSEs to configure an event for statistics and charging purposes.

##### 6.10.2.1.1	Pre-conditions

The originator can be an AE or CSE, and the originator wants to configure event collection policies at a receiving CSE. The receiving CSE conducts event collection according to the policies. The receiving CSE may establish its own event collection policies.

The originator, if different from the receiving CSE, is subscribed and registered to the receiving CSE.

##### 6.10.2.1.2	Signature – setEventCollectionPolicy

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| commonParameters | IN | NO | See Table A.2.1.1.2-1 |
| serviceId | IN | NO | The M2M Service Identifier (M2M-Serv-ID) |
| eventConfig | IN | NO | The configuration of the event collection policy |
| eventCollectionPolicyID | OUT | NO | The receiving CSE generates a unique policy ID for each policy. |
| responseType | OUT | YES | Unique response types for this service. Exception: Policy already exists |

Table 6.10.2.1.2-1 Event Collection – setEventCollectionPolicy capability

| Parameter name | Optional | Description |
| --- | --- | --- |
| eventType | NO | This attribute indicates the type of the event, such as timer based, data operation, storage based, etc. The eventType can be a combination of multiple sub-types, for example, it can be based on both a data operation and a timer, such as recording all RETRIEVE data operation during one Hour period of time. |
| serviceRoleIds | YES | Defines the specific service role. |
| eventStart | YES | This attribute indicates the start time of the event. It is mandatory if the eventType includes “timer based”. |
| eventEnd | YES | This attribute indicates the end time of the event. It is mandatory if the eventType includes “timer based”. |
| operationType | YES | This attribute defines the type of the operation to be collected by statistics, such as CREATE, RETRIEVE. It is mandatory if the eventType includes “data operation”. |
| dataSize | YES | This attribute defines the data size if an event is triggered when the stored data exceeds a certain size. It is mandatory if the eventType is “storage based”. |

Table 6.10.2.1.2-2 Event Collection – eventConfig Complex Data Type

Table 6.10.2.1.2-3  defines examples of eventType Complex Data Types. More events can be defined when more services are available.

| Parameter name | Optional | Description |
| --- | --- | --- |
| subscribeComplete | YES | This attribute defines the event when the Data Exchange entity completes the Subscribe service for a service consumer, such as an AE. The event recording shall be triggered when the Data Exchange service received the subscribeComplete response message. |
| publishComplete | YES | This attribute defines the event when the Data Exchange entity completes the Publish service for a service consumer, such as an AE. The event recording shall be triggered when the Data Exchange service received the publishComplete response message. |
| notifyComplete | YES | This attribute defines the event when the Data Exchange entity completes the Notify service for a service consumer, such as an AE. The event recording shall be triggered when the Data Exchange service received the NotifyComplete response message. |
| getServiceSubscriptionComplete | YES | This attribute defines the event when an entity, such as an AE, retrieves the Service Subscription. The event recording shall be triggered when the Service Subscription Administration receives the getServiceSubscriptionComplete response message. |
| addDeviceToServiceSubscriptionComplete | YES | This attribute defines the event when an entity, such as an AE, adds a device to a Service Subscription. The event recording shall be triggered when the Service Subscription Administration receives the addDeviceToServiceSubscriptionComplete response message. |
| deleteDeviceFromServiceSubscription | YES | This attribute defines the event when an entity, such as an AE, deletes a device to a Service Subscription. The event recording shall be triggered when the Service Subscription Administration receives the deleteDeviceToServiceSubscriptionComplete response message. |
| getDevicesForServiceSubscription | YES | This attribute defines the event when an entity, such as an AE, retrieves a device from a Service Subscription. The event recording shall be triggered when the Service Subscription Administration receives the getDevicesForServiceSubscriptionComplete response message. |
| addApplicationsToServiceSubscription | YES | This attribute defines the event when an entity adds M2M applications to a Service Subscription. The event recording shall be triggered when the Service Subscription Administration receives the addApplicationsToServiceSubscription response message. |
| deleteApplicationsFromServiceSubscription | YES | This attribute defines the event when an entity deletes M2M applications from a Service Subscription. The event recording shall be triggered when the Service Subscription Administration receives the deleteApplicationsFromServiceSubscription response message. |
| getApplicationsForServiceSubscription | YES | This attribute defines the event when an entity retrieves M2M applications for a Service Subscription. The event recording shall be triggered when the Service Subscription Administration receives the getApplicationsForServiceSubscription response message. |
| updateApplicationForDevice | YES | This attribute defines the event to update the M2M applications for a device associated with a Service Subscription. The event recording shall be triggered when the Service Subscription Administration receives the updateApplicationsForDevice response message. |
| downloadFirmware | YES | This attribute defines the event to execute the downloadFirmware request from an AE. The event recording shall be triggered when the Device Management service receives the downloadFirmware response message. |
| installFirmware | YES | This attribute defines the event to execute the installFirmware request from an AE. The event recording shall be triggered when the Device Management service receives the installFirmware response message. |
| getFirmwareInformation | YES | This attribute defines the event to execute the getFirmwareInformation request from an AE. The event recording shall be triggered when the Device Management service receives the getFirmwareInformation response message. |
| getFirmwareExecStatus | YES | This attribute defines the event to execute the getFirmwareExecStatus request from an AE. The event recording shall be triggered when the Device Management service receives the getFirmwareExecStatus response message. |
| reportFirmwareStatus | YES | This attribute defines the event to notify an AE about the status of a firmware operation based on a previous submitted operation request. The event recording shall be triggered when the Device Management service receives the reportFirmwareStatus response message. |
| upgradeFirmware | YES | This attribute defines the event when AE upgrades the firmware. The event recording shall be triggered when the Device Management service receives the upgradeFirmware response message. If the operation is for multiple devices, event recording shall be triggered for each single event. |
| GetDeviceInformation | YES | This attribute defines the event to allow an AE to retrieve the information about a device across the Mca reference point. The event recording shall be triggered when the Device Management service receives the getDeviceInformation response message. |
| GetDeviceCapabilities | YES | This attribute defines the event to allow an AE to retrieve the information about a device’s capabilities across the Mca reference point. The event recording shall be triggered when the Device Management service receives the getDeviceCapabilities response message. |
| enableDeviceCapability | YES | This attribute defines the event to execute an enableDeviceCapability request from an AE. The event recording shall be triggered when the Device Management service receives the enableDeviceCapability response message. |
| disableDeviceCapability | YES | This attribute defines the event to execute a disableDeviceCapability request from an AE. The event recording shall be triggered when the Device Management service receives the disableDeviceCapability response message. |
| getAreaNetworks | YES | This attribute defines the event to execute a getAreaNetworks request from an AE. The event recording shall be triggered when the Device Management service receives the getAreaNetworks response message. |
| updateDeviceForAreaNetwork | YES | This attribute defines the event to execute an updateDeviceForAreaNetwork request from an AE. The event recording shall be triggered when the Device Management service receives the updateDeviceForAreaNetwork response message. |

Table 6.10.2.1.2-3 Event Collection – eventType Complex Data Type

##### 6.10.2.1.3	Post-Conditions

Not Applicable

##### 6.10.2.1.4	Exceptions

- The originator has no access right to create the policy

##### 6.10.2.1.5	Policies for Use

Message Exchange Patterns: In-Out

##### 6.10.2.1.6	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the  request to the Supporting Service to perform the operation

Figure 6.10.2.1.6-1 setEventCollectionPolicy Diagram

##### 6.10.2.1.7	oneM2M Resource Interworking

The service capability aligns with the <eventConfig> resource and maps to the CREATE procedure for the resource.

#### 6.10.2.2	getEventCollectionPolicy

This service capability provides the ability for entities, such as an AE,  to retrieve the existing policies at a CSE.

##### 6.10.2.2.1	Pre-conditions

The originator can be an AE or CSE, and the originator wants to retrieve event collection policies at a receiving CSE.

The originator, if different from the receiving CSE, is subscribed and registered to the receiving CSE. The originator is only allowed to retrieve with the proper access right.

##### 6.10.2.2.2	Signature – getEventCollectionPolicy

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| commonParameters | IN | NO | See Table A.2.1.1.2-1 |
| eventCollectionPolicyID | IN | NO | See Table 6.10.2.1.2-2. The eventCollectionPolicyID specifies the specific event collection policy to retrieve, if the originator has such information. If the originator does not have the information regarding eventCollectionPolicyID, it indicates eventCollectionPolicyID with a specific value that represents “any IDs”, and use the filterCriteria to filter selected policies. |
| filterCriteria | IN | YES | See Table 6.8.1.1.1-1 |
| responseType | OUT | YES | Unique response types for this service. Exception: eventCollectionPolicyID does not exist |

Table 6.10.2.2.2-1 Event Collection – getEventCollectionPolicy capability

##### 6.10.2.2.3	Post-Conditions

Not Applicable

##### 6.10.2.2.4	Exceptions

- The originator has no access right to retrieve the policy

##### 6.10.2.2.5	Policies for Use

Message Exchange Patterns: In-Out

##### 6.10.2.2.6	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the  request to the Supporting Service to perform the operation

Figure 6.10.2.2.6-1 getEventCollectionPolicy Diagram

##### 6.10.2.2.7	oneM2M Resource Interworking

The service capability aligns with the <eventConfig> resource and maps to the RETRIEVE procedure for the resource.

#### 6.10.2.3	setEventCollectionTriggers

This service capability provides the ability for AEs and CSEs to configure specific triggers for event collection, based on the Event Collection Policy.

##### 6.10.2.3.1	Pre-conditions

The originator can be an AE or CSE, and the originator wants to configure event collection triggers based on existing event collection policy available at the collecting CSE.

##### 6.10.2.3.2	Signature – setEventCollectionTriggers

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| commonParameters | IN | NO | See Table A.2.1.1.2-1 |
| eventCollectionPolicyID | IN | NO | This attribute specify the policy used to define the specific event collection trigger. |
| collectingEntityID | IN | NO | This is the ID of the entity where the event is being collected. If not specified, the default collecting entity is the receiving CSE. |
| collectedEntityID | IN | NO | This is the ID of the entity that triggered the event collection. If not specified, the default is all entities triggered the event at the collecting entity. |
| eventReceiverID | IN | YES | In cases when there is another entity, other than the collecting entity (such as a CSE), wants to receive the collected event, this attribute provides the unique ID of this entity. |
| serviceRoleIds | IN | YES | Specifies the service roles that trigger the event collection. |
| serviceId | IN | YES | Specifies the services that trigger the event collection. |
| triggerStatus | IN | YES | This attribute indicates if the trigger is activated or not. If not defined, the trigger is activated. |
| eventCollectionTriggerID | OUT | NO | The receiving CSE generates a unique ID for each event collection trigger. |
| responseType | OUT | YES | Unique response types for this service. Exception: eventCollectionPolicyID is invalid collectingEntityID is invalid collectedEntityID is invalid eventReceiverID is invalid triggerStatus is invalid |

Table 6.5.2.2.2-1 Event Collection – setEventCollectionTriggers capability

##### 6.10.2.3.3	Post-Conditions

After the successful creation of event collection triggers, when the defined event happens at the collectingEntity, and when the event collection trigger status is ACTIVE, the collectingEntity shall collect the event. The supporting service shall send a recordEvent message to the Event Collection entity.

##### 6.10.2.3.4	Exceptions

- The originator has no access right to create the event collection triggers

##### 6.10.2.3.5	Policies for Use

Message Exchange Patterns: In-Out

##### 6.10.2.3.6	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the request to the Supporting Service to perform the operation

Figure 6.10.2.3.6-1 setEventCollectionTriggers Diagram

##### 6.10.2.3.7	oneM2M Resource Interworking

The service capability aligns with the <statsCollect> resource and maps to the CREATE procedure for the resource.

#### 6.10.2.4	getEventCollectionTriggers

This service capability provides the ability for AEs and CSEs to retrieve event collection triggers at a receiving CSE.

##### 6.10.2.4.1	Pre-conditions

Originating AEs and CSEs are subscribed to the CSE and registered to the targeting CSE.  Originator has the access right to retrieve.

##### 6.10.2.4.2	Signature – getEventCollectionTriggers

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| commonParameters | IN | NO | See Table A.2.1.1.2-1 |
| eventCollectionTriggerID | IN | YES | This attribute specifies which event collection triggers to retrieve. If not specified, any event collection trigger matching the filter criteria should be retrieved. If the originator does not have the information regarding eventCollectionTriggerID, it indicates with a specific value that represents “any IDs”, and use the filterCriteria to filter selected event triggers. |
| filterCriteria | IN | YES | See Table 6.8.1.1.1-1 |
| responseType | OUT | YES | Unique response types for this service. Exception: eventCollectionTriggerID does not exist |

Table 6.5.2.2.2-1 Event Collection – getEventCollectionTriggers capability

##### 6.10.2.4.3	Post-Conditions

Not Applicable

##### 6.10.2.4.4	Exceptions

- The originator has no access right to retrieve the event collection triggers

##### 6.10.2.4.5	Policies for Use

Message Exchange Patterns: In-Out

##### 6.10.2.4.6	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the request to the Supporting Service to perform the operation

Figure 6.10.2.4.6-1 getEventCollectionTriggers Diagram

##### 6.10.2.4.7	oneM2M Resource Interworking

The service capability aligns with the <statsCollect> resource and maps to the RETRIEVE procedure for the resource.

#### 6.10.2.5	recordEvent

This service capability provides the ability for a service (such as Data Exchange service) to trigger the collecting entity (such as a CSE) to record an event.

##### 6.10.2.5.1	Pre-conditions

Event Collection Triggers have been created by the setEventCollectionTriggers capability.

##### 6.10.2.5.2	Signature – recordEvent

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| commonParameters | IN | NO | See Table A.2.1.1.2-1 |
| eventCollectionPolicyID | IN | YES | This attribute specify the policy used to define the specific event collection trigger. |
| eventCollectionTriggerID | IN | NO | The service where the trigger happens provides the eventCollectionTriggerID being used. |
| eventDescription | IN | NO | This attribute describes the event triggered at the service. It is a subset of the eventConfig data structure. It contains one or more parameters defined in the eventConfig data type. |
| recordID | OUT | NO | The event collection service generates a unique recordID. |
| responseType | OUT | YES | Unique response types for this service. Exception:. Event recording cannot be completed |

Table 6.5.2.2.2-1 Event Collection – recordEvent capability

##### 6.10.2.5.3	Post-Conditions

Not Applicable

##### 6.10.2.5.4	Exceptions

Not Applicable

##### 6.10.2.5.5	Policies for Use

Message Exchange Patterns: In-Out

##### 6.10.2.5.6	Service Interactions

The request comes from the service where the event was triggered to the Event Collection entity.

Figure 6.10.2.5.6-1 recordEvent Diagram

##### 6.10.2.5.7	oneM2M Resource Interworking

Not Applicable

#### 6.10.2.6	getRecords

This service capability provides the ability for AEs and CSEs to retrieve the recorded events for statistical or charging purposes.

##### 6.10.2.6.1	Pre-conditions

Originating AEs and CSEs are subscribed to the CSE and registered to the receiving CSE.

##### 6.10.2.6.2	Signature – getRecords

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| commonParameters | IN | NO | See Table A.2.1.1.2-1 |
| eventRecordID | IN | NO | This attribute specifies which record to retrieve. If not specified, any event records matching the filter criteria should be retrieved. If the originator does not have the information regarding the eventRecordID, it indicates with a specific value that represents “any IDs”, and use the filterCriteria to filter selected records of events. |
| filterCriteria | IN | YES | See Table 6.8.1.1.1-1 |
| responseType | OUT | YES | Unique response types for this service. Exception: The eventRecordID |

Table 6.5.2.2.2-1 Event Collection – getRecords capability

##### 6.10.2.6.3	Post-Conditions

Not Applicable

##### 6.10.2.6.4	Exceptions

Not Applicable

##### 6.10.2.6.5	Policies for Use

Message Exchange Patterns: In-Out

##### 6.10.2.6.6	Service Interactions

The originator sends the request to the Event Collection entity to obtain the event records it is

interested in.

Figure 6.10.2.6.6-1 getRecords Diagram

##### 6.10.2.6.7	oneM2M Resource Interworking

Not Applicable

### 6.10.2	Event Record Template

| Information Element | Optional | Description |
| --- | --- | --- |
| eventRecordID | NO | It is the unique ID that identifies a specific event record. |
| eventCollectionTriggerID | NO | It is the unique ID that identifies a specific event collection triggering scenario, which triggers information recording for a specific event. |
| collectingEntityID | NO | This is the unique ID of the entity that collects the statistics. It can be an AE-ID or CSE-ID |
| collectedEntityID | NO | This is the unique ID of the entity whose service layer operation statistics are being collected. It can be an AE-ID or CSE-ID. |
| serviceProfileID | YES | An M2M Service Profile Identifier defines M2M Services and/or M2M Service Roles and AEs applicable to M2M Nodes. |
| eventDescription | NO | Describes the event triggered at the service. It is a subset of the eventConfig data structure. The specific structure depends on the specific event defined by the Event Collection Trigger. |
| Vendor Specific Information | YES | Defines Vendor specific information |

-----------------------End of change 1-------------------------------------------

-----------------------Start of change 2-------------------------------------------

# Annex G (informative): List of M2M Services [2]

This annex provides a list of M2M Services supported in this document as well as the list of associated roles mapped to each M2M Service.

Table G-1: M2M Services

| M2M Service (name) | M2M-Serv-ID | Roles |
| --- | --- | --- |
| Application and service management | 01 | 001-Software management |
| Device management | 02 | 002-Device Configuration 003-Device Diagnostics and Monitoring 004-Device Firmware Management 005-Device Topology |
| Location | 03 | 006-Location |
| Data exchange | 04 | 007-Basic data |
| Device onboarding | 05 | 008-onboarding |
| Security | 06 | 009-Security Administration |
| Event Collection | 07 | 010 – Event Collection |

Use of M2M Service Subscription across M2M Service Provider domains is subject to M2M Service Providers agreement.

The following table provides an example of mapping of Service Roles to resource types and operations. Such a table is to be configured by the SP to allow for the validation of requests according to the service subscription.

Table G-2: Mapping of Service Roles to Resource Types/Allowed Operations

| Service Role | Resource Type/Allowed Operations |
| --- | --- |
| 001: Software management | mgmtObj / CRUD mgmtCmd / CRUD software / CRUD |
| 002: Device Configuration | mgmtObj / CRUD mgmtCmd / CRUD deviceInfo / CRUD |
| 003: Device Diagnostics and Monitoring | mgmtObj / CRUD mgmtCmd / CRUD deviceInfo / CRUD deviceCapability / CRUD |
| 004: Device Firmware Management | mgmtObj / CRUD mgmtCmd / CRUD firmware / CRUD |
| 005: Device Topology | mgmtObj / CRUD mgmtCmd / CRUD areaNwkInfo / CRUD areaNwkDeviceInfo / CRUD |
| 006: Location | locationPolicy / CRUD container / CRUD subscription / CRUD |
| 007: Basic data | container / CRUD subscription / CRUD |
| 008: onboarding | m2mServiceSubscriptionProfile / CRUD serviceSubscribedNode / CRUD |
| 009: Security Administration | accessControlPolicy / CRUD |
| 0010: Event Collection | statsConfig / CRUD eventConfig / CRUD statsCollect / CRUD |

-----------------------End of change 2-------------------------------------------