| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Format:* | ARC |
| Date:* | 2014-09-15 |
| Contact:* | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Reason for Change/s:* | To clean up AE-ID and App-ID |
| CR against: Release* | Pre-release |
| CR against: TS/TR* | TS-0001 v0.8.0 |
| Clauses/Sub Clauses* | 7.1.14, 7.1.3, 7.1.2, 7.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or (missing) functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

- Introduce New AE-ID and change current AE-ID

Currently there is no way to identify AE before AE registration. Since security association(including authentication) is done before any one message is sent, we need to have new identifier of AE which identifies before security association.

Current AE-ID is noting more than address of AE so this contribution propose to change it to AE-Address and it indicates <AE> resource of that AE.

- Make App-ID unique

In ARC specification, App-ID is specified as just a string and it doesn’t guarantee any uniqueness. However, the usages of App-ID are CMDH(applying the same policy to the same App) and statistics(used for billing mainly). So this document suggests App-ID to be unique within M2M Service Provider domain.

## -----------------------Start of change 1-------------------------------------------

### 7.1.14	Application Entity Address (AE-Address)

An Application Entity Address (AE-Address) uniquely addresses an AE resident on an M2M Node, or an AE that requests to interact with an M2M Node. An AE-Address is used for all interactions within the M2M System.

The AE-Address is globally unique and when used internally to a specific M2M SP domain, it is sufficient to be unique within that M2M Service Provider domain. It is extended to become globally unique when used outside the M2M Service Provider boundaries. The IN-CSE shall perform this task of adding or removing identifier portions (identifying the M2M SP) according to clause 7.1.12.

Additionally the AE-Address, when used in the context of a specific CSE where the AE is registered, it is sufficient to be unique within the scope of that specific CSE. It is extended to become M2M Service Provider unique when used outside such specific CSE.

The hosting CSE of the AE shall perform this task of adding or removing the identifier portions according to clause 7.1.12.

### 7.1.3	Application Identifier (App-ID)

This is equivalent to the application name and is guaranteed to be unique within M2M Service Provider domain. It can be used for billing Application Provider or providing communication policies per an application. A Node shall be able to contain at most one AE per an Application.

Note: how M2M Service Provider assigns App-ID and makes it unique is not specified in this document.

## -----------------------End of change 1-------------------------------------------

## -----------------------Start of change 2-------------------------------------------

### 7.1.2	Application Entity Identifier (AE-ID)

Application Entity Identifier uniquely identifies Application Entity and AE shall have an its own AE-ID for its lifetime. AE-ID shall consist of M2M-SP-ID, Node-ID, and/or App-ID depending the format specified in clause 7.2.

Although AE-Address may be variable due to network configuration changed, AE-ID shall not be changed.

## -----------------------End of change 2-------------------------------------------

## -----------------------Start of change 3-------------------------------------------

## 7.2	M2M-SP-ID, CSE-ID and AE-ID and resource Identifier formats

As a general rule, the identifiers of AEs, CSEs and resources are globally unique. In order to optimize their use, the identifiers shall be shortened when their scope can be derived from their context of use by the CSEs and the AEs.  Such shortened identifiers are defined as 'relative' identifiers.

TheM2M system shall use the identifiers M2M-SP-ID, CSE-ID and AE-ID and resource identifiers according to the formats and the rules specified in the following table (table 7.2-1).

Table 7.2-1: Identifiers formats and use

|  | Format Name | Format | Rule of use |
| --- | --- | --- | --- |
| M2M-SP-ID format |  | Fully qualified domain name Examples: <scheme>://www.m2mprovider.com <scheme>://globalm2m.org Note: the <scheme> part, as stated in clause 7.1, is unique and protocol-independent | When The M2M-SP-ID is used, the FQDN format applies |
| AE-Address EQUIVALENT formats | CSE-relative-AE-Address (with respect to the context of the CSE hosting the AE) | The CSE-relative AE Address is a sequence of characters that may include any of the unreserved characters defined in the clause 2.3 of the RFC3986 [i.x], as well as the slash character. It shall not start with the slash character. The CSE-relative AE Address is unique within the context of the CSE. This value is the same as the name of <AE> resource. | On the Mca reference point: to refer to AEs that are hosted by the directly attached (Registrar) CSE. The hosting CSE is responsible for guaranteeing that the CSE-Relative-AE-Address is unique in the context of the hosting CSE. |
|  | SP-relative -AE-Address (with respect to the context of the SP hosting the AE) | /[CSE-ID]/CSE-relative-AE-Address It begins with a slash character, as specified in clause 4.2 of RFC3986 [i.12] under “absolute-path reference”. | On the Mca and Mcc reference points: to refer to AEs that are hosted by the M2M Service Provider domain to which AE is attached. |
|  | Absolute AE-Address | M2M-SP-ID/SP-relative-AE-Address The absolute AE-Adress shall conform to the URI format as defined in the IETF RFC 3986 [i.12]. | On the Mca and Mcc reference points: to refer to AEs that are hosted by a different M2M Service Provider domain with respect to the one to which the AE is attached and on the Mcc’ reference point for all the AEs |
| CSE-ID EQUIVALENT formats | SP-relative-CSE-ID (with respect to the context of the SP hosting the CSE) | M2M-SP-ID/SP-relative-AE-ID The absolute AE-ID shall conform to the URI format as defined in the IETF RFC 3986 [i.12]. | On the Mca and Mcc reference points: to refer to CSEs that are hosted by the same M2M Service Provider domain |
|  | Absolute CSE-ID | M2M-SP-ID/SP-relative-CSE-ID | On Mca and Mcc reference points: to refer to CSEs that are hosted by different M2M Service Provider domains and on the Mcc’ reference point for all the CSEs |
| Resource identifier equivalent formats | CSE-relative Resource ID | The CSE-relative Resource Identifier is a sequence of characters that may include any of the unreserved characters defined in the clause 2.3 of the RFC3986 [i.12], as well as the slash character. It shall not start with the slash character. The CSE-relative Resource Identifier is unique in the context of the CSE. Examples: container123 containers/c123 a1b2c3d4b0b00f0fa66a123456789abc a1b2c3d4-b0b0-0f0f-a66a-123456789abc cont/ b0b0-0f0f-a66a-123456789abc |  |
|  | SP-relative Resource ID (with respect to the context of the M2M Service Provider hosting the CSE) | The SP-relative Resource identifier is an absolute-path relative reference (beginning with a single slash), as defined in clause 4.2 of RFC3986 [i.12]. The SP-relative Resource Identifier is unique in the context of the Service Provider. | On the Mca and Mcc reference points: to refer to resources that are hosted by the same M2M Service Provider domain |
|  | Absolute Resource ID | M2M-SP-ID/SP-relative-Resource-ID | On Mca and Mcc reference points: to refer to resources that are hosted by a different M2M Service Provider domain and on the Mcc’ reference point for all the resources |
| AE-ID EQUIVALENT formats | SP-relative -AE-ID (with respect to the context of the SP hosting the AE) | Concatenation of Node-ID and App-ID | During Security Association to identify/authenticate AE and AE registration procedure on the Mca reference point |
|  | Absolute AE-ID | Concatenation of M2M-SP-ID, Node-ID and App-ID | During Security Association to identify/authenticate AEand AE registration procedure on the Mca reference point |

NOTE: This table still needs to be further fixed and be given more examples.

As a consequence, the hosting CSE shall convert the AEs global and relative identifier according to table 7.1.12-1 when a request is transmitted across the Mcc and Mca reference points.

As a consequence, the IN-CSE shall convert the AEs, CSEs and resource global and relative identifiers according to table 7.1.12-1when a request is transmitted across the Mcc’ reference point.

## -----------------------End of change 3-------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?