| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 Architecture |
| Source:* | Ericsson |
| Format:* | ARC14 |
| Date:* | 2014-10-25 |
| Contact:* | George Foti |
| Reason for Change/s:* | The purpose of M2M-Service-ID, and SRole-ID is unclear and requires clarification |
| CR against: Release* | Release-1 |
| CR against: TS/TR* | TS-0001 v1.1.0 |
| Clauses/Sub Clauses* | 9.6.5, D.12 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR con`tains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

## ----------------------------------first change---------------------------

### 7.1.12	Service Role identifier (SRole-ID)

In each M2M Service, one or multiple M2M Service Role(s) shall be defined by the M2M Service Provider. An M2M Service Role is defined as a set of privileges pertaining to resource types which are associated with M2M Services. See Annex G for examples of M2M Service Provider defined Service Roles.

The Service Role Identifier shall be used for service access authoriation.

## ---end of First change---------------------------

## ----------------------------------Second change---------------------------

### 7.1.13	M2M Service Profile Identifier (M2M-Service-Profile-ID)

An M2M Service Profile Identifier defines M2M Service Roles (see Annex G) applicable to M2M Nodes as well as the AEs resident on these nodes. Every M2M Service Profile is allocated an identifier so it can be retrieved for verification purposes.

The M2M-Service-Profile-ID enables the M2M Service Provider to bind AE(s) and M2M Service identifiers and/or M2M Service Roles identifiers to M2M nodes.

An M2M-Service-Profile-ID shall be allocated to every M2M Node

The M2M Service Profile Identifier has the following characteristics:

belongs to the M2M Service Provider;

dentifies the M2M Service Roles and AEs applicable to an M2M node. The M2M Service Roles define the M2M Services authorized for the M2M Service Profile (see Annex G)

## ---end of Second change---------------------------

## ----------------------------------Third change---------------------------

##### 10.1.1.2.2	Application Entity Registration procedure

The procedure for AE registration follows the procedure described in clause 10.1.1.1 with the following exception:

Originator: The Originator shall be the registering AE.

Receiver: The Receiver shall allow the creation of the <AE> resource according to the access control policy. The Receiver shall use, if present, the suggested name from the information parameter nm in the request. If the suggested name of the resource cannot be used (i.e. a resource with that name already exists) the Receiver shall reject the CREATE Request. If the request does not provide the optional nm, then the Receiver shall create the resource and assign a name to it. The Receiver shall derive the M2M-Service-Profile-ID and Node-ID provided from the security credentials of the AE (see clause 11.2.2). The receiver shall fetch the service subscription profile from <m2mServiceSubscriptionProfile> resource.  The receiver shall use the serviceRoles attribute for authorizing any subsequent operation initiated by the AE-ID allocated to the AE

Step 001: The Originator shall send the following information in the CREATE Request message:

fr:	AE-ID or empty.

Step 002: for the <AE> resource the Receiver cannot perform the action described in the first step of clause 10.1.1.1.

All the other parameters of the request and the steps that follow do not deviate from clause 10.1.1.1.

## ---end of Third change---------------------------

## ----------------------------------Fourth change---------------------------

# Table 9.6.19-2: Attributes of <m2mServiceSubscriptionProfile> resource

| Attributes of <m2mServiceSubscriptionProfile> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| resourceID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1 where this common attribute is described. If no accessControlPolicyIDs is given at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute |
| creationTime | 1 | RW | See clause 9.6.1 where this common attribute is described. |
| Labels | 0..1 (L) | RW | See clause 9.6.1 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1 where this common attribute is described. |
| serviceRoles | 0..1 (L) | RW | This attribute contains a list of Service Role IDs (SRole-ID) that are subscribed to in this service subscription. If the multiplicity of this attribute is 0, the role does not apply. |

## ---end of Fourth change---------------------------

## ----------------------------------Fifth change---------------------------

# Annex G (informative): List of M2M Services

This annex provides a list of M2M Services supported in this document as well as the list of associated roles mapped to each M2M Service.

Table G-1: M2M Services

| M2M Service (name) | M2M-Serv-ID | Service Roles (SRole-ID) |
| --- | --- | --- |
| Application and service management | 01 | 01-001: Software management |
| Device management | 02 | 02-001: Device Configuration 02-002: Device Diagnostics and Monitoring 02-003: Device Firmware Management 02-004" Device Topology |
| Location | 03 | 03-001: Location |
| Data exchange | 04 | 04-001: Basic data |
| Device onboarding | 05 | 05-001: onboarding |
| Security | 06 | 06-001: Security Administration |
| Groups | 07 | 07-001: Groups Management |
| Event collection | 08 | 08-001: Event Collection |

Use of M2M Service Subscription across M2M Service Provider domains is subject to M2M Service Providers agreement.

The following table provides an example of mapping of Service Roles to resource types and operations. Such a table is to be configured by the SP to allow for the validation of requests according to the service subscription.

Only Create request shall be verified.

Table G-2: Mapping of Service Roles to Resource Types

| Service Role (SRole-ID) | Resource Type |
| --- | --- |
| 00-000 : All services allowed | All services allowed |
| 01-001: Software management | mgmtObj mgmtCmd software |
| 02-001: Device Configuration | mgmtObj mgmtCmd deviceInfo |
| 02-002: Device Diagnostics and Monitoring | mgmtObj mgmtCmd deviceInfo deviceCapability |
| 02-003: Device Firmware Management | mgmtObj mgmtCmd firmware |
| 02004: Device Topology | mgmtObj mgmtCmd areaNwkInfo areaNwkDeviceInfo |
| 03-001: Location | locationPolicy container subscription |
| 04-001: Basic data | container subscription |
| 05-001: onboarding | m2mServiceSubscriptionProfile serviceSubscribedNode |
| 06-001: Security Administration | accessControlPolicy |
| 07-001 - Group Management | group fanOutPoint / vrirtual resource/ |
| 08-001 - Event Collection | statsConfig eventConfig statsCollect |

## ---end of Fifth change---------------------------