| CHANGE REQUEST |
| --- |
| Group Name:* | ARC 14.0 |
| Source:* | Yali Guo, Haier, guoyali@haierubic.com |
| Format:* | F2F conference |
| Date:* | 2014-10-31 |
| Contact:* | Yali Guo, Haier, guoyali@haierubic.com |
| Reason for Change/s:* | If the delete operation addresses the virtual child resource <fanOutPoint> and success to delete all member resources of a specific group, the member resources are not exist in the member hosting CSEs but the URIs of the member resources are still in the memberList of the <group> resource. |
| CR against: Release* | Rel-1 |
| CR against: TS/TR* | TS-0001-Functional_Architecture-V1_2_0 |
| Clauses/Sub Clauses* | 10.2.7.9 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

If the delete operation addresses the virtual child resource <fanOutPoint> and success to delete all member resources of a specific group, the member resources are not exist in the member hosting CSEs but their URIs are still in the memberList of the <group> resource. This will cause errors for the follow-up requests to this group. As all the member resources have been essentially deleted, we propose to accordingly delete the <group> resource.

### -----------------------Start of the 1st change -------------------------------------------

#### 10.2.7.9	Delete <fanOutPoint>

This procedure shall be used for deleting the content of all members resources belonging to an existing <group> resource.

# Table 10.2.7.9-1: <fanOutPoint> DELETE

| <fanOutPoint> DELETE |
| --- |
| Associated Reference Point | Mcc and Mca |
| Information in Request message | fr: Identifier of the AE or the CSE that initiates the Request to: The URI of the <fanOutPoint> virtual resource cn: The representation of the resource the Originator intends to create gid: The group request identifier |
| Processing at Originator before sending Request | The Originator shall request to delete the content of all members resources belonging to an existing <group> resource by using a DELETE operation. The request may address the virtual child resource <fanOutPoint> of the specific <group> resource of a group Hosting CSE to delete all members resources. The request may also address the URI that results from appending a relative URI to the <fanOutPoint> in order to delete only the corresponding attributes or child resources represented by the relative URI with respect to all member resources. The Originator may be an AE or a CSE. |
| Processing at Group Hosting CSE | For the DELETE procedure, the <group> Hosting CSE shall: Check if the Originator has WRITE permission in the <accessControlPolicy> resource referenced by the membersAccessControlPoliciIDs in the <group> resource. In the case membersAccessControlPolicyIDs is not provided the access control policy defined for the group resource shall be used. Upon successful validation, obtain the URIs of all member resources from the attribute membersList of the addressed <group> resource. Generate fan out requests addressing the obtained URIs (appended with the relative URI if any) to the member hosting CSEs as indicated in figure 10.2.2.6-1. fr parameter in the request is set to ID of the Originator from the request from the original Originator. In the case that the members resources contain a sub-group resource, generate a unique group request identifier, include the group request identifier in all the requests to be fanned out and locally store the group request identifier. If the <group> Hosting CSE determines that multiple members resources belong to one CSE according to the URIs of the members resources, it may converge the requests accordingly before sending out. This may be accomplished by the group Hosting CSE creating a <group> resource on the member Hosting CSE to collect all the members on that member Hosting CSE. After receiving the responses from the members hosting CSEs, respond to the Originator with the aggregated results and the associated memberIDs. If the request addresses the virtual child resource <fanOutPoint> to delete all members resources of a specific group and receives the successful response from all the Member Hosting CSE, the Group Hosting CSE locally delete the <group> resource. |
| Processing at Member Hosting CSE | For the DELETE procedure, the Members Hosting CSE shall: Perform the corresponding DELETE procedure for the resource type in the request (clause 10.2 resource specific procedures). Check if the request has a group request identifier. Check if the group request identifier is contained in the requested identifier stored locally. If match is found, ignore the current request and respond an error. If no match is found, locally store the group request identifier. Check if the original Originator has the DELETE permission on the addressed resource. Upon successful validation, perform the delete procedures for the corresponding type of addressed resource as described in other sub-clauses of clause 10.2. Send the corresponding response to the Group Hosting CSE. |
| Information in Response message | Converged responses from members hosting CSEs |
| Processing at Originator after receiving Response | None |
| Exceptions | Same request with identical group request identifier received Originator does not have the access control privileges to access the <fanOutPoint> resource |

### -----------------------End of changes ---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?