| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | Scenarios for OneM2M and AllJoyn Interworking |
| Source:* | Haier |
| Contact: | Yali Guo, guoyali@haierubic.com |
| Date:* | 2014-11-03 |
| Abstract:* | This contribution proposes to include several scenarios for the study of OneM2M and AllJoyn interworking. |
| Agenda Item:* | ARC |
| Work item(s): | WI0018- OneM2M and AllJoyn Interworking |
| Document(s) Impacted* | TR 0014 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

============================Start of 1st Change==============================

# X	Scenarios for OneM2M and AllJoyn Interworking

Several scenarios are presented in this section. The OneM2M system may support several of these scenarios simultaneously.

Figure 4-1 shows the scenario that the AllJoyn network is deployed in the field domain, the AllJoyn network communicates with an OneM2M Infrastructure Domain network. An AllJoyn APP accesses the OneM2M Infrastructure Domain network and remotely controls the devices in the AllJoyn network through the OneM2M Infrastructure domain. The vertical line represents the demarcation between the field domain and the infrastructure domain.

Figure 4-1: AllJoyn APP controls AllJoyn Network in the filed domain through OneM2M Infrastructure Domain

In Figure 4-2 the AllJoyn network is also deployed in the field domain, the difference with the above scenario in Figure 4-1 is that An OneM2M APP remotely controls the devices in the AllJoyn network through the OneM2M Infrastructure domain. Considering the OneM2M system may support interworking with multiple IOT technologies, i.e. there are many local networks in field domain using different IOT technologies, these local networks all have ability to interworking with an OneM2M platform for remote control. It’s possible to use multiple APPs each specially for one IOT technology to remotely control the local networks,  but if we can use a generic OneM2M APP to remotely control the devices using different IOT technologies, it will be more efficient.

Figure 4-2: OneM2M APP controls AllJoyn Network in the field domain through OneM2M Infrastructure Domain

Figure 4-3 provides the scenario that two AllJoyn Network in the field domain communicates with each other through OneM2M Infrastructure Domain. One device in an AllJoyn network may need to communicate with a device in another AllJoyn network, but if the two AllJoyn networks are deployed at different location, it is impossible for them to communicate directly. If the two AllJoyn Network are both able to communicate with the OneM2M Infrastructure Domain, it’s possible for them to communicate with each other through the OneM2M Infrastructure Domain.

Figure 4-3: Two AllJoyn Network in the field domain communicates with each other through OneM2M Infrastructure Domain

The scenario depicts in Figure 4-4 is similar with Figure 4-3, the difference is one field domain network is AllJoyn network, the other is the OneM2M Field Domain Network, they can communicate with each other through OneM2M Infrastructure Domain.

Figure 4-4: AllJoyn Network in the field domain communicates with OneM2M field domain Network through OneM2M Infrastructure Domain

Figure 4-5 provides the scenario that an AllJoyn Network in the field domain directly communicates with an OneM2M Field Domain Network. The assumption is the two networks are deployed in the same location, thus it’s possible for them to communication with each other locally without going through the OneM2M Infrastructure Domain.

Figure 4-5: AllJoyn Network in the field domain directly communicates with OneM2M field domain Network

============================End of 1st Change==============================