| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | TS-0007-downloadFirmware&installFirmware_update |
| Source:* | Weixiang Shao, ZTE Corporation, shao.weixiang@zte.com.cn |
| Contact: | Weixiang Shao, ZTE Corporation, shao.weixiang@zte.com.cn |
| Date:* | 2014-11 |
| Abstract:* | Update downloadFirmware&installFirmware |
| Agenda Item:* | TP#14 |
| Work item(s): | TS-0007 WI |
| Document(s) Impacted* | TS-0007 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Update TS for inclusion |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

#### 6.6.2.1	downloadFirmware

This service capability provides the ability for AEs to download device firmware.

##### 6.6.2.1.1	Pre-conditions

The pre-conditions for Mca Received Requests are met.

A correlation between a Management Adapter, the service capability and device exist.

##### 6.6.2.1.2	Signature - downloadFirmware

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| firmwareInfo | IN | NO | The device firmware information. Type FirmwareInfo, see 6.6.1.1.1.5 |
| deviceId | IN | YES | The unique device identifier in the context of the M2M Service Subscription. |
| reportPolicy | IN | YES | The policy used to report the state of the operation to the originating AE. See clause 6.6.1.1.1.1. |
| requestId | OUT | NO | The M2M Request Identifier (M2M-Request-ID) |
| firmwareReport | OUT | YES | The firmware management operation execution result or status. Type FirmwareReport, see 6.6.1.1.1.3. |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Issuer does not have a Management Adapter for the requested operation Report policy does not supported by the Management Adapter Firmware download failure,e.g. firmware miss dependency, firmware is too large for available program or data memory |

Table 6.6.2.1.2-1 Device Management Service –downloadFirmware capability

##### 6.6.2.1.3	Service Interactions

The interactions of service capabilities required for this service capability:

Issue the request to the Supporting Service to perform the operation

Figure 6.6.2.1.3-1 downloadFirmware Diagram

##### 6.6.2.1.4	Post-Conditions

The Management Adapter has submitted a request to the Management Server to download firmware.

##### 6.6.2.1.5	Exceptions

Not Applicable

##### 6.6.2.1.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.6.2.1.7	oneM2M Resource Interworking

This service capability is used to download firmware. The service capability aligns with the <firmware> resource and maps to the UPDATE procedure for the attribute update of the resource. The service capability also aligns with the <mgmtCmd> resource and maps to the EXECUTE procedure for the resource.

#### 6.6.2.2	installFirmware

This service capability provides the ability for AEs to install firmware on the device.

##### 6.6.2.2.1	Pre-conditions

The pre-conditions for Mca Received Requests are met.

A correlation between a Management Adapter, the service capability and device exist.

# The firmware to be installed exists on the device.

##### 6.6.2.2.2	Signature –installFirmware

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| firmwareInfo | IN | NO | The device firmware information. Type FirmwareInfo, see 6.6.1.1.1.5 |
| deviceId | IN | YES | The unique device identifier in the context of the M2M Service Subscription. |
| reportPolicy | IN | YES | The policy used to report the state of the operation to the originating AE. |
| requestId | OUT | NO | The M2M Request Identifier (M2M-Request-ID) |
| firmwareReport | OUT | YES | The firmware management operation execution result or status. Type FirmwareReport, see 6.6.1.1.1.3. |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Issuer does not have a Management Adapter for the requested operation Report policy does not supported by the Management Adapter Firmware install failure, e.g. firmware is missing dependency on the device, firmware is too large for available program or data memory |

Table 6.6.2.2.2-1 Device Management Service –installFirmware capability

##### 6.6.2.2.3	Service Interactions

The interactions of service capabilities required for this service capability:

Issue the request to the Supporting Service to perform the operation

Figure 6.6.2.2.3-1 installFirmware Diagram

##### 6.6.2.2.4	Post-Conditions

The Management Adapter has submitted a request to the Management Server to install firmware.

##### 6.6.2.2.5	Exceptions

Not Applicable

##### 6.6.2.2.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.6.2.2.7	oneM2M Resource Interworking

This service capability is used to install firmware. The service capability aligns with the <firmware> resource and maps to the UPDATE procedure for the attribute update of the resource. The service capability also aligns with the <mgmtCmd> resource and maps to the EXECUTE procedure for the resource.

#### 6.7.2.1	downloadFirmware

This service capability provides the ability to download the specific device firmware.

##### 6.7.2.1.1	Pre-conditions

A correlation between a Management Server, the service capability and device exist.

##### 6.7.2.1.2	Signature – downloadFirmware

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| firmwareInfo | IN | NO | The device firmware information. Type FirmwareInfo, see 6.6.1.1.1.5 |
| deviceId | IN | YES | The unique device identifier in the context of the M2M Service Subscription. |
| reportPolicy | IN | YES | The policy used to report the state of the operation to the originating AE. See clause 6.6.1.1.1.1. |
| requestId | IN | NO | The M2M Request Identifier (M2M-Request-ID) |
| firmwareReport | OUT | YES | The firmware management operation execution result or status. Type FirmwareReport, see 6.6.1.1.1.3. |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Report policy is not supported by the Management Adapter Firmware download failure, e.g. firmware is missing dependency on the device, firmware is too large for available program or data memory |

Table 6.7.2.1.2-1 Management Adapter –downloadFirmware capability

##### 6.7.2.1.3	Post-Conditions

The Management Adapter has submitted a request to the Management Server to download the firmware.

##### 6.7.2.1.4	Exceptions

Not Applicable

##### 6.7.2.1.5	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.7.2.1.6	oneM2M Resource Interworking

This service capability is used to download firmware. The service capability aligns with the <firmware> resource and maps to the UPDATE procedure for the attribute update of the resource. The service capability also aligns with the <mgmtCmd> resource and maps to the EXECUTE procedure for the resource.

#### 6.7.2.2	installFirmware

This service capability provides the ability to install firmware on a device.

##### 6.7.2.2.1	Pre-conditions

A correlation between a Management Server, the M2M Service Capability and device exist.

##### 6.7.2.2.2	Signature –installFirmware

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| firmwareInfo | IN | NO | The device firmware information. Type FirmwareInfo, see 6.6.1.1.1.5 |
| deviceId | IN | YES | The unique device identifier in the context of the M2M Service Subscription. |
| reportPolicy | IN | YES | The policy used to report the state of the operation to the originating AE. |
| requestId | IN | NO | The M2M Request Identifier (M2M-Request-ID) |
| firmwareReport | OUT | YES | The firmware management operation execution result or status. Type FirmwareReport, see 6.6.1.1.1.3. |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Report policy does not supported by the Management Adapter Firmware install failure, e.g. firmware is missing dependency on the device, firmware is too large for available program or data memory |

Table 6.7.2.2.2-1 Management Adapter –installFirmware capability

##### 6.7.2.2.3	Post-Conditions

The Management Adapter has submitted a request to the Management Server to install firmware.

##### 6.7.2.2.4	Exceptions

Not Applicable

##### 6.7.2.2.5	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.7.2.2.6	oneM2M Resource Interworking

This service capability is used to install firmware. The service capability aligns with the <firmware> resource and maps to the UPDATE procedure for the attribute update of the resource. The service capability also aligns with the <mgmtCmd> resource and maps to the EXECUTE procedure for the resource.