| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 |
| Title:* | TS-0007-Section 6_getManagementAdapter_update |
| Source:* | Weixiang Shao, ZTE Corporation, shao.weixiang@zte.com.cn |
| Contact: | Weixiang Shao, ZTE Corporation, shao.weixiang@zte.com.cn |
| Date:* | 2014-11 |
| Abstract:* | Update section 6 about getManagementAdapter |
| Agenda Item:* | TP#14 |
| Work item(s): | TS-0007 WI |
| Document(s) Impacted* | TS-0007 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Update TS for inclusion |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

#### 6.2.1.4	getManagementAdapter

This service capability obtains the Management Adapter instance that will be used to manage device based on the requested M2M Service Capability (e.g., downloadFirmware, installFirmware) and device.

##### 6.2.1.4.1	Pre-conditions

A correlation between a Management Adapter, the M2M Service Capability and device exist.

##### 6.2.1.4.2	Signature - getManagementAdapter

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| serviceId | IN | NO | The M2M Service Identifier (M2M-Serv-ID) of the M2M Service Capability |
| deviceId | IN | YES | The unique device identifier in the context of the M2M Service Subscription. |
| managementAdapter | OUT | NO | The returned instance of the Management Adapter service associated with the subscription. |
| responseType | OUT | NO | Response types: Management Adapter does not exist |

Table 6.2.4.1.2-1 Service Subscription - getManagementAdapter capability

Editor’s Note: The pre-conditions mention that the Management Adapter is associated with the M2M Service Capability but the argument is for the M2M Service. Need to determine if the Adapter is is associated with the M2M Service or M2M Service Capability (operation).

##### 6.2.1.4.3	Post-Conditions

Not Applicable

##### 6.2.1.4.4	Exceptions

Not Applicable

##### 6.2.1.4.5	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.2.1.4.6	oneM2M Resource Interworking

This service capability interworks with the following oneM2M Resource operations that are interworked are:

Not Applicable