| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Alcatel-Lucent |
| Format:* | ARC |
| Date:* | 2014-11-03 |
| Contact:* | Omar Elloumi |
| Reason for Change/s:* | AE-ID uniqueness, impact of service profile |
| CR against: Release* | oneM2M-TS-0001-V-1.2.0 |
| CR against: TS/TR* | 1 |
| Clauses/Sub Clauses* | 9.6 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or (missing) functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

### Introduction (from ARC 2014 1621 - Qualcomm)

- <m2mServiceSubcriptionProfile>

  - <serviceSubscribedNode> [0..n]

  - serviceRoles [0..1] (L)

  - NEW <serviceSubscribedAppRule> [0..n]
// Multiplicity = 0 => no applications are allowed at all
// Multiplicity > 0 => applications defined in each rule are

- NEW <serviceSubscribedAppRule> child resource:

  - applicableCredID [1] (L)
// List of credential IDs for which this rule is applicable, i.e. for registration requests coming into a CSE via an SAE end point that was authenticated using credentials that match with any of these credential-IDs, the current rule applies. This can contain ‘*’ for any credential ID or ‘None’ for not authenticated case. Also Wildcards within an element of this list are possible (e.g. ‘C123*X’ for any Credential ID that starts with ‘C123’ and ends with ‘X’) to define sets or ranges of Credential-IDs.

  - applicableCSE[1] (L) 
// List of CSE-ID(s) for which this rule is applicable, i.e. CSE-IDs of Registrar CSEs for which this rule shall be applicable in registration attempts. This can contain ‘*’ for any CSE. Also Wildcards within an element of this list are possible (e.g. ‘C123*X’ for any CSE-ID that starts with ‘C123’ and ends with ‘X’) to define sets or ranges of CSE-IDs.

  - allowedAppID [1] (L)
// List of App-ID that shall be considered to be allowed for AE registration requests received via any of the combinations of CSE-ID and SEA end points associated with credentialID defined in the previous two attributes. This can contain ‘*’ for any App-ID. Also Wildcards within an element of this list are possible (e.g. ‘C123*X’ for any App-ID that starts with ‘C123’ and ends with ‘X’) to define sets or ranges of App-IDs.

  - allowedAE [1] (L) 
// List of allowed AE-ID-Stems to be used for the registering AEs. This can contain zero or more specific AE-ID-Stem values and ‘S*’ for any Sxx-type AE-ID-Stem, ‘C*’ for any Cxx-type AE-ID-Stem, or ‘*’ for any AE-ID-Stem. Also Wildcards within an element of this list are possible (e.g. ‘C123*X’ for any CSE-ID that starts with ‘C123’ and ends with ‘X’) to define sets or ranges of AE-ID-Stems.

Examples of content in <serviceSubscribedAppRule> and what it would mean:

1)

Let’s assume some credential (no matter whether Cert or PSK) with the credential ID of ‘XXX123Y’ is associated with a specific AE that is an instance of an Application with App-ID ‘N11123’ and we always want to get this AE the same Sxx-type of AE-ID-Stem of ‘S9987’ but we only want to allow it to register from CSE ‘/123CSE’ or CSEs with an ID starting with ‘/2’ and ending with ‘CSE’. In that case a <serviceSubscribedAppRule> would contain the following

applicableCredID = [‘XXX123Y’], 
applicableCSE = [‘/123CSE’, ‘/2*CSE’],
allowedAppID = [‘N11123’],
allowedAE = [‘S9987’]

2)

Let’s assume some credential (no matter whether Cert or PSK) with the credential ID of ‘XXX555Y’ is associated with an Application with App-ID ‘N11199’. No matter which particular instance of this application is trying to register, we always want to get this AE an Sxx-type of AE-ID-Stem but we only want to allow it to register from CSEs with an ID starting with ‘/K2’ and ending with ‘CSE’. In that case a <serviceSubscribedAppRule> would contain the following

applicableCredID = [‘XXX555Y’], 
applicableCSE = [‘/K2*CSE’],
allowedAppID = [‘N11123’],
allowedAE = [‘S*’]

3)

Let’s assume some credential (no matter whether Cert or PSK) with the credential ID of ‘ZZ555Y’ is associated with a specific Node. On that Node we want to allow only two types of applications: One with App-ID ‘N11119’ and one with App-ID ‘N77779’. No matter which particular instance of this application is trying to register, we always want to get the ones with App-ID ‘N11119’ an Sxx-type of AE-ID-Stem and the one with App-ID ‘N77779’ a Cxx-type AE-ID-Stem. However we only want to allow those AEs to register from CSEs with an ID starting with ‘/Z4’ and ending with ‘CSE’. In that case we would need two <serviceSubscribedAppRule> child resources which would contain the following

applicableCredID = [‘ZZ555Y’], 
applicableCSE = [‘/Z4*CSE’],
allowedAppID = [‘N11119’],
allowedAE = [‘S*’]

applicableCredID = [‘ZZ555Y’], 
applicableCSE = [‘/Z4*CSE’],
allowedAppID = [‘N77779’],
allowedAE = [‘C*’]

4)

Let’s assume we want to allow certain applications (defined by App-ID) to register from certain CSE ‘/Z4765CSE’ with no further authentication at all (not authenticate case, sufficient that it comes from that CSE). One of the applications should only be allowed to be instantiated once and use a specific Sxx-type of AE-ID-Stem, another one should be allowed to be instantiated twice with specific Sxx-type AE-ID-Stem and a third one should be allowed to be instantiated arbitrarily often with an Cxx-type of AE-ID stem. In that case we would need two <serviceSubscribedAppRule> child resources which would contain the following

applicableCredID = [‘None’], 
applicableCSE = [‘/Z4765CSE’],
allowedAppID = [‘N11111’],
allowedAE = [‘S999987’]

applicableCredID = [‘None’], 
applicableCSE = [‘/Z4765CSE’],
allowedAppID = [‘N11112’],
allowedAE = [‘S999986’, ‘S999986’]

applicableCredID = [‘None’], 
applicableCSE = [‘/Z4765CSE’],
allowedAppID = [‘N11113’],
allowedAE = [‘C*’]

### -----------------------Start of change 1-------------------------------------------

### 9.6.19	Resource Type m2mServiceSubscriptionProfile

The <m2mServiceSubscriptionProfile> resource represents an M2M Service Subscription. It is used to represent all data pertaining to the M2M Service Subscription, i.e. the technical part of the contract between an M2M Application Service Provider and an M2M Service Provider.

Figure 9.6.19-1: Structure of <m2mServiceSubscriptionProfile> resource

The <m2mServiceSubscriptionProfile> resource shall contain the child resources specified in table 9.6.19-1.

Table 9.6.19-1: Child resources of <m2mServiceSubscriptionProfile> resource

| Child Resources of <m2mServiceSubscriptionProfile> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |
| [variable] | <serviceSubscribedNode> | 0..n | See clause 9.6.20 |

The <m2mServiceSubscriptionProfile> resource shall contain the attributes specified in table 9.6.19-2.

# Table 9.6.19-2: Attributes of <m2mServiceSubscriptionProfile> resource

| Attributes of <m2mServiceSubscriptionProfile> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. If no accessControlPolicyIDs is given at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute |
| creationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| serviceRoles | 0..1 (L) | RW | This attribute contains a list of Service Role IDs (S-RoleIDs) that are subscribed to in this service subscription. If the multiplicity of this attribute is 0, the role does not apply. |

### 9.6.20	Resource Type serviceSubscribedNode

The <serviceSubscribedNode> resource represents M2M Node information that is needed as part of the M2M Service Subscription resource. It shall contain information about the M2M Node as well as application identifiers of the Applications running on that Node.

Figure 9.6.20-1: Structure of <serviceSubscribedNode> resource

The <serviceSubscribedNode> resource shall contain the child resource specified in table 9.6.20-1.

Table 9.6.20-1: Child resources of <serviceSubscribedNode> resource

| Child Resources of <serviceSubscribedNode> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |

The <serviceSubscribedNode> resource shall contain the attributes specified in table 9.6.20-2.

Table 9.6.20-2: Attributes of <serviceSubscribedNode> resource

| Attributes of <serviceSubscribedNode> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. If no accessControlPolicyIDs is given at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute. |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| labels | 0..1 | RW | See clause 9.6.1.3 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| nodeID | 1 | WO | M2M-Node-ID of the node that is represented by this instance. |
| CSE-ID | 0..1 | WO | CSE-ID pertaining to this node (for nodes that have a CSE). |
| deviceIdentifier | 0..1 | WO | A list of device identifiers. A deviceIdentifier identifies a device using a Universally Unique IDentifier (UUID). The UUID specifies a valid, hex digit character string as defined in [RFC4122]. The format of the URN is urn:uuid:########-####-####-############ OPS URN: Identify a device using the format <OUI> "-" <ProductClass> "-" <SerialNumber> as defined in Section 3.4.4 of TR-069 [i-4]. The format of the URN is urn:dev:ops:<OUI> "-" <ProductClass> "-" <SerialNumber>. OS URN: Identify a device using the format <OUI> "-"<SerialNumber> as defined in Section 3.4.4 of TR-069 [i.4]. The format of the URN is urn:dev:os:<OUI> "-"<SerialNumber>. IMEI URN: Identify a device using an International Mobile Equipment Identifiers of 3GPP-TS_23.003 [i.26]. The IMEI URN specifies a valid, 15 digit IMEI. The format of the URN is urn:imei:############### ESN URN: Identify a device using an Electronic Serial Number. The ESN specifies a valid, 8 digit ESN. The format of the URN is urn:esn:######## MEID URN: Identify a device using a Mobile Equipment Identifier. The MEID URN specifies a valid, 14 digit MEID. The format of the URN is urn:meid:############## |
| ruleLinks | 0..1 (L) | RW | This attribute contains a list of links towards <serviceSubscribedAppRule> resources pertaining to this <serviceSubscribedNode>. See 9.6.xx for an explanation of the <serviceSubscribedAppRule> resource. This attribute shall exist only when the CSE-ID attribute is present. When the list is empty, it means no applications are allowed to register on the CSE which is indicated by the CSE-ID attribute. |

### 9.6.xx	Resource Type serviceSubscribedAppRule

The <serviceSubscribedAppRule> resource represents a rule that defines allowed App-ID and AE-ID combinations that are acceptable for registering an AE on a Registrar CSE. The rule in a <serviceSubscribedAppRule> resource shall apply for CSEs for which the associated <serviceSubscribeNode> resource is linked with the <serviceSubscribedAppRule> via the ruleLinks attribute of the <serviceSubscribedNode> resource. The rule contained in a <serviceSubscribedAppRule> resource  defines a mapping between

a)      one or more Credential-ID(s)

and

b)      combinations of one or more App-ID(s) and one or more AE-ID(s) which are allowed to be used for registering AE(s) that issued a registration request via a Security Association established with the credentials associated with the Credential-ID(s) listed in a)

When applications shall be allowed in situations where no Security Association has been established prior to issuing the registration request, the Credential-ID ‘None’ shall be used in the rule.

The parent resource of a <serviceSubscribedAppRule> resource is the <CSEBase> resource of the IN-CSE hosting the <serviceSubscribedNode> resource(s) that point to the <serviceSubscribedAppRule> resource.

Figure 9.6.xx-1: Structure of <serviceSubscribedAppRule> resource

The <serviceSubscribedAppRule> resource shall contain the child resource specified in table 9.6.xx-1.

Table 9.6.xx-1: Child resources of <serviceSubscribedAppRule> resource

| Child Resources of <serviceSubscribedAppRule> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |

The <serviceSubscribedAppRule> resource shall contain the attributes specified in table 9.6.xx-2.

Table 9.6.xx-2: Attributes of <serviceSubscribedAppRule> resource

| Attributes of <serviceSubscribedAppRule> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. If no accessControlPolicyIDs is given at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute. |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| labels | 0..1 | RW | See clause 9.6.1.3 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| applicableCredIDs | 0..1 (L) | RW | List of credential IDs for which this rule is applicable, i.e. for registration requests coming into a CSE via a Security Associtation Endpoint (SEA) [i.3], that was authenticated using credentials that match with any of these credential-IDs, the current rule applies. This can contain a ‘*’ for any credential ID or ‘None’ for not authenticated case. Also Wildcards within an element of this list are possible (e.g. ‘C123*X’ for any Credential ID that starts with ‘C123’ and ends with ‘X’) to define sets or ranges of Credential-IDs. |
| allowedApp-IDs | 0..1 (L) | RW | List of App-IDs that shall be considered to be allowed for AE registration requests received via Security Associtation Endpoint (SEA) [i.3] associated with credentialID stored in the attribute applicableCredID. This can contain ‘*’ for any App-ID. Also Wildcards within an element of this list are possible (e.g. ‘C123*X’ for any App-ID that starts with ‘C123’ and ends with ‘X’) to define sets or ranges of App-IDs. |
| allowedAEs | 0..1 (L) | RW | List of allowed AE-ID-Stems to be used for the registering AEs. This can contain zero or more specific AE-ID-Stem values, ‘S*’ for any SP-Assigned AE-ID-Stem, ‘C*’ for any CSE-assigned AE-ID-Stem, or ‘*’ for any AE-ID-Stem. Also Wildcards within an element of this list are possible (e.g. ‘C123*X’ for any AE-ID that starts with ‘C123’ and ends with ‘X’) to define sets or ranges of AE-ID-Stems. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Begin change 2---------------------------------------------

### 9.6.2	Resource Type accessControlPolicy

The Access Control Policies (ACPs) shall be used by the CSE to control access to the resources as specified in this document and in TS-0003 [i-3].

The ACP is designed to fit different access control models such as access control lists, role or attribute based access control.

The <accessControlPolicy> resource is comprised  privileges and selfPrivileges attributes which represent a set of access control rules  defining which entities (defined as accessControlOriginators) have the privilege to perform  certain operations (defined as accessContolOperations) within specified contexts (defined as accessControlContexts) and are used by the CSEs in making Access Decision to specific resources.

In a privilege, each access control rule defines which AE/CSE is allowed for which operation. So for sets of access control rules an operation is permitted if it is permitted by one or more access control rules in the set. Access control rule shall not conflict with other rules in the same privilege.

For a resource that is not of <accessControlPolicy> resource type, the common attribute accessControlPolicyIDs for such resources (defined in table 9.6.1.3.2-1) contains a list of identifiers which link that resource to <accessControlPolicy> resources. The CSE Access Decision for such a resource shall follow the evaluation of the set of access control rules expressed by the privileges attributes defined in the <accessControlPolicy> resources.

The selfPrivileges attribute shall represent the set of access control rules for the <accessControlPolicy> resource itself.

The CSE Access Decision for <accessControlPolicy> resource shall follow the evaluation of the set of access control rules expressed by the selfPrivileges attributes defined in the <accessControlPolicy> resource itself.

Figure 9.6.2-1: Structure of <accessControlPolicy> resource

The <accessControlPolicy> resource shall contain the child resource specified in table 9.6.2-1.

# Table 9.6.2-1: Child resources of <accessControlPolicy> resource

| Child Resources of <accessControlPolicy> | Child Resource Type | Multiplicity | Description | <accessControlPolicyAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |

The <accessControlPolicy> resource shall contain the attributes specified in table 9.6.2-2.

# Table 9.6.2-2: Attributes of <accessControlPolicy> resource

| Attributes of <accessControlPolicy> | Multiplicity | RW/ RO/ WO | Description | <accessControlPolicyAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| resourceID | 1 | WO | See clause 9.6.1.3 where this common attribute is described. | MA |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| labels | 0..1 | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| announceTo | 0..1 | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| announcedAttribute | 0..1 | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| privileges | 1 | RW | A set of access control rules that applies to resources referencing this <accessControlPolicy> resource using the accessControlPolicyID attribute. | MA |
| selfPrivileges | 1 | RW | A set of access control rules that apply to the <accessControlPolicy> resource itself. | MA |

The set of access control rules represented in privileges and selfPrivileges attributes are comprised of 3-tuples  (accessControlOriginators, accessControlContexts, accessControlOperations) with parameters shown in table 9.6.2-3 which are further described in the following clauses.

If privileges attribute contains no 3-tuples then this represent an empty set of the access control rules.

The selPrivileges attribute shall contain at least one 3-tuples.

The CSE access granting mechanism shall follow the procedure described in TS-0003 [i-3] in clause 7.1 (Access Control Mechanism).

Table 9.6.2-3: Parameters in access-control-rule-tuples

| Name | Description |
| --- | --- |
| accessControlOriginators | See 9.6.2.1 |
| accessControlContexts | See 9.6.2.2 |
| accessControlOperations | See 9.6.2.3 |

#### 9.6.2.1	accessControlOriginators

The accessControlOriginators is a mandatory parameter in an access-control-rule-tuple. It represents the set of Originators that shall be allowed to use this access control rule. The set of Originators is described as a list of parameters, where the types of the parameter can vary within the list. Table 9.6.2.1-1 describes the supported types of parameters in accessControlOriginators. The following Originator privilege types shall be considered for access control policy check by the CSE.

Table 9.6.2.1-1: Types of Parameters in accessControlOriginators

| Name | Description |
| --- | --- |
| domain | A SP domain or SP sub-domain |
| originatorID | CSE-ID or AE-ID which represent a Originator identity |
| all | Any Originators are allowed to access the resource within the accessControlOriginators constraints |

### When the originatorID is an AE-ID and the AE-ID-Stem starts with ‘S’ (see Table 7.2-1) and if the SP-relative format of the AE-ID is used for the originatorID, the access control policy applies irrespective the Registrar CSE of the Originator.

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?