| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 PRO |
| Source:* | InterDigital |
| Format:* | DRAFT |
| Date:* | 2014-11-10 |
| Contact:* | Guang Lu, guang.lu@interdigital.com Santhosh Kumar Jagadish, InterDigital, SanthoshKumar.Jagadish @InterDigital.com |
| Reason for Change/s:* | Updating the Subscription UPDATE procedure for sending notification verification request when notificationURI is updated with non-originator URIs. |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0001 v1.2.0 |
| Clauses/Sub Clauses* | Table 10.2.11.4-1 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

1	Rationale

If the “notificationURI” attribute of subscription resource is updated with non-originator URIs, notification verification request has to be sent to the updated non-originator URIs. Subscription UPDATE procedure has been updated with the same.

2	Proposed Changes

### -----------------------Start of change 1 -------------------------------------------

#### 10.2.11.4	Update <subscription>

This procedure shall be used to update an existing subscription, e.g. extension of its lifetime or the modification of the list of notificationURI(s). The generic update procedure is described in clause 10.1.3.

# Table 10.2.11.4-1: <subscription> UPDATE

| <subscription> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc, Mcc’ |
| Information in Request message | All parameters defined in table 8.1.2.1-1 apply with the specific details for: cn: attributes of the <subscription> resource as defined in 9.6.8 which need be updated, |
| Processing at Originator before sending Request | According to clause 10.1.3 |
| Processing at Receiver | According to clause 10.1.3 If a notificationURI is not the Originator, the hosting CSE shall send a Notify request to the notificationURI to verify this <subscription> update request. If it cannot initiate the verification, the hosting CSE shall return an unsuccessful response. If the hosting CSE initiate the verification, it shall check if the verification result in the Notify response is successful or not. If any notificationURI contained in a list fails verification then the <subscription> update process fails. If the latestNotify attribute is set, the hosting CSE shall assign attribute ec of value ‘latest’ of the notifications generated pertaining to the subscription created. |
| Information in Response message | According to clause 10.1.3 |
| Processing at Originator after receiving Response | According to clause 10.1.3 |
| Exceptions | According to clause 10.1.3 |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?