| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 ARC |
| Source:* | Nicolas Damour, Sierra Wireless (ndamour@sierrawireless.com) |
| Format:* | Face-to-Face Meeting |
| Date:* | 2014-11-14 |
| Contact:* | Nicolas Damour, Sierra Wireless (ndamour@sierrawireless.com) |
| Reason for Change/s:* | No need for a separate encoding attribute for contentInstance resources |
| CR against: Release* | v.1.2.0 |
| CR against: TS/TR* | TS-0001 |
| Clauses/Sub Clauses* | 9.6.7 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The contribution ARC-2014-1669R01 agreed at ARC#14.0 introduces a new attribute called “encoding” to specify the encoding of the content of a <contentInstance> resource, in addition to the “typeOfContent” attribute that contains an Internet Media Type (formerly known as MIME Type) to indicate the type of content present in the contentInstance. This “typeOfContent” attribute more precisely contains an Application Media Type (i.e. starting with “application/…”). For example, it could be “application/json”. It is correct that a CSE needs information about the actual encoding of the information, beyong the simple Application Media Type.

The IETF RFC 6838 on Internet Media Type Specifications and Registration Procedures states the following in its section 4.3:

### 4.3.  Parameter Requirements

Media types MAY elect to use one or more media type parameters, or

some parameters may be automatically made available to the media type

by virtue of being a subtype of a content type that defines a set of

parameters applicable to any of its subtypes.  In either case, the

names, values, and meanings of any parameters MUST be fully specified

when a media type is registered in the standards tree, and SHOULD be

specified as completely as possible when media types are registered

in the vendor or personal trees.

This means that while it would appear possible to include the encoding type information directly into the content-type as a parameter (using something like “application/json; encoding: utf-8”), it is in fact not possible because these parameters MUST be specified by the Internet Media Types already (in the same example, “application/json” does not specify an “encoding” parameter).

However, in oneM2M we can still combine the contentType information and an encoding information into a single resource attribute for the sake of efficiency. These parameters are expressed after a semi-column separator, after the registered name of the Application Media Type.

As a result, it is argued that there is no need for a supplementary attribute in the resource type “contentInstance”. Instead, it is possible to foresee these kinds of values in the “typeOfContent” attribute.

For example, we would have: “application/json; encoding: plain” or “application/xml; encoding: base64”

### -----------------------Start of change 1-------------------------------------------

### 9.6.7	Resource Type contentInstance

The <contentInstance> resource represents a data instance in the <container> resource. The content of the contentInstance can be encrypted.

Unlike other resources, the <contentInstance> resource shall not be modified once created. An AE shall be able to delete a contentInstance resource explicitly or it may be deleted by the platform based on policies. If the platform has policies for contentInstance retention, these shall be represented by the attributes maxByteSize, maxNrOfInstances and/or maxInstanceAge attributes in the <container> resource. If multiple policies are in effect, the strictest policy shall apply.

The <contentInstance> resource inherits the same access control policies of the parent <container> resource, and does not have its own accessControlPolicyIDs attribute.

Figure 9.6.7-1: Structure of <contentInstance> resource

The <contentInstance> resource shall contain the attributes specified in table 9.6.7-1.

# Table 9.6.7-1: Attributes of <contentInstance> resource

| Attributes of <contentInstance> | Multiplicity | RW/ RO/ WO | Description | <contentInstanceAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| resourceID | 1 | WO | See clause 9.6.1.3 where this common attribute is described. | MA |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| labels | 0..1 | WO | See clause 9.6.1.3 where this common attribute is described. | MA |
| creator | 0..1 | WO | See clause 9.6.1.3 where this common attribute is described. | NA |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| stateTag | 1 | RO | See clause 9.6.1.3 where this common attribute is described. The stateTag attribute of the parent resource should be incremented first and copied into this stateTag attribute when a new instance is added to the parent resource. | OA |
| announceTo | 0..1 | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| announcedAttribute | 0..1 | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| contentInfo | 0..1 | WO | Information on the content that is needed to understand the content. This attribute is a composite attribute. It is composed first of an Internet Media Type (as defined in the IETF RFC 6838) describing the type of the data, and second of an encoding information that specifies how to first decode the received content. Both elements of information are separated by a separator defined in [i.2]. | OA |
| contentSize | 1 | RO | Size in bytes of the content attribute. | OA |
| content | 1 | WO | Actual content of a contentInstance. This content may be opaque data or understandable with the help of the contentInfo. This may for example be an image taken by a security camera, or a temperature measurement taken by a temperature sensor. | OA |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?