| CHANGE REQUEST |
| --- |
| Group Name:* | ARC14.0 |
| Source:* | Qualcomm Inc. |
| Format:* | Full WG Meeting |
| Date:* | 2014-11-13 |
| Contact:* | Josef Blanz (jblanz@qti.qualcomm.com) |
| Reason for Change/s:* | Correct an attribute of [activeCmdhPolicy] that needs to be modifyable selectively by management AE or DM procedures |
| CR against: | TS-0001 v1.2.0 |
| Clauses/Sub Clauses Affected* | D.12.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Adopt the proposed changes |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

The [activeCmdhPolicy] resource contains a mgmtLink attribute that is intended to point to the currently active [cmdhPolicy] resource. According to the current state of stage 3 work, mgmtLink(s)pointing to other <mgmtObj> resources are intended to be handled in the same way as regular parent/child relationships and – therefore – would not be directly changable by applications. Since the [active CmdhPolicy] resource is different in that it could simply point to a selected [cmdhPolicy] resource, it is necessary to change this attribute to a regular attribute containing the resource ID of an [cmdhPolicy] resource.

### -----------------------Start of change 1-------------------------------------------

### D.12.1	Resource activeCmdhPolicy

A managed node can have one or more sets of [cmdhPolicy] resources assigned as children.

The [activeCmdhPolicy] resource is used to provide a link to the currently active set of CMDH policies. This identifies which set of CMDH policies is currently actively in use in the corresponding CSE. It allows the device management technology to activate a policy set independently of the download of a new set of CMDH policies in order to avoid potential race conditions. The [activeCmdhPolicy] and [cmdhPolicy] resources are children of the same <node> resource to which these policies apply.

Figure D.12.1-1: Structure of [activeCmdhPolicy] resource

The [activeCmdhPolicy] resource shall contain attributes specified in table D.12.1-1.

Table D.12.1-1: Attributes of [activeCmdhPolicy] resource

| Attributes of [activeCmdhPolicy] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceID | 1 | WO | See clause 9.6.1.3 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| labels | 0..1 | RO | See clause 9.6.1.3 where this common attribute is described |
| mgmtDefinition | 1 | WO | See clause 9.6.15. Has fixed value “activeCmdhPolicy”. |
| objectIDs | 0..1 (L) | RW | See section 9.6.15. |
| objectPaths | 0..1 (L) | RW | See section 9.6.15. |
| description | 0..1 | RW | See section 9.6.15. |
| activeCmdhPolicyLink | 1 | RW | The resource ID of the [cmdhPolicy] resource instance containing the CMDH policies that are currently active for the associated CSE, i.e. for the CSE which is hosted by the node that is represented by the parent <node> resource. |

### -----------------------End of change 1---------------------------------------------