| CHANGE REQUEST |
| --- |
| Group Name:* | ARC |
| Source:* | LG Electronics |
| Format:* |  |
| Date:* | 2014-10-13 |
| Contact:* |  |
| Reason for Change/s:* | Bug-fix for resource announcement |
| CR against: Release* |  |
| CR against: TS/TR* | oneM2M-TS-0001 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This is the follow-up contribution of ARC-2014-1654 regarding the issue: who can be the parent of <xxAnnc> resource.

Imagine the situation that (AE1 ( CSE1), (CSE1 ( CSE2) and (CSE2 ( CSE3)  have registration relationships each other. (NOTE: CSE1 has no registrationship with CSE3)

Now AE1 requests CSE1 to announe the “cse1base/ae1” resource on CSE1 to CSE2 and CSE3.

Even with the agreement on ARC-2014-1654, CSE1 cannot create “ae1Annc”(<AEAnnc>) resource on CSE3. This is because by the specification <AEAnnc> resource only can be created under <remoteCSEAnnc> and <remoteCSE> resource.

In this case, CSE1 did not created <remoteCSE> on CSE3, so there’s no room to create “ae1Annc” on CSE3.

The only condition that CSE1 can create “ae1Annc” on CSE3 is that “remoteCSE1”(<remoteCSE>) resource on CSE2 is already announced to CSE3 (e.g., “cse3base/remoteCSE1Annc”. However this cannot be guaranteed.

This is the only example for <AEAnnc> resource, when it comes to the other announce resource types, this occurs again.

Then we need a new room to create <xxAnnc> resource without any registration involvement between CSEs. This ontribution proposes to make <CSEBase> resouce be the new room for all announce resource types.

## ----------------------- Start of change 1 -----------------------

### 9.6.3	Resource Type CSEBase

A <CSEBase> resource shall represent a CSE. The <CSEBase> resource shall be the root for all resources that are residing in the CSE.

Figure 9.6.3-1: Structure of <CSEBase> resource

The <CSEBase> resource shall contain the child resources specified in table 9.6.3-1.

Table 9.6.3-1: Child resources of <CSEBase> resource

| Child Resources of <CSEBase> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <remoteCSE> | 0..n | See clause 9.6.4 |
| [variable] | <node> | 0..n | See clause 9.6.18 |
| [variable] | <AE> | 0..n | See clause 9.6.5 |
| [variable] | <container> | 0..n | See clause 9.6.6 |
| [variable] | <group> | 0..n | See clause 9.6.13 |
| [variable] | <accessControlPolicy> | 0..n | See clause 9.6.2 |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |
| [variable] | <mgmtCmd> | 0..n | See clause 9.6.16 |
| [variable] | <locationPolicy> | 0..n | See clause 9.6.10 |
| [variable] | <statsConfig> | 0..n | See clause 9.6.23 |
| [variable] | <statsCollect> | 0..n | See clause 9.6.25 |
| [variable] | <request> | 0..n | See clause 9.6.12 |
| [variable] | <delivery> | 0..n | See clause 9.6.11 |
| [variable] | <schedule> | 0..1 | See clause 9.6.9 |
| [variable] | <accessControlPolicyAnnc> | 0..n | See clause 9.6.2 |
| [variable] | <AEAnnc> | 0..n | See clause 9.6.5 |
| [variable] | <containerAnnc> | 0..n | See clause 9.6.6 |
| [variable] | <contentInstanceAnnc> | 0..n | See clause 9.6.7 |
| [variable] | <groupAnnc> | 0..n | See clause 9.6.13 |
| [variable] | <locationPolicyAnnc> | 0..n | See clause 9.6.10 |
| [variable] | <mgmtObjAnnc> | 0..n | See clause 9.6.15 |
| [variable] | <nodeAnnc> | 0..n | See clause 9.6.18 |
| [variable] | <remoteCSEAnnc> | 0..n | See clause 9.6.4 |
| [variable] | <scheduleAnnc> | 0..n | See clause 9.6.9 |

The <CSEBase> resource shall contain the attributes specified in table 9.6.3-2.

Table 9.6.3-2: Attributes of <CSEBase> resource

| Attributes of <CSEBase> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RO | See clause 9.6.1.3 where this common attribute is described. |
| labels | 0..1 (L) | RO | See clause 9.6.1.3 where this common attribute is described. |
| cseType | 0..1 | RO | Indicates the type of CSE represented by the created resource. Mandatory for an IN-CSE, hence multiplicity (1). Its presence is subject to SP configuration in case of an ASN-CSE or a MN-CSE. |
| CSE-ID | 1 | RO | The CSE identifier in SP-relative CSE-ID format (clause 7.2). |
| supportedResourceType | 1 (L) | RO | List of the resource types which are supported in the CSE. This attribute contains subset of resource types listed in clause 9.2. This also includes the supported optional attributes for each supported resource type. |
| pointOfAccess | 1 (L) | RO | Represents the list of physical addresses to be used by remote CSEs to connect to this CSE (e.g. IP address, FQDN). This attribute is exposed to its Registree. |
| nodeLink | 0..1 | RO | The resourceID of a <node> resource that is hosted as a child of the present <CSEBase> instance resource and represents the node specific information for the node on which this <CSEBase> instance resides. |
| notificationCongestionPolicy | 0..1 | RO | This attribute applies to CSEs generating subscription notifications. It specifies the rule which is applied when the storage of notifications for each subscriber (an AE or CSE) reaches the maximum storage limit for notifications for that subscriber. E.g. Delete stored notifications of lower notificationStoragePriority to make space for new notifications of higher notificationStoragePriority, or delete stored notifications of older creationTime to make space for new notifications when all notifications are of the same notificationStoragePriority. |

NOTE: All the attributes of this resource type can be changed by an offline configuration mechanism, but not over the reference points (all attributes are “RO”).

## ----------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?