| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Format:* | ARC |
| Date:* | 2015-01-22 |
| Contact:* | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Reason for Change/s:* | <serviceSubscribedAppRule> Resource Type Procedure |
| CR against: Release* | Pre-release |
| CR against: TS/TR* | TS-0001 v1.4.2 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or (missing) functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution provides procedures for <serviceSubscribedAppRule> which is newly introduced at TP#14.

## -----------------------Start of change 1-------------------------------------------

### 10.2.23	<serviceSubscribedAppRule> Resource Procedures

#### 10.2.23.1	Create <serviceSubscribedAppRule>

This procedure shall be used for creating a <serviceSubscribedAppRule> resource.

# Table 10.2.23.1-1: <serviceSubscribedAppRule> CREATE

| <serviceSubscribedAppRule> CREATE |
| --- |
| Associated Reference Point | Mca and Mcc |
| Information in Request message | All parameters defined in Table 8.1.2-2 apply with the specific details for: Content: The resource content shall provide the information as defined in clause 9.6.29. |
| Processing at Originator before sending Request | According to clause 10.1.1.1 |
| Processing at Receiver | According to clause 10.1.1.1 |
| Information in Response message | All parameters defined in Table 8.1.2-2 apply with the specific details for: Content: Address of the created <serviceSubscribedAppRule> resource, according to clause 10.1.1.1 |
| Processing at Originator after receiving Response | According to clause 10.1.1.1 |
| Exceptions | According to clause 10.1.1.1 |

#### 10.2.23.2	Retrieve <serviceSubscribedAppRule>

This procedure shall be used for retrieving the attributes of a <serviceSubscribedAppRule> resource.

# Table 10.2.23.2-1: <serviceSubscribedAppRule> RETRIEVE

| <serviceSubscribedAppRule> RETRIEVE |
| --- |
| Associated Reference Point | Mca and Mcc |
| Information in Request message | All parameters defined in Table 8.1.2-2 apply with the specific details for: Content: void |
| Processing at Originator before sending Request | According to clause 10.1.2 |
| Processing at Receiver | According to clause 10.1.2 |
| Information in Response message | All parameters defined in Table 8.1.2-2 apply with the specific details for: Content: attributes of the <serviceSubscribedAppRule> resource as defined in clause 9.6.29 |
| Processing at Originator after receiving Response | According to clause 10.1.2. |
| Exceptions | According to clause 10.1.2 |

#### 10.2.23.3	Update <serviceSubscribedAppRule>

This procedure shall be used for updating the attributes and the actual data of a <serviceSubscribedAppRule> resource.

# Table 10.2.23.3-1: <serviceSubscribedAppRule> UPDATE

| <serviceSubscribedAppRule> UPDATE |
| --- |
| Associated Reference Point | Mca and Mcc |
| Information in Request message | All parameters defined in Table 8.1.2-2 apply with the specific details for: Content: attributes of the <serviceSubscribedAppRule> resource as defined in 9.6.29 which need be updated, |
| Processing at Originator before sending Request | According to clause 10.1.3 |
| Processing at Receiver | According to clause 10.1.3 |
| Information in Response message | According to clause 10.1.3 |
| Processing at Originator after receiving Response | According to clause 10.1.3 |
| Exceptions | According to clause 10.1.3 |

#### 10.2.23.4	Delete <serviceSubscribedAppRule>

This procedure shall be used for deleting a <serviceSubscribedAppRule> resource.

# Table 10.2.23.4-1: <serviceSubscribedAppRule> DELETE

| <serviceSubscribedAppRule> DELETE |
| --- |
| Associated Reference Point | Mca and Mcc |
| Information in Request message | All parameters defined in Table 8.1.2-2 apply |
| Processing at Originator before sending Request | According to clause 10.1.4.1 |
| Processing at Receiver | According to clause 10.1.4.1 |
| Information in Response message | According to clause 10.1.4.1 |
| Processing at Originator after receiving Response | According to clause 10.1.4.1 |
| Exceptions | According to clause 10.1.4.1 |

## -----------------------End of change 1-------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?