| CHANGE REQUEST |
| --- |
| Group Name:* | ARC 15.3 |
| Source:* | ZTE (CCSA) |
| Format:* | Conference Call |
| Date:* | 2015-02 |
| Contact:* | Shao Weixiang, ZTE Corporation, shao.weixiang@zte.com.cn |
| Reason for Change/s:* | cleanup DM editor note |
| CR against: Release* | N/A |
| CR against: TS/TR* | TS-0007 |
| Clauses/Sub Clauses* | Whole document for DM editor note |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

It is proposed to clean device management editorial note：

1. In clause 6.6.2.6, delete the “Editors Note: Need to clarify the device’s reachability schedule.”

In clause 6.2.9.2 of TS-001, Reachability schedules; which are elements of a Node's policy, and specify when messaging can occur between Nodes. Reachability schedules can be used in conjunction with other policy elements. When reachability schedules are not present in a Node then that Node is expected to be always reachable.

In clause 9.6.3 of TS-001, Resource Type CSEBase has child resource schedule which defines the reachability schedule information of the entity. The absence of this resource implies the entity is always reachable.

In clause 9.6.9 of TS-001, Resource Type schedule

2. In “getAE” add output parameter “ReachabilitySchedule”. In“registerAE”, “refreshAERegistration”, add input parameter “ReachabilitySchedule”.

3. In clause 6.9 new operation add|update|get|deleteReachabilitySchedule.

4. In clause 7, add new operation description.

-----------------------Start of change -------------------------------------------

## 6.2	Service Subscription

#### 6.2.2.2	getAE

This service capability provides the ability to retrieve the Application Entity information and associated M2M Service Subscription Identifier associated with the Application Entity Identifier.

##### 6.2.2.2.1	Pre-conditions

Not Applicable

##### 6.2.2.2.2	Signature – getAE

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO | The Application Entity Id (AE-ID) |
| applicationId | OUT | NO | The Application Identifier (App-ID) for the AE |
| serviceSubscriptionId | OUT | YES | The M2M Service Subscription (M2M-Service-Profile-ID) for the AE |
| externalIds | OUT | YES | The external identifiers of the device that hosts the AE |
| reachabilitySchedule | OUT | YES | The contact reachability schedule information of the AE associated with the device node. The absence of this parameter implies the AE associated with the device node is always contact reachable. Type Schedule, see 6.9.1.4.1. |
| responseType | OUT | YES | Unique response types for this service. AE does not exist |

Table 6.2.2.2.2-1 Service Subscription – getAE capability

##### 6.2.2.2.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the service capability

Figure 6.2.2.2.3-1 Service Subscription – getAE Diagram

##### 6.2.2.2.4	Post-Conditions

Not Applicable

##### 6.2.2.2.5	Exceptions

Not Applicable

##### 6.2.2.2.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.2.2.2.7	oneM2M Resource Interworking

When an AE is registered using a CREATE operation on the <AE> resource, the AE is associated with the M2M Service Subscription which is returned along with the correlated AE information (e.g., Application, Device).

## 6.6	Device Management

#### 6.6.2.6	upgradeFirmware

This service capability is a complex operation for AEs to upgrade firmware on one or more devices. The service capability utilizes orchestration rules for the related management operations such as downloadFirmware, installFirmware, getFirmwareInformation, getFirmwareExecInstance and reportFirmwareStatus according to the business process.

This service capability permits AEs to upgrade the firmware on individual device, multiple devices or a group of devices. In addition the upgrade of the firmware is permitted based on a schedule for each of the operations.

##### 6.6.2.6.1	Pre-conditions

The pre-conditions for Mca Received Requests are met.

A correlation between Management Adapter, the service capability and devices or device group exist.

##### 6.6.2.6.2	Signature – upgradeFirmware

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| orchestrationRuleList | IN | NO | List of OrchestrationRule. Type OrchestrationRule, see clause 6.6.1.1.1.4. |
| reportPolicy | IN | YES | The policy used to report the state of the operation to the originating AE. Type ReportPolicy, see 6.6.1.1.1.1. |
| requestId | OUT | NO | The M2M Request Identifier (M2M-Request-ID) |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. Report policy is not supported by the Management Adapter The Orchestration Rules are not supported by the Management Adapter Operation exception: The device’s reachability schedule is inconsistent with the schedule of the Orchestration rule. |

Table 6.6.2.6.2-1 Device Management Service –upgradeFirmware capability

##### 6.6.2.6.3	Service Interactions

The interactions of service capabilities required for this service capability:

1) 	Issue the request to the Supporting Service to perform the operation

Figure 6.6.2.6.3-1 upgradeFirmware Diagram

##### 6.6.2.6.4	Post-Conditions

The Management Adapter has submitted a set of requests to the Management Server to manage firmware.

##### 6.6.2.6.5	Exceptions

Not Applicable

##### 6.6.2.6.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.6.2.6.7	oneM2M Resource Interworking

Not Applicable

## 6.9	Service Subscription Administration

###### 6.9.1.4	Supporting Rules6.9.1.4.1	Schedule Type

The Schedule is a simple type that describes the schedule information.

| Parameter | Optional | Description |
| --- | --- | --- |
| scheduleElement | NO | Expresses time periods defined by second, minute, hour day of month, month, and year. Supports repeating periods, and wildcards expressed as a list. The definition of a schedule is defined in clause 7.3.9 of TS-0004. |

Table 6.9.1.4.1-1 Type: Schedule

#### 6.9.2.15	addReachabilitySchedule

This service capability provides the ability to add a reachability schedule to an AE.This service capability shall be restricted to the Msc and Mca Reference Points.

##### 6.9.2.15.1	Pre-conditions

Not Applicable

##### 6.9.2.15.2	Signature –addReachabilitySchedule

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO | The Application Entity Identifier (AE-ID). |
| reachabilitySchedule | IN | YES | The contact reachability schedule information of the AE associated with the device node. The absence of this parameter implies the AE associated with the device node is always contact reachable. Type Schedule, see 6.9.1.4.1. |
| responseType | OUT | YES | Unique response types for this service. AE successfully added |

Table 6.9.2.15.2-1 Service Subscription Administration –addReachabilitySchedule capability

##### 6.9.2.15.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the addReachabilitySchedule capability

Figure 6.9.2.15.3-1 addReachabilitySchedule Diagram

##### 6.9.2.15.4	Post-Conditions

When parameters are present, the reachability schedule is added for the AE.

##### 6.9.2.15.5	Exceptions

Not Applicable

##### 6.9.2.15.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.15.7	oneM2M Resource Interworking

This service capability is used to add AE reachability schedule information. The service capability aligns with the <schedule> resource and maps to the CREATE procedure. However the linkage between the <schedule> resource and the AE does not exist.

#### 6.9.2.16	updateReachabilitySchedule

This service capability provides the ability to update an AE’s reachability schedule information.This service capability shall be restricted to the Msc and Mca Reference Points.

##### 6.9.2.16.1	Pre-conditions

Not Applicable

##### 6.9.2.16.2	Signature –updateReachabilitySchedule

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO | The Application Entity Identifier (AE-ID). |
| reachabilitySchedule | IN | YES | The contact reachability schedule information of the AE associated with the device node. The absence of this parameter implies the AE associated with the device node is always contact reachable. Type Schedule, see 6.9.1.4.1. |
| responseType | OUT | YES | Unique response types for this service. AE successfully updated |

Table 6.9.2.16.2-1 Service Subscription Administration –updateReachabilitySchedule capability

##### 6.9.2.16.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the updateReachabilitySchedule capability

Figure 6.9.2.16.3-1 updateReachabilitySchedule Diagram

##### 6.9.2.16.4	Post-Conditions

When parameters are present, the reachability schedule is updated for the AE.

##### 6.9.2.16.5	Exceptions

Not Applicable

##### 6.9.2.16.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.16.7	oneM2M Resource Interworking

This service capability is used to update AE’s reachability schedule information. The service capability aligns with the <schedule> resource and maps to the UPDATE procedure. The reference between an AE and a <schedule> resource does not exist as an oneM2M Resource attribute.

#### 6.9.2.17	getReachabilitySchedule

This service capability provides the ability to get an AE’s reachability schedule information. This service capability shall be restricted to the Msc and Mca Reference Points.

##### 6.9.2.17.1	Pre-conditions

Not Applicable

##### 6.9.2.17.2	Signature –getReachabilitySchedule

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO | The Application Entity Identifier (AE-ID). |
| reachabilitySchedule | OUT | YES | The contact reachability schedule information of the AE associated with the device node. The absence of this parameter implies the AE associated with the device node is always contact reachable. Type Schedule, see 6.9.1.4.1. |
| responseType | OUT | YES | Unique response types for this service. not successfully |

Table 6.9.2.17.2-1 Service Subscription Administration –getReachabilitySchedule capability

##### 6.9.2.17.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the getReachabilitySchedule capability

Figure 6.9.2.17.3-1 getReachabilitySchedule Diagram

##### 6.9.2.17.4	Post-Conditions

When parameters are present, the reachability schedule is gotten from the AE.

##### 6.9.2.17.5	Exceptions

Not Applicable

##### 6.9.2.17.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.17.7	oneM2M Resource Interworking

This service capability is used to get an AE’s  reachability schedule information. The service capability aligns with the <schedule> resource and maps to the RETRIEVE procedure. The reference between an AE and a <schedule> resource does not exist as an oneM2M Resource attribute.

#### 6.9.2.18	deleteReachabilitySchedule

This service capability provides the ability to delete a reachability schedule for an AE. This service capability shall be restricted to the Msc and Mca Reference Points.

##### 6.9.2.18.1	Pre-conditions

Not Applicable

##### 6.9.2.18.2	Signature –deleteReachabilitySchedule

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO | The Application Entity Identifier (AE-ID). |
| responseType | OUT | YES | Unique response types for this service. AE successfully deleted |

Table 6.9.2.18.2-1 Service Subscription Administration –deleteReachabilitySchedule capability

##### 6.9.2.18.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue the deleteReachabilitySchedule capability

Figure 6.9.2.18.3-1 deleteReachabilitySchedule Diagram

##### 6.9.2.18.4	Post-Conditions

When parameters are present, the reachability schedule is deleted from the AE.

##### 6.9.2.18.5	Exceptions

Not Applicable

##### 6.9.2.18.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.9.2.18.7	oneM2M Resource Interworking

This service capability is used to delete an AE’s reachability schedule information. The service capability aligns with the <schedule> resource and maps to the DELETE procedure. The reference between an AE and a <schedule> resource does not exist as an oneM2M Resource attribute.

## 6.11	Registration

#### 6.11.2.1	registerAE

This service capability enables an AE with the proper authorization to register with the M2M System. This service capability shall be restricted across the Mca Reference Point.

##### 6.11.2.1.1	Pre-conditions

The AE has not registered with the M2M System. An AE identifier may have been already allocated to the registering AE and acquired by the AE by means outside the scope of this specification.

##### 6.11.2.1.2	Signature – registerAE

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| pointOf Access | IN | NO | The point of Access of the registered AE. |
| applicationId | IN | NO | The Application Identifier (App-ID). |
| credentialId | IN | YES | Application Credential-ID used to identify the Application Entity for the Application. It is used to retrieve the corresponding M2M Service Subscription. |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator. |
| reachabilitySchedule | IN | YES | The contact reachability schedule information of the AE associated with the device node. The absence of this parameter implies the AE associated with the device node is always contact reachable. Type Schedule, see 6.9.1.4.1. |
| aeId | IN-OUT | Optional for IN only-Not Optional for OUT | Application Entity (AE-ID) is provided back in the response. |
| responseType | OUT | NO | Unique response types for this service: AE successfully registered AE not successfully registered M2M Service Subscription does not exist Invalid Application Credential Identifier. |

Table 6.11.2.1.2-1 Registration – registerAE capability

##### 6.11.2.1.3	Services Interaction

The interactions of service capabilities required for this service capability:

- Associate the AE with the M2M Service Subscription

- Issue the request to the Supporting Service.

- Send a notification to the Device Onboarding Supporting Service for a first-time application registration  in the event there is a subscription of the first contact event by the Supporting Service.

Figure 6.11.2.1.3-1 Registration – registerAE Diagram

##### 6.11.2.1.4	Post-Conditions

AE is registered and can start using service capabilities

The returned AE-ID shall be used in any subsequent operation related to that application

##### 6.11.2.1.5	Exceptions

Not Applicable

##### 6.11.2.1.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.11.2.1.7	oneM2M Resource Interworking

This service capability maps to the CREATE procedure of the <AE> resource.

#### 6.11.2.2	refreshAERegistration

This service capability enables an AE to refresh an existing AE registration with the M2M System. This service capability shall be restricted to the Mca Reference Points.

##### 6.11.2.2.1	Pre-conditions

The AE has successfully registered with the M2M System.

##### 6.11.2.2.2	Signature – refreshAERegistration

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO | The Application Entity Identifier (AE-ID) of the request originator. |
| pointOfAccess | IN | YES | The point of Access of the registered AE. POA is optional only if identical to the one in the refreshed registration |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator. |
| reachabilitySchedule | IN | YES | The contact reachability schedule information of the AE associated with the device node. The absence of this parameter implies the AE associated with the device node is always contact reachable. Type Schedule, see 6.9.1.4.1. |
| responseType | OUT | NO | Unique response types for this service: AE successfully refreshed Registration does not exist |

Table 6.11.2.2.2-1 Registration – refreshAERegistration capability

##### 6.11.2.2.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Issue a request to regresh the AE association with the M2M Service Profile

- Issue the request to the Supporting Service

Figure 6.11.2.2.3-1 Registration – refreshAERegistration Diagram

##### 6.11.2.2.4	Post-Conditions

The Application Entity registration is refereshed and can continue using service capabilities.

##### 6.11.2.2.5	Exceptions

Not Applicable

##### 6.11.2.2.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

##### 6.11.2.2.7	oneM2M Resource Interworking

This service capability maps to the UPDATE procedure of the <AE> resource.

## 7.6	Service Exposure (SE)

The SE Component acts as the primary interface for AEs to interact with the M2M Service Layer across the Mca Reference Point.

## 7.6.1	Service Exposure to Service Cross Reference

Data Exchange: subscribe, publish, sendMessage

Service Subscription Administration: getServiceSubscription, addNodeToServiceSubscription, deleteNodesFromServiceSubscription, getNodesForServiceSubscription, updateNodeForServiceSubscription, addApplicationRule, deleteApplicationRules, getApplicationRules, updateApplicationRule, addReachabilitySchedule, updateReachabilitySchedule, getReachabilitySchedule, deleteReachabilitySchedule

Device Management:  downloadFirmware, installFirmware, getFirmwareInformation, getFirmwareExecStatus, upgradeFirmware, getDeviceInformation, getDeviceCapabilities, enableDeviceCapability, disableDeviceCapability, getAreaNetworks, updateDeviceForAreaNetwork, rebootDevice, resetDevice, uploadDeviceLog, getDeviceLogs, getDeviceLogInformation, getSoftwareInformation, downloadSoftware, installSoftware, activateSoftware, deactivateSoftware, removeSoftware

Event Collecton: setEventCollectionPolicy, getEventCollectionPolicy, setEventCollectionTriggers, getEventCollectionTriggers, getEventRecords

Registration Services: registerAE, refreshAERegistration, deregisterAE

## 7.7	Management Adapter (MA)

The Management Adapter component provides services that are used to integrate or adapt Device Management requests to the Management Servers of existing device management technologies(e.g., TR-069, OMA-DM, and LWM2M) .

## 7.7.1	Management Adapter to Service Cross Reference

Management Adapter: All Service Capabilities

Device Management:  deviceManagementReport

## 7.8	Device Management (DM)

The Device Management component provides services to manage devices without consideration of the technology of Underlying Network.

### 7.8.1	Device Management to Service Cross Reference

Device Management: All Service Capabilities

# Annex D (Informative): Device Management Services

##### D.2.1.1.22	deactivateSoftware

This service capability provides the ability to execute a deactivateSoftware request from an AE.

###### D.2.1.1.22.1	Pre-conditions

The pre-conditions for Mca Received Requests are met.

A correlation between a Management Adapter, the M2M Service Capability and device exist.

###### D.2.1.1.22.2	Signature –deactivateSoftware

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| Common request input attributes | - | - | See Table A.2.1-1 |
| deviceId | IN | NO | The unique device identifier in the context of the M2M M2M Service Subscription. |
| version | IN | NO | The version of the software. |
| name | IN | NO | The name of the software. |
| reportPolicy | IN | YES | The policy used to report the state of the operation to the originating AE. See clause 6.6.1.1.1.1. |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. |

Table D.2.1.1.22.2-1 Device Management Service –deactivateSoftware capability

###### D.2.1.1.22.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Perform the Common Request Services for requests across the Mca Reference Point

- Retrieves the Management Adapter to be used for the device and M2M Service Subscription

- Issues the request to the Management Adapter to deactivates software

- Records the event

Figure D.2.1.1.22.3-1 deactivateSoftware Interaction Diagram

###### D.2.1.1.22.4	Post-Conditions

The Management Adapter has submitted a request to the Management Server to deactivates software.

The event is recorded.

###### D.2.1.1.22.5	Exceptions

No unique exceptions for this service capability.

Consumed services may throw exceptions which are forwarded by this service capability.

###### D.2.1.1.22.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

Maximum Response: 300ms

##### D.2.1.1.23	removeSoftware

This service capability provides the ability to execute a removeSoftware request from an AE.

###### D.2.1.1.23.1	Pre-conditions

The pre-conditions for Mca Received Requests are met.

A correlation between a Management Adapter, the M2M Service Capability and device exist.

###### D.2.1.1.23.2	Signature –removeSoftware

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| Common request input attributes | - | - | See Table A.2.1-1 |
| deviceId | IN | NO | The unique device identifier in the context of the M2M M2M Service Subscription. |
| version | IN | NO | The version of the software. |
| name | IN | NO | The name of the software. |
| reportPolicy | IN | YES | The policy used to report the state of the operation to the originating AE. See clause 6.6.1.1.1.1. |
| responseType | OUT | YES | Unique response types for this service. Note: Consumed services also provide response types. |

Table D.2.1.1.23.2-1 Device Management Service –removeSoftware capability

###### D.2.1.1.23.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Perform the Common Request Services for requests across the Mca Reference Point

- Retrieves the Management Adapter to be used for the device and M2M Service Subscription

- Issues the request to the Management Adapter to uninstall the software

- Records the event

Figure D.2.1.1.23.3-1 removeSoftware Interaction Diagram

###### D.2.1.1.23.4	Post-Conditions

The Management Adapter has submitted a set of requests to the Management Server to uninstall the software.

The event is recorded.

###### D.2.1.1.23.5	Exceptions

No unique exceptions for this service capability.

Consumed services may throw exceptions which are forwarded by this service capability.

###### D.2.1.1.23.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

Maximum Response: 300ms

# Annex F (Informative): Registration Services

##### F.2.1.1.1	registerAE

This service capability enables an AE to register with the M2M System. This service capability shall be restricted across the Mca Reference Point

###### F.2.1.1.1.1	Pre-conditions

The AE has not registered with the M2M System.

The pre-conditions for Mca Received Requests are met.

###### F.2.1.1.1.2	Signature – registerAE

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| Mca Common request input parameters | - | - | See Table A.2.1-1 |
| pointOf Access | IN | NO | The point of Access of the registered AE. |
| applicationId | IN | NO | The Application Identifer (App-ID). |
| credentialId | IN | YES | Application Credentials. It is used to retrieve the corresponding Service Subscription |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator |
| reachabilitySchedule | IN | YES | The contact reachability schedule information of the AE associated with the device node. The absence of this parameter implies the AE associated with the device node is always contact reachable. Type Schedule, see 6.9.1.4.1. |
| aeId | IN-OUT | Option for IN only-Not an Option for OUT | The Application Entity Identiifer (AE-ID) is provided back in the response |
| responseType | OUT | NO | Unique response types for this service: AE successfully registered AE not successfully registered |

Table  F.2.1.1.1.2-1  Registration Services – registerAE capability

###### F.2.1.1.1.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Perform the Common Request Services for requests across the Mca Reference Point

- Record the event

Figure F.2.1.1.1.3-1 Registration Services – registerAE Diagram

###### F.2.1.1.1.4	Post-Conditions

Event is recorded

###### F.2.1.1.1.5	Exceptions

No unique exceptions for this service capability.

Consumed services may throw exceptions which are forwarded by this service capability.

###### F.2.1.1.1.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

Maximum Response: 250ms

##### F.2.1.1.2	refreshAERegistration

This service capability enables an AE to refresh an existing registration with the M2M System

###### F.2.1.1.2.1	Pre-conditions

The pre-conditions for Mca Received Requests are met.

The AE is registered and allocated an aeId by the M2M System.

###### F.2.1.1.2.2	Signature – refreshAERegsitration

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| Mca Common request input parameters | - | - | See Table A.2.1-1 |
| aeId | IN | NO | The Application Entity Identifier (AE-ID) to be refreshed. |
| pointOfAccess | IN | YES | The point of Access of the registered AE. POA is optional only if identical to the one in the refreshed registration |
| expirationTime | IN | NO | The expiration time of the registration as requested by the Originator. |
| reachabilitySchedule | IN | YES | The contact reachability schedule information of the AE associated with the device node. The absence of this parameter implies the AE associated with the device node is always contact reachable. Type Schedule, see 6.9.1.4.1. |
| responseType | OUT | NO | Unique response types for this service: AE successfully refreshed Registration does not exist |

Table F.2.1.1.2.2-1 Registration Services – refreshAERegistration capability

###### F.2.1.1.2.3	Service Interactions

The interactions of service capabilities required for this service capability:

- Perform the Common Request Services for requests across the Msc Reference Point

- Record the event

Figure F.2.1.1.2.3-1 Registration Services – refreshAERegistration Diagram

###### F.2.1.1.2.4	Post-Conditions

Success case: The request is permitted.

Failure case: The request is not permitted and a response type is transmitted to the AE

###### F.2.1.1.2.5	Exceptions

No unique exceptions for this service capability.

Consumed services may throw exceptions which are forwarded by this service capability.

###### F.2.1.1.2.6	Policies for Use

Message Exchange Patterns: In-Out

Transaction Pattern: Participation allowed

Maximum Response: 50ms