| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#16 |
| Source:* | Sung-Chan Choi, Yong-Suk Park, Jaeho Kim, JaeSeung Song |
| Date:* | 2015-03-23 |
| Contact:* | Sung-Chan Choi (csc@keti.re.kr) |
| Reason for Change/s:* | Add one possible value regarding result content parameter |
| CR against: Release* | Rel.1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS0001-v1.6.1 |
| Clauses/Sub Clauses* | 8.1.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

In TS-0001, there is a result content request parameter which enables the requestor to be able to set the indication of the expected components of the result of the requested operation. This CR is to add one possible value which is child-resources.

The reason is that if the child-resource-references are about the references of the sensor data, in order for the requestor to receive the sensor data, the requestor needs to request again using acquired child resource references. It would be inefficient to request the data again using resource references because the sensor data size is very small.

As this CR does not change existing feature or functionality and proposes an additional value that was missed in Release 1, this CR is proposed as small technical enhancements.

### -----------------------Start of change 1-------------------------------------------

### 8.1.2	Request

Result Content: optional result content: Indicates what are the expected components of the result of the requested operation. The Originator of a request may not need to get back a result of an operation at all. This shall be indicated in the Result Content parameter. Which exact settings of Result Code are possible depends on the requested operation specified in Operation. Possible values of Result Content are:

attributes: Representation of the requested resource shall be returned as content, without the address(es) of the child resource(s). This is the default value. For example, if the request is to retrieve a <container> resource, the address(es) of the <contentInstance> child-resource(s) is not provided. When this is used for Create operation, only assigned/modified attributes shall be included in the content. This setting is not valid for a Notify operation.

hierarchical-address: Representation of the address of the created resource. This shall be only valid for a Create operation. The address shall be in hierarchical address scheme.

hierarchical-address+attributes: Representation of the addresss in hierarchical address scheme and assigned/modified attributes of the created resource. This shall be only valid for a Create operation.

-	attributes+child-resources: Representation of the requested resource, along with a nested representation of all of its child resource(s) in line with any provided filter criteria as given in the Filter Criteria parameter shall be returned as content. When this setting of Result Content is used, optionally the Originator may  request to limit the response by a maximum total size or a maximum number of allowed nesting levels. For example, if the request is to retrieve a <container> resource that only has <contentInstance> children, the attributes of that <container> resource and a nested representation of all of its <contentInstance> child-resource(s) are provided. This setting is only valid for a Retrieve operation.

child-resources: Representation of  all of the child resource(s) of the requested resource, along with a nested representation of all of its child resource(s) in line with any provided filter criteria as given in the Filter Criteria parameter shall be returned as content. When this setting of Result Content is used, optionally the Originator may  request to limit the response by a maximum total size or a maximum number of allowed nesting levels. For example, if the request is to retrieve a <container> resource that only has <contentInstance> children, only a nested representation of all of its <contentInstance> child-resource(s) are provided. This setting is only valid for a Retrieve operation.

attributes+child-resource-references: Representation of the requested resource, along with the address(es) of the child resource(s), possibly limited by a maximum number of retrieved links, shall be returned as content. For example, if the request is to retrieve a <container> resource, the <container> resource and the address(es) of the <contentInstance> child-resource(s) are provided. This setting is not valid for a Notify operation.

child-resource-references: Address(es) of the child resources, possibly limited by a maximum number of retrieved address(es), without any representation of the actual requested resource shall be returned as content. For example, if the request is to retrieve a <container> resource, only the address(es) of the <contentInstance> child-resource(s) is provided. This setting is not valid for  a Notify operation.

nothing: Nothing shall be returned as operational result content. This setting is not valid for a retrieve operation. This setting is the default when a Notification was requested by the Operation parameter. For example, if the request is to delete a resource, this setting indicates that the response shall not include any content.

original-resource: Representation of the original resource pointed by the link attribute in the announced resource shall be returned as content, without the address(es) of the child resource(s). This setting is only valid for a RETRIEVE Request where the To parameter targets the announced resource.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?