| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 17.0 |
| Source:* | KT Corp. (TTA) |
| Date:* | 2015-05-17 |
| Contact:* | Francisco Sang-Eon Kim (kim.sangeon@kt.com) |
| Reason for Change/s:* | Request message parameters are not consistent with between Request Message at 8.1.2 and Section 10.1.1.1 for Non-registration related CREATE procedure. Response Message parameters are not consistent with between Response Message at 8.1.3 and 10.1.1.1.1 for Non-registration related CREATE procedure. |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001-V2.1.0 |
| Clauses/Sub Clauses* | 10.1.1.1 Non-registration related CREATE procedure |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: ARC-2015-1882R01 <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

First, Request message parameters for Non-registration related CREATE procedure:

Parameters of Request Message are specified with mandatory, conditional and optional at 8.1.2.

The mandatory parameters for Request Message are To, From, Operation and Request Identifier.

The conditional parameters for Request Message are Content and Resource Type. These conditional parameters are mandatory for CREATE operation.

The optional parameters for Request Message are Role, Name, Originating Timestamp, Request Expiration Timestamp, Result Expiration Timestamp, Response Type, Result Content, Result Persistence, Operation Execution Time, Event Category, Delivery Aggregation, Group Request Identifier, Filter Criteria and Discovery Result Type.

It is specified for mandatory parameters which is not mandatory parameters such as Resource Type, Name and Content at Step001 in CREATE Request message for Figure 10.1.1.1-1

Second, Response message parameters for Non-registration related CREATE procedure:

Parameters of Response Message are specified with mandatory, conditional and optional at 8.1.3.

The mandatory parameters for Response Message are Response Code and Request Identifier.

The conditional parameters for Response Message are Content. The Content parameter is optional for CREATE operation.The optional parameters for Response Message are To, From,  Originating Timestamp,  Result Expiration Timestamp,  Event Category and Status Code.

It is stated that “The Receiver shall respond with a Response message that shall contain the following parameters”  for To, From, Request Identifier, Content at Step003.

The Step 003, also, has missed Response Code for mandatory parameter.

### -----------------------Start of change 1-------------------------------------------

#### 10.1.1.1	Non-registration related CREATE procedure

This procedure is valid for all resources which are not related to registration.

Originator requests to create a resource by using the CREATE method. See clause 8.1.2 for the parameters to be included in the Request message.

Registrar CSE, when the Originator is an AE, shall validate the create request based on the Resource Type parameter against the M2M Service Subscription Profile of the AE (validation is done against serviceRoles attribute).

Hosting CSE If the request is allowed by the given privileges, the Receiver shall create the resource.

Figure 10.1.1.1-1: Procedure for CREATEing a Resource

Step 001: The Originator sends the following parameters in the CREATE Request message:

Mandatory Parameters:

- Operation: C (Create);

- To: Address of the parent of  the new resource to be created by this request;

# From: ID of the Originator (either the AE-ID or CSE-ID);

- Request Identifier: Identifier provided by the Originator. Needed for correlation of responses regarding this Request.

- Resource Type: Type of resource to be created;

- Content: attributes of the resource to be provided by the Originator.  All attributes with a multiplicity greater or equal to one and an access mode of RW or WO in the definition of the resource type for which a resource shall be created by the issued CREATE Request shall be present in the Content parameter of the Request, except for the following common attributes that are only optionally present:

expiration time.

Optional Parameters:

- Name: optional name of the resource to be provided by the Originator.

Step 002: The Receiver shall:

- Check if the Originator has the appropriate privileges for performing the request. Privileges are part of the attribute accessControlPolicyIDs of the targeted resource. In case that such an attribute does not exist, the Receiver shall check the accessControlPolicyIDs of the parent resource. This lookup of accessControlPolicyIDs attribute in case of non-existence shall be performed recursively until a parent with such an attribute is found.

- Verify that the name for the created resource as suggested in the Name parameter, if provided by the Originator in the CREATE Request message, does not already exist among child resources of the target resource. If no child within the targeted resource exists with the same name as suggested by the Name parameter, use that name for the resource to be created. If Name is not provided by the Originator, assign a name generated by the Receiver to the resource to be created.

NOTE :	The name of a resource in general is not the same as its Resource ID. While a name of a resource only needs to be unique among the children of the same parent resource, the Resource ID needs to be unique in context of the Hosting CSE. When the name of the resource to be created is assigned by the Receiver, it may choose to use a name that is identical to the Unstructured-CSE-relative-Resource ID.

Assign a Resource-ID (see resourceID attribute in common attribute table 9.6.1.3.2-1) to the resource to be created.

Assign values for mandatory RO mode attributes of the resource and override values provided for other mandatory attributes, where needed, and where allowed by the resource type definition and if not provided by the Originator itself.

the Receiver shall assign a value to the following common attributes specified in clause 9.6.1.3:

a)	parentID;

b)	creationTime;

c)	expirationTime: if not provided by the Originator, the Receiver shall assign the maximum value possible (within the restriction of the Receiver policies). If the value provided by the Originator cannot be supported, due to either policy or subscription restrictions, the Receiver will assign a new value.

d)	lastModifiedTime: which is equals to the creationTime;

e)	Any other RO (Read Only) attributes within the restriction of the Receiver policies.

The Receiver shall check whether a creator attribute is included in the  Content parameter of the request.  If included, the creator attribute shall not have a value in the Content parameter of the request. If  the creator attribute is included in the request and the creator attribute is supported for the type of resource being created, then the Receiver shall interpret this as an indication for it to include the creator attribute in the resource to be created.  The Receiver shall assign a value equal to the value carried in the From request parameter.  In the event that the originator provides a value for the creator attribute within the request, this request shall be deemed invalid.

On successful validation of the Create Request, the Receiver shall create the requested resource.

The Receiver shall check if the created resource is a child of a parent resource having a stateTag attribute and increment the parent’s stateTag if present.

Step 003: The Receiver shall respond with a Response message that contains the following parameters:

Mandatory Parameters:

# Response Code: whether the requested operation was successful, unsuccessful or acknowledgement

# Request Identifier: Identical to the one provided by the Originator of the Request.

- Optional Parameters:

- Content: Optionally the address and/or content of the created resource. If Result Content value in the request was address, then the Receiver shall provide the hierarchical address of the created resource in the Content parameter. If Result Content value in the request was attributes, then the Receiver shall provide the assigned or overidden attributes (step 0002) in the Content parameter. If Result Content value in the Request was address+attributes, then the Receiver shall provide the hierarchical address of the created resource and the assigned or overridden attributes (step 0002) in the Content parameter.

- To: Optional. ID of the Originator. This parameter shall be present in the Response when the Originator is not a Registree of the Hosting CSE. In case this is a response carrying the result of an operation triggered by a non-blocking synchronous request the information provided in the notification target list within the Response Type parameter shall be used for sending the Response to the Request as notification(s) to the targets in the list.

# From: Optional. ID of the Receiver. This parameter shall be present in the Response when the Originator is not a Registree of the Hosting CSE.

See clauses 8.1.3 and 8.1.4 for the parameters to be included in the Response message.

General Exceptions:

- The Originator does not have the privileges to create a resource on the Receiver. The Receiver responds with an error.

The resource with the specified name (if provided) already exists at the Receiver. The Receiver responds with an error.

The provided information in Content is not accepted by the Receiver (e.g. missing mandatory parameter). The Receiver responds with an error.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?