| Input Contribution |
| --- |
| Meeting ID* | ARC 17.0 |
| Title:* | <schedule> Resource Procedures |
| Source:* | Francisco Sang-Eon Kim, KT Corp. (TTA), kim.sangeon@kt.com |
| Uploaded Date:* | 2015-05-09 |
| Document(s) Impacted* | TS-0001-V2.1.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | This contribution is proposed to include at section 10 ‘Information Flows’ in TS-0001-V2.1.0 which is not specifiec for <schedule> Resource Procedures. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 10.2.X	<schedule> Resource Procedures

#### 10.2.X.1	Create <schedule>

This procedure shall be used to create an <schedule> resource.

Table 10.2.X.1-1: <schedule> CREATE

| <schedule> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in Table 8.1.2-2 apply the specific details for: Content: The resource content shall provide the information as defined in clause 9.6.9 |
| Processing at Originator before sending Request | According to clause 10.1.1.1. |
| Processing at Receiver | According to clause 10.1.1.1. |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: Address of the created <scheduler> resource, according to clause 10.1.1.1 |
| Post-Processing at Originator | According to clause 10.1.1.1 |
| Exceptions | According to clause 10.1.1.1 |

#### 10.2.X.2	Retrieve <schedule>

This procedure shall be used to retrieve attributes and child resource information of the <schedule> resource.

Table 10.2.X.2-1: <schedule> RETRIEVE

| <schedule> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc'. |
| Information in Request message | All parameters defined in Table 8.1.2-2 apply the specific details for: Content: void |
| Processing at Originator before sending Request | According to clause 10.1.2. |
| Processing at Receiver | According to clause 10.1.2. The Receiver shall check access control rules defined in selfPrivileges of the <accessControlPolicy> resource>. |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: Address of the created <scheduler> resource, according to clause 10.1.1.1 |
| Post-Processing at Originator | According to clause 10.1.2 |
| Exceptions | According to clause 10.1.2 |

#### 10.2.X.3	Update <schedule>

This procedure shall be used to update attributes information of the < schedule> resource.

Table 10.2.X.3-1: <schedule> UPDATE

| <schedule> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc'. |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: Content: attributes of the <schedule> resource as defined in clause 9.6.9 which need be updated. |
| Processing at Originator before sending Request | According to clause 10.1.3 |
| Processing at Receiver | According to clause 10.1.3 |
| Information in Response message | According to clause 10.1.3 |
| Post-Processing at Originator | According to clause 10.1.3 |
| Exceptions | According to clause 10.1.3 |

#### 10.2.X.4	Delete <schedule>

This procedure shall be used to delete the <schedule> resource.

Table 10.2.X.4-1: <schedule> DELETE

| <schedule> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: Content: attributes of the <schedule> resource as defined in clause 9.6.9 which need be deleted. |
| Processing at Originator before sending Request | According to clause 10.1.4.1 |
| Processing at Receiver | According to clause 10.1.4.1. |
| Information in Response message | According to clause 10.1.4.1 |
| Post-Processing at Originator | According to clause 10.1.4.1 |
| Exceptions | According to clause 10.1.4.1 |