| Input Contribution |
| --- |
| Meeting ID* | ARC 17.3 |
| Title:* | TS-0014 Clause 5 descriptions |
| Source:* | Tim Carey, ALU, timothy.carey@alcatel-lucent.com |
| Uploaded Date:* | 2015-06-19 |
| Document(s) Impacted* | TS-0014 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Add to next TS-0014 Baseline |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Item 1:

Add new descriptions for Architecture to clause 5.

# 5	Architecture Model

## 5.1	Introduction

The architecture model followed in the present document is based on the architecture model in Annex F of TS-001 [2] that describes how interworking between CSEs and non-oneM2M solutions and protocol using specialized Interworking  Proxy application Entities (IPE). The present document descibes the LWM2M IPE that supports the following scenarios:

Figure 5.1-1 - LWM2M Interworking Scenarios

In the scenarios depicted in Figure 5.1-1, the Hybrid and LWM2M Applications represent applications that implement the LWM2M Client role defined in the LWM2M Protocol [3].

## 5.2	Reference Model

The LWM2M Interworking reference model utilizes the Functional Architecture’s reference model in TS-0001 [2]; augmenting the TS-0001 reference model with capabilities provided by the LWM2M IPE.

Figure 5.2-1 - LWM2M Reference Model

Note: The AE in the reference model could be registered with the same CSE as the LWM2M IPE.

## 5.3	Types of Interworkings

LWM2M IPEs provide the following types of interworkings:

- Interworking using the <containter> resource for transparent transport of encoded LWM2M Objects that are available to AEs as depicted in Figure 5.3-1.

- Interworking with full mapping of the semantics of LWM2M Objects to semantically enabled resources that are available to AEs as depicted in Figure 5.3.-2.

- While depicted outside the hosting CSE, the <container> resources are hosed a CSE (e.g., CSE1)

Figure 5.3-1 - LWM2M Transparent Transport Interworking

In Figure 5.3-1, the LWM2M Objects are provided by the LWM2M Application to the LWM2M IPE using the LWM2M Protocol. The LWM2M IPE then encapsulates the LWM2M Objects in <container> resources and then hosts the <container> resource in a CSE using the Mca reference points for use by AEs. The AE accesses the <container> resource from the CSE that hosts the resource using the Mca reference point. Once the AE receives the <container> resource, the AE extracts the LWM2M Object from the <container> resource for the AE’s purpose. Clause 7 describes this type of interworking in greater detail.

Figure 5.3-2 - LWM2M Objects Semantic Transport Interworking

In Figure 5.3-2, the LWM2M Objects are provided by the LWM2M Application to the LWM2M IPE using the LWM2M Protocol. The LWM2M IPE then interworks the LWM2M Objects into <container> resources. The <container> resources are based on the oneM2M defined Abstract Information Model and optionally the Semantic Ontology. The LWM2M IPE hosts the <container> resource in a CSE across the Mca reference for use by other AEs. The AE accesses the <container> resource from the CSE that hosts the resource using the Mca reference point. Once the AE receives the <container> resource, the AE encodes the information using the oneM2M Abstract Information Model definition and optionally the Semantic Ontology for the AE’s purpose. Clause 8 describes this type of interworking in greater detail.

## 5.4	Composition of the Interworking Proxy Entity

The LWM2M IPE participation in the LWM2M Protocol as described in clause 5 does so in the role of a LWM2M Server to which LWM2M Applications (LWM2M Clients) interact. For each LWM2M Client (Endpoint) that is maintained by the LWM2M Server in the LWM2M IPE, the LWM2M IPE shall instantiate and maintain an instance of a Resource of type <AE>.

Figure 5.4-1 - LWM2M IPE Architecture

# Text boxes

Hybrid Application

CSE(s)

LWM2M Interface

Mca

LWM2M

IPE

Mca

(note 1)

LWM2M Application

LWM2M

IPE

Mca

LWM2M Interface

LWM2M Application

CSE

LWM2M Protocol

LWM2M

IPE

Mca

AE

Mca

ASN/MN/IN

CSE

Mcc/Mcc’

MN/IN