| CHANGE REQUEST |
| --- |
| Meeting:* | WG2 Architecture - ARC 18 |
| Source:* | Ericsson |
| Date:* | 2015-06-16 |
| Contact:* | George Foti |
| Reason for Change/s:* | See introduction |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> Subscription/Notification Enhancement MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 V 2.2.0 |
| Clauses/Sub Clauses* | 9.6.31, 9.6.32, 9.6.33, 9.6.34 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR included storial changes only

### -----------------------Start of change 1-------------------------------------------

### 9.6.31	Resource Type notificationTargetDisposition

Editor’s Note: The name of the resource type should be improved.

The <notificationTargteDisposition> resource is a child resource of a <subscription> resource and lists a reference to the policy to be followed by the hosting CSE for every Target Notification of a subscription. The policy is applied by the hosting CSE when it receives a request to stop receiving a notification from a Target Notification. If no policy is defined for the Target Notification, then the hosting CSE shall apply the default policy. The default policy is either created by the subscription originator or the hosting CSE shall have a system created default one to apply. The system created default policy shall be configurable by the M2M Service Provider   .

Figure 9.6.31-1: Structure of <notificationTargetDisposition> resource

Table 9.6.31-1:  Child resources of <notificationTargetDisposition> resource

| Child Resources of <notifcatioonTargetDisposition> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |

Table 9.6.31-2: Attributes of <notificationTargetDisposition> resource

| Attributes of <notificationTargets> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. If no accessControlPolicyIDs is given at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute. |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| notificationTargetURI | 1 (L) | RW | address(es) of the resource subscriber receiving a notification.The notificationTarget URI must be listed in the subscription resource attribute notificationURI, otherwise the default policy shall apply . |
| notificationlPolicyID | 1 | RW | A link to the <notificationDeletionPolicy> resource applicable to the notificationTargetURI. If none is specified than the default policy shall apply to the targetNotificationURI. See clause 9.6.Z for an explanation of the <notificationDeletionPolicy > resource. |

### 9.6.32	Resource Type notificationDeletionPolicy

Editor’s Note: The name of the resource type should be improved.

The <notificationDeletionPolicy> resource is a child resource of <CSEBase> resource and lists the policies to be applied by the hosting CSE. A policy has a rules(s), representd by the <policyDeletionRules> and an action. The action is applied when the rules in the policy are fulfilled.

Rules are grouped in 2 groups to support a combination of rules for flexbiblilty eg. ((rule 1 AND rule 2) OR rule 3)  A maximum  of two groups of  <policyDeletionRules> can be defined. The relationship to be applied between the 2 groups (AND/OR) shall be defined in the ruleRelationShip attribute. If  no rules are defined for a <notificationDeletionPolicy> then the action is executed

Each policy has a label which can take any form. There shall be at minimum a single notificationDeletionPolicy which can be defined by the subscription originator  with the label “default” to be applied when no specific policy is defined for a Target Notification. If a default policy is required and nne is defined by the subscription originator then the syetem defined default policy shall be applied

Figure 9.6.32-1: Structure of <notificationDeletionPolicy> resource

Table 9.6.32-1::  Child resources of <notificationDeletionPolicy> resource

| Child Resources of <notifcatioonTarget> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <policyDeletionRules> | 0..2 | Groups listing the of rules that apply to this policy and that needs to be fulfilled for the listed action to take place, Only two groups of rules shall be supported. See 9.6.33 |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |

Table 9.6.32-2: Attributes of <notificationDeletionPolicy> resource

| Attributes of <notificationTargets> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. If no accessControlPolicyIDs is given at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute. |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| action | 1 | RW | Defines the action to be performed if the groups of rules are fulfilled. The action includes at least one of the following; accept request, reject request, seek authorization from subscription originator before responding, or inform the subscription originator without taking any action; the subscription originator may update the subscription at a later time to remove the Target Notification |
| policyLabel | 1 | RW | At minimum a default policy must be specified. The policyLabel “Default” must be used in this case. |
| rulesRelationship | 0..1 | RW | Shall be either AND or OR This attribute is mandatory if more than on policy DeletionRule is specified |
| creator | 0..1 | RO | The AE-ID or CSE-ID of the entity which created the resource. |

### 9.6.33	Resource Type policyDeletionRules

Editor’s Note: The name of the resource type should be improved.

The <policyDeletionRules> resource lists the rules to be applied by the hosting CSE during policy execution. Each <policyDeletionRules> can define any number of rules with an AND or OR relationship to be applied between them.  The attribute deletionRules Relation define the relationship between rules. It can have an AND or OR value

Figure 9.6.33-1: Structure of <policyDeletionRules> resource

Table 9.6.33-1::  Child resources of <policyDeletionRules> resource

| Child Resources of <notifcatioonTarget> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |

Table 9.6.33-2: Attributes of <rules> resource

| Attributes of <notificationTargets> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. If no accessControlPolicyIDs is given at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute. |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| deletionRule | 0..1(L) | RW | Lists the applicable rules. The rules include at minimum; time of the day, geaographical location of the Target Notification. Where the rule applies |
| deletionRuleRelation | 0..1 | RW | Defines the relation to be applied between the deletionRule Can take the value AND or OR. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 9.6.34		Resource Type notificationTargetRemoval

Editor’s Note: The name of the resource type should be improved.

The <notificationTargetRemoval> resource is a virtual resource, which does not have a representation and it is the child resource of  a <subscription> resource. Whenever a Delete Request is sent to the <notificationTargetRemoval> resource from a Notification Target which wants to remove itself from the Notification Target list (i.e., notificationURI) later, the Notifier shall act according to the action attribute defined in the <notificationDeletionPolicy> resource which is linked from the <notificationTargteDisposition> resource defined for the specific notificationURI . If no specific policy is defined for the notification URI then the default policy shall apply.

Figure 9.6.34-1: Structure of <notificationTargetRemoval> resource

### -----------------------End of change 2-------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?