| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#18.0 |
| Source:* | Darold Hemphill, iconectiv, dhemphill@iconectiv.com |
| Date:* | 2015-07-08 |
| Contact:* | Darold Hemphill, iconectiv, dhemphill@iconectiv.com |
| Reason for Change/s:* | App-ID format and required attributes |
| CR against: Release* | 2.0 |
| CR against: WI* | Active WI-0029 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 ver 2.2.0 |
| Clauses/Sub Clauses* | Clause 7.2, Table 7.2-1 and Clause 7.1.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

App-ID is defined in TS-0001 ver 2.2.0 clause 7.2, Table 7.2-1 as:

Either "R[authority-ID]/[registered-App-ID]" or "N[non-registered-App-ID]"

If the first letter is "R", then authority-ID and registered-App-ID are assigned by the registration authority. The registered-App-ID is managed by the owner of authority-ID.

If the first letter is "N", then non-registered-App-ID is not registered by the registration authority.

Work Item 29 (WI-0029) is to clarify use of App-ID. The new requirements listed below were created by REQ-2015-0585R01 in support of WI-0029.

| Requirement ID | Description | Release |
| --- | --- | --- |
| OPR-a | The format for registered App-IDs shall be able to support use by people and systems to readily determine whether the App-ID is registered and the Registration Authority which issued the App-ID, App Developer and App Name. | 2 |
| OPR-b | The oneM2M System Registration Authorities shall be able to collect and maintain supporting required information when assigning an App-ID. | 2 |

# Proposing a new App-ID Format

Release One defined the registered App-ID in Table 7.2-1 as:

R[authority-ID]/[registered-App-ID]

We propose the following format for App-ID for Release Two:

R[authority-ID]-[applicationRegistrant]-[appName]-{operatingSystem}-{sequenceNo}-{white-label}

The components in square brackets are required for all registered App-IDs. The components in curly braces are optional. The dash is proposed as a separator between components to avoid escaping the forward slash character. Separators are only required when needed to positional identify a component.

The proposed components are:

[authority-ID] aka Registration Authority: Steering Committee Ad Hoc group suggested A1, A2 etc. (authority 1).

[applicationRegistrant]: This is the company, organization or individual that is requesting an App-ID.

[appName] aka appName: application name with spaces removed

[operatingSystem] (optional): Android, iOS, Windows, Linux. Operating System is optional because some applications e.g., HTML app, are independent of OS.

{sequenceNo} (software version – optional): A sequence number is associated to the software version to simplify reference.  Sequence number is optional since not all applications e.g., HTML apps, will have a software version number. The customer will provide a software version, where appropriate. The Registration authority will map the software version to a sequence number.

{white-label} Customer Identifier (optional): Application Registrant can make the white-label customer identifier abstract e.g., A=Comcast, B=Verizon or mnemonic e.g., CC, VZ.

Examples App-IDs

Minimal App-ID: RA1-FJTU-HomeManagement

Complete App-ID: RA1-FJTU-HomeManagement-Win-14-X

Mixed App-ID: RA1-FJTU-HomeManagement--14 (OS is not specified so the position is left blank followed by the sequence number

### -----------------------Start of change 1-------------------------------------------

Either "R[authority-ID]-[applicationRegistrant]-[appName]-{operatingSystem}-{sequenceNo}-{white-label} " or "N[non-registered-App-ID]"

If the first letter is "R", then the App-ID is assigned and managed by the Registration Authority.

If the first letter is "N", then non-registered-App-ID is not registered by the Registration Authority.

### -----------------------End of change 1---------------------------------------------

# Proposing Required Attributes for App-ID

We propose listing App-ID required attributes to Section 7.1.3.

### -----------------------Start of change 2-------------------------------------------

### 7.1.3	Application Identifier (App-ID)

An Application Identifier (App-ID) uniquely identifies an M2M Application in a given context. More precisely, there are two types of App-ID: Registration Authority defined App-ID (registered App-ID) and non-registered App-ID. The establishment of the registered App-ID is guaranteed to be globally unique; the non-registered App-ID is not guaranteed to be globally unique. The detail format is described in clause 7.2.

Registered App-IDs will be stored in an App-ID Registry along with the following required attributes.

- Registration Authority – Registration Authority ID assigned by oneM2M Steering Committee e.g., A1, A2 etc.

- App-ID – automatically generated from required and optional attributes

- Application Registrant – code used to identify the Application Registrant, which may be a company, organization or individual

- Application Name – application name without company or version information and spaces removed

- Application Name (localized) – in native language e.g., Chinese

- Application Description – marketing description of the functionality provided by the application

- Application Status – GA, End of Life, Beta, Test, etc.

- Create Date – date the App-ID was created

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?