| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 18.0 |
| Source:* | KT Corp. (TTA) |
| Date:* | 2015-07-23 |
| Contact:* | Francisco Sang-Eon Kim (kim.sangeon@kt.com) |
| Reason for Change/s:* | The scheduleElemet attribute is not clear to implement requirement TS. |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> |
| CR against: TS/TR* | TS-0001V2.2.0 |
| Clauses/Sub Clauses* | Clause 9.6.9 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

ARC-2015-1965R01 has been discussed for 'OET parameter and Resource Type schedule Release 2' during the ARC 18.0.

It deals with scheduleElements and scheduleType attribute.

## One of the comments is that issues need to be separated. This is about schedulePurpose attribute.

## Background history

The oet (operation execution time) parameter for Request message agreed with ARC-2013-0401R03 at 16th October 2013 and included to TS-0001V0.2.1 at 28th October 2013.

The schedule resource agreed with ARC-2013-0521R02 (11th December 2013) and included to TS-0001V0.3.1 at 18th December 2013.

KT had proposed  and discussed additional element for schedule resource by ARC-2015-1878R01 during the TP17 in May 2015.

## Review schedule resource and related parameter of Request message

TS-0001-V2.2.0 describes operation execution time as one of the paramers in clause 8.1.2 since October 2013.

The followinga are description of operation execution time in TS-0001-V2.2.0.

-----------------------------------------------------

Operation Execution Time: optional operation execution time: indicates the time when the specified operation Operation is to be executed by the target CSE. A target CSE shall execute the specified operation of a Request having its operational execution time indicator set, starting at the operational execution time. If the execution time has already passed or if the indicator is not set, then the specified operation shall be immediately executed, unless the request expiration time, if set, has been reached.

Example usage of operational execution time includes asynchronous distribution of flows, which are to be executed synchronously at the operational execution time.

NOTE 6:	Time-based flows could not supported depending upon time services available at CSEs.

-----------------------------------------------------

The agreed contribution, ARC-2013-0521R02, is described scheduleElement in summary of discussion.

-----------------------------------------------------

A “scheduleElement” is a string comprising 7 fields separated by white space. The allowed values are used together with 6 special characters in each “scheduleElement”

| Field name | Mandatory | Allowed values | Allowed special characters |
| --- | --- | --- | --- |
| Seconds | Yes | 0-59 | * / , - |
| Minutes | Yes | 0-59 | * / , - |
| Hours | Yes | 0-23 | * / , - |
| Day of Month | Yes | 1-31 | * / , - L # |
| Month | Yes | 1-12 or JAN-DEC | * / , - |
| Day of Week | Yes | 0-6 or SUN-SAT | * / , - L # |
| Year | Yes | 1970–2099 | * / , - |

Asterisk ( * )

The asterisk indicates that the expression matches for all values of the field. E.g., using an asterisk in the 5th field (month) indicates every month.

Slash ( / )

Slashes describes periodicity within ranges. For example 3-59/15 in the 2nd field (minutes) indicates the third minute of the hour and every 15 minutes thereafter within the hour. The form "*/..." is equivalent to the form "start range-end range/periodicity", over the range of the field. */2 in the 2nd field (minutes) indicates every other minute. 2013/1 in the 7th field (years) indicates to repeat every year after 2013.

Comma ( , )

Commas are used to separate items of a list. For example, using "MON,WED,FRI" in the 6th field (day of week) means Mondays, Wednesdays and Fridays.

Hyphen ( - )

Hyphens define ranges. For example, 2000-2010 indicates every year between 2000 and 2010 AD, inclusive.

L

'L' stands for "last". When used in the day-of-week 6th field, it allows you to specify constructs such as "the last Friday" ("5L") of a given month. In the day-of-month 4th field, it specifies the last day of the month.

Hash ( # )

'#' is allowed for the day-of-week 6th field, and must be followed by a number between one and five. It allows you to specify constructs such as "the second Friday" of a given month.

-----------------------------------------------------

On the other hand, TS-0004-V1.2.0 is described scheduleElement as follow at clause 7.3.9:

-----------------------------------------------------

The scheduleElement attribute represents the list of scheduled tasks with the time of the execution.

The each entry of the scheduleElelement attribute shall consist of a line with 6 field values (See Table 7.3.8.1-4).

The time to be matched with the schedule pattern shall be interpreted in UTC timezone.

Table 7.3.9.1-4:  Definition of m2m:scheduleEntry string format

| Field Name | Range of values | Note |
| --- | --- | --- |
| Second | 0 to 59 |  |
| Minute | 0 to 59 |  |
| Hour | 0 to 23 |  |
| Day of the month | 1 to 31 |  |
| Month of the year | 1 to 12 |  |
| Day of the week | 0 to 6 | 0 means Sunday |

Each field value can be either an asterisk ('*': matching all valid values), an element, or an elements separated by commas(',').

An element shall be either a number or two numbers separated by a hyphen ('-': matching between two values).

-----------------------------------------------------

ARC-2013-0521R02 agreed six special characters to indicate scheduleElement but it is not clearly stated to TS-0001.

Special characters for scheduleElement described in TS-0004 are asterisk, comma, hyphen.

I would like to propose to use four special character with scheduleElement: asterisk, comma, hyphen and slash.

-----------------------------------------------------

### Resource Type schedule is described as followed at clause 9.6.9 in TS-0001-V2.2.0

A child <schedule> resource of the <CSEBase> and <remoteCSE> resources shall indicate the time periods when the CSE can send and receive the request.

A child <schedule> resource of the <AE> resource shall indicate the time periods when the application of a node can be accessed.

A child <schedule> resource of the <subscription> resource shall indicate the time periods when the notifications can be sent to be Receiver.

A purpose and operation for <schedule> resource is different among  ‘time perios when the CSE  can send and receive the request’,  ‘time periods when the application of a node can be accessed’, ‘time perios when the notifications can be sent to be Receiver’.

A schedule for ‘application of a node can be accessed’ provides only time information without initiation of operation, i.e. passive operation.

A schedule for ‘CSE can send and receiver the request’ and ‘notifications can be sent to be Receiver’ provides time information with operation, i.e. active operation.

## Discussion

Issue 1:

What is meaning of OET parameter  which is specified “operation execution time indicates the time when the specified operation Operation is to be executed by the target CSE.”?

The OET parameter can be used to define time for the future which is scheduled time to excute either CREATE, RETRIEVE, UPDTE, DELETE or NOTIFY. Request message shall be included operation parameter.

Issue 2:

Resource Type <statsCollect> is needed operation (C/R/U/D)  with collectPeriod attribute as specified clause 7.3.25 in TS-0004. TS-0001 is specified <statsCollect> Resource Type at clause 9.6.25

Does the schedule for <statsCollect> have functionality to allow reachability to resource ?

Issue 3:

What kinds of fields are used for scheduleElement ?

Option A: TS-0001 is described 6 fields: second, minute, hour, day of month, month, year

Option B: ARC-2013-0521R02, agreed proposal, is described 7 field: second, minute, hour, day of month, month, day of week, year

Option C: TS-0004 is described 6 field: second, minute, hour, day of month, month of the year, day of week at Table 7.3.9.1-4

|  | second | minute | hour | day of month | month | day of week | year |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Option A TS-0001 | ( | ( | ( | ( | ( |  | ( |
| Option B ARC-2013-0521R02 (Original Proposal) | ( | ( | ( | ( | ( | ( | ( |
| Option C TS-0004 | ( | ( | ( | ( | ( | ( |  |

Issue 4:

What kinds of special characters are used for scheduleElement ?

Option A: 3 special characters are used: Asterisk ( * ), Comma ( , ), Hyphen ( - )

This is described at TS-0004

Option B: 4 or 5 special characters are used: Asterisk ( * ), Slash ( / ), Comma ( , ), Hyphen ( - ) and L

In case of 4 characters, L is expected to exclude due to limited usage.

Option C: 6 special characters are used as proposed by original proposal which is ARC-2013-0521R02.

But, the usage of # is not clear.

If  proposal of ‘change request 1’ is difficult to accept to include clause 9.6.9, I would like to propose to remove ‘Operation Execution Time’ parameter at clause 8.1.2 as ‘change request 2’. Because ‘Operation Execution Time’ paerameter is not used at all. It also can be interpreted ambiguously to use ‘Operation Execution Time’ which is for future time for schedule.

Also, <statsCollect> resource Type should be revised to delete collectPeriod attribute.

-------------

The <statsCollect> resource shall contain the attributes specified in table 9.6.25-2.

Table 9.6.25-2: Attributes of <statsCollect> resource

| Attributes of <statsCollect> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| accessControlPolicyIDs | 1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. |
| creator | 0..1 | RO | The AE-ID of the entity which created the resource. This can also be the CSE-ID of the IN-CSE if the IN-CSE created the resource. |
| statsCollectID | 1 | RO | This is the unique ID to identify a specific statistics collection scenario. It is created by the IN-CSE when the <statsCollect> resource is first created. |
| collectingEntityID | 1 | WO | This is the unique ID of the entity that requests the collection of statistics. For example, it can be an AE-ID or CSE-ID. |
| collectedEntityID | 1 | WO | This is the unique ID of the entity whose request triggered the configured event for statistics collection. For example, it can be an AE-ID or IN-CSE-ID. If no specific value is provided for this attribute, the IN-CSE interprets it as "any entity". |
| statsRuleStatus | 1 | RW | This attribute indicates whether the rule is "active" or "inactive". |
| statModel | 1 | RW | This attribute indicates the collection model, such as "Subscriber based", "event based", etc. |
| collectPeriod | 0..1 | RW | Expresses time periods defined by second, minute, hour day of month, month, and year. Supports repeating periods, and wildcards expressed as a list. |
| eventID | 0..1 | RW | This attribute refers to the <eventConfig> resource that defines the events that can be collected by the IN-CSE. It is mandatory if the statModel attribute is set to "event based". |

## 2nd Discussion: schedulePurpose

Clause 9.6.9 clearly describes usage of the <schedule> resource .

The <schedule> resource contains scheduling information. The usage of the <schedule> resource is slightly different depending on the associated resource type, such as follows:

A child <schedule> resource of the <CSEBase> and <remoteCSE> resources shall indicate the time periods when the CSE can send and receive the request.

A child <schedule> resource of the <AE> resource shall indicate the time periods when the application of a node can be accessed.

A child <schedule> resource of the <subscription> resource shall indicate the time periods when the notifications can be sent to be Receiver.

A <schedule> resource linked as mgmtLink attribute of the <cmdhNwAccessRule> resource shall indicate the time periods when use of specific underlying networks is allowed.

According to the clause 9.6.1.1, Resource Type Summary, there are several resources that have child resource of <schedule> resource.

  - <CSEBase>

  - <remoteCSE>

  - <AE>

  - <subscription>

<statsCollect> resource may have scheduleElement. This is the collectPeriod attribute. Although attribute name is different between scheduleElement and collectPeriod, the meaning is identical.

What is difference of usage between child resource of <schedule> in <CSEBase>, <remoteCSE>, <AE>, <subscription>  resource and scheduleElement attribute in <statsCollect> resource ?

For example, what is difference <statsCollect> resource with child resource of <schedule> compared to <statsCollect> resource with scheduleElement attribute?

Why are different  usage of <schedule> resource and scheduleElemet  attribute?

A <schedule> resource can be used either distributed scheme or centralized scheme

A distributed scheme to use <schedule> resource is combination of other resource e.g. child resource.

A centralized scheme to use <schedule> resource has one <schedule> resource to control scheduled work.

For example, cron table conteol several job with one resource (file).  oneM2M needs to identify operation such as create, retrieve, update, delete and notify  however the cron table controls execution which is one operation.

This contribution is about centralized  control for scheduled work.

In the centralized scheme, information about purpose of schedule and scheduled work is needed.

### -----------------------Start of change 1-------------------------------------------

### 9.6.9	Resource Type schedule

The <schedule> resource contains scheduling information. The usage of the <schedule> resource is slightly different depending on the associated resource type, such as follows:

A child <schedule> resource of the <CSEBase> and <remoteCSE> resources shall indicate the time periods when the CSE can send and receive the request.

A child <schedule> resource of the <AE> resource shall indicate the time periods when the application of a node can be accessed.

A child <schedule> resource of the <subscription> resource shall indicate the time periods when the notifications can be sent to be Receiver.

A <schedule> resource linked as mgmtLink attribute of the <cmdhNwAccessRule> resource shall indicate the time periods when use of specific underlying networks is allowed.

An Originator shall have the same access control privileges to the <schedule> resource as it has to its parent resource.

Figure 9.6.9-1: Structure of <schedule> resource

The <schedule> resource shall contain the child resource specified in table 9.6.9-1.

Table 9.6.9-1: Child resources of <schedule> resource

| Child Resources of <schedule> | Child Resource Type | Multiplicity | Description | <scheduleAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | None |

The <schedule> resource shall contain the attributes specified in table 9.6.9-2.

Table 9.6.9-2: Attributes of <schedule> resource

| Attributes of <schedule> | Multiplicity | RW/ RO/ WO | Description | <scheduleAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | MA |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. | MA |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. | NA |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | MA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. | NA |
| scheduleElement | 1 (L) | RW | Expresses time periods defined by second, minute, hour day of month, month, and year. Supports repeating periods, and wildcards expressed as a list. | OA |
| schedulePurpose | 1 | RW | The purpose of schedule: Allow reachability to resource. Execute operation of scheduled work. | OA |
| scheduledWork | 0..1 | WO | An operation and resource | OA |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?