| CHANGE REQUEST |
| --- |
| Meeting:* | ARC-18.0 |
| Source:* | Qualcomm Incorporated |
| Date:* | 2015-07-13 |
| Contact:* | Josef Blanz (jblanz@qti.qualcomm.com) |
| Reason for Change/s:* | Some details on “Hierarchical” addressing are not specified in Release 1 of TS-0001. While the specification is not broken, it leaves room for ambiguities and may result in long Resource-IDs. This CR suggests to resolve these issues in line with document ARC-2015-xxxx. |
| CR against: Release* | Release 2 |
| CR against: WI* | Active MNT Maintenace STE Small Technical Enhancements / WI-0039 Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 v 2.2.0 |
| Clauses/Sub Clauses* | 7.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

In order to achieve a more efficient and more precise specification on how to construct Resource-IDs for the “Hierarchical” resource addressing method, it is proposed to adopt the following details on ‘Structured-CSE-relative-Resource-ID’ and ‘Unstructured-CSE-relative-Resource-ID’

The ‘Unstructured-CSE-relative-Resource-ID’ shall comply with the following restrictions

- The ‘Unstructured-CSE-relative-Resource-ID’ format of the Resource-ID for the <CSEBase> resource representing the Receiver CSE shall be selected from one of the following

  - the literal “.” (dot),

  - the value of the ‘resourceId’ attribute of that <CSEBase> resource,

  - the value of the ‘resourceName’ attribute of that <CSEBase> resource.

- The ‘Unstructured-CSE-relative-Resource-ID’ of any direct child of the <CSEBase> resource representing the Receiver CSE shall be selected from one of the following

  - the value of the ‘resourceId’ attribute of that resource,

  - the value of the ‘resourceName’ attribute of that resource in case it is not identical to any ‘resourceId’ attribute value of any resource hosted on the Receiver CSE.

- The ‘Unstructured-CSE-relative-Resource-ID’ of any indirect child of the <CSEBase> resource representing the Receiver CSE shall be equal to the value of the ‘resourceId’ attribute of that resource

The ‘Structured-CSE-relative-Resource-ID’ shall comply with the following structure

Structured-CSE-relative-Resource-ID = {parent-segment}/{child-segment}[/{subsequent-child-segment}]

where the following assumptions hold:

- { } denotes a placeholder for a sequence of characters that may include any of the unreserved characters defined in the clause 2.3 of the IETF RFC 3986 [i.12 of TS-0001].

- Each placeholder in { } is termed a “segment” in this context.

- [ ] denotes zero or more occurrences of the argument between [ and ].

- {parent-segment} is the ‘Unstructured-CSE-relative-Resource-ID’ of a parent resource that is the starting ancestor used to address the target resource.

- {child-segment} is equal to the ‘resourceName’ attribute value of the specific child resource – among the children of the resource that is identified by {parent-segment} – which is

  - either the next ancestor on the path to the target resource,

  - or the target resource itself.

- {subsequent-child-segment} is equal to the ‘resourceName’ attribute value of the specific child resource – among the children of the resource that is identified by the “/”-separated concatenation of the previous segments – which is

  - either the next ancestor of the target resource,

  - or the target resource itself.

### -----------------------Start of change 1-------------------------------------------

## 7.2	M2M-SP-ID, CSE-ID, App-ID and AE-ID and resource Identifier formats

As a general rule, the identifiers of AEs, CSEs and resources are globally unique. In order to optimize their use, the identifiers shall be shortened when their scope can be derived from their context of use by the CSEs and the AEs. Such shortened identifiers are defined as 'relative' formats of the identifiers.

TheM2M system shall use the identifiers M2M-SP-ID, CSE-ID, App-ID and AE-ID and resource identifiers according to the formats and the rules specified in the following table (table 7.2-1).

Table 7.2-1: Identifier formats and rules of use

| Identifier Name | Absolute & Format-Designator or Relative & Format-Designator & Context | Format | Rule of use |
| --- | --- | --- | --- |
| M2M-SP-ID | Absolute M2M-SP-ID | The M2M-SP-ID shall conform to the FQDN format s defined in the IETF RFC 1035 [i.9] prefixed by '//' The format then has the structure of //{FQDN} Where {FQDN} is a placeholder for the Fully Qualified Domain Name of the M2M Service Provider Domain Examples: //www.m2mprovider.com //globalm2m.org The following two M2M-SP-IDs could be used to separate two service segments: //automotive.m2m.telematics-service-company.com //building-management.m2m.telematics-service-company.com | Whenever The M2M-SP-ID is used, only an Absolute format of the M2M-SP-ID defined herein applies |
| CSE-ID | Relative SP-relative-CSE-ID Context: M2M-SP Domain hosting the CSE | The SP-relative-CSE-ID begins with a slash character '/' and is followed by a sequence of characters that may include any of the unreserved characters defined in the clause 2.3 of the IETF RFC 3986 [i.12]. The SP-relative-CSE-ID is unique within the context of the M2M-SP Domain hosting the CSE. The M2M-SP is assigning the SP-Relative-CSE-ID and is responsible for guaranteeing that the SP-Relative-CSE-ID is unique in the context of the hosting M2M-SP Domain. Examples: /123A38ZZY /CSE090112 /3ace4fd3 | On the Mca and Mcc reference points: to refer to CSEs that are hosted by the same M2M Service Provider domain. |
|  | Absolute Absolute-CSE-ID | Concatenation according to the format {M2M-SP-ID}{SP-relative-CSE-ID} where {M2M-SP-ID} and {SP-relative-CSE-ID} are placeholders for the M2M-SP-ID and the SP-relative-CSE-ID format of the CSE-ID, respectively. The Absolute-CSE-ID complies with what is specified in clause 3 of RFC3986 [i.12] under "hier-part". Examples: //www.m2mprovider.com /C3219 //m2m.thingscompany.com/ab3f124a | On Mca and Mcc reference points: to refer to CSEs that are hosted by different M2M Service Provider domains and on the Mcc' reference point for all the CSEs |
| AE-ID | Relative AE-ID-Stem Context: Registrar CSE of the AE or M2M-SP Domain hosting the AE | The AE-ID-Stem is a sequence of characters that may include any of the unreserved characters defined in the clause 2.3 of the IETF RFC 3986 [i.12]. The first character of the AE-ID-Stem has a specific meaning and its value shall be as follows: Fist character of AE-ID-Stem is 'C' The AE-ID-Stem is assigned by the Registrar CSE of the AE. In this case, the AE-ID-Stem shall be unique within the context of the Registrar CSE of the AE. The Hosting CSE is responsible for guaranteeing that the AE-ID-Stem is unique in the context of the Hosting CSE. Examples: C190XX7T Ca3e3f3ab Fist character of AE-ID-Stem is 'S': The AE-ID-Stem is assigned by the M2M-SP. In this case, the AE-ID-Stem shall be unique within the context of the M2M-SP Domain. The M2M-SP is responsible for guaranteeing that the AE-ID-Stem is unique in the context of the M2M-SP Domain. Examples: S190XX7T Sa3e3f3ab Use of other values for the first character of AE-ID-Stem is reserved. Which of the cases above shall apply will be determined during the AE registration procedure. The details of the process how an AE-ID-Stem unique within the M2M-SP Domain is assigned by the M2M-SP are described in the AE registration procedure description. | On the Mca reference point: To refer to AEs that registered to the CSE where the Originator is registered. |
|  | Relative SP-relative-AE-ID Context: M2M-SP Domain hosting the AE | In the case the AE-ID-Stem starts with the letter 'C', the SP-relative-AE-ID is a concatenation according to the format {SP-relative-CSE-ID}/{AE-ID-Stem} where {SP-relative-CSE-ID} and {AE-ID-Stem} are placeholders for the SP-relative-CSE-ID of the Registrar CSE of the AE and the AE-ID-Stem format of the AE-ID, respectively. Examples: /CSE090112/ C190XX7T /3ace4fd3/ Ca3e3f3ab In the case the AE-ID-Stem starts with the letter 'S', the AE-ID-Stem is unique within the M2M-SP Domain. In that case the SP-relative-AE-ID is a concatenation according to the format /{AE-ID-Stem} where {AE-ID-Stem} is a placeholders for the AE-ID-Stem format of the AE-ID. Examples: /S190XX7T /Sa3e3f3ab The SP-relative-AE-ID begins with a slash character '/', and it complies with what is specified in clause 4.2 of IETF RFC 3986 [i.12] under "absolute-path reference". | On the Mca and Mcc reference points: To refer to AEs that are registered with other CSEs than the one of the Originator of the request but hosted by the M2M Service Provider domain to which Originator is attached. |
|  | Absolute Absolute-AE-ID | The Absolute-AE-ID format of the AE-ID is a concatenation according to the format: {M2M-SP-ID}{SP-relative-AE-ID} where {M2M-SP-ID} and {SP-relative-AE-ID} are placeholders for the M2M-SP-ID and the SP-relative-AE-ID format of the AE-ID, respectively. The absolute AE-ID complies with what is specified in clause 3 of IETF RFC 3986 [i.12] under "hier-part". Examples: //m2m.prov.com /CSE3219/C9886 //m2m.things.com/ab3f124a/Ca2efb3f4 //m2m.things.com/S98821 | On the Mca and Mcc reference points: to refer to AEs that are hosted by a different M2M Service Provider domain with respect to the one to which the Originator of a request is attached and on the Mcc' reference point for all the AEs |
| Resource identifier | Relative Unstructured-CSE-relative-Resource-ID Context: CSE hosting the Resource | An Unstructured-CSE-relative-Resource-ID is a sequence of characters that may include any of the unreserved characters defined in the clause 2.3 of the IETF RFC 3986 [i.12]. An Unstructured-CSE-relative-Resource-ID is unique in the context of the CSE hosting the resource. The Hosting CSE of the resource is responsible for guaranteeing that Unstructured-CSE-relative-Resource-IDs are unique in the context of the Hosting CSE. More details on valid methods to construct an Unstructured-CSE-relative-Resource-ID format of a resource identifier are specified in Clause 9.3.1 . The Unstructured-CSE-relative-Resource-ID for resource types other than <AE> or <AEAnnc> shall not start with any of the reserved characters stated in the AE-ID definition. Examples: container123 a1b2c3d4b0b00f0fa66a123456789abc xxyz1234 | On the Mca reference point: To refer to resources that are hosted by the CSE receiving a request targeting a resource. |
|  | Relative Structured-CSE-relative-Resource-ID Context: CSE hosting the Resource | A Structured-CSE-relative-Resource-ID is a sequence of characters that may include any of the unreserved characters defined in the clause 2.3 of the IETF RFC 3986 [i.12], as well as the slash character. It shall not start with the slash character. A Structured-CSE-relative Resource-ID is unique in the context of the CSE hosting the resource. The structure represents a chain of parent-child-relationships using resource IDs or resource names of parents and resource names of their children for segments that are separated by the '/' character. The Hosting CSE of the resource is responsible for guaranteeing that resource names – which are used to construct Structured-CSE-relative-Resource-ID formats – are unique in the context of a set of sibling resources sharing the same parent resource on the Hosting CSE. More details on valid methods to construct a Structured-CSE-relative-Resource-ID format of a resource identifier are specified in Clause 9.3.1 . Example: streetX/houseY/roomZ/temperature CA/San_Diego/Mira_Mesa/trafficFlow | On the Mca reference point: To refer to resources that are hosted by the CSE receiving a request targeting a resource. |
|  | Relative SP-relative Resource-ID Context: M2M-SP Domain hosting the Resource | Concatenation according to the format: {SP-relative-CSE-ID}/{Unstructured-CSE-relative Resource ID} {SP-relative-CSE-ID}/{Structured-CSE-relative Resource ID} where {SP-relative-CSE-ID}, {Unstructured-CSE-relative Resource ID}, {Structured-CSE-relative Resource ID} are placeholders for the SP-relative-CSE-ID format of the CSE-ID and the Unstructured-CSE-relative-Resource-ID or a Structured-CSE-relative-Resource-ID format of the Resource ID, respectively. The SP-relative-Resource-ID begins with a slash character, and it complies with what is specified in clause 4.2 of IETF RFC 3986 [i.12] under "absolute-path reference". The SP-relative Resource ID is unique in the context of the Service Provider. Examples: /CSE987776/a234361 /af542a/ CA/San_Diego/Mira_Mesa /abcCSE/ streetX/houseY/roomZ/temp | On the Mca and Mcc reference points: to refer to resources that are hosted by the same M2M Service Provider domain as the M2M SP domain hosting the CSE receiving a request for accessing the resource. |
|  | Absolute Absolute Resource ID | Concatenation according to the format: {M2M-SP-ID}{SP-relative Resource ID} where {M2M-SP-ID} and {SP-relative Resource ID} are placeholders for the M2M-SP-ID and the SP-relative Resource ID format of the Resource ID, respectively. The Absolute-CSE-ID complies with what is specified in clause 3 of IETF RFC 3986 [i.12] under "hier-part". Examples: //m2m.thing.com/xyzCSE/x3z5r43 //m2m.iot.com/ab13/HouseA/RoomB/Temp | On Mca and Mcc reference points: to refer to resources that are hosted by a different M2M Service Provider domain than the M2M SP domain hosting the CSE receiving a request for accessing the resource. and on the Mcc' reference point for all resources |
| APP-ID | App-ID | Either "R[authority-ID]/[registered-App-ID]" or "N[non-registered-App-ID]" If the first letter is "R", then authority-ID and registered-App-ID are assigned by the registration authority. The registered-App-ID is managed by the owner of authority-ID. If the first letter is "N", then non-registered-App-ID is not registered by the registration authority. | AE Registration Procedure described in clause 10.1.1.2.2. |

The Registrar CSE of an AE shall convert between a Registree AE's SP-relative  and CSE-relative identifier (=AE-ID-Stem) according to table 7.2-1 when a request issued on the Mca reference point is forwarded across the Mcc  reference point.

As a consequence, the IN-CSE shall convert AE's, CSEs and resource's absolute and AP- or CSE-relative identifiers according to table 7.2-1when a request is transmitted across the Mcc' reference point.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## 9.3	Resource Addressing

### 9.3.1	Generic Principles

An address of a resource is a string of characters used to uniquely identify the targeted resource within the scope of a request to access the resources. The scope of a request can be:

CSE-relative: The request is targeting a resource that resides on the same CSE as the Receiver CSE of the request. In that case a CSE-relative format of a resource ID can be used to address the resource.

SP-relative: The request is targeting a resource that resides on a CSE within the same M2M SP domain as the Originator of the request. In that case an SP-relative format of a resource ID can be used to address the resource.

Absolute: The request is targeting a resource that resides on a CSE that is within an M2M SP domain that is different from the M2M SP domain of the Originator of the request. In that case the absolute format of a resource ID shall be used to address the resource. Note that the absolute format of the resource ID will always be acceptable also in other cases.

A single resource may have more than one way of constructing a resource ID, via which access to the resource can be provided.

There are two different methods for addressing a resource within the oneM2M resource structure with three different variants each depending on the scope of the request to access the resource. The ways how the resource IDs shall be constructed in each case are as follows.

Table 9.3.1-1 Resource addressing methods

| Method | Request Scope |
| --- | --- |
|  | CSE-Relative | SP-Relative | Absolute |
| Non-Hierarchical | Use the 'Unstructured-CSE-relative -Resource-ID' format of the resource ID as defined in table 7.2-1. | Use the 'SP-relative Resource-ID' format of the resource ID constructed with the 'Unstructured-CSE-relative-Resource-ID' as defined in table 7.2-1. | Use the 'Absolute-Resource-ID' format of the resource ID constructed with the 'Unstructured-CSE-relative -Resource-ID' as defined in table 7.2-1. |
| Hierarchical | Use the 'Structured-CSE-relative -Resource-ID' format of the resource ID as defined in table 7.2-1. | Use the 'SP-relative Resource-ID' format of the resource ID constructed with the 'Structured-CSE-relative-Resource-ID' as defined in table 7.2-1. | Use the 'Absolute-Resource-ID' format of the resource ID constructed with the 'Structured-CSE-relative-Resource-ID' as defined in table 7.2-1. |

These two methods with three variants shall all be supported by all M2M Nodes, notably the CSEs receiving requests, before they proxy these requests any further, where applicable.

The ‘Unstructured-CSE-relative-Resource-ID’ as defined in table 7.2-1 shall comply with the following restrictions. Note that these restrictions need to rely on terminology (resource types and resource attributes) that are defined in Clause 9.6

- The ‘Unstructured-CSE-relative-Resource-ID’ format of the resource ID of a <CSEBase> resource representing the Receiver CSE shall be selected from one of the following

  - the literal “.” (dot),

  - the value of the resourceId attribute of that <CSEBase> resource,

  - the value of the resourceName attribute of that <CSEBase> resource.
	
In order to avoid any ambiguities in addressing resources, the value of the resourceName attribute of that <CSEBase> resource shall not be identical to any resourceId attribute value of any resource hosted on the Receiver CSE

- The ‘Unstructured-CSE-relative-Resource-ID’ of an indirect child of the <CSEBase> resource representing the Receiver CSE shall be equal to the value of the resourceId attribute of that resource

- The ‘Unstructured-CSE-relative-Resource-ID’ of any direct child of the <CSEBase> resource representing the Receiver CSE shall be selected from one of the following

  - the value of the resourceId attribute of that direct child resource,

  - the value of the resourceName attribute of that direct child resource 

In case the value of the resourceName attribute of that direct child resource is identical to any resourceId attribute value of any resource hosted on the Receiver CSE, using this value as an ‘Unstructured-CSE-relative-Resource-ID’ will result in addressing the resource that got this value assigned in the resoureId attribute.

For hierarchical addressing the resource ID of a known ancestor of the targeted resource shall be used in combination with one or more resourceName attribute values of child or sub-child resource(s) to represent parent-child relationships of resources for all of the above request scopes. The following rules for constructing the ‘Structured-CSE-relative-Resource-ID’ format used in hierarchical addressing of a resource shall apply:

Structured-CSE-relative-Resource-ID = {parent-segment}/{child-segment}[/{subsequent-child-segment}]

where the following assumptions hold:

- { } denotes a placeholder for a sequence of characters that may include any of the unreserved characters defined in the clause 2.3 of the IETF RFC 3986 [i.12], see also table 7.2-1.

- Each placeholder in { } is termed a “segment” in this context.

- [ ] denotes zero or more occurrences of the argument between [ and ].

- {parent-segment} is the ‘Unstructured-CSE-relative-Resource-ID’ of a parent resource that is the starting ancestor used to address the target resource with hierarchical addressing.

- {child-segment} is equal to the resourceName attribute value of the specific child resource – among the children of the resource that is identified by {parent-segment} – which is

  - either the next ancestor on the path to the target resource,

  - or the target resource itself.

- {subsequent-child-segment} is equal to the resourceName attribute value of the specific child resource – among the children of the resource that is identified by the “/”-separated concatenation of the previous segments – which is

  - either the next ancestor of the target resource,

  - or the target resource itself.

  - Examples for resource addressing are given in Annex XXX.

The CSE-ID of the particular CSE that is represented by a specific instance of a <CSEBase> resource, which is the first segment in the path portion of an SP-relative or Absolute format of a Resource, allows to easily distinguish different CSEs on the same IP host.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3---------------------------------------------

# Annex XXX (informative):
Resource addressing examples

## XXX.1	Example resource tree

## In this Annex, a set of resources organized according to the resource tree depicted in Figure XXX.1-1 is assumed. The depicted resources are assumed to be hosted on a CSE with SP-relative-CSE-ID equal to “/IN-CSE-0001”. Furthermore, the M2M-SP-ID is assumed to be “//m2m.service.com”.

### Figure XXX.1-1

### XXX.2 Valid resource IDs

Table XXX.2-1 Addressing  (resourceId=”00000004”, resourceName=”00000005”)

| Scope | Method |
| --- | --- |
|  | Non-Hierarchical | Hierarchical |
| CSE-Relative | 00000004 | ./00000005 bigFatCse/00000005 00000000/00000005 |
| SP-Relative | /IN-CSE-0001/00000004 | /IN-CSE-0001/./00000005 /IN-CSE-0001/bigFatCse/00000005 /IN-CSE-0001/00000000/00000005 |
| Absolute | //m2m.service.com/IN-CSE-0001/00000004 | //m2m.service.com /IN-CSE-0001/./00000005 //m2m.service.com /IN-CSE-0001/bigFatCse/00000005 //m2m.service.com/IN-CSE-0001/00000000/00000005 |

Table XXX.2-2 Addressing  (resourceId=”00000007”, resourceName=”roomTemperature”)

| Scope | Method |
| --- | --- |
|  | Non-Hierarchical | Hierarchical |
| CSE-Relative | 00000007 | ./00000005/roomTemperature bigFatCse/00000005/roomTemperature 00000000/00000005/roomTemperature 00000004/roomTemperature |
| SP-Relative | /IN-CSE-0001/00000007 | /IN-CSE-0001/./00000005/roomTemperature /IN-CSE-0001/bigFatCse/00000005/roomTemperature /IN-CSE-0001/00000000/00000005/roomTemperature /IN-CSE-0001/00000004/roomTemperature |
| Absolute | //m2m.service.com/IN-CSE-0001/00000007 | //m2m.service.com/IN-CSE-0001/./00000005/roomTemperature //m2m.service.com/IN-CSE-0001/bigFatCse/00000005/roomTemperature //m2m.service.com/IN-CSE-0001/00000000/00000005/roomTemperature //m2m.service.com/IN-CSE-0001/00000004/roomTemperature |

Table XXX.2-3 Addressing  (resourceId=”00000006”, resourceName=”roomTemperature”) :

| Scope | Method |
| --- | --- |
|  | Non-Hierarchical | Hierarchical |
| CSE-Relative | 00000006 | building-0001/floor-01/kitchen/roomTemperature ./building-0001/floor-01/kitchen/roomTemperature bigFatCse/building-0001/floor-01/kitchen/roomTemperature 00000000/building-0001/floor-01/kitchen/roomTemperature 00000001/floor-01/kitchen/roomTemperature 00000002/kitchen/roomTemperature 00000005/roomTemperature |
| SP-Relative | /IN-CSE-0001/00000006 | /IN-CSE-0001/building-0001/floor-01/kitchen/roomTemperature /IN-CSE-0001/./building-0001/floor-01/kitchen/roomTemperature /IN-CSE-0001/bigFatCse/building-0001/floor-01/kitchen/roomTemperature /IN-CSE-0001/00000000/building-0001/floor-01/kitchen/roomTemperature /IN-CSE-0001/00000001/floor-01/kitchen/roomTemperature /IN-CSE-0001/00000002/kitchen/roomTemperature /IN-CSE-0001/00000005/roomTemperature |
| Absolute | //m2m.service.com/IN-CSE-0001/00000006 | //m2m.service.com/IN-CSE-0001/building-0001/floor-01/kitchen/roomTemperature //m2m.service.com/IN-CSE-0001/./building-0001/floor-01/kitchen/roomTemperature //m2m.service.com/IN-CSE-0001/bigFatCse/building-0001/floor-01/kitchen/roomTemperature //m2m.service.com/IN-CSE-0001/00000000/building-0001/floor-01/kitchen/roomTemperature //m2m.service.com/IN-CSE-0001/00000001/floor-01/kitchen/roomTemperature //m2m.service.com/IN-CSE-0001/00000002/kitchen/roomTemperature //m2m.service.com/IN-CSE-0001/00000005/roomTemperature |

Table XXX.2-4 Addressing  (resourceId=”00000005”, resourceName=”kitchen”) :

| Scope | Method |
| --- | --- |
|  | Non-Hierarchical | Hierarchical |
| CSE-Relative | 00000005 | building-0001/floor-01/kitchen ./building-0001/floor-01/kitchen bigFatCse/building-0001/floor-01/kitchen 00000000/building-0001/floor-01/kitchen 00000001/floor-01/kitchen 00000002/kitchen |
| SP-Relative | /IN-CSE-0001/00000005 | /IN-CSE-0001/building-0001/floor-01/kitchen /IN-CSE-0001/./building-0001/floor-01/kitchen /IN-CSE-0001/bigFatCse/building-0001/floor-01/kitchen /IN-CSE-0001/00000000/building-0001/floor-01/kitchen /IN-CSE-0001/00000001/floor-01/kitchen /IN-CSE-0001/00000002/kitchen |
| Absolute | //m2m.service.com/IN-CSE-0001/00000005 | //m2m.service.com/IN-CSE-0001/building-0001/floor-01/kitchen //m2m.service.com/IN-CSE-0001/./building-0001/floor-01/kitchen //m2m.service.com/IN-CSE-0001/bigFatCse/building-0001/floor-01/kitchen //m2m.service.com/IN-CSE-0001/00000000/building-0001/floor-01/kitchen //m2m.service.com/IN-CSE-0001/00000001/floor-01/kitchen //m2m.service.com/IN-CSE-0001/00000002/kitchen |

Table XXX.2-5 Addressing  (resourceId=”00000001”, resourceName=”building-0001”) :

| Scope | Method |
| --- | --- |
|  | Non-Hierarchical | Hierarchical |
| CSE-Relative | 00000005 building-0001 | ./building-0001 bigFatCse/building-0001 00000000/building-0001 |
| SP-Relative | /IN-CSE-0001/00000005 /IN-CSE-0001/building-0001 | /IN-CSE-0001/./building-0001 /IN-CSE-0001/bigFatCse/building-0001 /IN-CSE-0001/00000000/building-0001 |
| Absolute | //m2m.service.com/IN-CSE-0001/00000005 //m2m.service.com/IN-CSE-0001/building-0001 | //m2m.service.com/IN-CSE-0001/./building-0001 //m2m.service.com/IN-CSE-0001/bigFatCse/building-0001 //m2m.service.com/IN-CSE-0001/00000000/building-0001 |

Table XXX.2-6 Addressing  (resourceId=”IN-CSE-0001”, resourceName=”bigFatCse”) :

| Scope | Method |
| --- | --- |
|  | Non-Hierarchical | Hierarchical |
| CSE-Relative | . bigFatCse 00000000 | N/A |
| SP-Relative | /IN-CSE-0001/. /IN-CSE-0001/bigFatCse /IN-CSE-0001/00000000 | N/A |
| Absolute | //m2m.service.com/IN-CSE-0001/. //m2m.service.com/IN-CSE-0001/bigFatCse //m2m.service.com /IN-CSE-0001/00000000 | N/A |

### -----------------------End of change 3---------------------------------------------

# Comments

This paragraph is subject to another CR in ARC-2015-2020