| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 18 |
| Source:* | KT |
| Date:* | 2015-07-21 |
| Contact:* | JongHoon Han (jonghoon.han@kt.com) Francisco Sang-Eon Kim (kim.sangeon@kt.com) |
| Reason for Change/s:* | There is an ambiguous Response message when the result of operation is larger than value of the limit condition of filterCriteria. |
| CR against: Release* | Release-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001-V2.2.0 |
| Clauses/Sub Clauses* | 8.1.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

There is an ambiguous Response message when the result of operation is larger than value of the limit condition of filterCriteria in R, U and D Request message.

For example the Originator send a request to the Receiver as below:

GET/root?label=one&limit=128

- Case 1. The Receiver have 100 resources matching the logical condition as label=one.

  - It works very well because the number of matching resources is less than 128.

  - The Reciever sends a Response message including retrieved result with successful Response Code.

- Case 2. The Receiver have 128 resources matching the logical condition as label=one.

  - It works very well because the number of matching resources is 128.

  - The Receiver sends a Response message including retrieved result sith successful Response Code.

- Case 3. The Receiver have 150 resources matching the logical condition as label=one.

  - The Receiver sends a Response messge including 128 maximum resources according to the Retrieve operation and successful Response Code.

  - Problem 1. A resource, that the Originator expected, might not include in the Content because there is no explanation of which resources should be included in Content parameter. Even if the Originator sends the same request to the Receiver, the Content of Response message can vary depending on the state of the Receiver.

For example the Originator send a request to the Receiver as below:

PUT/root?label=one&limit=128

- Case 1. The Receiver has 100 resources matching the logical condition as label=one.

  - It works very well because number of matching resources is less than 128.

  - The Reciever updates all of the matching resources. Then the Receiver sends a Response message with information of update operation and successful Response Code.

- Case 2. The Receiver has 128 resoures matching the logical condition as label=one.

  - It works very well because the number of matching resources is 128.

  - The Reciever updates all of the matching resources. Then the Reciever sends a Response message with information of update operation and successful Response Code.

- Case 3. The Receiver have 150 resoures matching the logical condition as label=one.

  - Problem: After updating up to 128 resources among the matched resources, the Receiver sends a Response message with information of update operation result and successful Response Code. The resources, the Originator expected, might not be updated. In this case is this process successful or unsuccessful?

In both case 3, it is hard to say that these processes are successful.  To solve these ambiguous problems, partialSsuccessful is added into the Response Code of Response message and additional information about operation result is also added into the Content of Response message.

#### -----------------------Start of change 1-------------------------------------------

### 8.1.3	Response

The Response received by the Originator of a Request accessing resources over the Mca and Mcc reference points shall contain mandatory and may contain optional parameters. Certain parameters may be mandatory or optional depending upon the Requested operation (CRUDN) or the mandatory response code. In this clause, the mandatory parameters are detailed first, followed by those that are conditional, and then by those that are optional:

Mandatory Parameters:

Response Code: response code: This parameter indicates whether the requested operation was successful, unsuccessful, partialSuccessful or is an acknowledgement:

A successful code indicates to the Originator that the Requested operation has been executed successfully by the Hosting CSE.

An unsuccessful code indicates to the Originator that the Requested operation has not been executed successfully by the Hosting CSE.

An partialSuccessful code indicates to the Originator that the Requested operation has been executed partial successfully by the Hosting CSE.

An acknowledgement indicates to the Originator that the Request has been received and accepted by the attached CSE, i.e. by the CSE that received the Request from the issuing Originator directly, but the Request operation has not been executed yet. The success or failure of the execution of the Requested operation is to be conveyed later.

Details of successful, unsuccessful and acknowledge codes are provided in clause 6.8 of oneM2M Protocol Specification (TS-0004) [i.2].

Request Identifier: Request Identifier. The Request Identifier in the Response shall match the Request Identifier in the corresponding Request.

Conditional Parameters:

Content: resource content:

If Response Code is successful then:

The Content parameter may be present in a Response in the following cases:

Create (C): Content is the address and/or the content of the created resource depending on Result Content value (i.e. attributes, address and address+attributes).

Update (U): Content is the content replaced in an existing resource. If attributes are created at an existing resource, Content includes the names of the attributes created and their associated values. If attributes are updated at an existing resource, Content includes the names of the attributes updated and their associated values. If attributes are deleted at an existing resource, Content includes the names of the attributes deleted.

Delete (D): Optionally, Content is the content actually deleted.

The Content parameter shall be present in a Response in the following cases:

Retrieve (R): Content is the retrieved resource content or aggregated contents of discovered resources.

If present in the Request, Result Content, indicates which components of the result of the requested operation are to be included in the Response.

If Response Code is unsuccessful then the Content parameter may be present in a Response to provide more error information.

If Response Code is partialSuccessful then the Content parameter may be present in a Response to provide partially successful results and additional information. Partially successful results are the result of completed operation at the Receiver. Additional information is the remaining resource information after requested operation has been executed partial successfully.

If Response Code is acknowledgment then the Content parameter:

Shall contain the address of a <request> resource if the response was an acknowledgement of a non-blocking request and the <request> resource type is supported by the Receiver CSE.

Is not present otherwise.

Optional parameters:

To: ID of the Originator or the Transit CSE .

From: ID of the Receiver.

The To and From parameters can be used in the response for specific protocol bindings (e.g., MQTT)

Originating Timestamp: originating timestamp of when the message was built.

Result Expiration Timestamp: result expiration timestamp. The Receiver shall echo the result expiration timestamp if set in the Request message, or may set the result expiration timestamp itself.

Example usage of the Receiver setting the result expiration timestamp is when the value of the delivery time is dependent upon some changing Receiver context e.g. Result message deadline for aircraft position based upon velocity.

Event Category: event category: Indicates the event category that should be used to handle this response. The definition of event category is the same as in the case of requests in clause 8.1.2.

Example usage of "event category" set to specific value X: When the response is targeted to an entity that is different from the Transit CSE currently processing the response message and is not an AE registered with the Transit CSE that is currently processing the response message, the response may be stored in the Transit CSE that is currently processing the response on the way to the destination of the response message until it is allowed by provisioned policies for that event category X to use a communication link to reach the next CSE on a path to the destination of the response message or until the result expiration timestamp is expired.

Status Code: status code of the Response (e.g. authorization timeout, etc.).

Table 8.1.3-1 summarizes the parameters specified in this clause for the Response messages, showing any differences as applied to successful C, R, U, D or N operations, and unsuccessful operations. "M" indicates mandatory, "O" indicates optional, "N/A" indicates "not applicable".

Table 8.1.3-1: Summary of Response Message Parameters

| Response message parameter/success or not | Response Code = Ack | Response Code = successful: Operation = Create | Response Code = successful: Operation = Retrieve | Response Code = successful. Operation = Update | Response Code = successful. Operation = Delete | Response Code = successful Operation = Notify | Response Code = unsuccessful Operation = C,R,U,D or N | Response Code = partialSuccessful Operation = R, U or D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Response Code - successful, unsuccessful, partialSuccessful, ack | M | M | M | M | M | M | M | M |
| Request Identifier - uniquely identifies a Request message | M | M | M | M | M | M | M | M |
| Content - to be transferred | O (address of <request> resource if response is ACK of a non-blocking request) | O (The address and/or the content of the created resource) | M (the retrieved resource content or aggregated contents of discovered resources) | O (The content replaced in an existing resource. The content of the new attributes created. The name of the attributes deleted.) | O (The content actually deleted) | N/A | O (Additional error info) | M (Partially successful result and additional info) |
| To - the identifier of the Originator or the Transit CSE that sent the corresponding non-blocking request | O | O | O | O | O | O | O | O |
| From - the identifier of the Receiver | O | O | O | O | O | O | O | O |
| Originating Timestamp - when the message was built | O | O | O | O | O | O | O | O |
| Result Expiration Timestamp - when the message expires | O | O | O | O | O | N/A | O | O |
| Event Category - what event category shall be used for the response message | O | O | O | O | O | O | O | O |
| Status Code - (e.g. authorization timeout, etc.) | O | O | O | O | O | O | O | O |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?