| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 19.0 |
| Source:* | FUJITSU |
| Date:* | 2015-08-28 |
| Contact:* | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com |
| Reason for Change/s:* | <exact change/s to be provided below> |
| CR against: Release* | Release-2 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 V2.3.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Existing DMR Common Function (<container> and <contentInstance>) does not meet the requirements:

| OSR-090 | The oneM2M System shall be able to forward the M2M Application Data to M2M Application without storing the data. |  |
| --- | --- | --- |
| OSR-091 | The oneM2M System shall be able to notify interested oneM2M entities when it detects forwarded M2M Application Data was not delivered within expected time duration. |  |

### -----------------------Start of change 1-------------------------------------------

### 6.2.3	Data Management and Repository

#### 6.2.3.1	General Concepts

One of the purposes of CSEs is to enable AEs to exchange data with each other.

The Data Management and Repository (DMR) CSF is responsible for providing data storage and mediation functions. It includes the capability of collecting data for the purpose of aggregating large amounts of data, converting this data into a specified format, and storing it for analytics and semantic processing. The data can be either raw data transparently retrieved from an M2M Device, or processed data which is calculated and/or aggregated by M2M entities.

NOTE:	Collection of large amounts of data is known as the Big Data Repository and is not part of the present document.

#### 6.2.3.2	Detailed Descriptions

The DMR CSF provides the capability to store data such as Application data, subscriber information, location information, device information, semantic information, communication status, access permission, etc. The data stored by the DMR CSF enables management of the data and provides the foundation of Big Data.

The following are examples of DMR CSF functionalities:

- Ability to store data in an organized fashion so it is discernible. This includes storage of contextual information such as data types, semantic information, time stamps, location, etc., to complement the data stored in order to access and search the data based on a set of parameters. This is part of data semantics capability which is not part of the present document.

- Provides the means to aggregate data received from different entities.

- Ability to grant access to data from remote CSEs and AEs based on defined access control policies, and trigger data processing based on data access.

- Ability to provide the means to perform data analytics on large amount of data to allow service providers to provide value-added services.

- Ability to forward M2M data from an AE to another AE without storing it.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 9.6.x	Resource Type dataSink

The <dataSink> resource represents a data sik for M2M Applications. It is used to forward M2M data from a M2M application to other AEs. When an AE NOTIFYed  M2M data against a <dataSink> resource, then subscriber of <dataSink> resource will be NOTIFYed with the M2M data.

Figure 9.6.x-1: Structure of <dataSink> resource

The <dataSink > resource shall contain the child resources specified in table 9.6.x-1.

Table 9.6.x-1: Child resources of <dataSink> resource

| Child Resources of <dataSink > | Child Resource Type | Multiplicity | Description |  |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 |  |

The <dataSink> resource shall contain the attributes specified in table 9.6.x-2.

Table 9.6.x-2: Attribute of <dataSink> resource

| Attributes of <container> | Multiplicity | RW/ RO/ WO | Description |  |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |  |
| resourceID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |  |
| resourceName | 1 | WO | See clause 9.6.1.3 where this common attribute is described. |  |
| parentID | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |  |
| expirationTime | 1 | RW | See clause 9.6.1.3 where this common attribute is described. |  |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 where this common attribute is described. If no accessControlPolicyIDs are provided at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute |  |
| labels | 0..1 (L) | RW | See clause 9.6.1 where this common attribute is described. |  |
| creationTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |  |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |  |
| stateTag | 1 | RO | See clause 9.6.1.3 where this common attribute is described. |  |
| creator | 0..1 | RO | The AE-ID or CSE-ID of the entity which created the resource. |  |
| maxSubscribers | 0..1 | RO | Maximum number of direct child <subscription> resources in the <dataSink> resource. |  |
| maxPayloadSize | 0..1 | RO | Maximum size in bytes of data to be NOTIFYed. |  |
| ontologyRef | 0..1 | RW | A reference (URI) of the ontology used to represent the information that to be NOTIFYed. |  |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 10.2.x	<dataSink> Resource Procedures

#### 10.2.x.1	Create <dataSink>

This procedure shall be used for creating a <dataSink> resource.

Table 10.2.x.1-1: <container> CREATE

| <container> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: Content: The resource content shall provide the information as defined in clause 9.6.6 |
| Processing at Originator before sending Request | According to clause 10.1.1.1 |
| Processing at Receiver | According to clause 10.1.1.1 |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: Address of the created <container> resource, according to clause 10.1.1.1 |
| Processing at Originator after receiving Response | According to clause 10.1.1.1 |
| Exceptions | According to clause 10.1.1.1 |

#### 10.2.4.2	Retrieve <dataSink>

This procedure shall be used for retrieving the attributes of a <dataSink> resource.

Table 10.2.x.2-1: <container> RETRIEVE

| <container> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: Content: void |
| Processing at Originator before sending Request | According to clause 10.1.2 |
| Processing at Receiver | According to clause 10.1.2 |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: attributes of the <container> resource as defined in clause 9.6.6 |
| Processing at Originator after receiving Response | According to clause 10.1.2 |
| Exceptions | According to clause 10.1.2 |

#### 10.2.4.3	Update <dataSink >

This procedure shall be used for updating the attributes and the actual data of a <dataSink> resource.

Table 10.2.4.3-1: <dataSink > UPDATE

| <dataSink > UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: Content: attributes of the <dataSink> resource as defined in clause 9.6.x which need be updated |
| Processing at Originator before sending Request | According to clause 10.1.3 |
| Processing at Receiver | According to clause 10.1.3 |
| Information in Response message | According to clause 10.1.3 |
| Processing at Originator after receiving Response | According to clause 10.1.3 |
| Exceptions | According to clause 10.1.3 |

#### 10.2.x.4	Delete <dataSink>

This procedure shall be used for deleting a <dataSink > resource.

Table 10.2.4.4-1: <dataSink> DELETE

| <dataSink> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 apply |
| Processing at Originator before sending Request | According to clause 10.1.4.1 |
| Processing at Receiver | According to clause 10.1.4.1 with the following: If the IN-CSE is the receiver and it has created an entry in the DNS to allow access to the CSE across multiple M2M domains, then it shall delete the entry from the DNS |
| Information in Response message | According to clause 10.1.4.1 |
| Processing at Originator after receiving Response | According to clause 10.1.4.1 |
| Exceptions | According to clause 10.1.4.1 |

#### 10.2.x.5	Notify <dataSink>

This procedure shall be used for notifying a <dataSink> resource.

Table 10.2.13.8-1: <dataSink> NOTIFY

| <dataSink> NOTIFY |
| --- |
| Associated Reference Point | Mca, Mcc, and Mcc’ |
| Information in Request message | All parameters defined in table 8.1.2-2 apply with the specific details for: To: Address of <dataSink> resource Content: The M2M data to be forwared to the subsriber of <dataSink> resource. See TS-0004 for details about the data format to be specified. |
| Processing at Originator before sending Request | According to clause 10.1.5. |
| Processing at Receiver | According to clause 10.1.5 with following: Hosting CSE shall NOTIFY the received content for each subscriber of the <dataSink>. |
| Information in Response message | All parameters defined in table 8.1.3-1 apply. |
| Processing at Originator after receiving Response | According to clause 10.1.5. |
| Exceptions | According to clause 10.1.5. |

### -----------------------End of change 3---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

REQ-2015-0622R02

REQ-2015-0622R02