| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#19.0 |
| Source:* | ZTE Corporation (CCSA) |
| Date:* | 2015-09-08 |
| Contact:* | Weixiang Shao, ZTE Corporation, shao.weixiang@zte.com.cn |
| Reason for Change/s:* | Add introduction about 3GPP MTC features |
| CR against: Release* | Rel-2.0 |
| CR against: WI* | Active / WI-0037 MNT Maintenance / < Work Item number (optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | oneM2M-TR-0024-v0.0.1 |
| Clauses/Sub Clauses* | 2.2, 5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The CR Proposes to add introduction about 3GPP MTC features: Architecture enhancements for service capability exposure (AESE), Monitoring Enhancements (MONTE), Support High Latency Communications (HLCom), Group based Enhancements (GROUPE).

### -----------------------Start of change 1-------------------------------------------

# 2	References

## 2.2	Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[i.2] 	3GPP TR 23.708 V13.0.0: " Architecture enhancements for service capability exposure"

[i.3] 	3GPP TR 23.789 V13.0.0: "Monitoring Enhancements"

[i.4] 	3GPP TR 23.709 V13.0.0: "Study on Optimizations to Support High Latency Communications"

[i.5] 	3GPP TR 23.769 V13.0.0: "Group based Enhancements"

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

# 5	Introduction to 3GPP Service Capability Exposure

## 5.1	3GPP MTC features

## 5.1.1	Architecture enhancements for service capability exposure

3GPP TR 23.708 V13.0.0 [i.2] studies and evaluates architecture enhancements for a service capability exposure framework wherein 3GPP system provided service capabilities are exposed via one or more standardized APIs, e.g. the OMA-API(s).

The Service Capability Exposure Function (SCEF) provides solutions for different key issues:

    - Support for setting up an AS session with required QoS

    - Support for changing the chargeable party at session set-up or during the session

    - Support of 3rd party interaction on information for predictable communication patterns

    - Support for informing a 3rd party about potential network issues

    - Support for 3GPP resource management for background data transfer

## 5.1.2	Monitoring Enhancements

3GPP TR 23.789 V13.0.0 [i.3] studies and evaluates architectural enhancements required for 3GPP systems to provide monitoring service capability.

Monitoring is intended for monitoring of configured events. This comprises of means that allow for activating monitoring of specific events, the event detection and the reporting to authorised users, e.g. for use by applications or logging. For MTC Devices, it is desirable that the network detects and reports events (including location) caused by those. If such an event is detected, the network might be configured to perform special actions, e.g. limit the access or reduce the allocated resource. The Service Capability Exposure Function (SCEF) supports function of configuration of events and reporting of events.

## 5.1.3	Support High Latency Communications

3GPP TR 23.709 V13.0.0 [i.4] captures the study result of possible system enhancements to support applications that communicate with devices that are not reachable for a long period over the 3GPP IP connectivity and being able to support large number of such devices in the system without negatively affecting the system performance.

5.1.4	Group based Enhancements3GPP TR 23.769 V13.0.0 [i.5] studies and evaluates architectural enhancements required for Group based features.

Solutions for issues:

  - Solutions for group level NAS congestion control (internal 3GPP function – no action by oneM2M)

  - Solutions for message delivery for a group of devices using MBMS

  - SCS/AS uses an API to the SCEF to access MBMS services

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?