| CHANGE REQUEST |
| --- |
| Meeting:* | ARC#19.0 |
| Source:* | ZTE Corporation (CCSA) |
| Date:* | 2015-08-28 |
| Contact:* | Weixiang Shao, ZTE Corporation, shao.weixiang@zte.com.cn |
| Reason for Change/s:* | Add introduction about 3GPP MTC feature: GROUPE |
| CR against: Release* | Rel-2.0 |
| CR against: WI* | Active / WI-0037 MNT Maintenance / < Work Item number (optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | oneM2M-TR-0024-v0.0.1 |
| Clauses/Sub Clauses* | 2.2, 5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The CR Proposes to add introduction about 3GPP MTC feature: Group based Enhancements (GROUPE).

### -----------------------Start of change 1-------------------------------------------

# 2	References

## 2.2	Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[i.5] 	3GPP TR 23.769: "Group based Enhancements"

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

# 5	Introduction and analysis to 3GPP Service Capability Exposure

## 5.1	3GPP MTC features

## 5.1.4	Group based Enhancements

3GPP TR 23.769 [i.5] studies and evaluates architectural enhancements required for Group based features.

- Key Issues and Solutions:Message delivery to a group of devices

  - Group message delivery using MBMS is more suitable to deliver group messages to large numbers of group members in a particular geographical area. The BM-SC (Broadcast Multicast Service Centre) allocates a TMGI (Temporary Mobile Group Identity) for a specific MBMS user service. The SCEF is connected to the BM-SC. SCS/AS provides the content to be broadcasted and additional information to SCEF, SCEF needs to support the group messaging functionality. This solution has limited applicability and does not support all the scenarios, e.g. UEs not supporting MBMS, UEs located on areas where MBMS is not deployed. For such scenarios where the UE cannot receive messages via MBMS, message delivery may occur via unicast communication, e.g. via user plane or via the methods using SMS.

- Selection of delivery mechanisms for messaging to a group

  - It has been decided that the SCS/AS is responsible for making selection decisions.

- Group-specific NAS Level Congestion Control

  - Solution: NAS Level Congestion Control based on APN and group identifier. A 3gpp internal group identifier internal-group-id is used. It is part of the subscriber data in the HSS and is sent by the HSS to the MME/SGSN as part of normal EPS signalling. The UE is not aware of the Group identifier such that no modifications on the UE are required. It is lightweight, but still offers flexibility to block either mobility management or session management signalling depending on how to best address the current congestion situation with minimal impact on other UEs and services.

- Group based addressing and identifiers

  - Group membership can be static or can evolve dynamically, with group members being added and/or removed during the lifetime of a group. The Service Capability Server (SCS) / Application Server (AS) can create new groups with associated group members, and can remove existing groups. SCS/AS specific groups are identified by External-Group-IDs. HSS add or remove an Internal-ID from a group that the HSS maintains.SCEF may contain internal functionality related to a group of users, e.g., a Group Management Function (GMF). Through this internal function, the SCEF can maintain a local copy of the binding of the Internal-IDs (e.g. IMSI) and External-IDs (e.g..MSISDN) of group members with the group's Internal-Group-ID and External-Group-ID and other information needed for the delivery of group services.

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?