| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 19.0 |
| Source:* | Gemalto |
| Date:* | 2015-08-28 |
| Contact:* | François Ennesser, Gemalto, francois.ennesser@gemalto.com |
| Reason for Change/s:* | Section 11 of TS-0001 is not fully aligned with TS-0003. |
| CR against: Release* | Release-2 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 V2.3.0 |
| Clauses/Sub Clauses* | 11.1, 11.2.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: ARC-2015-2091 NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

Discussions around App-ID following contribution TP-2015-0735 concluded that in light of the current state of TS-0003 (Release 1), some text in section 11 of TS-0001 should be clarified.

This document is the Release 2 mirror of the Release 1 CR and does not attempt to take into account possible Release 2 enhancements to TS-0003 (further alignments may be needed to reflect Release 2 evolution of TS-0003).

### -----------------------Start of change 1-------------------------------------------

## 11.1	Enrolling M2M Nodes and M2M Applications for oneM2M Services

Though M2M Nodes in the field domain are assumed to communicate without human involvement, individuals or organizations remain responsible for setting the access control policies used to authorize their M2M Nodes to access M2M services. In the following text, M2M Nodes refers to M2M field nodes.

In particular, individuals or organizations acquiring M2M Nodes can subscribe to a contract with an M2M Service provider (M2M Service Subscription) under which they enrol their M2M Nodes (e.g. using identifiers pre-provisioned on the nodes, such as Node-ID). This in turn may require an M2M Service provisioning step (including Security provisioning) that takes place on the target M2M Nodes themselves, for which interoperable procedures are specified by oneM2M (see clause 11.2.1). Following M2M service provisioning, the nodes can be identified and authenticated for association with an M2M Service Subscription, whose properties reflect the contractual agreement established between their owner and the M2M Service Provider.

Similarly, it may be possible for an M2M Service Provider to mandate that an M2M Application accessing M2M services be associated with a security credential used to authorize specific operations to instances of that M2M Application, i.e. AEs (see clause 11.2.2). This step facilitates the deployment and management of M2M Applications that are instantiated in great numbers, as it enables all instances of an M2M Application to be managed through common security policies that are set once for all. It also enables keeping control over M2M Applications issued by untrusted sources.

The above steps may be delegated to an M2M trust enabler, when this role is not assumed by the M2M Service Provider.

### -----------------------End of change 1 ---------------------------------------------

### -----------------------Start of change 2 -------------------------------------------

### 11.2.2	M2M Application Enrolment

This procedure is an optional step that enables the M2M SP and/or M2M Application provider to control which M2M Applications are allowed to use the M2M services. It assumes that the M2M Application is associated to a credential used for controlling authorization and that its intended access rights be provisioned in the M2M Service Subscription. The security credential associated with the App-ID or AE-ID may be used to grant specific authorization to M2M Application instances to access an approved list of M2M services, or revoke access to all instances of undesirable M2M Applications. Such authorization shall take place between registrar CSE and AE as specified in the present document and the oneM2M Security Solutions Technical Specification [2].

### -----------------------End of change 2 ---------------------------------------------